Jet Reconstruction and
Energy Scale Determination
in ATLAS
Ariel Schwartzman
3rd Top Workshop: from the Tevatron to ATLAS
Grenoble, 23-Oct-2008

---
Outline
ATLAS Calorimeters
Calorimeter signal reconstruction:
Towers
Topological clusters
Jet energy calibration techniques:
Monte Carlo cell energy density and layer weighting
Data driven in-situ calibration
High pT jet calibration methods
Semi-leptonic b-jet energy scale
Light quark jet calibration using top quark events
Tracking input to jet reconstruction

---
ATLAS Calorimeters
Non-compensating:
  e/h ~ 1.4
%eta = 1.3 %eta = 0.8 %eta = 1.8 %eta = 3.2
abs %eta < 4.9
200,000 channels
%DELTA%eta %DELTA%phi_{barrel} = (0.003 x 0.1) (0.025 x 0.025) (0.05 x 0.025) 1.375 < abs %eta < 3.2 abs %eta < 1.4 3.2 < abs %eta < 4.9
EM Calorimeter:
  LAr/Lead, fine granularity:
  Central: (3 layers)
  EndCap: (3 layers)
  Forward: (1 layer, LAr/Copper)
  26-36 radiation lengths.
%DELTA%eta %DELTA%phi sim (0.1 x 0.1) - (0.2 x 0.1) abs %eta < 1.7
Hadronic Calorimeter:
  Iron/scintillator tiled readout
  3 depth segments
  Barrel:
  EndCap: Lar/Copper: 4 layers
  Forward: Lar/Tungsten: 2 layers
  7-9 interaction lengths.

---
Calorimeter Signal Reconstruction (I)
Calorimeter Towers:
  Cells are projected onto a fixed grid
  in pseudo-rapidity and azimuth.
  Tower bin size:
   All cells are used, weighted by
   geometric factors.
   Noise compensation via re-summation:
 Negative signal towers are merged with positive energy neighbor
 towers within DR<0.35 until the total proto-tower energy is above 0.
 Isolated negative energy towers are dropped.
%DELTA%eta %DELTA%phi = 0.1 x 0.1

---
Calorimeter Signal Reconstruction (II)
abs E > 2 %sigma_{noise}
Topological Clusters:
Taking advantage of the fine ATLAS
calorimeter granularity, build
3-dimensional clusters:
Find seeds cells with energy
significance |S| > 4
Add all neighboring cells with |S|>2
Add direct neighbors with |S| > 0
Split clusters with more than one
local maxima.
Topological clusters can serve as input to jet
algorithms and also provide alternative
noise suppression for towers.
4/2/0 clustering

---
Calorimeter Jet Calibration
Two different approaches:
Global calibration: particle level jet energy calibration
Monte Carlo based:
Calorimeter cell energy density weighting
Calorimeter layer energy weighting
Data based:
in-situ calibration using physics processes: minimum bias,
photon+jet, di-jets) (similar to DZero approach)
Light jet energy scale from W→jj in Top events.
Local calibration: calibration of calorimeter clusters
Monte Carlo based:
Attempt to separate EM from HAD clusters and
apply individual corrections, before jet reconstruction.
Additional jet-level energy scale correction required.

---
Cell Energy Density Calibration (I)
Use cell energy density as an estimator of the electromagnetic/
hadronic components of jet showers:
EM showers are characterized by high energy density depositions.
Hadronic showers are broader and less dense.
Cells with low energy density indicate hadronic signals in a
non-compensating calorimeter:
Weight low energy density cells by a factor of the order of e/π
High energy density cells receive a weight ~ 1.0
Weights are derived using Monte Carlo QCD events:
cell weights are parametrized and optimized with respect to the
truth particle jet energy, accounting for non-compensation and
correcting for dead material and out-of-cone.
Additional corrections are needed to restore the jet energy scale.
[Technique inspired by H1]

---
Cell Energy Density Calibration (II)
Determine a set of cell weights, depending on calorimeter region
(cell location) and cell energy density ρ = Ecell/Vcell.
Match reconstructed 0.7 cone jets with their corresponding particle
jets and adjust the weights such that the reconstructed jet
energy, on average, is identical to the particle jet energy and the
energy resolution is optimized:

---
Layer Weighting Technique
Hadronic showers start to develop in the EM calorimeter, and extend
to the hadronic layers, whereas EM particles are completely contained
within the EM layers.
Introduce longitudinal weighting such that hadronic showers are
treated as electromagnetic/hadronic in nature as they develop in
the calorimeter.
In order to account for the event-by-event fluctuations of the EM
content of the hadronic showers, the longitudinal weights are derived
in three bins of EM fraction (pT dependent).
Weights derived from QCD Monte Carlo simulations.

---
Global Jet Calibration Performance (I)
Cone 0.7 Jets, |η|<0.7
Cone 0.7 Jets, E = 1TeV
Cell weights
Cell weights
Layer weights
Layer weights
EM scale
EM scale
Jet energy response linearity within 2% as a function of jet pT
and Eta.
Weights are derived from Monte Carlo and applied to Monte Carlo:
restoration of scale by construction.

---
Global Jet Calibration Performance (II)
Cone 0.7 Jets, 0.7<|η|<1.5
Cone 0.7 Jets, |η|<0.7
EM scale
EM scale
Layer weights
Layer weights
Cell weights
Cell weights
~25% jet energy resolution improvement @ 100 GeV
Cell energy density weighting results in slightly better resolution
than layer weighting, but its performance may be more sensitive
to pile-up and Monte Carlo modeling of hadronic showers.

---
Local Hadron Calibration (I)
Calibrate calorimeter cluster signals to the hadronic scale,
independently of the jet context. Pure Monte Carlo technique,
based on the average response of GEANT 4 single pion simulations.
1- Electromagnetic/hadronic cluster classification:
- cluster depth location, energy density, direction, and energy.
- assumes 2/3 of pions are charged.
- 90% (50%) tagging efficiency of charged (neutral) pions @ 5 GeV.
2- Out-of-cluster corrections:
- compensate for energy not deposited inside clusters due to noise
  suppression thresholds during clustering.
3- Dead material corrections.
4- Jets are built from hadronic calibrated clusters.

---
Local Hadron Calibration (II)
Final jet energy scale correction is needed to account for out-of-cone energy, cluster misclassification, and jet specific effects.

---
In-situ Jet Energy Calibration (I)
Validation/Corrections of Monte Carlo based calibration methods.
Data driven determination of the jet energy scale (similar to DZero)
Different corrections for
tower and cluster jets.
Cell response equalization in phi at fixed eta and layer
and normalization of response as a function of Eta.
Average subtraction of the jet energy not originating from
the hard scatter interaction.
Jet response normalization in Eta.
(tag and probe di-jet balance)
Absolute hadronic jet energy scale. Z/γ+jet balance, MPF.

---
In-situ Jet Energy Calibration (II)
Equalization of the jet energy response in pseudo-rapidity
di-jet pT balance:
Tag jet in central calorimeter region
Probe jet back-to-back
A = {p^{tag}_T - p^{probe}_T} over { (p^{tag}_T + p^{probe}_T)/2}

---
In-situ Jet Energy Calibration (III)
Absolute energy scale determination:
Missing ET Projection Fraction:
  (DZero approach): balances photon
  against the hadronic recoil measured
  by towers.
Cone 0.4 Jets
MPF measures the hadronic response
relative to that of the photon:
R_recoil over R_tag = 1 + {MET . hat n_tag} over {p^{tag}_T}
MPF method requires good understanding of missing ET and additional
out-of-cone showering correction.
Alternative approach for early data: Z/γ+jet balance:
needs Monte Carlo to correct to particle level.
EM scale

---
High pT Jet Calibration
Track angle method:
based on the correlation
between track ΔR and jet pT.
Multi-jet pT balance:
Use low pT jets to
calibrate high pT jets:
  Relative response calibration
  using calibrated low pT jets.
Jet 1
Jet 2
Jet 3

---
Semi-leptonic b-jet Energy Scale
Monte Carlo based correction for
b-jets containing muons.
Correction derived after the hadronic
jet energy scale, to account for the
missing neutrino energy.
Parametrized as a function of the
fraction of transverse momentum
carried by the muon:
Jet |η|<1.2
Jet |η|<1.2
p^{jet+%mu}_{T, corr} = [C(x)]^{-1} p^{jet+%mu}_{T, reco} x = p^{%mu}_{T, reco} over p^{jet}_{T, reco}
Response

---
Jet Energy Scale from W→jj (I)
Take advantage of the large top quark production cross section at
the LHC to calibrate the light quark jet energy scale in-situ, from
hadronic W decays.
Select events by requiring high missing ET, one high pT isolated
lepton, and at least four jets, two of them b-tagged.
Purity between 65% and 80% depending on the number of
jets (2, ≥2) and the minimum jet pT (20GeV-40GeV)
Expect ~7000 (1200) W→jj pairs
in 1fb-1 of data with loose (tight)
selections.
Two techniques:
   1- Iterative rescaling method:
  2- Template method
E^{corr} = K(E)E
M^{PDG}_{W} = sqrt{K(E_1)K(E_2)} M_{jj}
Combinatorial
background
Exactly 4 jets, pT>40GeV

---
Jet Energy Scale from W→jj (II)
Template method:
build di-jet invariant mass templates with two parameters:
overall jet energy scale (α)
relative jet energy resolution (β)
fit histograms to data.

---
Tracking Input to Jet Reconstruction
Program to use tracking information
to improve calorimeter jet energy
reconstruction and resolution
New approach, conceptually
different from energy flow
techniques:
Jet energy resolution of
non-compensating calorimeters is
driven by the jet-to-jet fluctuations
in the EM content of the hadronic shower:
  Use tracks to extract information about jet topology and fragmentation,
  and correct jet response as a function of (track) jet particle composition
Track multiplicity
Charged E fraction
Track-Jet width
 Pt leading track
  (improved energy
   resolution, hadronic
   flavor tagging)
Jet-Vertex E Fraction
   (pile-up energy
    correction,
    vertex selection)
muons
calo-clusters
(b-jet energy
measurement)

---
Track-based Jet Calibration
40GeV < pT < 60GeV
Jet energy scale calibrates the average
energy response: <Rjet>(pT,η) = 1
Improve jet resolution by accounting for the
jet-to-jet response dependence on the ratio
of charged to total transverse momentum.
Correction applied after cell weighting calibration
Cone 0.4 Jets, |η|<0.7
ftrk = {sum{p^{trk}_T}} over {p^{jet}_T}

---
Summary
Several techniques for jet calibration in ATLAS:
In-situ data-driven techniques for initial jet energy scale
determination, including W→jj from semi-leptonic tt events.
Monte Carlo based techniques to improve jet energy resolution:
Cell energy density weighting
Layer weighting
 Local hadronic calibration
Track-based corrections to further improve jet energy resolution
based on jet-by-jet fragmentation properties.
Experimental program to feedback knowledge on detector
back to Monte Carlo to improve jet calibration.