## Slide 1
R. Garoby
https://indico.in2p3.fr/conferenceDisplay.py?confId=10090
2nd ESSnuSB Open Meeting
CERN 26-27 May 2014
SPL R&D and ESSnuSB

## Slide 2
Status of the SPL
Low energy n Superbeam option
Pending issues & synergies with ESSnuSB

## Slide 3: SPL main characteristics
 | Option 1 | Option 2
Energy (GeV) | 2.5 or 5 | 2.5 and 5
Beam power (MW) | 2.25 MW (2.5 GeV) or 4.5 MW (5 GeV) | 5 MW (2.5 GeV) and 4 MW (5 GeV)
Protons/pulse (x 1014) | 1.1 | 2 (2.5 GeV) + 1 (5 GeV)
Av. Pulse current (mA) | 20 | 40
Pulse duration (ms) | 0.9 | 1 (2.5 GeV) + 0.4 (5 GeV)
2 ´ beam current Þ 2 ´ nb. of klystrons etc .
Re-use of LEP RF components in Front-end (Linac4)
Ion species H−
Output Energy 5 GeV
Bunch Frequency 352.2 MHz
Repetition Rate 50 Hz
High speed chopper < 2 ns
(rise & fall times)
Required for muon production (Neutrino Factory)
Required for flexibility and low loss in accumulator
Required for low loss in accumulator
General features
Options
n facility
RIB facility

## Slide 4: SPL potential front end: Linac4!
Doubled beam brightness for LHC luminosity: reduced space charge (factor 2 in bg2 ) with a higher PSB injection energy
Long term reliability using modern design, (concerns for Linac2 vacuum ).
Flexible operation and reduced loss with new technologies (chopping, H- injection).
Higher intensity for non-LHC users.
Prepare for a possible high-intensity upgrade (neutrino facility).
New 160 MeV H- linear accelerator, will replace Linac2 as injector to the PS Booster.
First step of the LIU upgrades.
Bunch Frequency 352.2 MHz
Max. Rep. Frequency 2 Hz
Max. Beam Pulse Length 0.4 ms
Max. Beam Duty Cycle 0.08 %
Chopper Beam-on Factor 65 %
Chopping scheme: 222 transmitted /133 empty buckets
Source current 80 mA
RFQ output current 70 mA
Linac pulse current 40 mA
Tr. emittance (source) 0.25 p mm mrad
Tr. emittance (linac exit) 0.4 p mm mrad
Max. repetition frequency for accelerating structures 50 Hz
Test stand
(Construction Project started in January 2008)
Notes: No space for energy upgrade – parallel to the present Linac2

## Slide 5: Linac4
CCDTL
PIMS
3MeV
50MeV
103MeV
160MeV
Length: 80 m
19 klystrons [13 x 1.3 MW (LEP), 6 x 2.8 MW (new)]
Normal conducting accelerating structures of 4 types: RFQ, DTL, CCDTL, PIMS
Single frequency: 352.2 MHz
Duty cycle: 0.1% phase 1 (Linac4), 3-4% phase 2 (SPL), (design: 10%)
H- ion current:
40 mA (avg.),
65 mA (peak)
CHOPPER
RFQ
H-
3MeV
45keV
DTL
Drift Tube
Linac
18.7 m
3 tanks
1+2 klystrons
4.7 MW
111 PMQs
Pi-Mode Structure
22 m
12 tanks
4+4 klystrons
~12 MW
12 EMQuads
Cell-Coupled Drift Tube
Linac
25 m
21 tanks
7 klystrons
7 MW
21 EMQuads
Chopper
& Bunchers
3.6 m
11 EMquad
3 cavities
Radio
Frequency
Quadrupole
3 m
1 Klystron
550 kW
RF volume
source
(DESY)
45 kV
Extrac.

## Slide 6: SPL block diagram
SC-linac [160 MeV ® 5 GeV] with ejection at intermediate energy
Medium beta cavities: b = 0.65
High beta cavities: b = 1
“Up-to-date” CDR to be published in 2014
Length: ~500 m
Medium b cryomodule
High b cryomodules
Ejection
20 x 3
b=0.65 cavities
10 x 8
b=1 cavities
13 x 8
b=1 cavities
2.5 GeV
Debunchers
5 GeV – 4 MW
High b cryomodules
From Linac4
0 m
0.16 GeV
129 m
0.73 GeV
280 m
2.5 GeV
505 m
5 GeV

## Slide 7: SPL cavities development
Medium beta cavities b = 0.65
  1 designed and ordered from industry by IPN Orsay (Guillaume Olry et al.) to be tested in 2014 at CEA Saclay in vertical cryostat and later in Cryho-lab (Horizontal test cryostat)
High beta cavities b = 1
  1 designed and ordered from industry by CEA Saclay (Guillaume Devanz et al.) to be tested in 2014 at CEA Saclay in vertical cryostat and later in Cryho-lab (Horizontal test cryostat)
  5 designed and ordered (4 from industry, 1 from CERN workshop) by CERN for tests at CERN (SM18) in Short cryo-module of 4 cavities
Collaboration with ESS (Lund) with contributions from IN2P3 and CEA and support from the E.U.

## Slide 8: Niobium cavities from industry (RI)
4 Niobium cavities fabricated and delivered by RI (December 2013)

## Slide 9: Niobium cavities at CERN
Tooling for EB welding of Nb cavity is fabricated.
cavity fabrication at CERN
Repair of first monocell
Material defects observed after electro-polishing.
Repaired with new e-beam welding machine from outside (W#1 and W#3) and inside (W#2)
Half-cells and beam tubes fabricated by spinning.
RF measurements.

## Slide 10: Electro-Polishing (EP)
Cathode and tooling manufacturing
Improve main pump flow control and compressed air connection
Allow crane direct acces to the electropolishing hut
- Monocell TESTS:
A second set of electropolishing sessions were done to bring the total removed thickness to 200 microns.
It was possible to set different working temperatures and compare them with the simulation data
Working at lower temperatures results in less pitting.
Cavity is currently undergoing RF test
Paper TUP047 bat SRF with all multiphysics simulation details
Temperature | Total current inward / A | 
 | Simulation | Real cavity
10 °C | 21 | 18
15 °C | 37 | 36
25 °C | 70 | 57
- 5 Cell electropolishing preparation:
Tooling for EP

## Slide 11: Helium tank
Helium tank designed by CERN (Stainless steel).
5 items under fabrication by CEA (with SDMS).
Stainless Steel He tank (CEA)

## Slide 12: RF tests on couplers at CEA
CEA test bench with
two SPL cylindrical window couplers,
Double Walled Tubes and Test Box cavity
Test of RF couplers (CEA)
Cylindrical
window
Disk
window
Development of
two types of couplers

## Slide 13: Cryomodule
Cavity
Helium tank
Inter-cavity
support
Thermal shield
Vacuum vessel
RF coupler
Thermal shield tie-rod
Cold-to-warm
transition
Magnetic shielding
Insulation vacuum
relief plate
Cryogenic circuit
burst disk
Gate valve
Two-phase pipe
Cavity tuner
Double-walled
tube
He phase separator
Cryogenic lines port
Assembly of supporting system mock-up
Inner part of supporting system mock-up
Collaboration with ESS (Lund) with contributions from IN2P3 and CEA

## Slide 14: Tests systems and cavity reception area (Bdg. 252)
Cell-by-cell tuning system with RF bead-pull and mechanical measurements.
Cavity tuner: measurement of cavity detuning versus mechanical deformation.
Tooling for test in vertical cryostat: fabricated and available at CERN
Reception area in bdg.252

## Slide 15: SM18 Assembly & cryogenic infrastructure
Cryogenics
  New cryogenic transfer line: commissioned December 2013
  Modification of 2 Vertical Cryostats for 2K Operation: completed March 2013
  Specifications of He distribution for Horizontal Cryostats (2K and 4.5 K operation) completed
SRF processing infrastructure
  Main Clean Room Upgrade and Extension: to be finished in December 2013
  Ultra-Pure Water Station delivered and commissioned: October 2013
  Rinsing Cabinet delivered: October 2013
  Diagnostics
    2nd sound measurement by OSTs: operational (more work required for interpretation…)
    Temperature mapping system for SPL cavities: work in progress…

## Slide 16: SM18 RF infrastructure
Valve box
RF
distribution
Cryo line interface
Cryo-module
1.5 MW Thales klystron – Mid-2014
Klystron modulator – Delivered May 2014
New Low Level RF at 704 MHz – End 2014

## Slide 17: High Power IOT development (704 MHz)
    Two 1.5 MW IOTs being ordered by ESS
    Test set-up in preparation at CERN
    Full characterization in 2015-2016 (joint ESS-CERN)
Collaboration with ESS (Lund)

## Slide 18: SPL R&D schedule
2014
2015
Preparation of components
Assembly of CM
Start of test of string of four
b =1 cavities in a short cryo-module

## Slide 19
Status of the SPL
Low energy n Superbeam option
Pending issues & synergies with ESSnuSB

## Slide 20: Arguments for a linac-based proton driver
1. Safe and proven set-up
There is no doubt that an sc linac can be built to reliably deliver multi-MW of beam power up to 4-8 GeV. Proof of existence is given by SNS.
2. Acceleration up to a few GeV in a single machine
Accelerating up to the final energy in a linac avoids beam transfers and guarantees very low beam loss in the accelerator itself.
3. “Easy” ring(s)
Synchrotron(s) is (are) needed to transform the long linac pulse (nx100 ms) into shorter pulse(s). It is however much simpler than an RCS because of:
- no space charge
- no need to accelerate ( CW power supply and magnets, ordinary vacuum chamber, simpler RF system, no capture loss…)
- ~no time for instabilities to develop.

## Slide 21: Linac-based proton driver: principle [1/2]
SPL-based 5 GeV – 4 MW proton drivers have been designed [SPL + 2 fixed energy rings (accumulator & compressor)] which meet these requirements
References:
  SPL based proton driver/ R. Garoby, talk at NuFact06, http://nufact06.physics.uci.edu/Workshop/Slides/RGaroby_SPL3_Pdriver.ppt
  Feasibility Study of Accumulator and Compressor for the 6-bunches SPL-based Proton Driver / M. Aiba, CERN-AB-2008-060
  A first analysis of 3-bunches and 1-bunch scenario for the SPL-based Proton Driver / M. Aiba, CERN-AB-Note-2008-048-BI
  Beam Stability in the SPL Proton Driver Accumulator for a Neutrino Factory at CERN / E. Benedetto, http://nufact09.iit.edu/wg3/wg3_benedetto-splstability.ppt, to be published
  SPL-based Proton Driver for a Neutrino Factory at CERN, M. Aiba, E. Benedetto, R. Garoby, M. Meddahi, poster nb.25 (this workshop)
Parameter | Basic value | Range
Beam energy [GeV] | 10 | 5 - 15
Burst repetition rate [Hz] | 50 | ?
Number of bunches per burst (n) | 4 | 1 – 6 ?
Total duration of the burst [ms] | ~ 50 | 40 - 60
Time interval between bunches [ms] (tint) | 16 | ~ 50/(n-1)
Bunch length [ns] | 2 | 1 - 3
Specifications
(from ISS report)

## Slide 22: Linac-based proton driver: principle [2/2]
Beam accumulation
  Accumulator ring
        Charge exchange injection
        ~nx100ms accumulation time
        Isochronous (h=0): beam frozen longitudinally to preserve Dp/p
        No RF (=> minimum impedance)
        1-6 bunches of ~120 ns length
Bunch compression
  Compressor ring
        Large RF voltage (large stored energy & minimum RF power) (=> bunch rotation on stored energy)
        Large slippage factor h => rapid phase rotation in few x10ms,
        ~2ns rms bunch length @ extraction to the target (=> moderate DQ because of dispersion)
Synchronization between rings
  - Ratio of circumferences guaranteeing correct positioning of successive bunches inside the compressor without energy change in any ring

## Slide 23
Generation of 6 bunches [1/4]
SPL
Accumulator

## Slide 24
Accumulation | Duration = 400 ms | 
Compression | t = 0 ms | 
 | t = 12 ms | 
 | t = 24 ms | 
 | t = 36 ms | 
 | etc. until t = 96 ms | 
Accumulator
[120 ns pulses -
60 ns gaps]
SPL beam
[42 bunches -
21 gaps]
Compressor
[120 ns bunch -
V(h=3) = 4 MV]
Target
[2 ns bunches – 6 times]
Generation of 6 bunches [2/4]

## Slide 25: Bunch rotation (case of 6 bunches) [3/4]
from M. Aiba

## Slide 26: Main Parameters (case of 6 bunches) [4/4]
from M. Aiba

## Slide 27: Synchrotons lattices (6 bunches)
from M. Aiba
ACCUMULATOR
COMPRESSOR

## Slide 28: Charge exchange injection
from M. Aiba

## Slide 29: Foil lifetime
From M. Aiba
Inelastic scattering results in permanent damage to the foil
… with the proposed model, foil lifetime is ~6 times lower than estimated
with elastic scattering only !
Need to actively develop laser-based stripping
Need to pursue the analysis and improve the model

## Slide 30: Beam delivery on 4 targets & horns
Principle:
Use of 2 bipolar kickers (or bipolar pulsed magnets): ± 45˚ rotation wrt the z axis
K1 (K2) deflects to D1 and D3 (D2 and D4)
Need of 1 compensating dipole per beam line (1 angle for each target):
  Apply a symmetry in the system
Angle of deflection (rad)
Kinetic energy
(GeV)
Magnetic length (m)
Magnetic field (T)
2000mm
T1
T2
T4
T3
z
3D view
side view
E. Bouquerel – IPHC, EUROnu meeting, March 27, 2012
>>KEY PARAMETER<<

## Slide 31: Collective effects [1/6]
6-bunches scenario (the CERN baseline)
  Accumulator ring
        Isochronous (h=0), no RF, ~400ms, beam frozen longitudinally to preserve Dp/p
        6 bunches, 120 ns total bunch length
  Compressor ring
        rapid phase rotation in ~36ms, strong RF, large slippage factor h
        ~2ns rms bunch length @ extraction to the Target
Fast (t<400ms) instabilities may arise in accumulator
No synchrotron motion to stabilize
Collective effects studies aim at:
  quantifying the risk of instabilities
  finding cures
  setting limits to the machine impedance
From E. Benedetto

## Slide 32: Collective effects [2/6]
EM interactions of the beam with the environment
→ wake-fields(t) & impedances(w)
In the transverse plane:
  Resistive wall (beam pipe finite resistivity)
  Narrow-band resonators (RF cavities, cavity-like objects)
  Broad-Band (BB) resonator (beam-pipe discontinuities)
  Electron cloud
In the longitudinal plane:
  Narrow-band resonators (RF cavities,…)
  BB resonator (kickers & other discontin)
Mainly single-bunch
(since neglecting narrow-band)
PESSIMISTIC analysis:
  → assumed full intensity, while:
  → accumulation (400 ms): intensity going from 0 →max
From E. Benedetto

## Slide 33: Collective effects [3/6]
Localized impedance source
Analytical estimations & simulations
HEADTAIL: macroparticles code
→ G.Rumolo, F.Zimmermann, CERN-SL-Note-2002-036-AP
→ D.Quatraro, G.Rumolo et al., Proceedings PAC’09
  Impedance localized @ few positions
    transfer matrix to the next one
  Bunch sliced longitudinally
  Each slice interacts w. impedance:
    leaves a wake-field behind
    gets a kick
From E. Benedetto

## Slide 34: Collective effects [4/6]
Accumulator parameters designed to match:
  SPL incoming beam
  Compressor requirements
    for time-structure @ target
Flat bunch with smooth edges → longitud SC
Transverse emittance (not normalized)
3 p mm mrad:
→ beam size @ target
→ space-charge
→ injection foil heating
Bunch length 120ns & energy spread 5 MeV → structure @ target
-
→ M. Aiba, CERN-AB-2008-060 BI
From E. Benedetto

## Slide 35: Collective effects: conclusions [5/6]
The 6-bunch option is under control
Space Charge → OK! it guided in definition of emittance & bunch length/shape in the design
Machine impedance:
  narrow-band component → negligible (no RF-cavities)
  resistive wall → not an issue (long risetime)
  longitudinal BB → Zl/n < 4 W + error-bar (fR) (~few Ohm easily achieved in modern machines)
  transverse BB → OK! fast rising instability cured by DQ (chromaticity (|x|~ 1.3) or octupoles)
From E. Benedetto

## Slide 36: Collective effects: conclusions [6/6]
  transverse BB
    need DQ ~ 0.02, → ok for tune footprint/ resonance
    assumed Rt=1MW/m → Scaling laws with higher value of BB impedance
  e-cloud → not an issue (flat & long bunch → no multipacting)
3-bunches option as well seems feasible
From E. Benedetto

## Slide 37
Status of the SPL
Low energy n Superbeam option
Pending issues & synergies with ESSnuSB

## Slide 38: Comparison ESSnuSB vs SPL-based setup
 | SPL | ESSnuSB
Beam power | 4 MW | 5 MW
Beam energy | 5 GeV | 2 GeV
Repetition rate | 50 Hz | 14 Hz
Nb. of protons/pulse | 1014 | 1.1 10 15
Linac pulse length | 0.4 ms | 2.86 ms
Lower energy & smaller rep. rate
=> 11 x protons/pulse
Smaller rep. rate, similar linac current &
11 x protons/pulse
=> Much longer pulse length
H- generation
H- stripping
Collective effects in accumulator
Beam loss
Stress on target
Linac rep. rate and duty factor
Collective effects in accumulator

## Slide 39: Key pending issues
Linac
  H- ion source
  Beam loss management
  High power RF equipment (power supplies/modulators, Couplers…)
  Field stability in cavities (mechanical vibrations)
  Water and cryogenics cooling infrastructure
  Electrical infrastructure
  Radioprotection
Accumulator
  H- stripping
  Collective effects
  Beam loss management
  Radioprotection
Target
  Design for 360 kJ/pulse
Generic interest for the accelerator community
ESS specific
Within reach of on-going SPL coupler development
Generic interest: advanced development at CERN
ESS specific
Generic interest for the accelerator community
ESS specific

## Slide 40: Summary
Linac4 in construction. Fully operational at the end 2016.
R&D for the SPL is continuing, focused on design, construction and test of four b=1 cavities in a short cryo-module:
  Design and development of “cheap” high power couplers (8 built; 4 successfully tested today).
  Extensive investment for superconducting cavities fabrication and test (e-beam welding machine, ep bench, optical bench…)
  2 five-cell copper cavities, one bulk-niobium monocell produced,
  4 five-cell bulk Niobium manufactured by industry (RI),
  One five-cell bulk Niobium in fabrication at CERN with an R&D approach,
  Equipment for testing at high RF power (704 MHz) a string of 4 cavities cooled at 2 K in SM18
Potential future work in synergy with ESSnuSB:
  H- source (Linac4 performance and long term interest)
  Field stability in superconducting cavities (combination experiment / simulation)
  H- stripping (long term interest)

## Slide 41
THANK YOU
FOR YOUR ATTENTION!

## Slide 42
n applications of the SPL

## Slide 43: SPL-based proton driver for n physics
Conventional Superbeams
Accumulation of HP-SPL beam in a fixed energy Accumulator
(4-5 GeV, 4MW beam power)
Fast ejection onto target(s)
Low energy n beam
Medium energy n beam
Phase 1: SPS (400 GeV -700 kW)
Phase 2: HP-PS (50 GeV – 2 MW)
LP-SPL as 4 GeV injector of a High Power 50 GeV synchrotron
(50 GeV, 2 MW beam power)

## Slide 44: SPL-based proton driver for n physics
Accumulation of beam from the High Power SPL in a fixed energy Accumulator (4-5 GeV, 4MW)
Bunch compression («rotation») in a separate Compressor ring
Fast ejection of few (3-6) short (2 ns) bunches to target
Neutrino Factory