## Slide 1: Readout ASIC for SiPM detector of the CTA new generation camera (ALPS)
N.Fouque, R. Hermel, F. Mehrez, Sylvie Rosier-Lees
LAPP (Laboratoire d’Annecy le Vieux de Physique de Particules)
03/07/2014

## Slide 2: ALPS chip – bloc scheme

## Slide 3: ALPS chip– Layout sent to fabrication 03/03/2014
AMS BiCMOS 0.35µm
96 pin out
Die size:
about 3.673 X 3.298 mm2
To be tested at the beginning of June
We haven’t received it yet!

## Slide 4: Pre-amplifier
16 channels: adapted to 4x4 SiPM matrix
Principle:
  Low input Impedance about 20 ohm.
  Fast response < 5ns
  => Current mode
Dynamic range:
  From 1 up to about 2000 photoelectron (pe)
  Signal to noise ratio (SNR) > 5
  => 2 Gains
  HG covers from 1 to about 125 pe
  LG covers from 11 to about 2000 pe
  Gain ratio about 92, gain overlap 1 decade
Voltage output
Low power consumption < 30mW at this stage (from simulation)

## Slide 5: Pre-amplifier simulation (1)
Simulated SiPM signal 1pe
High gain response
t = 2.8 ns

## Slide 6: Pre-amplifier – simulation (2)
Chart: DR & Linearity
| 1 | 2 | 5 | 10 | 30 | 50 | 70 | 90 | 100 | 125 | 200 | 300 | 500 | 700 | 900 | 1000 | 1500 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000
VLG (mV) | 0.1414 | 0.2794 | 0.6979 | 1.408 | 4.383 | 7.543 | 10.84 | 14.19 | 15.86 | 20.06 | 33.53 | 51.69 | 85.13 | 114.4 | 140.3 | 152.2 | 204 | 248.6 | 343.6 | 453 | 522 | 561.9 | 587.4
VHG (mV) | 13.05 | 26.18 | 65.94 | 133.3 | 415 | 711.5 | 1017 | 1310 | 1435 | 1713 | 2151 | 2196 | 2221 | 2232 | 2237 | 2239 | 2246 | 2249 | 2254 | 2257 | 2259 | 2261 | 2263
gain_ratio | 92.2914 | 93.7008 | 94.4835 | 94.6733 | 94.684 | 94.3259 | 93.8192 | 92.3185 | 90.4792 | 85.3938 | 64.1515 | 42.484 | 26.0895 | 19.5105 | 15.9444 | 14.7109 | 11.0098 | 9.0467 | 6.56 | 4.9823 | 4.3276 | 4.0238 | 3.8526
RMS (mV) | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761
RMS = 2.08 mV
SNR = 6.2

## Slide 7: Analog sums and gain control
Weighted sum of the 16 preamp outputs by digitally controlled resistors
Each resistor has a R-2R like architecture :
  Preamp always sees the same load (better for linearity)
  8 bits resolution for gain adjustment
  Noisy channels can be digitally removed
CR shaping included in each channel
  Adjustable Vref to match the discriminator threshold
+
-
Pa_1
Pa_2
Pa_16
R1
R2
R16
Rf
Vref
Out_sum
(to discri for HG)
Schematic (principle)
Layout of 1 resistor
Custom opamp

## Slide 8: Trigger (DAC + discri)
Discriminator (full custom) :
  Dual bipolar input stage to minimize offset
  Self-biased
  Buffered digital output for trigger
10 bits DAC for threshold
  AMS standard cell
  Digitally controlled threshold
Layout
Slow control
DAC
Discri

## Slide 9
FPGA Firmeware
ALPS IC
USB connection
LabviewFPGA
ALPS chip
Inputs:
Electrically generated
Inputs:
With interface
Inputs:
Photo generated (from SiPM)
Analog Outputs
Test board- Scheme

## Slide 10: Test board- Labview Interface
ALPS Slow Control registers
DAC: overvoltage adjustment
High/low gain adjustment
DAC: discriminator threshold
ALPS Probe Registers
High gain output
Low Gain output

## Slide 11: Perspective:
Planned tests:
  Electrical tests
  Tests with false signals
  ALPS chip functionality and performance tests
  SiPM tests and measurements