## Slide 1: Revisit BG study 2010
Hiro Nakayama

## Slide 2: BG study in 2010
Need to estimate SuperKEKB background
No SuperKEKB loss simulation, no GEANT4 model at that time
Only way is to extrapolate measurement at KEKB
Extrapolation is only based on design Touschek lifetime of SuperKEKB (and assumed vacuum level)
  Shielding effect, collimator efficiency were assumed to be same
Scaling factor is different for each background source
Each background source should be measured separately
 A. Beam-size scan, B. Vacuum bump, C. luminosity scan was done
A&B: 2+1 days, by Nakayama et al
C: 3day, by C. Kiesling et al

## Slide 3: Touschek study (LER)
 | Beam size Max(4.3mm) | 3.5mm | 2.8mm | 2.2mm | Beam size Min(1.3mm)
Current Max (1450mA) |  |  |  |  | 
1100mA |  |  |  |  | 
750mA |  |  |  |  | 
Current Min (~300mA) |  |  |  |  | 
①
Mask
OPEN
② （Mask V close）
⓪
Maskを探る
③ （Mask OPEN）
④ （Mask H close）
⑥ （Mask OPEN）
⑤ （Mask OPEN）
1.6mmも取った
1.6mmも取った
Currentを変えるとBeam sizeがふらついてしまう
⑧
xy を変化
⑦ （Mask both open, varyNbunch ）
3点だけ取った
Beam size sweep by changing isizeBump
~30 minutes for each run
Notes: First, We took the data of size sweep at max current for three mask condition.
Then change current andd took data for mask open.

## Slide 4: Touschek study: LER Vopen-Hopen I=1450mA
16:23-16:49
run574 16:14:54-16:57:07
bhsm06:/h063/dstprod/dat/e000073/Rawdata/0000/energy/05/e000073r000574.raw
Event rate=427.84Hz, event num = 1043725
x6 x2

## Slide 5: Vacuum bump study: LER Vclose-Hopen 1450mA
LER(Run856)
22:26 Start
22:35 Mask set to the correct value
22:39-42 Injection, D03 ion-pump OFF
22:42 stop Injection
22:42-46 Run(D03 ion-pump OFF)
22:46 D03 ion-pump ON
22:46-56 Run(default)
22:56-23:51 Run(D02 ion-pump OFF,NEG ON)
23:30 NEG current (70%->80%)
23:51 Run stop
x2

## Slide 6: Communication with machine group
Two pre-meetings for brainstorming (April, June)
  Detailed plan for each study item
  Which tuning knob should be used for our purpose?
Studies were performed only during day shifts
  night shifts were for vacuum baking
Report at KCG (machine-detector) meeting next morning after every study

## Slide 7: Analysis of BG study data
DAQmon record(or Uehara-database)
  Specify day, hour, min, sec
  Beam life time (0 during injection)
  CDC current, TOF rate, etc..
  those stored every few seconds, sent to KEKB EPICS
Belle raw data
  Taken by Belle DAQ with random trigger
  Extract data from corresponding run
  SVD occupancy, ECL Edep

## Slide 8: a. Touschek/Beam-gas machine study
June 2010
Single beam(HER/LER only), random trigger
Vary vertical beam size to separate Touschek effect from beam-gas effect
Measure SVD,CDC,ECL background level and extrapolate for SuperKEKB based on assumptions
Sugihara(Tokyo)

## Slide 9: Extrapolation towards SuperKEKB
KEKB machine study results can be extrapolated for SuperKEKB
Extrapolation strategy
  Measure k and t at KEKB by machine study
  Assume same kTouschek, kbeam-gas, tbeam-gas at SuperKEKB
  For tTouschek at SuperKEKB, use optics simulation result
  Other BG (SR, Rad.Bhabha, beam-beam BG) are not included
I: beam current, t: life time
k: proportional constant

## Slide 10: How to measure tTouschek, tbeam-gas
Beam life(min)
CDC current(mA)
(hour)
Beam size(mm)
smaller
size
moreBG
shorter
life
1/life (min-1)
1/sy (mm-1)
1/tTouschek
1/tbeam-gas
(hour)
(hour)
Nominal
beam size
(~2um)
sy∞, Touschek 0

## Slide 11: How to measure kTouschek,kbeam-gas
CDC BG/i (mA/mA)
1/life (min-1)
1/tbeam-gas
1/tTouschek
BGTouschek
BGbeam-gas
Nominal
beam size
(~2um)
slope: kTouschek
slope: kbeam-gas
160min10min

## Slide 12: Extrapolated BG levels at SuperKEKB
CDC 400+-40 uA (cf. ~20uA@2003)
 ~120 kHz/wire or less at layer 6 or outer
60+-5 GeV/event
 wave form fitting (x1/7)  ~9 GeV/event
1300+-200 hits/event (>3000 electron)
 shorter integration time (2ms75ns)
 ~400 event/trigger, occupancy: 0.7%+-0.01% <10% (SVD2)
(estimated from SVD, >3000 electron)
 3.2M pixels in 1st layer, integration time: 20ms
 Occupancy = 1.0±0.1%
(not including low-pt tracks or <few keV gammas)
Assumptions:
Use tTouschek from optics simulation: 8.7min(LER), 15.3min(HER)
Use same tbeam-gas from KEKB machine study: 800min(LER), 3400min(HER)
Use same kTouchek, kbeam-gas from KEKB machine study
CDC
SVD
ECL
SR, QED, beam-beam BG are not included
Chart: 
| HER_beam-gas | LER_beam-gas | HER_Touschek | LER_Touschek
 | 7.9081 | 5.3662 | 139.3464 | 248.2759
LER/total: 60~70%,
Touschek/total: >90%
CDC
PXD
PXD 1st: 14mm
SVD2 1st : 30mm
Smaller results than DEPFET meeting @Valencia for SVD/PXD is due to >3000electron cut

## Slide 13: QED machine study
May 2010
Both beam colliding, random+Bhabha trigger,
Vary luminosity to separate lumi-dependent contribution
  Change vertical beam separation/vertical beam size/beam current
Measure SVD hit multiplicity
  Lumi-dependent but non-QED
  components are removed by
  correction using CDC currents.
  (we expect no QED hits on CDC)
MPI
Lumi-dependent

## Slide 14: SVD hit rate vs. luminosity
Elena (BG meeting 3rd Aug.)
  Our MC expect 1.5 hits@ 1st layer at 10/nb, while SuperB MC expect 22hits
z/phi

## Slide 15
Elena (BG meeting 3rd Aug.)
Another approach by reconstructed tracks is ongoing (A. Moll)

## Slide 16: literatures
Belle2notes for Touschek/Beam-gas study (chap. 3) https://belle2.cc.kek.jp/~twiki/bin/view/Archive/Belle2note0005
Belle2notes for QED study
https://belle2.cc.kek.jp/~twiki/bin/view/Archive/Belle2note0012 Reports at BGM, daily report slides at KCG meetings, etc https://www.dropbox.com/sh/ws2nyeju3q16jhw/AABhnahmhFyQ82lfC4mt1GZla?dl=0

## Slide 17: Remarks for phase2 planning
Phase2 is most similar to physics run situation, but still different from it
  Smaller beta function (less Toucheck, Beam-gas)
  Worse vacuum level (more Beam-gas)
  Smaller luminosity (less RBB/2-photon)
  VXD only located at phi=0 (other directions are not checked by VXD)
We still need some extrapolation (based on simulation etc..), which is different for each background source.
Disentangle each contribution is still important for extrapolation
How beast sensors can contribute to more reliable extrapolation?
Sub-detector data-taking mode should also be cared
Other purpose of phase2
  “playground” for the functions needed for physics run
  Beam abort/interlock, collimator control (incl. feedback), SuperKEKB-Belle communication, etc…
  Whole Belle DAQ, ROI finding, Injection Veto, etc…

## Slide 18: backup

## Slide 19: BG study
S.Sugihara (Univ. of Tokyo)
2010.07.01
Notes: I will report the BG study
To estimate BG of super KEKB

## Slide 20: Beam background at superKEKB
To estimate BG levels at superKEKB,
we need to know kvac,ktou, and tvacKEKB ,ttouKEKB,tvacsuperKEKB ,ttousuperKEKB
BG sources :
Touschek effect
Beam-gas scattering
(SR light)
(Radiative Bhabha)
Notes: Possible BG sources at superKEKB are touschek effect, beam-gas scattering, sinchrotron radiation, radiative bhabha scattering.
In this study, we estimate the BG from toudchek and beam-gas scattering.
Ignore the other BG
To estimate BG of super KEKB , we used this equation. This equation sais BG should be proportional to beam current over lifetime.
To estimate BG, we need to measure proportional constant and life time of current KEKb of each BG source.
For each BG source.
We measure 4 parameter and we know life time of super KEKB
We take the data of CDC current ,SVD PIN diode,TOF hit rates ,ECL hit count.

## Slide 21: Previous BG study in 2009
2009
Touschek : beam size dependence only
Vacuum : life time decrease not enough to calculate kvac
2010
Touschek :beam size dependence,
(bunch) current dependence,
N bunch dependence(LER),
mask dependence
vacuum : change vacuum level much worse
Notes: This is the results of previous BG study.
For touschek BG, we took the data of beam size sweep only.
So we took bunch current dependence , number of bunch dependence, mask condition dependence this time.
For beam-gas BG, life time decrease not enough to calculate constant for beam-gas BG last year.
So we change vacuum level worse.

## Slide 22
Touschek study
(2010/06/7-8)

## Slide 23: Movable mask settings for Touschek LER
D06/D03, H1/H2/H3/H4/V1/V2/V3/V4
H_close=12
H_open=20
V_close=physics run setting
V_open=V_close+1.0(D03V4:V_close+0.5)
Notes: This is a mask condition.
We changed the mask at D6 and D3.
Horizontal mask close ,we set the horizontal mask at 12 mm.

## Slide 24: Mask dependence(LER)
Both open
H close
V close
Current=1450mA
Horizontal masks reduce Touschek BG when vertical masks are open.
CDC current(uA)
1/life(1/min)
Notes: This is mask dependence of CDC currrent as a function of inverse size.
Red line is mask open,green s horizontal close,
This plot means, horizontal masks reduce touschek BG when vertical mask open.

## Slide 25: Current dependence(LER)
1450mA
1100mA
750mA
mask: both open
CDC current per beam curret (uA/mA)
1/life(1/min)
BG is proportional to the beam current.
1/life(1/min)
Notes: BG is proportional to the beam current.
1450
Similar BG level

## Slide 26: Nbunch dependence(LER)
Nbunch=1585(normal)
Nbunch=796(half)
Ibunch=1485mA/1585
same Ibunch
1/life (min)
1/size(1/mm)
Notes: Contaminant by injection
Even though life time is the same the N bunch changes

## Slide 27: Movable mask settings for Touschek HER
D09/D12, H1/H2/H3/H4/V1/V2/V3/V4
H_close=13 (D12H4:19)
H_open=20 (D12H4:19)
V_close=physics run setting
V_open=V_close+1.5(D09V1,D12V1:V_close+1.0)

## Slide 28: Mask dependence(HER)
Both open
H close
V close
Current=850mA
CDC current(uA)
1/life(1/min)
Negative slope
in case of H close
Notes: When beam size is large, beam hits horizontal mask (when closed) and generates more BG.
Negative slope in case of H close

## Slide 29: Current dependence(HER)
850mA
650mA
400mA
mask: both open
BG is proportional to the beam current.
CDC current per beam curret (uA/mA)
1/life(1/min)
Notes: Within 30 % error

## Slide 30: Summary(1) – Touschek
LER 1450mA
V close
When size=~2um(nominal),
1/tTou = 0.87 x 1/ttotal
1/tTouschek
1/tOther
1/size(1/um)
1/life(1/min)
When size=~1.5um(nominal),
1/tTou = 0.81 x 1/ttotal
HER 850mA
V close
1/tTouschek
1/tOther
1/size(1/um)
1/life(1/min)
Notes: This graph shows the inverse
Error of each data is error of mean at each beam size.
If beam size is smaller life of touschek become small although 1/lief_other is the same value
From this fitting , we get the life time of touschek and other BG.
Nominal beam size of KEKb is 2 um,
Inverse life time of touschek BG is 7.4 times larger than other BG.

## Slide 31: Summary(1) –cont.
CDC cur./beam cur.(mA/mA)
1/life(1/min)
Ktou=0.67(mA/mA*min)
LER 1450mA
V close
Ktou=0.89(mA/mA*min)
CDC cur./beam cur.(mA/mA)
1/life(1/min)
HER
850mA
V close
Notes: 傾き=slope
Ten to the power of fifth = 10^5

## Slide 32
Vacuum bump study
(2010/06/23)

## Slide 33
We changed vacuum level at
  D12(ion pump),D1(ion pump ,NEG) :HER
  D3(ion pump),D2(ion pump,NEG) :LER
To calculate kvac(=D BG/D(1/t)) ,
we made vacuum level much worse than 2009
(*beam energy changed from Touschek study)
Notes: LER:3.58923.6438
HER:8.20388.3286GeV)

## Slide 34: Mask settings for Vacuum bump study
D09/D12, H1/H2/H3/H4/V1/V2/V3/V4(HER)
D06/D03, H1/H2/H3/H4/V1/V2/V3/V4(LER)
H_open=20(D12H4:19)
V_close=physics run setting
Notes: This is a mask condition.
We opened Horizontal mask, annd use vertical mask of physics run setting

## Slide 35: HER vacuum
Kvac (D1)=50±(1E-4) mA*min/mA
CDC current/beam current(uA/mA)
1/life(1/min)
Current=850mA
D1 NEG
current= 850mA
Notes: K vac

## Slide 36: LER vacuum
Kvac(D2)=9.2±(3.4E-5) mA*min/mA
CDC current/beam current(uA/mA)
1/life(1/min)
D2 NEG
current= 1450mA

## Slide 37: summary
 | Kvac(CDC) | tvac | Ktou (CDC) | ttou | ttotal | CDC current
HER(KEKB) | 50 | 4275 | 0.89 | 1002 | 811 | 10.5
LER(KEKB) | 9.2 | 858 | 0.67 | 129 | 112 | 23.1
Total BG is 23 times higher than current KEKB BG.
 | Kvac(CDC) | tvac | Ktou (CDC) | ttou | ttotal | CDC current
HER(superKEKB) | 50 | 4275 | 0.89 | 10 | 10 | 262
LER(superKEKB) | 9.2 | 858 | 0.67 | 5 | 5 | 521
Total:33.6
Total:783
Same as KEKB
From latest optics simulation
From this BG study

## Slide 38: To do
Analysis for BGs on other detectors
  SVD PIN diode
  TOF rates
  ECL hit count

## Slide 39: backup

## Slide 40: Comparison with 2003
 | Ktou(LER) | Kvac(HER D1)
2003 | 0.11 | 120
2010 | 0.67 | 50
2003 vacuum bump study
Notes: If mask setting is difference, this slope changes. we are now checking the setting of 2003 setting

## Slide 41: 2009 result(Touschek)
2009.12.7 18:10-18:53(HER)
2009.12.8 15:30-16:00(LER)
1/τ min
1/τ min
1/σy mm
1/σy mm
We can see Touschek effect for both HER and LER
Ratio of touschek and others
KHER = 0.0012
KLER = 0.037
cut for fit
Notes: Touschek 効果が見えました。

## Slide 42: 2009 result(vacuum)
Life time/min
2009/12/07 19:00-21:20(HER)
CDC current/mA
Average vacuum 10-9Pa
D1
D12
Life time didn’t change enough to calculate Kvac
Notes: Beam life time didn’t change enough to calculate k_vac
Life time が変化しなかった。

## Slide 43: run summary(LER Touschek)
Run No. | time | mask | Current(mA) | sy(mm) | Ring | 
564 | 12:04-13:15 | open | 350-1450 | 1 | LER | Current sweep
567 | 15:12-15:43 | V close | 1450 |  | LER | Size sweep(1450mA Vclose)
574 | 16:23-16:49 | open | 1450 |  | LER | Size sweep(1450mA open)
575 | 17:04-17:43 | H close | 1450 |  | LER | Size sweep(1450mA H close)
576 | 18:34-19:10 | open | 750 |  | LER | Size sweep(750mA open)
577 | 19:31-19:57 | open | 1100 |  | LER | Size sweep(1100mA open)
580 | 21:05-21:28 | open |  |  | LER | Size sweep(Nbunch=half open)
584 | 22:15-22:35 | open |  |  | LER | xysweep

## Slide 44: run summary(HER Touschek)
Run No. | time | mask | Current(mA) | sy(mm) | Ring | 
594 | 12:37-13:12 | open | 850 |  | HER | Size sweep(850mA open)
595 | 13:40-14:05 | V close | 850 |  | HER | Size sweep(850mA V close)
596 | 14:40-15:01 | H close | 850 |  | HER | Size sweep(850mA H close)
597 | 15:28-15:58 | open | 400 |  | HER | Size sweep(400mA open)
598 | 16:51-17:20 | open | 650 |  | HER | Size sweep(600mA open)

## Slide 45: LER touschek

## Slide 46: Touschek study (LER)
 | Beam size Max(4.3mm) | 3.5mm | 2.8mm | 2.2mm | Beam size Min(1.3mm)
Current Max (1450mA) |  |  |  |  | 
1100mA |  |  |  |  | 
750mA |  |  |  |  | 
Current Min (~300mA) |  |  |  |  | 
①
Mask
OPEN
② （Mask V close）
⓪
Maskを探る
③ （Mask OPEN）
④ （Mask H close）
⑥ （Mask OPEN）
⑤ （Mask OPEN）
1.6mmも取った
1.6mmも取った
Currentを変えるとBeam sizeがふらついてしまう
⑧
xy を変化
⑦ （Mask both open, varyNbunch ）
3点だけ取った
Beam size sweep by changing isizeBump
Notes: First, We took the data of size sweep at max current for three mask condition.
Then change current andd took data for mask open.

## Slide 47: ① Current sweep
I: 300→1450mA
s: 1.5mm
Mask: both open
Very unstable beam size
 Difficult to see current dependence only
Beam Current
CDC current
Beam size

## Slide 48: ② Size sweep (V close)
I: 1450mA
s: 4.31.0mm
Mask: V close
hour
hour
hour

## Slide 49: ② Size sweep (V close)
I: 1450mA
s: 4.31.0mm
Mask: V close
Horizontal beam size(um)

## Slide 50
I: 1450mA
s: 1.44.2mm
Mask: V/H open
③ Size sweep (both open)
hour
hour
hour

## Slide 51
I: 1450mA
s: 4.21.0mm
Mask: H close
④ Size sweep (H close)
hour
hour
hour

## Slide 52
I: 750mA
s: 1.14.2mm
Mask: V/H open
⑤ Size sweep (@750mA)
hour
hour
hour

## Slide 53
I: 1100mA
s: 4.31.2mm
Mask: V/H open
⑥ Size sweep (@1100mA)
hour
hour
hour

## Slide 54: Mask dependence(LER TOF)
Both open
H close
V close
TOF rates(Hz)
1/life(1/min)
Notes: Vcloseを1/life=0に外挿すると、０になる。CDCも同じ

## Slide 55: HER touschek

## Slide 56: Touschek study (HER)
 | Beam size Max(3.4mm) | 2.8mm | 2.1mm | 1.7mm | Beam size Min(1.2mm)
Current Max (850mA) |  |  |  |  | 
650mA |  |  |  |  | 
400mA |  |  |  |  | 
Current Min (~200mA) |  |  |  |  | 
② （Mask V close）
⓪
Maskを探る
ibumpを探る
① （Mask OPEN）
③ （Mask H close）
⑤ （Mask OPEN）
④ （Mask OPEN）

## Slide 57: ① Size sweep (both open)
1/life
I: 850mA
s: 1.23.4mm
Mask: V/H open

## Slide 58
I: 850mA
s: 3.31.2mm
Mask: V close
② Size sweep (V close)
Negative slope?

## Slide 59
I: 850mA
s: 1.43.4mm
Mask: H close
③ Size sweep (H close)
BG increase with larger beam size?
Negative slope?

## Slide 60
④ Size sweep (@400mA)
I: 400mA
s: 4.01.0mm
Mask: V/H open
Negative slope?

## Slide 61
I: 650mA
s: 3.61.4mm
Mask: V/H open
⑤ Size sweep (@650mA)

## Slide 62: Summary (1) (touschek ,LER vclose)
LER 1450mA
Vclose
Projection,
1/size(1/um)
1/life(1/min)
Notes: This is the inverse life of LER when vertical mask close as a function of inverse size.
To fit the graph, I split the data by each beam size region ,then calculate mean and error of mean at each beam size.

## Slide 63: vacuum

## Slide 64: HER Vacuum bump
Run 854 (6/23 18:37-21:10)
I=850mA, sy=2.1um, Mask: V close
D1
Average
D1 NEG ON
SVD
CDC
TOF
CDC current =40uA, stop

## Slide 65: LER Vacuum bump
Run 856 (6/23 22:26-23:51)
I=1450mA, sy=4.2um, Mask: V close
D2
Average
D2 NEG ON
SVD
CDC
TOF
CDC current =40uA, stop

## Slide 66: Summary(LER)
 | Kvac(CDC) (mA/mA*min) | Ktou (CDC)(mA/mA*min) | tvac / ttou
HER | 50 | 0.89 | 4.3
LER | 9.2 | 0.67 | 6.7
HER : 800min 10min
LER : 110min  5min
If touschek is dominant
LER 1/t :0.00930.2
1/ttou :0.0078 0.2 1/tother 0.001165 0.001165(assumption)
BG is 23 times higher than KEKB
superKEKB/KEKB
=(0.2*0.67 + 0.001165*9.2 ) * 3600 / (0.0078*0.67 + 0.001165*9.2) * 1450
=521/23.1 = 22.6

## Slide 67: Summary(HER)
 | Kvac(CDC) (mA/mA*min) | Ktou (CDC)(mA/mA*min) | tvac / ttou
HER | 50 | 0.89 | 4.3
LER | 9.2 | 0.67 | 6.7
HER : 800min 10min
LER : 110min  5min
If touschek is dominant
HER 1/t :0.00170.1
1/ttou :0.000997 0.1 1/tother 0.000234 0.000234(assumption)
BG is 24 times higher than KEKB (HER)
SuperKEKB/KEKB
=(0.1*0.89 + 0.000234*50)*2600 / (0.000997*0.67+0.000234*50) * 850
=262/ 10.5 = 24.6

## Slide 68: Summary(total BG)
KEKB LER + HER = 23.1 + 10.5 = 33.6
SuperKEKB LER + HER = 521 + 262 = 783
23 times higher than current KEKB

## Slide 69: Worst case(injector limit)
HER : 600min 3min
LER : 110min  2min
HER
SuperKEKB/KEKB =(1/3*0.89 + 0.000234*50 ) * 2600 / (0.000997*0.67 + 0.000234*50) * 850
=801/ 10.5 = 76
LER
superKEKB/KEKB =(0.5*0.67+0.001165*9.2)*3600 / (0.0078*0.67 +0.001165*9.2) * 1450
=1245/23.1 = 54
Total
(1245+801)/(23.1+10.5) = 61