## Slide 1: ILD Mechanical structure DHCAL Barrel and Endcaps
Design, Integration & Services
J.C Ianigro
- IPN Lyon -

## Slide 2: ILD mechanical structure Contents
Barrel design
Endcaps design
Thermal studies
Services
Perspectives

## Slide 3: Barrel design
Stainless steel 1 wheel (8 mod.) 5 wheels
Weight (t): 88 t 440 t
Detectors W. (t): 36.8 t 184 t
Total Weight (t) : 124.8 t 624 t
Ext. Diameter 6770 mm
Int. Diameter 4116 mm
Lenght 4700 mm
Thickness wheel face = 10 mm
Thickness absorbers= 15 mm
Ext. Diameter : 6770 mm
Int. Diameter :4116 mm
Lenght : 940 mm
x8

## Slide 4: Barrel design
Barrel supports in the cryostat
Modification 2 modules to support on rails
Need to reduce 2 small chambers to integrate services

## Slide 5: Barrel design – Support in cryostat
Disymmetrical supports 9-15 H
Gravity and Detectors mass
Directionnal deformation axis Z (// gravity) (mm)
Max deformation : 0.34 mm for position around 9-15H

## Slide 6: Barrel design - Support in cryostat
Vision of the influence of absorbers deformation = no problem for GRPC
Directionnal deformation axis (// gravity) (mm)
Wheel Max deformation : 0.34 mm – 0.09 mm relative zone
Module Max deformation : 0.07 mm
Gravity and Detectors mass
symmetrical supports

## Slide 7: Barrel design
ECAL + TPC impact
Deformation DHCAL + ECAL + TPC = 0.4 mm max
Directionnal deformation axis (// gravity) (mm)
DHCAL with 8 x ECAL modules (8x2.5 t)
And TPC (4t)
9-15H supports
ECAL Loads on points

## Slide 8: Barrel design : wheel assembly & detectors integration
Wheel Building
Building Method
Step 1 : Module building
  48 plates welded to make a module
Step 2 : Modules assembly to wheel
  8 modules in position on specific tool
  welding and rotation
Step 3 : wheel on specific tool for transport
Welding method : EBW
Tight continuous weld
Low distortion
Narrow weld and narrow heat affected zone
Filler metal is not required
180°
1.Module building
2. Module Assembly with rotation
Collaboration with CIEMAT for test structure feasability

## Slide 9: Barrel design : wheel assembly & detectors integration
Barrel Building & GRPC Detectors insertion
Transport of GRPC with specific structure to surface building point
GRPC insertion around the 5 wheels
Connection of gaz, HT, datas and cooling for each GRPC
Services installation on each 8 spaces in zone A, ready to be connected
Zone A
Common services
Ready to be connected
GRPC insertion
with specific tool
Damper transport structure for GRPC
Notes: 9

## Slide 10: Barrel design : wheel assembly & detectors integration
Barrel Building & services connecting
Barrel insertion structure coud be divided in 5 parts screwed together
Wheels linked and services connection in 32 zones
Barrel assembly
5 wheels going down separatly on specific structure
5 wheels linked together on the barrel insertion structure
Welded barrel support structure - steel
Transport to the loading aera and area
weight = 76 t Cost : 600 K€
Notes: 10

## Slide 11: Barrel design : wheel assembly & detectors integration
Barrel Building & services connecting
Barrel with 5 linked wheels inserted
rails inside the yoke
fixation inside the yoke on both sides
services installation along the yoke to patch pannels
Barrel insertion
Services issues to patch pannels
CMS « enfourneur »
Notes: 11

## Slide 12: End caps design
Endcap
One module
Module Weight : 50 t
Detectors weight : 22.5 t
Total weight : 72.5 t
One endcap made of 4 modules
Endcap Weight : 200 t
Detectors weight : 90 t
Total weight : 290 t
Material : stainless steel
2 endcaps
8 sides -> 16 sides
Encap : 48 detectors
Welded structure
Idem barrel

## Slide 13: End caps design
One module composition
3655
2218
48 detection planes
One detection plane consisted of 4 detectors
GRPC plane : S = 8.5 m²
192 detectors
P = 467.5 Kg
P/module = 22.5 t
3153
750
750
933
493

## Slide 14: End caps design - Ring
Ring between barrel and endcap
  Placed around the ECAL endcap
8 modules
1704
2541
1092
Ring weight = 18.4 t
Module weight = 2.3 t
2xrings
Ring ( 18.4 + 8 ) + Barrel endcap (290 ) = 316.4 t
Screwed on endcap

## Slide 15: End caps design - Ring
Ring between barrel and endcap
  7 GRPC planes by modules 21/modules 168 /ring
1298
800
1006
GRPC : S = 2.55 m² P = 140 Kg
P/module = 980 Kg
432
1086
648

## Slide 16: End caps design - Ring
Endcap : GRPC insertion + support tool
Same support for Barrel wheel
GRPC insertion
with specific tool
Support structure for
One endcap made of 4 modules
Total weight : 290 t

## Slide 17: Endcaps design
Endcap deformation
  Fixed by center tube (no magnetic field)
Max deformation : 0.5 mm

## Slide 18: Thermal studies on GRPC
12 x 6 chipsets modelisation = 1/2 detector
Heat flux on chipset = 0.133 W x 72 = 9.6 W
Heat exchange with air ambient 22°C on 2 faces and 3 sides
2 absorbers steel stainless 2.5 mm
72 chipsets 1.4 mm
1 pcb plate 1.4 mm
1 spacer polycarbonate 1.4 mm
1 glass 0.7 mm
1 frame pcb 1.2 mm
1 glass 1.1 mm
Laminar flow in gap of 2 mm between GRPC and absorbers

## Slide 19: Thermal studies on GRPC
Chipset
Absorber in contact with chipset
Tmax = 26.4°C
Heat extraction on 1 side absorbers for one detector = 9.6 w (no P.P)
Air ambient is OK for a plate alone - for ILC M3 cooling placed around
Water cooling is needed for ILD Barrel – 0 W transmission to other detectors

## Slide 20: Barrel Services
Cooling Options
Low heat to extract
Big exchange surface : material with acceptable conductivity
  Leak-less water cooling : no risk for electronic and other detectors, pressure between 0,8 and 1bar (cavitation), balanced network, pneumatic activators needed
  Bi-phasic gas like CO2 : High Pressure (100 bars), expensive connexions (no leak), small diameter tubes, important exchange coefficient
  Mono-phasic gas like C6F14
  Water cooling : probably the best solution with coper plate/tubes

## Slide 21: Barrel Services
Services : Barrel
Cooling for Dif : Blue / Red
  2 loops by module
  Ø14 for principal
  Ø2 for distribution alternative
Gaz For GRPC : green / pink
  2 loops by module
  Ø14 for principal
  Ø4 for distribution alternative
  High Tension : Brown
  Ø14 for supply
  Data acquisition : Beige
  Ø14 for collecting
  Issues : 8 zones 168 x 47
47
168

## Slide 22: Endcaps Services
Services : Endcap+ring
Cooling for Dif : Blue / Red
  2 loops by GRPC
  14 for principal
  Ø2 for distribution alternative
Gaz For GRPC : green / pink
  2 loops by GRPC
High Tension : Brown
  Ø14 for supply
Data acquisition : Beige
  Ø14 for collecting
  Issues : 8 tubes outing 98 x 47

## Slide 23: ILD mechanical structure. Perspectives
Simulations have to be done in this configuration
  Endcaps deformation with magnetic field
  Yoke deformation with endcap weight
  Flow studies
Design evolution
  Interfaces optimization
  Services optimization