## Slide 1: Common DAQ
Taikan Suehara
(Kyushu University, Japan)

## Slide 2: CALICE DAQ Task Force
Members
  SiECAL – R. Cornat, F. Magniette, TS
  ScCAL – M. Reinecke, J. Kvasnicka
  SDHCAL – L. Mirabito, C. Combaret
Quasi-Monthly meeting
  10th Dec. – Kickoff
  19th Jan. – Overview of each technologies

## Slide 3: Mandate of TF
2 years
1st year: Solve the issues related to combined running with current hardware and summarize it to a document
2nd year (??): Run the combined tests

## Slide 4: Personal comparison
 | SiECAL | ScE/AHCAL | SDHCAL
Manpower | ** | *** | *
Strategy | Minimal mod | Scratch build | Minimal mod
CCC | UK original | ZedBoard | DCC
CCC clock | 50 MHz | 40 MHz | 50 MHz
8b/10b encode | yes | No | yes
BX clock (TB) | 2.5 MHz | 250 kHz | 
DIF-LDA | HDMI | HDMI | USB+HDMI
LDA | GDCC | ZedBoard | Raspberry+DCC
LDA-PC | Ethernet raw | TCP | TCP
Software | Calicoes | Labview (will be C++) | DIM (from DELPHI)

## Slide 5: Things to be considered
Common master clock frequency
  To assure simultaneous BX counting
Common BX clock frequency
BUSY treatment
 Common CCC? or just clock synchronization?
High level DAQ software (EUDAQ?)
  Run control, event building, run number, monitoring,…
Common data format (LCIO class)
Partial or optional sharing of firmware and software
etc.

## Slide 6: CALICE DAQ 3? must...
have common clock freq and master CCC
  Slave CCC can be either common or individual
can run on both ILC and TB mode?
  Needs busy treatment?
can be controlled via the same master
  Maybe EUDAQ (with modification)
can store data in consistent way
  LCIO with structure well-defined CALICE-wide
do work-sharing to live in minimal human resource!

## Slide 7: Practical combined run

## Slide 8: Si and Sc DAQ
Si CCC
SKIROC2
SPIROC2
Si DIFs
Sc DIFs
GDCC/LDA
xLDA
PC
PC
Sc CCC
Flexi cable
HDMI
Ethernet
Coaxial
Clock
Readout cycle
Spill
Sc CCC provides master clock of 50 MHz to Si CCC (Sc master clock is 40 MHz, converted)

## Slide 9: Timing chart
spill
Sc busy
Si
“spill”
~400 ms
Sc
livetime
readout
readout
“Readout cycle” number is consistent, but Si busy not considered

## Slide 10: Combined DAQ for Si + Sc
Run control
Labview
calicoes/pyrame
Sc hardware
Si hardware
Sc data
Si data
Data collector
LCIO file(s)
Event display (not finalized)
start/stop
EUDAQ
start/stop run #
Combined LCIO obtained in online DAQ

## Slide 11: Screenshot of EUDAQ
Master PC (Linux): EUDAQ + CALICOES (Silicon)
Slave PC (Windows): LabView (Scintillator)
Successfully took data for more than a week

## Slide 12: Output files

## Slide 13: To do in silicon before next Si+Sc
Analysis
  Data loss rate (seems small enough now...)
  Combined tracking
Hardware
  Supply BUSY
    Sc can be faster next time
    at least necessary in “parasitic” TB
  More layers, new layers
  UDP transfer??

## Slide 14: Si+SDHCAL: to be addressed
Common clock
  Si CCC can accept clock (50 MHz)
  SDHCAL?
BX/acq# (readout cycle) consistency
  How to assure?
BUSY? or only working in fixed periods?
Common start/stop + run number
  Interface to EUDAQ
Event data to EUDAQ
  TCP connection in the Si+Sc case

## Slide 15: Appendix: To do for me
Integration of CALICOES2
  Should be investigated very soon
Integration of EUDAQ2
  And specify issues to be solved
BGA SKIROC test board
  I must finish this in March (Japanese fiscal year)
Test of new FEB/sensor
  I hope we can receive the new FEB asap... (and GDCC)