## Slide 1: SiPM R&D status
CTA-LST meeting
February 2015

## Slide 2: Outline
Characterization tests of a SiPM based detector.
  Aim to conclude the readout circuit specifications
Readout electronics:
  Read-out ASIC design and simulation…ALPS
  Board test design and test facilities preparation
  ASIC performance verification with & without the detector

## Slide 3: SiPM detector@ LAPP
Goal:
to extract our ASIC’s specifications.
Hamamatsu detector:
4x4 macro pixel array
1 macro pixel =3x3 mm2 SiPM.
1 macro pixel = 3600 micro pixel(50µm).
1 macro pixel = an array of parallel-connected G-APDs
Notes: Date d’obtention de 4x4SiPM ?

## Slide 4
Test Bench
Test with light source.
An interface of gain stage and inversion => compatible with the HESS2 module.
SiPM matrix
interface board
DAQ system

## Slide 5: Photodetector tested : 4x4 MPPC Hamamatsu matrix (16 3x3 mm² pixels) : one pixel spectrum measured at room temperature
Measurement on 16 pixels - 4x4 SiPM matrix (16 3x3 mm² pixels)
with the LAPP test bench , using the HESS readout system
Optimal operating HV : 72V
Temperature ~ 25 °C

## Slide 6: Photodetector tested: 4x4 MPPC Hamamatsu matrix (16 3x3 mm² pixels) : Measured spectra at room temperature
(Ref S11829-3344MF)

## Slide 7: Photo detector characterization (conclusion)
@ room temperature ~25 degrees
Photoelectron ranging from : 371 to 490 (ADC counts) for HV=72 Volts, equivalent to a gain of 5 105
Spread ~ 10 %
  On-chip gain adjustment (pixel per pixel)
  On chip pixel overvoltage adjustment
  (performance optimization: gain and cross talk)

## Slide 8: Read-out ASIC specification
16 readout channels per chip
  1 p.e. measurement with S/N  5
  2000 p.e. full scale split in 2 gains
  On-chip gain adjustment
  On-chip DAC for pixel overvoltage adjustment
  Trigger :
    Fast discriminator with programmable threshold
  2 differential analog outputs
  Interface with DRAGON / NECTAR
  + Service functions: Slow control registres, DACs, …

## Slide 9: ALPS chip – bloc scheme

## Slide 10: Pre-amplifier
16 channels: adapted to 4x4 SiPM matrix
Principle:
  Low input Impedance about 20 ohm.
  Fast response < 5ns
  => Current mode
Dynamic range:
  From 1 up to about 2000 photoelectron (pe)
  Signal to noise ratio (SNR) > 5
  => 2 Gains
  HG covers from 1 to about 125 pe
  LG covers from 11 to about 2000 pe
  Gain ratio about 92, gain overlap 1 decade
Voltage output
Low power consumption < 30mW at this stage (from simulation)
Notes: Now the preamplifier consists of 16 channels. It has a low input impedence of about 20ohm and a fast response below 5ns thanks to the current convoyor technique.
It measures a range between 1 and 2000pe with signal to noise ratio at least 5 so we made it by 2 gains, the HG covers the first part of the dynamic range and then comes the role of the LG.
The two gains overlap over a decade with a ratio of about 92, making it useful for calibration purposes.
this stage consumes less than 30mW

## Slide 11: Pre-amplifier simulation (1)
Simulated SiPM signal 1pe
High gain response
t = 2.8 ns
Notes: Here is in green a signal corresponding to 1pe simulated at the output of the SiPM model
In blue is the HG response to this signal, it has a fast rising time less than 3 ns and a good amplitude

## Slide 12: Pre-amplifier – simulation (2)
Chart: DR & Linearity
| 1 | 2 | 5 | 10 | 30 | 50 | 70 | 90 | 100 | 125 | 200 | 300 | 500 | 700 | 900 | 1000 | 1500 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000
VLG (mV) | 0.1414 | 0.2794 | 0.6979 | 1.408 | 4.383 | 7.543 | 10.84 | 14.19 | 15.86 | 20.06 | 33.53 | 51.69 | 85.13 | 114.4 | 140.3 | 152.2 | 204 | 248.6 | 343.6 | 453 | 522 | 561.9 | 587.4
VHG (mV) | 13.05 | 26.18 | 65.94 | 133.3 | 415 | 711.5 | 1017 | 1310 | 1435 | 1713 | 2151 | 2196 | 2221 | 2232 | 2237 | 2239 | 2246 | 2249 | 2254 | 2257 | 2259 | 2261 | 2263
gain_ratio | 92.2914 | 93.7008 | 94.4835 | 94.6733 | 94.684 | 94.3259 | 93.8192 | 92.3185 | 90.4792 | 85.3938 | 64.1515 | 42.484 | 26.0895 | 19.5105 | 15.9444 | 14.7109 | 11.0098 | 9.0467 | 6.56 | 4.9823 | 4.3276 | 4.0238 | 3.8526
RMS (mV) | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761 | 2.0761
RMS = 2.08 mV
SNR = 6.2
Notes: Here is the simultaed performance of the pre amplifier
In red is the HG which is linear till 125pe then it saturates so we continue on the LG path in blue that covers a range between 11 and 2000pe
In green we see the constant gain ratio over 1 decade covered by both gains
In orange we see the noise level about 2mV and please notice the single pe detection with a SNR about 6 on the HG

## Slide 13: Analog sums and gain control
Weighted sum of the 16 preamp outputs by digitally controlled resistors
Each resistor has a R-2R like architecture :
  Preamp always sees the same load (better for linearity)
  8 bits resolution for gain adjustment
  Noisy channels can be digitally removed
CR shaping included in each channel
  Adjustable Vref to match the discriminator threshold
+
-
Pa_1
Pa_2
Pa_16
R1
R2
R16
Rf
Vref
Out_sum
(to discri for HG)
Schematic (principle)
Layout of 1 resistor
Custom opamp
Notes: As for the gain of each channel is adjustable by a R-2R net structure with 8 bits resolution so the preamplifier always sees (drives) a constant load of R, and an additional bit is used to eliminate the noisy channel (to eliminate the channel if noisy)
Voltage reference is used in order to fix the work point of the sum and to match the discriminator threshould

## Slide 14: Trigger (DAC + discri)
Discriminator (full custom) :
  Dual bipolar input stage to minimize offset
  Self-biased
  Buffered digital output for trigger
10 bits DAC for threshold
  AMS standard cell
  Digitally controlled threshold
Layout
Slow control
DAC
Discri
Notes: Now To produce the trigger signal: discriminator with a bipolar input is used to minimize the offset
Self biased????
Threshould of 10 bits resolution is produced by std cell DAC. And it is slow controlled

## Slide 15: ALPS chip– Layout sent to foundry 03/03/2014, received end July
AMS BiCMOS 0.35µm
96 I/O pins
Die size: 3.673 X 3.298 mm2

## Slide 16
FPGA Firmeware
ALPS IC
USB connection
LabviewFPGA
ALPS chip
Inputs:
Electrically generated
Inputs:
Photo -generated (from SiPM)
Analog Outputs
Test board- Scheme

## Slide 17: Test board- Labview Interface
ALPS Slow Control registers
DAC: overvoltage adjustment
High/low gain adjustment
DAC: discriminator threshold
ALPS Probe Registers
High gain output
Low Gain output

## Slide 18: Tests to perform on ALPS:
Planned tests:
  Electrical tests
    PA gains and dynamic range
    Gain control tests
    Sum function tests
    Noisy channel suppression
  Test and measurements with SiPM and light source
    Starts on February 2015

## Slide 19: PA gains and dynamic range
Gain ratio lower than simulated (20 vs 80) : Effects of test board and signal injection parasitics
Better results expected with SiPM tests
Chart: Pre-amplifier test
| 367 | 330 | 294 | 262 | 235 | 207 | 185 | 166 | 146 | 130 | 119 | 105 | 93 | 83 | 74.3 | 66.099999999999994 | 58.8 | 52.4 | 46.5 | 41.5 | 13.1 | 4.01 | 1.28 | 0.41 | 0.14000000000000001 | 0.05
out_HG_test | 1870 | 1870 | 1850 | 1850 | 1850 | 1850 | 1850 | 1850 | 1850 | 1850 | 1850 | 1850 | 1800 | 1660 | 1550 | 1400 | 1280 | 1150 | 1030 | 920 | 301 | 98 | 31.2 | 9.8 | 3.1 | 1
out_LG_test | 223 | 207 | 203 | 185 | 169 | 157 | 144 | 132 | 121 | 112 | 103 | 93 | 83 | 76 | 68 | 60.6 | 55 | 48.8 | 43.3 | 36.9 | 12.4 | 3.97 | 1.23 | 0.41 | 0.14 | 0.05
out_HG_test/out_LG_test | 8.3857 | 9.0338 | 9.1133 | 10 | 10.9467 | 11.7834 | 12.8472 | 14.0152 | 15.2893 | 16.5179 | 17.9612 | 19.8925 | 21.6867 | 21.8421 | 22.7941 | 23.1023 | 23.2727 | 23.5656 | 23.7875 | 24.9322 | 24.2742 | 24.6851 | 25.3659 | 23.9024 | 22.1429 | 20
1 p.e. equivalent level on HG
All measurements shown with averaged signals

## Slide 20: Gain control function - LG
Chart: Vin = 201mV & G= 0.5
 | 16 | 17 | 16 | 15 | 14 | 15 | 16 | 14 | 17 | 16 | 15 | 16 | 17 | 16 | 16 | 16
Chart: Vin = 201mV & G= 1
 | 32 | 33 | 32 | 31 | 28 | 30 | 31 | 30 | 32 | 32 | 33 | 31 | 32 | 32 | 30 | 31
Chart: Vin = 201mV & G= 1.5
 | 48 | 50 | 45 | 45 | 43 | 44 | 45 | 44 | 49 | 49 | 46 | 44 | 47 | 47 | 44 | 48
Chart: Vin = 201mV & G= 2
 | 61 | 64 | 62 | 59 | 58 | 59 | 60 | 58 | 66 | 63 | 59 | 59 | 62 | 59 | 57 | 60

## Slide 21: Sum of 2 channels
Chart: Sum of 2 inputs on LG ; Vin=146 mV
| 0 | 0.5 | 1 | 1.5 | 1.9921875
ch5 | 0 | 69 | 135 | 201 | 269
ch16 | 0 | 78 | 146 | 215 | 297
ch5+ch16-m | 0 | 146 | 274 | 401 | 547
ch5+ch16-c | 0 | 147 | 281 | 416 | 566
Chart: Sum of 2 inputs on HG ; Vin=3.6 mV
| 0 | 0.5 | 1 | 1.5 | 1.9921875
ch5 | 0 | 205 | 401 | 591 | 781
ch16 | 0 | 210 | 417 | 597 | 817
ch5+ch16-m | 0 | 421 | 791 | 1151 | 1541
ch5+ch16-c | 0 | 415 | 818 | 1188 | 1598

## Slide 22: Gain equalization
Chart: Vin = 146mV on LG (dispersion=4%)
Vin=146mV, LG_mean | 103.6 | 109.4 | 107.4 | 104.4 | 109 | 107.2 | 106.2 | 105.4 | 116.8 | 115.8 | 109.4 | 113.4 | 118 | 113.4 | 111.8 | 118
Chart: Vin = 146mV on LG (dispersion ≈ 0.5%)
corrected real output | 100 | 101 | 101 | 101 | 100 | 100 | 100 | 100 | 100 | 100 | 101 | 100 | 100 | 100 | 101 | 101
Chart: Vin=21mV on HG (dispersion≈1.7%)
 | 1102 | 1094 | 1078 | 1102 | 1078 | 1090 | 1102 | 1116 | 1102 | 1078 | 1080 | 1058 | 1058 | 1060 | 1064 | 1078
Chart: Vin =21mV on HG (dispersion≈0.2%)
corrected without pedestal | 1140 | 1140 | 1140 | 1140 | 1140 | 1140 | 1140 | 1130 | 1140 | 1140 | 1140 | 1140 | 1140 | 1140 | 1140 | 1140