## Slide 1: ATLAS Lar Calorimeter trigger electronics phase I upgrade LDPB Firmware Development Environment (ABBA, LATOME)

## Slide 2: Revision history
Version | Date | Author | Description
0.1 | 14/01/2015 | Nicolas Chevillot | First draft
0.2 | 03/03/2015 | Nicolas Chevillot | 
0.3 | 01/06/2015 | Nicolas Chevillot | Updated with latest changes

## Slide 3: Agenda
Description of ABBA/LATOME(AMC) working group
Description of development environment
  e-group
  JIRA project
  GIT repository
  Simulation and compilation

## Slide 4: ABBA/LATOME(AMC) working group
Multiple projects
   Have a common environment for all projects
Developers spread across the world
  CPPM/LAPP (France)
  University of Dresden (Germany)
  University of Tokyo (Japan)
  University of Arizona (USA)
  Budker INP and Novosibirsk State University (Russia)
   Need to have a way to share code
Developers organized in teams working on dedicated parts of the design
   Need to be able to protect areas of code

## Slide 5: Development environment
CERN provides multiple tools
  JIRA project
  GIT repositories
Can be accessed from anywhere
atlas-lar-ldpb-firmware
GIT repository
Remote computer(s)
Local computer(s)
Registered member of atlas-lar-ldpb-firmware e-group
gitolite-admin
GIT repository
atlas-lar-ldpb-firmware
e-group
ATLAS LAr LDPB firmware
JIRA project
CERN

## Slide 6: e-group
CERN e-group: atlas-lar-ldpb-firmware
  Need to be member of the e-group to be able to access the JIRA and GIT
  Request access to e-group owner:
    Nicolas Chevillot: nicolas.chevillot@lapp.in2p3.fr
  https://e-groups.cern.ch/e-groups/Egroup.do?egroupId=10158278&searchValue=atlas-lar-ldpb-firmware
  Current members:
    Aad, Georges
    Camplani, Alessandra
    Chevillot, Nicolas
    Dinkespiler, Bernard
    Dumont-Dayot, Nicolas
    Duval, Pierre-Yves
    Enari, Yuji
    Hentges, Rainer Guenter
    Johns, Kenneth
    Starz, Steffen
    Tanaka, Junichi
    Wingerter, Isabelle
    Zhulanov, Vladimir

## Slide 7: JIRA Project
CERN JIRA Project: LDPBFW
  https://its.cern.ch/jira/browse/LDPBFW
  Tasks/Bugs tracking system
  Used to plan for tasks, i.e. implement such feature, or improve something
  Used to track bugs in the firmware
  GIT commits can be linked to JIRA
  Simple workflow with 4 state: Open, In progress, Closed and Reopened
create issue
start progress
close issue
start progress
reopen issue
close issue
stop progress
close issue
Open
In progress
Closed
Reopened

## Slide 8: JIRA Project
CERN JIRA Project: LDPBFW
  Issue are classified in components:
    env, doc
    ABBA: abba-back-all, abba-front-all (need maybe to split into multiple components)
    LATOME: latome-doc, latome-fpga, latome-ipctrl, latome-istage, latome-lli, latome-mon, latome-osum, latome-remap, latome-ttc, latome-user
    undecided: in case component is not yet known
  Issues are assigned to component owner
    Can be reassigned to a particular developer

## Slide 9: GIT repository
CERN GIT repository: atlas-lar-ldpb-firmware
  Need to be member of e-group
  Web access: https://git.cern.ch/web/atlas-lar-ldpb-firmware.git
  GIT clone: https://git.cern.ch/web/atlas-lar-ldpb-firmware
  Tracks different revisions of the firmware
  Allows to share code between group members
  Restricts access to parts of the firmware (using the CERN gitolite-admin repository)
  Contains:
    doc: working environment documentation
    env: working environment scripts
    ABBA, LATOME: current projects
    .git: GIT specific files
    .gitignore: GIT list of files that cannot be committed in the repository (i.e. temporary files, …)
  Could hold more projects related to LDPB!

## Slide 10: GIT repository
GIT workflow
  GIT is using clone, pull, add, commit, push commands
  Using a simple no branch workflow. Might need to reconsider this option if complexity increases
Local user 2
master
CERN
Local user 1
clone
Feature/Bug correction
Feature/Bug correction
clone
push
pull
add / commit
add / commit
push

## Slide 11: GIT repository
GIT commits
  Need to identify clearly which JIRA issue and component(s) the commit applies to
  Commit header should follow the convention:
    LDPBFW-<JIRA issue number> (<comma separated list of components>) <Description>
    Example:
      LDPBFW-15 (env, LATOME-ipctrl) Missed asynchronous reset.
  As much as possible each commit should be linked to a JIRA issue

## Slide 12: GIT repository
Access rights
  Each folder’s access rights are handled in the CERN gitolite-admin repository
  Request to e-group owner to update access rights:
    Nicolas Chevillot: nicolas.chevillot@lapp.in2p3.fr
  https://git.cern.ch/web/gitolite-admin.git/blob/HEAD:/conf/subs/atlas-lar-ldpb-firmware.conf

## Slide 13: GIT repository
Tools
  GIT can be used either on Windows through Cygwin or in linux environment
  Command line tool or GUI, i.e. Tortoise GIT (Windows)

## Slide 14: Simulation and compilation environment
Environment based on makefile/python/TCL scripts
  Based on hdl-make (CERN Open Hardware): http://www.ohwr.org/projects/hdl-make
  Handle dependencies to minimize compile time
  Concept of modules, can be used to batch build projects (i.e. testbenches) for regression testing
  Supports Cygwin ≥ v1.7.33 (Windows) or Linux environment (tested on SciLinux v6.1):
    Git ≥ v2.1.1
    Make ≥ v4.1
    Python ≥ v2.7.8
  Strongly recommends using Linux based environment (much faster)
  Note: the structure of the environment is inspired from LHCb project. Work from Guillaume Vouters and others.
Simulation environment
  Based on Modelsim/Questa tool ≥ v10.2c
  Dependencies are built automatically
  Faster rebuild
  Optional GUI, can be used to remotely build project on faster machine
Synthesis environment
  Based on Quartus II ≥ v13.1. ABBA using v13.1, LATOME using v15.0.
  Optional GUI, can be used to remotely build project on faster machine

## Slide 15: Simulation and compilation environment
Each project holds multiple sub-projects
  A sub-project is a simulation testbench, design to be compiled or a design unit
  Described using a python file: Manifest.py
# Simulating the design
action = "simulation"
# Simulation tool is Modelsim v10.2c
sim_tool = "modelsim"
#sim_tool_version = "10.2c"
# Compilation tool is Quartus v14.1, used in simulation for Altera primitives
#comp_tool = "quartus"
#comp_tool_version = "14.1"
# Top module used for simulation
top_module = "fpga_tb.fpga_tb(struct)"
# Waveforms for simulation
sim_do_cmd = "wave.do"
# Additional options for modelsim
vcom_opt = ""
vsim_opt = "-voptargs=+acc -i -multisource_delay latest -t ps +typdelays"
# List of modules
modules = {
"local" : [
"$PROJECT_ROOT_PATH/src/fpga",
"$PROJECT_ROOT_PATH/src/testbench",
],
}
# Default library
library = "fpga_tb"
# List of source files for the 'fpga' module testbench
files = [
"fpga_tb.vhd",
]

## Slide 16: Simulation and compilation environment
Top-level interfaces are described in a python file: top_level.py
  Interfaces are either:
    Signals
    Altera Avalon Streaming (Avalon ST) or Avalon Memory Mapped (Avalon MM)
    Custom interfaces (combination of Altera Avalon ST/MM and or signals)
  Python file used to automatically generate:
    Documentation, i.e. interfaces tables for LAr-LATOME-FW
    https://git.cern.ch/web/atlas-lar-ldpb-firmware.git/blob/HEAD:/LATOME/doc/LAr-LATOME-FW/LAr-LATOME-FW.pdf
    VHDL Code skeleton for each modules, including testbench
    VHDL code skeleton documented using doxygen comments

## Slide 17: Simulation flow
Source files
(.vhd, .v, …)
Configuration files
(manifests, makefile)
Relations makefile and manifests
VHDL/Verilog Parser
Makefile generator
Simulation makefile
VHDL/Verilog compiler
Compiled
Libraries
Modelsim
simulator
Modelsim
Build environment
Input files
Environment targets:
  clean, relations, generating libraries, simulation

## Slide 18: Compilation flow
Environment targets:
  clean, quartus_project, quartus_gui, ..., compilation
Source files
(.vhd, .v, .tcl, …)
Configuration files
(manifests, makefile)
Makefile generator
Compilation makefile
Synthesis
Compiled
FPGA
Quartus
Build environment
Input files

## Slide 19: Synthesis flow
Chart: 
| lappc-f533 (Windows 8) | lappc-f460 (Windows 7) | lappc-f561 (NFS) (Sci Linux 6) | lappc-f561 (local) (Sci Linux 6) | chevillotn-UX31A (Windows 8)
quartus_project | 0.14825 | 0.099067 | 0.13275 | 0.19488 | 0.29103
quartus_map | 5.7849 | 6.3861 | 4.7127 | 4.3387 | 6.3045
quartus_fit | 9.1257 | 10.6143 | 8.1873 | 8.0006 | 12.6112
quartus_asm | 0.93862 | 1.0964 | 0.80768 | 0.79665 | 0.23067
Synthesis of ABBA_PH0 project: (time in minutes)