## Slide 1
Clermont-Ferrand requests
for the Test Beam
Vidyo meeting, 29 July 2015
François Vazeille
Remote HV System
Front End electronics
Hypothesis:
Some Mini-Drawers are dedicated to special studies,
like for example the PMT pulse studies.

## Slide 2
Remote HV System
● Available hardware at the Test Beam
HV Regulation crate (Now in Bld 175).
HV Source power supply (Tesla).
2 times 125 m long HV cables
+ 1 cable 50 m long to lengthen one long cable for tests.
8 HV Bus cards.
4 HV Opto cards (Scheme 1)
- 2 already calibrated (Used for the TileCal Note, now at home).
- 2 tested but not fully calibrated now in Bld 175.

## Slide 3
● Three uses are proposed with 3 different set-ups A, B and C
4
4
3
4
1
2
3
Pulse studies: at least 2 PMT Blocks (PMT, FATALIC shaper)
FATALIC chain study: Complete or partial.
Comparison of the
2 HV options using,
Chicago electronics.
A
B
C
HV Bus cards: 1 in set-up A, 2 in set-up B, 2 in set-up C.
In set-up C: we requested in previous meetings to instrument Drawers 3 and 4
in order to have a better routing of the internal HV cables using their
dedicated cables trays.
- Only 2 Drawers can be supplied in the same time  Only 2 long HV cables.
The same HV Opto boards (Calibrated) and HV Micro board will be used in the 3 set-up’s.

## Slide 4
- Set-up A: Common use for pulse studies, open to possible other tests.
- Set-up B: FATALIC tests (Seen next slides).
- Set-up C: comparison of the ANL and Remote HV options:
 HV Stability studies over a rather long period.
 Noise studies at the readout level
including additional tests with HV cable extension of 50 m
 125+50= 175 m long cable.
● Goals of the 3 set-up’s

## Slide 5
Front end electronics (FATALIC)
- See the Wednesday Vidyo 1 July 2015 talk for details
https://indico.cern.ch/event/394859/
- Pulses at the output of the FATALIC shaping for the 3 gains,
sent to a digital scope via buffers (on the All-in-1 card) and flat cables.
- At least one PMT Block … even though several All-in-1 cards will be equipped.
- Requested: enough statistics from different particles at various energies.
● FATALIC pulse studies

## Slide 6
● Other electronics studies with FATALIC4b
(The new version delivered in August)
 WARNING:
- Too short R&D time to compete with other option by using the whole chain.
- Nevertheless, systematic tests are scheduled from 2 possible set-ups:
▪ Whole chain from FATALIC to the Daughter Board versions 3 or 4
 Readout from the Back End electronics.
▪ And/or Partial chain from FATALIC to the Main Board (New or Version ¼)
depending from the debugging time of the new version
 Readout from Romeo’s labVIEW system.
 FORESEEN TESTS
- Data acquisition: communication in between the various boards,
calibration with DAC, etc.
- Noise studies.
- Automatic High/Low gain changes (Medium gain always delivered) .
- Calculation of gain ratios.
- Linearity studies.
- Time scanning (T0 scan) .
Comment:
What is the TileCal policy with respect to the clock (Beam/Clock timing)?