## Slide 1: A portable and directional fast neutron detector MIMAC FASTn
Nadine Sauzet
Laboratoire de Physique Subatomique et de Cosmologie
(LPSC-Grenoble)
(UJF Grenoble 1, CNRS/IN2P3, Grenoble INP)
LABEX ENIGMASS –MIMAC valorization

## Slide 2: Summary
Context
Valorization project strategy
Operational requirements overview
Technical development
Economic feasibility analysis

## Slide 3: Project roots
  MIMAC project (MIcro-TPC Matrix of Chambers) :
  Instrumentation dedicated to directional non baryonic dark matter detection,
  Developed at LPSC-Grenoble (electronics, gas system, data acquisition, mechanical structure, quenching measurements),
  Fast neutrons constitute a background to reject.
      So why not develop a fast neutron detector,
      based on these concepts

## Slide 4: Interest of a new fast neutron detector in the existing market
  Presently, on the market, fast neutron detectors :
  Require the use of 3He (limited supply) ou 6Li (regulated nuclear matter),
  Require neutron moderation,
  Can’t give quickly the energy of the fast neutron emitted,
  Can’t give the emission direction,
  Have a fix operation range.
      MIMAC FastN can address all that !

## Slide 5: Markets targeted
Detection of neutron sources and fissile matters for customs
Homeland Security
Medical sector
Radioprotection
Neutron fields characterization (for BNCT or hadrontherapy)
Radioactive area characterization,
Monitoring for mobile worksite,
Search of lost sources.
Nuclear physics
Neutron beams characterization
(for nuclear industry, neutronography, waste characterization )

## Slide 6
Context
Valorization project strategy
Operational requirements overview
Technical development
Economic feasibility analysis

## Slide 7: MIMAC valorization strategy (1)
DESIGN
Operational requirements
Technical specifications
Technical solutions, development, supply chain
Procurements
Prototype assembly
Tests
PROTOTYPE MANUFACTURING
Technological solutions validated
DEMO
for prospective customers
Status today

## Slide 8: MIMAC valorization strategy (2)
Intellectual property
Market analysis (competitors / customers)
Economic feasability
Start-up
Know-how transfer
Industrial prospective
?

## Slide 9: MIMAC valorization strategy (3)
  Selected project in the frame of the DIRE prematuration program
  Funding for :
    A prototype manufacturing,
    Market analysis and economic feasibility analysis support,
    Software development.
  Program duration :
    One year
    End : September, 2016

## Slide 10
Context
Valorization project strategy
Operational requirements overview
Technical development
Economic feasibility analysis

## Slide 11: MIMAC FastN requirements overview
Neutron spectrum reconstruction above 100 keV
Neutron source location
Portable detector
Adapted to industrial areas
« Press-button » operation
No regulated matters
No high gas pressure
Industrial supplies
Energy range adaptable
Large detection volume
Operation
User friendly
Manufacturing
Limited maintenance
Quick installation
Adapted to careless transport
Long duration operation

## Slide 12: Fast neutrons detection principle (1)
Detection based on a nuclear recoil tracking, that results from the interaction between a neutron and a gas nucleus.
Recoil Energy max = 64 % Neutron Energy
Neutron
Helium nucleus
Helium recoil
Gas mixture

## Slide 13: Detection principle (2)
Drift in a ionization chamber,
Gas amplification in a MicroMegas,
Readout on a pixelated anode, sampled roughly at 20 ns.

## Slide 14: Gas choice (1)
  MIMAC detector
  MIMAC FASTn
Mixture of fluorinated gas and flammable gas
CF4
CHF3
C4H10
Not compatible with industrial areas
Mixture of non regulated and non-flammable gas
He
CO2
Pressure around 700 mbar
Easy cheap supply

## Slide 15: Gas choice (2)
Setting of the electrical parameters.
Typical neutron energy range = [120 keV ; 6 MeV]
  Example of a recoil track with its associated measured energy in a He/CO2 mixture :
Deposited energy

## Slide 16
Objective :
  Discriminate helium recoils (resulting from neutron/gas nucleus interaction), from electrons and other recoils
Origin of electrons :
  Compton electrons resulting from gamma rays interaction with the detector walls,
  β desintegration of nucleii intrinsic to the detector.
Origin of other recoils :
  Carbon and oxygen recoils (constituent of the gas),
  Protons recoils due to neutron reactions with aluminium.
Helium recoils selection (1)

## Slide 17: Helium recoils selection (2)
Neutron beam [ 100 keV ; 10 MeV ]
C and O recoils
He recoils
Compton electrons
Proton recoils
Proton recoils

## Slide 18: GEANT4 simulations (1)
Simulation set-up :
Cage field
Cathode
Micro-patterned detector
Neutron source

## Slide 19: GEANT4 simulations (2)
Electron track length = f(energy)
Proton track length = f(energy)
Branch n° 2
Branch n° 1
Gamma induced branch

## Slide 20: Energy calibration (1)
Exploitation of the neutron capture reaction : 10B(n,α)
  with thermal and epithermal neutrons
  10B + n 7Li* + α 7Li + α + γ (94 %)
  10B + n 7Li + α (6 %)
Strategy :
  Integration of a natural boron layer, inside the neutron detector,
  Identification of the end-points of α and Li particles distributions.
Particule | Energy end-point | Track length max
94 % |  | 
α | 1,47 MeV | 4,1 cm
Li | 840 keV | 2,8 cm
6 % |  | 
α | 1,78 MeV | 5,2 cm
Li | 1,16 MeV | 3,3 cm

## Slide 21: Energy calibration (2)
Experiment performed at INFN / Legnaro :
  In collaboration with Buenos Aires, Grenoble, Cadarache, Legnaro, Sevilla
Objective :
  Concept validation with a He/CO2 mixture : faisability to build a fast neutron spectrum
  Angular distribution measurement
Principle :
  Deuteron beam of 1,45 MeV
  A thin 9Be target of 10 μm
  Neutron detector : IRSN detector, adapted for operation with He/CO2 gas mixture.

## Slide 22: Energy calibration (3)
Configuration of the experiment :
  Moderation of neutrons with polyethylene plates
15 cm
9Be Target
Moderator
Neutron detector

## Slide 23: Energy calibration (4)
Lithium track and energy :
Alpha track and energy :

## Slide 24: Energy calibration (5)
Energy spectrum with thermal neutrons :
Raw spectrum, after minimal cuts : After data selection :
α (1,47 MeV)
Li (840 keV)
α (1,47 MeV)
Li (840 keV)

## Slide 25: Detection of a few MeV neutrons
  Preliminary spectra with 9Be(d(1,45 MeV),n) :
  At 90° At 35° :
Structures emerge
Quantitative analysis to perform

## Slide 26
Context
Valorization project strategy
Operational requirements overview
Technical development
Economic feasibility analysis

## Slide 27: Detector preview
  MIMAC detector
  MIMAC FASTn
DIRE prematuration program

## Slide 28
Context
Valorization project strategy
Operational requirements overview
Technical development
Economic feasibility analysis

## Slide 29: Economic feasilibity analysis
Intellectual property analysis conclusion :
  No patent,
  Protection with a know-how license,
  Software protection.
Market analysis :
  First panorama of competitors, based on their application targets :
    6 manufacturers identified, mainly focused on homeland security.
    To be completed with the support of FIST contacts.
  First contacts with potential users in the medical sector : fast neutron therapy, hadrontherapy.
  First cost analysis with the prototype development.

## Slide 30: Short term perspective
Application field
December 2015
Eneutron > 10 MeV
Assembly / tests
Upgrade
Development / Source location algorithm / tests
Prototype
Software
February 2015
April 2015
August 2015
Economic feasibility analysis
June 2015
Market study, cost analysis completion