## Slide 1: QA-QC Meeting Cosmic Bench
11 January 2016

## Slide 2: Aim of the Cosmic Bench
Efficiency characterisation
Identify problems along the whole detection chain: dead strips, inefficiences, connexion problems …
Requirements: gas, HV, electronics cards (not the final VMM electronics, we will use the DREAM electronics

## Slide 3: Set up
Re-use the cosmic bench of the M-Cube project with a modification of the structure that has already been designed

## Slide 4: Procedure
Scanning region 1.5× 0.5 m2 (a few days to scan the whole module),
5 steps ~5 days to scan a whole module~1 week
Use the M cubes modules in coincidence with our module
M cube is equipped with DREAM electronics
Our modules will be also equipped with DREAM electronics
We have already ordered the DREAM electronics corresponding to 1/5 of the surface~4096 channels8 cards

## Slide 5: To do list
Platform: finalise the design (with Didier, Christoph and Marc) and order it
Design and adaptation cards Zebra connectors to DREAM connecteurs Multiplexing (we will read only 1 over 2 strips)
Start looking at the data of the DREAM electronics to be familiarised with it

## Slide 6: Dimensions des panneaux

## Slide 7: Prix
Configuration souhaitée (1/5 de la surface équipé= 4096 channels)
Le cout total estimé est de l’ordre ~70 k€
Agrandissement plateforme existante: 5 k€
Détecteurs M-cube référence :
  6 détecteurs x 5 k€ = 30 k€
DAQ Electronique pour équiper le 4 kcannaux du module NSW + électronique détecteurs M-cube:
  4+2= 6 cartes FEU et tout leur environment : 35 k€