## Slide 1
Leonardo Ristori
TTC Meeting
CEA Saclay, 5-8 July 2016
PIP-II SSR1 Cryomodule
Technical Issues

## Slide 2: Topics
The Fermilab SSR1 Cryomodule
Study on vacuum manifold
Study on cool-down for alignment
String Assembly Challenges
Cryomodule Assembly Strategy
Spoke Tuner
  Requirements
  Prototype
  Production
Coupler
  Requirements
  Prototype Test to Failure
  Production
  Electro-deposited bellows
  Low pressure gap window

## Slide 3: SSR1 Cryomodule
Segmented approach
2 K operation
2 bar relief
8 SRF Cavities + Couplers
4 SC Magnets
4 BPMs

## Slide 4: SSR1 Cryomodule
5.2 m long
8 Cav + 4 Magnets
Bottom-supported elements with warm strongback
Tuner access ports
Current leads
Alignment
viewports
Couplers
L. Ristori, T. Nicol, Y. Orlov, D. Passarelli, M. Parise
http://accelconf.web.cern.ch/AccelConf/PAC2013/papers/thpma09.pdf

## Slide 5: SSR1 Cryomodule R&D Goals
Validate new spoke cavity cryomodule design concepts
  Room temperature strongback
  Individual support posts to control axial motion
  Conduction cooled magnet current leads (not new, but new to us)
  Single-window coaxial input coupler
  Integral beam instrumentation
  Determine the practicality of tuner access ports
Validate alignment concepts
  Gain experience with the required alignment tolerances
  Verify alignment stability during cooldown
Verify static and dynamic heat load estimates
Clean-Room assembly in New Facility (Lab 2)
  Gain experience with strings of spoke cavities, solenoids, and beam instrumentation, e.g. cleanroom operations, shipping and handling, etc.

## Slide 6: SSR1 String Assembly: Beam-line vacuum
High vacuum level (< 5E-5 Torr) is needed inside the beam line volume before the introduction of liquid helium.
Maximum acceptable time set to 12 hours
Measurements (very conservative conditions, moisture in cavities)
Vacuum Pump
Pressure Gauges
Vacuum simulation (ideal scenario)
Ultimate pressure is below 5e-5 Torr
The high-vacuum level at room temperature can be achieved pumping down by the beam ports only. Furthermore, simulations performed on the entire string with clean components show that the achievable pressure would be of 7E−8 Torr pumping from both ends.
Ultimate pressure is below 1e-7 Torr
Vacuum Manifold is not needed!
High-vacuum Simulations and Measurements on the SSR1 Cryomodule Beam-line, D. Passarelli et al., Proceedings of SRF2015, Whistler, BC, Canada
Work by M. Parise

## Slide 7: Cool-down displacements
Thanks to strong-back at room temperature, no longitudinal displacements.
Vertical displacements of magnets and cavities are the same, since the supporting structures are made of same material ( same thermal contraction)
Predicted beamline shift: down ~1mm, will be pre-set

## Slide 8: SSR1 String Assembly: design features
Interconnection cavity-cavity
Interconnection cavity-magnet-BPM-cavity
SSR1
Type A
SSR1 Type B
Edge-welded bellows assembly
Al-diamond seals
SiBr set screws
316L stainless nuts and washers
Hydro-formed bellows assemblies
Al-diamond seals
SiBr set screws
316L stainless nuts and washers
Solenoid
BPM
SSR1 Type B
SSR1 Type B
SSR1 Type B
SSR1
Type A
SSR1
Type A
SSR1
Type A
Gate Valve
Gate Valve
20mm
Coupler (cold-end)

## Slide 9: Cavity-Cavity Connection
Bellows allow enough room to perform the assembly (tested outside the cleanroom)
extended
compressed
Cleanliness?
Edge-welded bellows were subjected to cleaning and extensive testing in cleanroom.
Results were excellent and repeatable.
US cleaning sufficient, HPR better.

## Slide 10: Cavity-Magnet String on Rail System
String Assembly....
To purge or not to purge?
Purging seems the better approach in this case
Re-entrant shape of cavity endwalls prone to turbulence
Vicinity of connections to high e-field regions, high risk
First cleanroom assembly for new facility
First non 9-cell cryomodule at Fermilab
Work by D. Passarelli – M. Parise

## Slide 11: Rail System – staged outside cleanroom

## Slide 12: Magnet-BPM Installation Tool
Magnet, BPM, 2 bellows, assembled and HPR washed prior to installation
Aligned using modular system employing independent devices for each DOF
Bellow alignment braces still not finalized
Gas Springs (Compression)
Tension Wires
Modular alignment system
Work by M. Parise

## Slide 13: Cryomodule Assembly Strategy (not finalized)
In cleanroom, Rough alignment done, clocking is fixed. String with rail system comes out of cleanroom.
String is made rigid by tooling (not pictured) and lifted by crane
String is lowered on strongback assembly, on 2nd rail system
Cold mass assembly is completed (tuners, 2-phase, current leads, piping, MLI). Final alignment is done.
Cold mass inserted in vacuum vessel (rollers not pictured). Alignment is checked.
1
2
3
4
5

## Slide 14: SSR1 Tuner: Requirements

## Slide 15: Prototype Tuner
Cartridge with motor and piezos
Installation of cartridge
Alignment system for main arms
D. Passarelli

## Slide 16: SSR1 Tuner: Testing
Performance of the Tuner mechanism for SSR1 Resonators During Fully Integrated Tests at Fermilab, D. Passarelli et. al., Proceedings of SRF2015, Whistler, Canada, THPB061
Tuning is achieved with cavity always under compression
Spec is > 135kHz range
Motor and Piezos are in series
Preload of Piezos is achieved by engaging the motor up to 80 kHz shift
Studies of microphonics control of the SSR1 cavity have being carried out using this tuner mechanism.

## Slide 17: Production SSR1 Tuner
Based on the experiences gained assembling and testing the prototype tuner we’re updating the design of the tuner for the production version.
Main changes:
  Clearance with beam connections
  Integration of commercial encapsulated piezos stack (same used for LCLS-II). Replacing the “homemade” ones which are considered less reliable.
  Easier installation: improve connections among parts
  Easier handling: reduce the overall weight of components without loosing stiffness (efficiency)
Work by D. Passarelli
Notes: Add image of new tuner

## Slide 18: 325 MHz Power Coupler
Parameter | Value
Frequency | 325 MHz
Pass band (S11<0.1) | > 1 MHz
PIP-II Operating power (CW reflection) | 15 kW
Acceptance Testing power | 30 kW
HV bias | ~ 4kV
Electro-magnetic design
Parameters | Value
Thermal intercepts (nominal) | 5 K and 80 K
Temperature at 5 K intercept | < 15 K
Temperature at 80 K intercept | < 125 K
2K heat load (30 kW) | < 1 W
5K heat load (30 kW) | < 6 W
80K heat load (30 kW) | < 11 W
Antenna tip temperature (30 kW) | < 330 K
Antenna cooling media | Air
Air flow rate (30 kW) | < 2 g/s
Max cooling air pressure drop | < 1.0 bar
Thermal design
Work by S. Kazakov

## Slide 19: 1 Prototype Tested to Failure (reached 47 kW, successful)
Work by S. Kazakov

## Slide 20: Failed Coupler
Work by S. Kazakov

## Slide 21: Production Couplers
Much better quality visually than prototypes
High Power Tests this month
Work by S. Kazakov

## Slide 22: Electro-Deposited Bellows
Alternative to copper-plating (which has lots of potential issues)
PROS
Flexible and elastic
Vacuum integrity
Flawless internal finish
Very tight tolerance on shape
CONS
25um internal layer of Nickel is slightly magneti, not a problem for PIP-II
limited suppliers
Work by O. Pronitchev

## Slide 23: Ceramic Window with Low Pressure Gap
Low pressure gas is kept between windows
Advantages:
  reliability as two windows
  compact as single window (antenna can be easily cooled)
  lower bending forces on window, compared to single window of same total thickness
Occurrence leaks can be detected: decrease of pressure in gap indicates of crack in inner window, increasing pressure in gap indicates of crack in outer window.
Any single crack is not fatal for accelerator.