## Slide 1
TTC Meeting Paris
BESSY VSR- R&D of SRF Cavities
TTC Meeting Paris
5.- 8.07.2016
Adolfo Vélez
Institute for Superconducting Radio Frequency (FG-ISRF)

## Slide 2
OUTLINE
  BESSY VSR, Design Specifications and Challenges
  Development of SRF Cavities for BESSY VSR-BESSY III
    Design Techniques
    HOM loads
    Module integration
  Prototypes
    Copper Prototypes
    Single Cell cavity
    5-Cell VSR cavities
    High Power Couplers
  Testing & Infrastructure
A.Vélez, TTC Meeting Paris

## Slide 3: The concept of BESSY VSR
1
10
10−4
10−3
10−2
10−1
1
10
0.1
Bunch current (mA)
RMS bunch length (ps)
User optics
Low alpha optics
Bursting instability begins
Ith roughly proportional to V´rf σ2
Limited pulse length in storage ring
At high current beam becomes unstable
  For ps pulses, flux is reduced by nearly 100
BESSY II @ present
Normal conducting cavity system
A.Velez, SRF15 Whistler CA
  Low alfa operation only 12 days/year
  (all beamlines) ------- Low flux
  Femtoslicing is continuously operated
  ( only 1 beamline) ---------- Low flux
  Can we design a system offering both possibilities simultaneously?
Hardware (RF cavities)
Machine optics

## Slide 4: The concept of BESSY VSR
Limited pulse length in storage ring
Hardware (RF cavities)
At high current beam becomes unstable
  For ps pulses, flux is reduced by nearly 100
BESSY II @ present
1
10
10−4
10−3
10−2
10−1
1
10
0.1
Bunch current (mA)
RMS bunch length (ps)
Low alpha
User optics
Low alpha optics
Ith roughly proportional to V´rf σ2
100 × more voltage gradient
User optics
Machine optics
  Supply short pulses down to 1.5 ps
    100× more bunch current
  Low α permits few 100 fs
  Configure BESSYVSR so 1.5 ps and 15 ps bunches can be supplied simultaneously for maximum flexibility and flux!

## Slide 5: The concept of BESSY VSR
Voltage: 1.5 MV @ 0.5 GHz
Voltage / MV
Present
15 ps bunch
Time (ns)
Phase I
1.5 ps bunch
Voltage: 20 MV @ 1.5 GHz
sum voltage
Voltage: 20 MV @ 1.5 GHz
+ 17.1 MV @ 1.75 GHz
Phase II
Time (ns)
Time (ns)
~ 4.2 m
cavity V1,f1
cavity V2,f2
BESSY II , SC Upgrade
1.5GHz and 1.75GHz ---- RF beating
(modulate RF focusing)
Odd (voltage cancelation, 15 ps bunches)
Even (voltage addition, long.focussing, 1.7 ps)
G.Wüstefeld et al.
„Simultaneous long and short electron bunches in the BESSY II storage ring“
IPAC2011

## Slide 6
R&D of SRF Cavities for BESSY VSR
R&D of SRF Cavities
R&D of SRF Cavities
Goals:
  Design, fabrication and testing of fully dressed „extremely-damped“ 1.5 GHz Nb cavities (Waveguide damped)
  Development of HOM loads, tuners and neccesary ancillaries
  Fabrication of Copper and Niobium prototypes to validate the proposed RF design techniques
  Design and fabrication of High Power Couplers
  Development of RF sources for cavity operation
  Prototype testing and commissioning: HoBiCaT and Testinghalle Vertical Test Stand.
Collaboration partners
  Helmholtz Association POF-III Topic „Accelerator Research and Development“: DESY, HZDR
  External: Jefferson Lab (USA), TU Dortmund and Uni Rostock
Budget: 2.5 M€

## Slide 7
SRF Design specifications and challenges
SRF System
CW operation @ high field levels E=20MV/m
On the edge field values on the surface (discharges, quenching)
High beam current (Ib=300mA), close to 0 beam loading
Cavities must be highly damped (CBIs)
Exotic cavity design (damping end-groups)
Cavity fabrication processes not mature
Challenges
2@1.5 GHz
2@1.75 GHz
Specifications

## Slide 8
Damping Technique
W.G. Dampers chosen
  High power capabilities
  Natural cut-off
  Damping efficiency
  Long distance to loads (dust contamination)‘
  Compact option
High HOM damping level required to avoid CBI‘s
Impedance tresholds with feedback:
  5e4 Ω, longitudinal modes
  1e7 Ω/m, transverse modes
Cav. Design and HOM Damping

## Slide 9
H
H
E
E
a
a
b
b
End-groups and Damping
Modified
WG. Damping
(b ≠ a/2)
A.Velez et al. WEPMA013
IPAC15
Enlarged beam-tubes
2xTE10
4xTE01
f = 2.755 GHz TM Dipole
A.Velez et al. MOPP071, LINAC‘14
A.Velez, SRF15 Whistler CA
Calculations show high HOM damping level required to avoid CBI‘s
  5e4 Ω, longitudinal modes
  1e7 Ω/m, transverse modes

## Slide 10
TM011 Mon.
TE211 Quad.
TE111 Dip.
TE011
TE211
TE111
TM110
Courtesy of M.Ruprecht
All analyzed modes except 1 are below the Impedance threshold (with feedback)
Highly damped 1.5 GHz Cavity

## Slide 11
TM010 π mode
Dipole HOM
End-groups and Damping
Long WG needed in order to avoid Q droping ( Lwg>400 mm )
Localized end-group modes close to WG cut-off, HOM load matching issues
WG width tapered (88mm-91mm)
fcut=1.64 e9
R/Q=15
Qext=1600
f=1.7 e9

## Slide 12
TM010 π mode
Dipole HOM
End-groups and Damping
WG width tapered (88mm-91mm)
fcut=1.64 e9
R/Q=7.3
Qext=60
f=1.69 e9
Long WG needed in order to avoid Q droping ( Lwg>400 mm )
Localized end-group modes close to WG cut-off, HOM load matching issues

## Slide 13
Courtesy of H.W.Glock
HOM Power
Energy lost by bunch
48,5% fundamental band
51,5% HOMS
Energy going to HOMS
67,6% transmitted to waveguides
32,4% travels through beam-pipe
HOM Power = 1.3 KW (5 WG) + 800 W (up/downstream)
Max Power on load = 300 W

## Slide 14
HOM loads
Collaboration with Jefferson Lab
Sinergy with bERLinPro
Water-cooled loads
In design process
Specifications scaled to Max. values on WG + BP power (460W per load)
3 prototype loads (Q4 2016) + series of 15 (2017)
Dust production test (particle counting)
Low power + High Power tests @ JLab
Thermal analysis results
Imported RF power losses mapped to the absorber
Structural analysis results
First load designs fro bERLinPro

## Slide 15
Module length 4.2 m
Cold String related aspects
Preliminary module related considerations (only cold-string)
Limited length straight section, does everything fit inside?
Many elements. Different frequencies, different sizes
Below design, impedance issues
Cavity cross talking.
Realistic HOM power on WG. Can we add extra absorbing elements, ie. BP absorbers?
Tapered bellow transitions
Coupler kicks. Which is the good orientation?
Concatenation Studies

## Slide 16
Concatenation studies
First Power calculations of complete cold string (1.5 GHz + 1.75 GHz)
Confirm HOM load specifications
Validate Impedance budget
Tune bellow transitions
High computing resources
Work in progress, still preliminary results!

## Slide 17
Prototypes, 1.5 GHz 5-cell Cu Cavity
Validate Fabrication Techniques, relatively new development (deep drawing, spring backs, weld shrincage …)
WG loaded cavity with Copper WG extentions
Validate EM design
Under fabrication by Research Instruments (RI)
To be delivered by October 16
@1.75 GHz prototype foreseen
A.Vélez, BESSY-II MAC,14-15.06.2016

## Slide 18
Prototypes, 1.5 GHz Single-cell Niobium Cavity
150 mm
100 mm
Rvts 280 mm
110 mm
Niobium single-cell with one sided WG end-group loaded with 2 WG + 1 FPC + 100 mm beam-pipe extension
150 mm extended beam-pipe on the other side (same diameter as copper model)
Fabrication drawings based on the existing copper model
BCP surface treatment
WG flanges? Q drop due to proximity to fundamental mode. Nb flange + Indium sealing ?
Notes: .

## Slide 19
Prototypes, 1.5 GHz Single-cell Niobium Cavity
150 mm
100 mm
Rvts 280 mm
110 mm
Niobium single-cell with one sided WG end-group loaded with 2 WG + 1 FPC + 100 mm beam-pipe extension
150 mm extended beam-pipe on the other side (same diameter as copper model)
Fabrication drawings based on the existing copper model
BCP surface treatment
WG flanges? Q drop due to proximity to fundamental mode. Nb flange + Indium sealing ?
bERLinPro Linac cav
Notes: .

## Slide 20
High Power Couplers
2 x 16 KW CW Couplers
@ 1.5 GHz
Close to 0 beam loading expected, high Qext>1e7 with low power < 10kW
Adjustable coupling is required due to parking (different temperature) and impedance control (within power budget)
Design based on the Cornell 60kW injector Coupler
A.Vélez, BESSY-II MAC,14-15.06.2016
“HIGH POWER TESTS OF INPUT COUPLERS FOR CORNELL ERL INJECTOR”, V. Veshcherevich et al

## Slide 21
Testing, Bead Pulls
EM cavity characterisation
Schwarzschildstraße RF Lab
Tuning machine is foreseen
Warm bead-pull
Cold bead-pull
Cold Bead-Pull
installation in
HOBICAT
Novel design
Inside HOBICAT horizontal test module
Evaluates field profile of SRF cavities
in SC state
Comissioned with a 9 cell Tesla Cavity
Able to characterize HOMs
Results to be published
Cold Bead-Pull Test Results
3/9 Pi

## Slide 22
Testing & Infrastructure
1.5 GHz Single-cell Niobium Cavity
  To be tested in small VTS (HoBiCaT), minor modifications
1.5 GHz 5-cell Niobium Cavities
  Undressed cavities
  To be tested in large VTS, Testing Hall 1 in operation by Q2 2017
  Dressed cavities
  To be tested in Horizontal Test Stand HoBiCaT
  Low power tests
    500 Watts broadband Amp @1.5 GHz+1.75 GHz (to be ordered)
  High power Tests,
    16kW transmitter, SSA
    RF infrastructure: WGs, circulator, water loads …
    Installation in HoBiCaT
1.5 GHz & 1.75 GHz 5-cell Copper Cavites
  To be tested in Schwarzschildstraße RF Lab

## Slide 23
A.Vélez, BESSY-II MAC,14-15.06.2016
Thank you for your attention!