## Slide 1
A. Neumann, TTC meeting at Saclay, 5th-8th July 2016
WG 3, Wednesday
bERLinPro SRF systems - R&D topics and discussion
T. Galek, U. Rostock

## Slide 2
SRF for bERLinPro continued
Gun module covered within
talk on Tuesday
Today:
Booster and Linac status
and open issues

## Slide 3
Booster cavity design
Variation of input coupler section with new 88mm Ø beam tube leaves RF properties unchanged
New „Golf Tee“ coupler tip to increa- coupling, lower penetration depth, lower kick
Coupling section similar to KEK booster design to allow easy integration
Will be equipped with blade tuner as Gun using four symmetric piezos (Cornell)
New transition
Nice and shiny
Cornell cell shape
Made from sheet metal

## Slide 4
Task of the Booster module
The booster module needs to accelerate the beam from 2.3 to 6.5 MeV,
impose an energy chirp and is part of the low emittance injection scheme (see B. Kuske et al., IPAC16).
Two cavities will deliver 210 kW beam power, one is operated in zero-crossing
Operating field level is rather low (Eacc=10 MV/m)
Main issues are minimization of coupler kicks by proper alignment and orientation, control of dark current to a minimum level by varying cavity positions in module
Most critical item is the design and production of the power coupler.

## Slide 5
Emittance growth: CST PIC vs. ASTRA (thanks to S. Wesch)
For a similar misalignment scenario the ”golf tee” coupler is less perturbing the beam’s emittance than the original KEK design (blue vs. green curve)
In the misaligned case the emittance growth is on the percent level, but there is a rather strong kick at 0.4 mrad
For an aligned twin ”golf tee” the emittance growth is negligible (≤1e-3) and the focusing strength changes by 10 % with a 3 % imbalance between both vertical planes in the misaligned case (on-crest)

## Slide 6
Current Booster module layout
Zero-crossing cavity
HOMs, one type
106 mm beam tube
88mm
88mm
106mm
Minimize
required tapering in
module
Decided to have only
one HOM type
Cavities are oriented to minimize coupler kicks (low effect) and amount of possible dark current upstream to cathode (ASTRA/CST 3D field based simulations, M. McAteer et al. IPAC16)
However, coupler port accesibility and layout of cryogenics partially omitted to follow best orientation  Module design finalized w.r.t. required mechanical
2.1 MV cavities
Beam

## Slide 7
Optimizing Booster w.r.t. dark current on cathode
M. McAteer et al., IPAC16
RF phase
Iris
Surface field and normalized Fowler-Nordheim emission
1st cavity zero-crossing
Most effect by distance
cavity 2 to 3

## Slide 8
Some problems during production
Weld repair inside
Weld repair outside
Courtesy G. Ciovati, JLab
2 cavities showed 1 mm Ø hole in the equator weld. They were fixed by inserting
a small high grade Nb cylinder and following welding this area.
Those spots do not seem to be of any problem for the field range required.

## Slide 9
Status Booster Cavities
Booster cavity vertical tests at JLab before and after helium vessel welding (except for BB004) at 1.8 K.
Due to leakage problems below l point at the FPC NbTi flanges, cavity BB001 was only measured at 2.0 K.
The booster cavities all are beyond specifications.
Maximum field with helium vessel mostly 10% lowered after helium vessel welding
For cavity BB003 a field emitter was uncovered after HV welding, for BB002 the emitter vanished
All field emission onset are above the field level of 10 MV/m for bERLinPro
3 out of 4 cavities showed problem of leaking NbTi flanges in superfluid helium

## Slide 10
Next steps Booster
First Booster cavity was measured with new CMM tool. At first glance quite some deviations from drawings  compare with JLab CMM data
This cavity is mounted on support platform and will be tested in HoBiCaT coming quarter
Horizontal tests will show whether the helium leaks found during vertical tests at NbTi flange are of any problem for module operation.
The tapered input coupler section at
the 88mm beam tube side
BB003
Deviations will complicate coupler alingment: Variation of Qext and coupler kicks may result

## Slide 11
Linac Cavity
Operating and RF parameters:
Eacc= 20 MV/m in CW
Beam current: 2 x 100 mA 180 deg. phase shiftes w.r.t. RF
 Low peak field ratios and strong HOM damping required

## Slide 12
Linac Cavity requirements and main design goals
The string needs to deliver 14.8 MV per cavity, thus Eacc⋍20 MV/m
Strong HOM damping required because of interaction with two 100 mA beams Qext lowest dipole ≤5.104
Beam is injected with 6.5 MeV, still soft  coupler kicks and emittance preservation need to be considered…….further power overhead and tuning because of incomplete recovery in one cavity
Low to zero beam power, thus high QL operation at low power possible High mechanical stability required
Beam tube absorbers
Bellows
Bellows and absorbers required but also risk for cavity operation
(Wakes, dust)
110 mm beam tube
Iris 72 mm
5 WG+
1 TTF-III
Current coupler arrangement

## Slide 13
The Linac RF design
Cornell
JLAB
Combine Cornell‘s low peak field design with JLab‘s HOM damping approach
Cornell‘s ERL mid-cell + modified end-cells
5 waveguides
to cover HOM polarizations: Well defined cutoff
TTF-III for variable coupling: High QL operation possible
3rd order
spline nose transition to low cutoff beam tube
F. Fors, JLab

## Slide 14
Module coupler kicks (S. Wesch, A. Neumann)
Old end-group:
Blue: All left
Red: 1 left, 2 right
Yellow: left, right, left
New design, worst case
De≤0.5 %
50x80 mm
50x105 mm

## Slide 15
First module based HOM/Wake studies
Study influence of length of interconneting beam tube on HOM spectrum
Comparing reference run done with full cavity as half cell open boundary somewhat inaccurate
Mode of TM020 type closed to beam harmonic at 3.9 GHz. Typically they have low impedance because of transit time effect
Resolution of Wake calculation limited as very high computational effort
But three different sets of interconnecting groups exist:
5WG+1TTF
4WG+2TTF
6WG
Absorber

## Slide 16
Intense Eigenmode search at 2.6, 3.9 and 5.2 GHz
200 MHz
1e6
1e-4
2.6 GHz
3.9 GHz
5.2 GHz
H.-W. Glock

## Slide 17
Concatenation study of complete string (U. Rostock)
180°
Alternative 1, second version is by rotating first cavity around longitudinal axis by 180 deg
Both orientations show similar performance
T. Galek et al.

## Slide 18
One problem: What type of first flange?
Problems:
WG close to iris for HOM propagation and damping
TM010 mode leakage to WG part  requires SC state thus LHe cooling  Include WG into helium vessel  Complicated weld order
Bellow has to be put on cavity before end-group: Heat treatment, outside BCP??
At what distance to place first flange?
What type of flange, even Nb on Nb?
How long to fabricate WG, as this affects HPR effectiveness
Endgroups will
be made by deep-
drawing
JLab: AlMg gasket, needs well polished surface, expensive, time consuming

## Slide 19
Qualifying flanges/gaskets
First test last week:
Warm test: ok
Quick cooldown 77K: leak
Warm: ok
Slow cool + retighten screws: ok
Warm: ok
Cooling
Vacuum
Pump
port
VATSEAL:
Waveguide
stub
with gasket
to test:
Stainless on stainless
or NbTi on stainless
Gaskets: Copper or copper coated with silver
Requires brazing of steel on Niob: Limit on heat treatment below 600 °C

## Slide 20
Acknowledgements
Thanks to all collaboration partners and
A. Frahm, M. Schuster, J. Ullrich, F. Göbel, S. Klauke, B. Hall, H-W. Glock, P. Echevarria, A. Ushakov, F. Glöckner, D. Böhlick, M. Schmeißer