## Slide 1
Radiation hardness. Tests and Plans.
FATALIC option
Tile Week Upgrade Session (17 February 2016)
François Vazeille (LPC Clermont-Ferrand)
Summary of the radiation ATLAS policy
▪ NIEL (neutrons), TID (photons), SEE (protons).
▪ Tests of 20 components or cards.
▪ NIEL: tests before/after neutron exposure, no obligation of on-line monitoring,.
▪ TID/SEE: on-line monitoring.
TileCal context for TID/SEE
we cannot imagine to test 20 MB or 20 DB (Too much expensive)
 tests of components on dedicated cards.
 Particular cases of Remote HV option and active Dividers
▪ Remote HV option: Radiation tests not requested.
▪ Active Dividers: Tests completed ATL-TILECAL-INT-2015-001
“NIEL and TID certifications of the active dividers of the Tile Calorimeter
of the ATLAS detector for the Phase II upgrade”

## Slide 2
 FATALIC option:
components of All-in-One + FATALIC + Main Board
▪ We have enough available FATALIC4 chips for individual tests.
▪ We must establish the list of components for the All-in-One and MB cards.
- What are the components common to other options ?
Examples: Voltage regulators (Very few for the FATALIC option: only 1.6 V),
charge injection system., amplifier for voltage monitoring…
- What are the specific components ?
Examples: FPGA’s (on Main Board).
▪ We must design and produce the support cards and the monitoring systems.