## Slide 1
Requested hardware
for Clermont-Ferrand in the test beam
2015 September 23
Roméo Bonnefoy and François Vazeille
This material is provided by LPC and Collaboration:
in these slides, the material provided by Collaboration is in red,
this one provided by LPC in blue.
Comment: the planning of the installation has to be discussed.

## Slide 2
Check of the routing of the 125 m long HV cables that can be connected either
to the Demonstrator on the EB module at the A side or to the LB module at
the C side.
Check of the working of the 125 m long HV cables.
Check of the installation of the 2 HV bus cards in the Demonstrator and of the
2 short internal HV cables, with in particular the connections with the flat
connectors on the boards, and of the grounding cables.
Installation of the 2 other HV Bus boards on the pulse and FATALIC drawers,
plus the 2 correspondent short internal HV cables and grounding cables.
- Put the loads on the free channels.
Installation of the HV remote crate in the counting room, with its connections
to the HV Prague source and to the DCS via CANbus.
Installation (without connections) of the 50 m long HV cable that will be used for
specific tests to lengthen one 125 m long HV cable.
Working tests of the Remote system:
▪ Measurements with a multimeter of the individual applied HVs (That requests
the access to the Drawers.
▪ Working of the system via the DCS.
Comments: spare elements will be stored somewhere (HV Bus cards, HV Opto cards,
HV Micro cards).
HV Remote system

## Slide 3
Mini-Drawer close to the Patch Panel in LB Module 0 side C.
2 PMT Blocks with All-in-One boards equipped with FATALIC4b
+ Proto Main Board.
2 flat cables 3 m long driving the pulses to the scope(s)
and going through the Patch Panel.
Laboratory LV Power Supplies: see the radiation problems.
Scope(s) on the Table.
Either Clermont-Ferrand scopes
 Simultaneous records of 6 or 4 pulses with a common beam trigger.
or records in several steps.
or CERN scope if it is compatible with the pulses: see the CERN scope.
 Records in several steps depending from the scope possibilities.
Connections of the scope to a laptop in the counting room,
provided by LPC team or CERN depending from the scope, using an Ethernet cable.
Cooling.
Particle pulse library

## Slide 4
FATALIC tests
Installation of FATALIC/All-in-one sets inside PMT Blocks (10 maximum).
Installation of PMT Blocks in the FATALIC Drawer.
Installation of the Main Board (LPC Version) and of the Daughter Board.
Installation of the Laboratory LV Power Supplies common with pulses.
All connections + cooling.
In fact, 3 strategies can be considered, depending from the LPC work status:
Option A: Main Board + Daughter board set up
▪ The requested connections are the standard Demonstrator connections,
but for the LVs.
Option B: Main Board + USB connection
▪ The DB is replaced by the 2 USB links via a small card close to the MB.
▪ The 2 USB links must be routed across the Patch Panel.
▪ A dedicated PC records the data, plus an Ethernet cable and a laptop outside.
Option C: Main Board Prototype (1/4 MB) + USB connection
▪ The DB is replaced by 1 USB link via a small card close to the MB.
▪ The USB link must be routed across the Patch Panel.
▪ A dedicated PC records the data, plus an Ethernet cable and a laptop outside.