## Slide 1
SIGMA: a detector for γ-ray spectroscopy & imaging Dr Laura Harkness-Brennan
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
@LauraHBPhysics

## Slide 2: Outline
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
DESPEC at FAIR
DEGAS
SIGMA detector design
Theoretical response

## Slide 3: DESPEC
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Low Energy Branch of Super-FRS, FAIR
Half-lives, isomer decays & 𝛽-decays to be measured for 1st time in exotic nuclei
Implanting short-lived exotic nuclei into AIDA
Observe subsequent decays in DEGAS HPGe detector array

## Slide 4: AIDA
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
80x80x1mm Si DSSD (128x128 strips)
ASIC, low (<12keV) noise

## Slide 5: AIDA
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
80x80x1mm Si DSSD (128x128 strips)
ASIC, low (<12keV) noise

## Slide 6: DEGAS Requirements
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk

## Slide 7: DESPEC Challenges
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Efficient detection of 𝛾-rays 50keV to 5MeV
Wide focal plane: 24 x 8 cm2
Low yields in high background
Prompt radiation flash
Correlating events for (1) isomeric decay (t1/2 10ns-100ms, 1mHz-1Hz rate) and (2) 𝛽-delayed 𝛾-ray emission from exotic ions implanted in AIDA

## Slide 8: Methodology
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Use gamma-ray tracking to (1) suppress background & (2) correlate to 𝛽 detected in AIDA
Requirements: segmented detector with excellent energy resolution and <1mm3 position resolution, digital acquisition electronics for pulse shape analysis and deconvolution of pile-up events

## Slide 9: Point (small) contact detectors
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Low capacitance
Excellent energy resolution (~0.5keV @ 122keV, 1.7keV @ 1332keV)
Broad Energy Germanium (BEGe) detectors
  GERDA, MAJORANA neutrinoless double 𝛽 decay
  ALBEGA

## Slide 10: Development of SIGMA
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Segmented Inverted-coaxial GerMAnium Detector
Low electronic noise -> excellent energy resolution
Expected factor of 2-3 improvement in position resolution over gamma-tracking arrays (R Cooper NIM A 665 2011)
Simpler to analyse multiple interactions
Fewer readout channels
Reduction in cost and complexity
FieldGen/SigGen: D Radford

## Slide 11: SIGMA Segmentation
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
P-type crystal, 8 longitudinal rings, 2 concentric segments on front face, 8 sectors, 1 core segment, 1 point-like contact
Longitudinal, z
Radial, r
Azimuthal, ϕ
Small contact
80mm
75 mm

## Slide 12: Data Acquisition
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Multi-channel readout
V1724 digitisers (each 8 x channel)
14-bit 100MHz
Data: timestamp, energy, digitised trace
Energy calculation – MWD algorithm, parameters to be optimised for long charge collection times
Post processing: PSA and tracking

## Slide 13: Project status
Key Milestones
2016
SIGMA detector in production
DAQ tested with unsegmented SAGe well detector
Integrated Geant4/SigGen/FieldGen model
2017
Detector to be delivered
PSA and gamma-ray tracking evaluation
2018
Imaging demonstrated, in-beam tests
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk

## Slide 14: Theoretical signals
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Signals calculated by FieldGen/SigGen (Radford)
Basis set generated

## Slide 15: Position sensitivity
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk

## Slide 16: Drift times
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
dt=t95%-t0%

## Slide 17: Theoretical signals
Development of the SIGMA detector
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Single Interaction
Double Interaction

## Slide 18: Multiple Interactions
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Geant4 x,y,z,E and fieldgen/siggen

## Slide 19: SIGMA DEGAS Array
Development of the SIGMA detector
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Investigate performance of various configurations of SIGMA detector arrays for DEGAS (Marc Labiche and Jon Wright)
Array efficiency calculations to be compared with previously investigated DEGAS array configurations (M Doncel 2015)

## Slide 20: Geant4 model
Development of the SIGMA detector
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Dewar
Preamp housing
HPGe crystal
Cryostat
AGATA G4 toolkit

## Slide 21: Geant4 model
Development of the SIGMA detector
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
Under investigation – Jon Wright

## Slide 22: Absolute Efficiency (Geant4)
Development of the SIGMA detector
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
To be reproduced experimentally
55% relative efficiency at 1332 keV

## Slide 23: Peak to Total (Geant4)
Development of the SIGMA detector
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
To be reproduced experimentally

## Slide 24: Summary
DESPEC requires an array for spectroscopy of 𝛾 transitions following 𝛽, alpha and isomer decay of exotic nuclei in the AIDA implantation detector
SIGMA detector will use point-like contact technology to provide excellent energy resolution and segmentation/PSA will provide position resolution
SIGMA detector will be evaluated for future 𝛾-ray tracking and event-by-event correlation with AIDA events, and industrial imaging
Comparisons to be made between ORNL and Liverpool detectors

## Slide 25: Collaboration and Thanks
AGATA/GRETINA Collaboration Meeting ljh@liverpool.ac.uk
University of Liverpool: Jon Wright , Andy Boston, Dan Judson, Paul Nolan, Robert Page, Fiona Pearce, Carl Unworth
STFC Daresbury: Marc Labiche, John Simpson
Special thanks to David Radford at ORNL and to Ren Cooper, Heather Crawford, Marco Salathe (and others) at Berkeley