## Slide 1: Einstein Probe
A mission to explore the transient X-ray sky
Shuang-Nan Zhang (IHEP/NAOC)
on behalf of
Weimin Yuan (PI of EP, NAOC)
on behalf of the EP team (based at NAOC & IHEP)

## Slide 2: 2020+ : multi-wavelength & multi-messenger time-domain astronomy
Multi-wavelength
Multi-messenger
GW, neutrino
radio
optical
X-ray
γ-ray
Time
LOFAR、SKA
LSST
Soft X-ray yet to cover
Adv. LIGO
LIGO/VIRGO/Kangra
IceCube
SVOM

## Slide 3: Needs for more sensitive surveys of X-ray transients
Largely unexplored
SWIFT/BAT
MAXI
SVOM/Eclairs
Requirements: higher sensitivity, large FoV, and high cadence
Z>10 GRBs

## Slide 4: Electromagnetic sources of gravitational wave events
High frequency GW
radio
X-ray
IR/optical
γ-ray
NS-NS/BH-NS mergers
EM spectrum
GW
LIGO/VIRGO
EM counterparts
Of great scientific significance
Notes: One particularly exciting topic is detecting the EMC of GW events.
LIGO and VIRGO are expected to

## Slide 5
Lobster-eye micro-pore optics for wide-field imaging
Ideal for X-ray wide-field monitor
lobster eye in the optical
Concept proposed by R. Angel in 1979
Device industrialised in recent years
20μ
True imaging
Wide FoV, no vignetting effect
Good angular resolution: ~ arcmin (c.f. ~ degrees for Swift, MAXI, …)
High sensitivity
Low weight

## Slide 6: Development of X-ray MPO applications at NAOC
Development started form 2010 at X-ray Imaging Lab, NAOC
(lead: Zhang S.-N.)
Prototype MPO lobster-eye camera and X-ray image
true focal spot

## Slide 7: Einstein Probe (EP)
a small mission for time-domain all-sky monitoring in soft X-ray to discover high-energy transients and study variability
one order-of-mag. more sensitive than those currently in orbitwith X-ray follow-up & fast alert downlink capability
payload
Wide-field X-ray telescope (12 modules)
  3600 sq. deg. (1.1 sr) vignetting free FoV in 0.5-4keV band
Follow-up X-ray telescope, 0.5-10keV
Payload weight: 450kg (~900kg total)
Fast alert data downlink (and possible uplink)

## Slide 8: EP payload
X-ray optics: lobster-eye MPO
Detectors: CMOS array
Focal length: 370mm
FoV: 3600 sqr. deg. (1.1 sr)
FWHM: ~ 5 arcmin
Bandpass: 0.5-4 keV
  Wide-field X-ray telescope (WXT)
X-ray optics: Wolter-I type
Focal length: 1.6m
Effective area: > 120cm2 @1keV
FWHM: < 2 arcmin (30” goal)
FoV: ~30 arcmin
Detector: CCD
Bandpass: 0.5-8 keV
  Fellow-up X-ray telescope (FXT)
WXT
FXT
star sensor
FoV

## Slide 9: Wide-field X-ray telescope
12 modules
~300 sq.deg. each
Weight: 240kg
Power: ~300W
detector: back illuminated CMOS
Available: back illuminated
2cm x 2cm (2kx2k)
future: 6cm x 6cm 4kx4k
energy resolution 210 eV
@ 5.9 keV @ room temp.
CMOS chip for test and the design of focal plane unit for a WXT module

## Slide 10: Simulated performance of WXT
PSF (simulated)
Effective area (simulated)
FWHM ~ 5 arcmin
Ir coating
Zhao et al. 2017, Exp. Astro.

## Slide 11: Monitoring sensitivity of EP

## Slide 12: Core science goals
Uncover quiescent Black holes at all astrophysical mass scales and other compact objects via capturing their transient flares
Detect and localize electromagnetic-wave sources of gravitational-wave events by synergy with GW detectors
Systematic survey of soft X-ray transients and variability of X-ray sources at high sensitivity and high cadence

## Slide 13
Scientific objectives: systematic survey of transients & monitoring variability in X-ray
High-redshift GRB
Trace first stars/BH
Early universe
BH Tidal disruption
Quiescent MBH finder
BH accretion/jets
SN shock breakout
SN physics
Size of progenitors
Active galactic nuclei
Extreme gravity, BH accretion/jets/growth
SGR/magnetar
extreme magnetic Field
Star X-ray flares
Magnetic fields
Corona activity
BH X-ray binary
Extreme gravity
BH physics/accretion
Thermal nuclear burst
Neutron stars physics
X-ray flash
& LL GRB
GRB physics
Neutron-star merger
EM counterparts of GW sources
Notes: EP will detect X-ray transients from our neighbour stars, magnetars, bursts form neutron star and white dwarfs,
BH X-ray binaries in our Galaxy and nearby galaxies, intermediate-mass BH, TDE of SMBH in normal galaxies, and
Active galactic nuclei, and to the high-redshift GRB (perhaps at redshift around 10 and beyond).
It can also detect charge exchange emission from comets in our solar system.
The research will have impact on essentially all the fields of astrophysics.

## Slide 14: Estimated detection rates of selected transients
Type of events | Estimated detections per year
Tidal disruption events (TDE) | 20-120
TDE with jets | 20 - 40
SN shock breakout | 7
GRB z > 6 (8) | 7 (3)
magnetar | 1
X-ray flash | ~10
Low-luminosity GRB | < 8
SFXT | ~ 13
Stellar flares | In large number

## Slide 15: Mission profile
Orbit: 600km, incl. < 30deg
Observation mode
  Survey mode: a series of pointings to the night-sky, each 11min exposure
  cover the whole night sky in 3 orbits (97min each)
  Follow-up mode: pointed observation with FXT (WXT remains operation)
  Possible ToO mode
On-board transient data reduction
Quick alert data downlink
  Baseline: Beidou navigation system
  VHF network (French)
Nominal lifetime: 3 (+2) years
Night-sky zone

## Slide 16: Current status
Among the top candidate missions in the 13th-5-year plan of CAS’s space science program; Currently under the final critical review, and the final adaption is expected to happen recently
Proposed launch: 2021/22
China’s space science & exploration road map
D. Normile 2016 Science

## Slide 17: Summary
Time domain astronomy has come of a golden age of multi-wavelength & multi-messenger
New technology is needed to look both deeper & wider in soft X-rays
MPO lobster-eye is such a promising technique
The Einstein Probe is a small yet ambitious mission, which is expected to explore new discovery space …...
Thank you
http://ep.bao.ac.cn