## Slide 1: TrueBeam model with GATE INSERM U1037 (CRCT) Toulouse Jeremy LESTE, Tony YOUNES, Sara BEILLA, Xavier FRANCERIES, Laure VIEILLEVIGNE, Luc SIMON, Manuel BARDIES
OpenGate Technical Meeting
May 11th 2017
Clermont-Ferrand

## Slide 2: The Varian TrueBeam Linear Accelerator
Two real machines are available at IUCT-Oncopole
CRCT Team15
TrueBeam
Assessment and validation for clinical situation

## Slide 3: The Varian TrueBeam Linear Accelerator
Confidential data provided by the manufacturer (available on myvarian.com)
The Truebeam Package includes :
  A geometry description Some geometrical details are missing
  .IAEAphsp and .IAEAheader files (version 2)
    Approx. 50 Gb for each energy mode: 6FF, 6FFF, 10FF, 10FFF
    21 bytes/part
    All particles start from a plane located before primary jaws

## Slide 4: The model
A bash script generates the TrueBeam macro files for GATE including:
  Phase space planes
    One to attach IAEA files provided by Varian
    One to attach IAEA files generated by a previous GATE simulation (speed up the computation)
  X and Y Jaws
  Mylar
  Baseplate
  A set of simple phantoms
  MLC HD (120 leafs, central leafs ok, last leafs in progress)
  EPID (work in progress)
  CT scan (possible but not with the script)

## Slide 5
User choose: (using a configuration text file)
  X/Y field size
  Gantry rotation (head)
  MLC file from Varian Eclipse TPS (static ok, dynamic work in progress)
  EPID (distance)
  A macro for the “phantom”
  A macro for the Gate Actor
The model
Possibility to split in multiple jobs adapted to our clusters architecture
    new one 25 iMacs (100 cores – 3.2 GHz)
    Managed by HTCondor
    Using a Docker Gate Image (works approx. as a virtual machine)
      See: manureva/ubuntu-gate:16.04-7.2

## Slide 6: Validation in water
Beilla et al.
Physica Medica in press

## Slide 7: Validation in very low density media
Beilla et al.
Physica Medica in press
Phantom Water/Cork
IUCT clinical algorithm: Eclipse AAA v13
d=0,12 (Lung -DIBH)
(Deep Inspiration Breath Hold, ex. lung SBRT)

## Slide 8: Assessment for a lung cancer patient (SBRT)
Beilla et al. Physica Medica in press
d=0,12 (Lung –DIBH)
AAA:
Over-estimates dose in lung ?
Underestimates dose in tumor ?

## Slide 9: MLC: Heterogeneity study
Younes et al. Accepted at AAPM 2017
Relative dose absorbed dose (%)
Distance (mm)

## Slide 10: MLC: Output Factor study
Younes et al. Accepted at AAPM 2017

## Slide 11: EPID (electronic portal imager device)
Project STEREPID (Physicancer 2016): to use EPID dose images for QA and 3D in-vivo dosimetry (small fields + SBRT)
Monte Carlo simulation gives a predictive dose image
Comparison with dose image acquired on the TrueBeam
EPID dose images
Gate output : Dose.raw

## Slide 12: EPID (electronic portal imager device)
First results in agreement with measurement but need improvement
Details of the EPID composition missing
Low sensibility (need a significant amount of particle)
  Compromise of resolution and statistic noise

## Slide 13: Thank you