## Slide 1: Switched Mode Power Supply (DC/DC buck converter)
1-Why use a DC/DC converter ?
2-Architecture
3-Conduction modes
  Continuous Conduction Mode
  Discontinuous Conduction Mode
4-Stability
  Voltage Mode
  Current Mode
  Modulator transfer function
  Filter transfer function
  Compensator transfer function
  Overall transfer function
5-Efficiency
6-Characteristics

## Slide 3: Why use a DC/DC converter ?
VbatPow
SMPS
GndPow
SMPS
OUT
LDO
LDO
OUT
3.6V
1.2V
RF
The SMPS converts the battery voltage to a lower voltage with high efficiency. That is, little power is lost in the converter itself. An SMPS output voltage of only 100mV above the LDO output voltage is sufficient for the LDO to perform normally. Thus, the LDO efficiency is in turn greatly improved.
The role of the LDO is to filter the output voltage ripple produced by the SMPS.

## Slide 4: Switched Mode Power Supply (DC/DC buck converter)
1-Why use a DC/DC converter ?
2-Architecture

## Slide 5: Architecture
Buck or down converter: output voltage is lower than the battery voltage.
The following basic blocks combine to form a complete DC/DC converter:
Ramp generator
Error amplifier
Pulse Width Modulator
Control logic
Output filter
All elements can be integrated except the output filter which is made up of an external inductor (some microH) and capacitors (some microF). A parameter to keep in mind for integration purpose is the thickness of these components which must be compatible with the package.
Vmod

## Slide 6: Architecture
The error voltage is compared to the ramp voltage to produce a PWM signal which in turns set on or off the output power transistors.
When the output voltage becomes lower than the reference voltage, the error signal increases so does the duty cycle of the PWM signal. Therefore, the power Pmos transistor is acting more frequently than the Nmos leading to a higher output current.

## Slide 7: Architecture
The modulator output is a rectangular wave. This rectangle is averaged by the output filter and applied to the load.
Vbat
Pmos ON
Pmos OFF
Ton
Toff
Vmod
t
Vbat
The duty cycle is defined as :
T

## Slide 8: Architecture
The output DC voltage is therefore the average of the rectangular pulse waveform, or:
Where D is the duty cycle of the output and is defined as the time the output is connected to Vbat divided
by the period of the witching frequency.
Notice that the frequency of the ramp signal determines the frequency of the modulator output, which is the
switching frequency of the converter.

## Slide 9: Switched Mode Power Supply (DC/DC buck converter)
1-Why use a DC/DC converter ?
2-Architecture
3-Conduction modes
  Continuous Conduction Mode
  Discontinuous Conduction Mode

## Slide 10: Continuous conduction mode
Iself
Iout
t
High current
Iout
t
Iout
t
Low current
Iself > 0
Iself = 0
Iself < 0

## Slide 11: Continuous conduction mode
DTs
(1-D)Ts
Vbat
T
Iself
(Vbat-Vout)/L
(-Vout)/L
Vmod
Iout
Icapa
I=0
Imax
Imin
Vout
V
DTs/2
(1-D)Ts/2

## Slide 12: Continuous conduction mode
Current ripple:
Voltage ripple:

## Slide 13: Discontinuous conduction mode
Iself
Iout
t
High current
Iout
t
Low current

## Slide 14: Discontinuous conduction mode
DTs
(1-D)Ts
Vbat
T
Iself
(Vbat-Vout)/L
(-Vout)/L
Vmod
Iout
Icapa
I=0
Imax
Imin
Iout=0

## Slide 15: Switched Mode Power Supply (DC/DC buck converter)
1-Why use a DC/DC converter ?
2-Architecture
3-Conduction modes
  Continuous Conduction Mode
  Discontinuous Conduction Mode
4-Stability
  Voltage Mode
  Current Mode
  Modulator transfer function
  Filter transfer function
  Compensator transfer function
  Overall transfer function

## Slide 16: Voltage mode regulation
Gain
Compensation
Network
H2(p)
Ramp generator
PWM
Vmod
LC filter
H1(p)
Vout
Vref
Vramp
Verror
This scheme comprises an error amplifier, a PWM modulator and an LC filter. It also includes a compensation network around the error amplifier to make the loop stable.
This compensation network contains at least one pole and two zeros (to cope with the second order pole of the LC filter), the ultimate goal being to obtain a closed loop transfer function equivalent to a first order system.

## Slide 17: Current mode regulation
Gain
Compensation
Network
H2(p)
Ramp generator
PWM
Vmod
LC filter
H1(p)
Vout
Vref
Vramp
In this kind of regulation, the inductor current is just subtracted to the output of the compensation network. This second internal loop helps to stabilize the system by forcing the loop to behave like a first order system in high frequency
Iself

## Slide 18: Modulator transfer function
Of the three blocks that make up the buck converter, the modulator is the only one with no frequency dependence. The modulator is basically a voltage-controlled rectangle wave generator.
Ton
Toff
Vmod
Vbat
T
Vramp
Verror
Thus, the duty cycle can be expressed as:

## Slide 19: Modulator transfer function
The modulator transfer function is the change in the average value of Vmod divided by a change in the error voltage:
This is the gain of the modulator. In reality, this block has also time delays which cause phase shift. However, this phase shift usually is not a problem for the calculation of loop gain and phase and can be neglected in a first step. It will be addressed later in the design phase through transient simulation. (or by use of more advanced SPECTRE RF simulation).

## Slide 20: Filter transfer function
The modulator provides a pulse train, bounded by the battery voltage, whose duty cycle is determined by an applied control voltage. The output filter performs the averaging function that converts this pulse train into the output voltage of the converter. The cut-off frequency of the filter must therefore be an order of magnitude lower than the switching frequency.
Because the goal of a dc/dc converter is to have high efficiency, the output filter consists of reactive components which do not dissipate power. This filter operates as a low pass filter in the frequency domain and is as simple as a second-order LC filter terminated by the load resistance. Therefore, the load resistance is a critical component of the filter and must be known in order to predict the filter’ s performance, the loop response and the stability of the converter.

## Slide 21: Filter transfer function
Ideal LC filter

## Slide 22: Filter transfer function
LC filter with parasitic

## Slide 23: Filter transfer function
At the cutoff frequency the phase shift of -180dg is very sharp in an ideal filter and is somewhat smoothed in a real filter. These series resistances (usually referred to as ESR) in both the inductor and the output capacitor help to stabilize the loop.
The gain slope is –40 dB per decade of frequency increase above the LC cutoff frequency.
From these considerations, we guess that two zeros have to be inserted in the loop to compensate for this brutal phase shift.
The filter transfer function is then at first order:

## Slide 24: Compensator transfer function
This chapter describes the design of the compensator for the voltage mode buck converter.
The error amplifier has to amplify the difference between the reference voltage and the output voltage with sufficient accuracy (i.e. low static error).
Its compensation network must also compensate for the 180dg phase shift of the LC filter in order to make the system stable (i.e. behaves like a derivator around the filter resonance frequency). Additionally, it must ensure sufficient bandwidth for the overall loop.

## Slide 25: Compensator transfer function
Ro is inserted to set the DC level on node Vout:
The compensator DC gain is then:
Vout
Verror
Compensator schematic

## Slide 26: Compensator transfer function
The compensator transfer function is then:
Assuming an ideal opamp:
Vout
Verror
Compensator schematic

## Slide 27: Compensator transfer function
=64dB
R0/(R0+R1)=-11.5dB
=52.5dB
Zero1: 1/R2.C2
Zero2: 1/R1.C3 (R3<<R1)
Fu’ : 1/R1.C2 (C1<<C2)
Pole1: 1/R3.C3
Pole2: 1/R2.C1 (C1<<C2)
Zero1
Zero2
Pole1
Pole2
Fu”

## Slide 28: Compensator transfer function
f<z1 : integrator
z1 < f < z2 : gain
z2 < f < p1: derivator
p1 < f < p2: gain
R3
c
p2 < f : integrator
c
c
c

## Slide 29: Overall transfer function
Rload
Vout
Verror
Vmod

## Slide 30: Overall transfer function
A classical strategy for placing the poles and zeros is demonstrated here. Besides deciding where to place the poles and zeros, the compensator gain also determines the crossover frequency of the loop.
First, the loop crossover frequency has to be chosen and is based on the switching frequency and the desired loop transient response.
Although the selection of the filter components have not been discussed, they are mainly chosen based on dynamic issues in the circuit design. Remember that the current ripple (respect. the voltage ripple) is inversely proportional to the L value (respect. to the LC product).
Usually, the output inductor and capacitor are decided before the compensator design is started.
The ESR(Electrical Serial Resistor) of these components have to be taken into account due to their impact on the efficiency and the stability of the loop.
The roll-off behavior C=f(V) and the inductor saturation current L=f(IL) have also to be considered. (i.e. the inductance must be compatible with the maximum current involved).

## Slide 31: Overall transfer function
Step 1: Calculate the resistor R0
Given a current consumption Iref through R0:
Step 2: Calculate the Resistor Divider Values
Step 3: Calculate the filter’s resonant frequency
Step 4: Place a first zero slightly below the filter’s resonant frequency
Step 5: Place a pole at the crossover frequency

## Slide 32: Overall transfer function
Step 6: Calculate the required gain of the compensator at the desired crossover frequency
Step 7: Set the gain of the compensator
(Note that at this frequency, the system behaves like an amplifier with a gain of R2/R3)
Step 8: Place a second zero just below the filter resonance
Step 9: Place a second pole about a decade above the crossover frequency

## Slide 33: Overall transfer function

## Slide 34: Switched Mode Power Supply (DC/DC buck converter)
1-Why use a DC/DC converter ?
2-Architecture
3-Conduction modes
  Continuous Conduction Mode
  Discontinuous Conduction Mode
4-Stability
  Voltage Mode
  Current Mode
  Modulator transfer function
  Filter transfer function
  Compensator transfer function
  Overall transfer function
5-Efficiency

## Slide 35: Efficiency
Since the battery provides an average current of Iout during the time D.Ts (and nothing during the remaining time (1-D).Ts ), its average current along a period Ts is:
The power provided by the battery can then be expressed as:
The output power is given by:
In case of an ideal DC/DC converter, the efficiency can then be expressed as:
Of course, in a real world, some losses deteriorate the efficiency.

## Slide 36: Efficiency
Three kinds of losses degrade the efficiency of an SMPS.
1-Joules losses:
They are due to the current which flows through the resistive path.
output power Pmos : .D
output power Nmos : .(1-D)
ESR inductor:
ESR capacitor: usually negligible
Example: Vbat=3V Vout=1.5V Iload=20mA, Ronp=0.96Ω, Ronn=0.53Ω, ResrL=1.5Ω, ResrC=5mΩ
output power Pmos :
output power Nmos :
ESR inductor:

## Slide 37: Efficiency
2-Switching losses:
They originate from the charging(discharging) of the parasitic capacitors associated with each device.
Dynamic power in switched capacitor system:
Phase 1
Phase 2

## Slide 38: Efficiency
2-Switching losses:
Example:
Cgs: NMOS +PMOS grid/source capacitor : Cgs=2.51pF
Cgb: NMOS +PMOS grid/bulk capacitor : Cgb=2.71pF
Cdb: NMOS +PMOS drain/bulk capacitor : Cdb=2.8pF
Cgd: NMOS +PMOS grid/drain capacitor : Cgd=1.88pF
= 840uW
3-Quiescent losses:
This comes from the bias current of each stage.
Example: Iq=200uA, Vbat=3V
=600uW
4-Efficiency:
Example: Pout=60mW

## Slide 39: Efficiency
Iout

## Slide 40: Switched Mode Power Supply (DC/DC buck converter)
1-Why use a DC/DC converter ?
2-Architecture
3-Conduction modes
  Continuous Conduction Mode
  Discontinuous Conduction Mode
4-Stability
  Voltage Mode
  Current Mode
  Modulator transfer function
  Filter transfer function
  Compensator transfer function
  Overall transfer function
5-Efficiency
6-Characteristics

## Slide 41: Characteristics
The various operating requirements are namely:
Battery voltage (Vbat)
Output voltage (Vout)
Output current range (Iout some mA)
Maximum output voltage ripple (Vripple some mV)
Clocking frequency (Fck some MHz)
Notice that in RF design, the clock frequency must be chosen carefully depending on some spectrum specifications.
Some additional requirements:
Load regulation : precision of output voltage while output current is changing
Load transient : response to an output current step
Line regulation : precision of output voltage while battery voltage is changing
Line transient : response to a battery voltage step
Efficiency (quiescent current)
Startup time

## Slide 42: Characteristics
Load transient : response to an output current step
DC/DC converter
Vout
Vbat
VOUT
Some tens of mV

## Slide 43: Characteristics
Load regulation : precision of output voltage while output current is changing
DC/DC converter
Vout
Vbat
Iout

## Slide 44: Characteristics
Line transient : response to a battery voltage step
DC/DC converter
Vout
Vbat
VOUT
Some tens of mV

## Slide 45: Characteristics
Line regulation : precision of output voltage while battery voltage is changing
DC/DC converter
Vout
Vbat
Vbat

## Slide 46
Patent 1 et 2

## Slide 47: To add
Boucle locale _ boucle globale _ Article de geelen