## Slide 1: Revue des mesures de temps ASIC/FPGA du pôle MicRhAu

## Slide 2: Time line
2013
2014
2015
2016
2017
24-ch, TDC of 25 psRMS Tsinghua university for RPC/MGRPC
CRONOTIC
32-ch, LSB:20ps target
Remarque : erreur incompressible de pas de quantifiquation
LSB~RMS*sqrt(12)
LSB ≠ resolution RMS
HODOPIC
DLL
LSB=200ps
Resolution=700psRMS
TDC_BRICK
VGRO
LSB=60ps
Phase Detect~1psRMS S-curve
XOR ring oscillator
CRONOTIC2
Multi-detecteur de phase
[TODO, Thèse CIFRE]
C. Girerd,
VGRO sur Cyclone III
LSB=20ps over 2.4ns range
CMS_muon  Sept2017
64-ch, TDC of 35 psRMS
(Generator)
200 psRMS With detector
[TODO]
FPGA
ASIC

## Slide 3: TDC_BRICK (IBM 130nm)
Slow Ring
Oscillator
Fast Ring
Oscillator
Phase
detector
N0
Counter
Enable
Latch
Start
Stop
N1
Counter
Enable
TDC result
- Simple architecture: Low Area, low consumption, can implemented in standard cells
The TDC resolution is given by the frequency difference between oscillators
In theory the resolution can be very small, as small as the frequency difference
ASIC | [1] Youngmin Park Wentzloff | [2] Jianjun Yu
Process | 65 nm | 130 nm
Resolution | 1 ps * | 8 ps
DNL/INL | 0.5/0.8 ** | 0.5/0.8
FPGA | [3] Sachin S. Junnarkar | This Work
Process | ALTERA Stratix II | Cyclone III
Resolution | 11.8 ps (rms) | ~ 10 ps *
DNL/INL | 0.5 / 1 | -
*Range 0 to 130 ps
** Simulation
* under test
Slides from C.Girerd

## Slide 4: TDC_BRICK (IBM 130nm)
Si LSB=60ps  OK sur 1ns
Sdev [s]
Delay_IN Pas=150[ps]
Si LSB=150ps  OK sur 3ns
Si LSB=20ps  pas OK
period [ns]=f(code)
Xtalk
Presenté à VLSI 2014, marseille

## Slide 5: TDC_BRICK (IBM 130nm)
Propagation delay D to Q
Propagation delay CLK to Q
Minimum set-up time = 15 ps
(include generator jitter)
6 ps width
RMS resolution = 1ps
(include generator jitter)

## Slide 6: Clock reference of 1 GHz is used as stop signal on the fast oscillator
Slow
Oscillator
Fast
Oscillator
Phase
detector
slow
Counter
Enable
fast
Counter
TDC result
Event (start)
D
Vdd
Q
R
Clk_Ref (stop)
D
Q
R
D
Q
R
Vdd
Reset
Ready
T = (N0*T0)-(N1*T1)
t
1
2
3
4
5
Event
Stop
T
Phase detection
Clk ref
Start
Oscillator stop
T0
T1
1
2
CRONOTIC (TSMC 130nm)

## Slide 7: CRONOTIC (TSMC 130nm)
Simplified TDC channel
Top Clk ref (40 MHz)
Clk ref.
period
1 to 2 ns
Event (Trigger)
Ready
S
E
R
I
A
L
I
Z
E
R
c
start
Osc.
ASIC (1 ch.)
stop count
stop count
Signal processing Board
In slow calib.
Slow
Oscillator
Fast
Oscillator
c
c
c
Calibration
c
Phase
detector
I2C
start
Osc.
In fast calib.
c
Slow counter
10 bits
Fast counter
10 bits
Fine
counter
Coarse
counter
RST global
Fast Clk ref.
Generator (PLL)
TX_SLVS
RX_SLVS
(Clk ref = k * 40MHz)

## Slide 8: CRONOTIC (TSMC 130nm)
TSMC 130 nm process
32 channel
Triple-voting rad-hard digital
Dimensions :
  2,400 x 2,450 mm2
Submitted Nov 2nd 2016
ASIC returned from fab by end of January
Packaging is done (CQFP 128)
Test board must be designed, it started by beginning of March
Credit : M. Dahoumane

## Slide 9: CRONOTIC 2
Deux Ring oscillateurs (f_Slow < f_Fast)
8 éléments de retard en différentielle  16 transitions S(1) à S(8), S(1) à S(8) et F(1) à F(8), F(1) à F(8)
Une matrice de détection de phase PDij avec i=[1..8] et j=[1..8]
La résolution LSB = delay_slow – delay_fast
Réduire le temps mort, et le jitter cumulé
Détecteur de phase multiples

## Slide 10: CRONOTIC 2
T_Hit = (Ns Ts - Nf Tf ) + (ns τs – nf τf )
T_Hit= (16N+n)(τs-τf)  avec Ts=16τs, Tf=16τf si Ns=Nf et ns=nf

## Slide 11
Re-ordonner la position des détecteur de phase
time [ns]