## Slide 1: Characterization of detectors for the inner tracking system of the ALICE experiment on the LHC
Master thesis supervised by Felix Reidt and Boris Hippolyte | June 13, 2017
Natalia Emriskova, M2 PSA
00

## Slide 2: outline
  ALICE ITS upgrade
      ALICE collaboration
      Current detector and ITS
      Upgrade motivations
      ITS upgrade layout
      ALPIDE pixel chip
  Test beam framework
    Test beam setup
    One telescope plane
    Analysis software
  3. Analysis steps
    Efficiency profile
    Multiple scattering
    Pixel response from data
    Pixel response model
  4. Pixel matrix edge
  5. Dead double column
  Conclusion & outlooks

## Slide 3: 1 ALICE ITS upgrade
ALICE = A Large Ion Collider Experiment
  International collaboration
  1800 members – 174 institutes – 42 countries
  Studying Quantum Chromodynamics (QCD) and Quark-Gluon Plasma (QGP)
  Experiment at the Large Hadron Collider (LHC) at CERN
1.1 ALICE collaboration
Notes: QGP = state of matter with extreme temperature and energy density

## Slide 4: 1 ALICE ITS upgrade
1.2 Current Inner Tracking System
Pixel
Drift
Strip
Inner Tracking System (ITS)

## Slide 5: 1 ALICE ITS upgrade
ALICE physics program:
  Thermalization and hadronization of charm and beauty in QGP
  In-medium (QGP) parton energy loss
  Quarkonia dissociation
ITS upgrade goals:
  Highly efficient tracking with special emphasis on very low momenta.
  Very precise reconstruction of secondary vertices from decaying charm and beauty hadrons.
1.3 Upgrade motivations

## Slide 6: 1 ALICE ITS upgrade
Beam pipe diameter
29.8 mm → 19.2 mm
First detection layer
39 mm → 22 mm
Number of layers
  6 → 7
Silicon pixel sensors
  resolution: 5 µm
Read out rate
1kHz → 50 kHz (Pb-Pb)
200 kHz (p-p)
Low material budget
1.4 ITS upgrade layout

## Slide 7: 1 ALICE ITS upgrade
1.5 ALPIDE pixel chip
Notes: Analog electronics in pixels, digital signal is propagated to the periphery which is a small inactive region at the bottom
The ALPIDE chip does in-pixel amplification and discrimination. Furthermore, in-pixel hit-buffers can store the hits. The chip is readout using in-matrix data-sparsification based on a priority encoder. Only the addresses of hit pixels arrive at the small periphery, which contains biasing and off chip communication.

## Slide 8: 1 ALICE ITS upgrade
1.5 ALPIDE pixel chip – detection principle
Notes: Charge sharing

## Slide 9: 1 ALICE ITS upgrade
1.5 ALPIDE pixel chip – two important features
Periphery circuit
Pixel Matrix
1. Guard ring
2. Double columns
ALPIDE
Guard ring

## Slide 10: 2 Test beam Framework
Side view:
Top view:
0
1
2
Pion beam
of 6 GeV/c
4
5
6
Device Under Test
(DUT)
3
Y
Z
Z
X
2.1 Test beam telescope

## Slide 11: 2 Test beam Framework
Periphery circuit
Active Matrix
Y
X
0
ALPIDE chip
2.2 One telescope plane

## Slide 12: 2 Test beam Framework
Y
X
0
DUT ALPIDE chip
edge
column 1023
2.3 Analysis software
Analysis Processor:
Include the borders
EUTelescope modifications
100 μm
cut borders

## Slide 13: 2 Test beam Framework
Y
X
0
Active
Matrix
DUT ALPIDE chip
cut
column 850
edge
column 1023
2.3 Analysis software
Analysis Processor:
Include the borders
Converter:
  Create an artificial edge
EUTelescope modifications

## Slide 14: 2 Test beam Framework
Y
X
0
Active
Matrix
Dead double
columns
DUT ALPIDE chip
cut
column 850
edge
column 1023
2.3 Analysis software
Analysis Processor:
Include the borders
Converter:
  Create an artificial edge
  Dead-double-column Finder: 0 ≤ X ≤ 850 off
EUTelescope modifications

## Slide 15: 2 Test beam Framework
DUT ALPIDE chip
Y
X
0
Active
Matrix
cut
column 850
edge
column 1023
Analysis Processor:
Include the borders
Converter:
  Create an artificial edge
  Dead-double-column Finder: 0 < X < 851 off
  Analysis Processor:
  Set 10 bins / pixel on X
EUTelescope modifications
Cut region
2.3 Analysis software
+ development of post-processing macros

## Slide 16: 3 analysis
n
k
3.1 Efficiency profile

## Slide 17: 3 analysis
Matrix edge
Artificial edge
3.1 Efficiency profile

## Slide 18: 3 analysis
3.1 Efficiency profile

## Slide 19: 3 analysis
3.1 Efficiency profile
Artificial edge
Physical edge
one pixel
one pixel
Cut
Edge

## Slide 20: 3 analysis
3.2 Multiple scattering model
µ
cut
Erfc(x)
Step function
Error function
x
x
x
ε
ε
ε

## Slide 21: 3 analysis
3.2 Multiple scattering model
Artificial edge
Physical edge
one pixel
one pixel

## Slide 22
3 analysis
3.3 Cluster shapes
Notes: Impinging point inside one pixel

## Slide 23: 3 analysis
3.4 Pixel response from cluster shapes
Systematic uncertainty dominating
Residual misalignment of the data

## Slide 24: 3 analysis
last rejected pixel
3.4 Pixel response from cluster shapes
Notes: Don’t comment the chi2
Explicite which ic compared and in which range

## Slide 25: 3 analysis
3.5 Pixel response model
Before convolution
After convolution

## Slide 26: 4 Pixel matrix edge
last pixel
Notes: Compare to the 100 micron gap

## Slide 27: 5 Dead double column
2 pixel columns

## Slide 28: Conclusion
In-pixel response study of the ALPIDE chip using test beam data
The sensor edge:
  Multiple scattering – minor effect
  Pixel response dominant
  Efficiency loss du to the guard ring ~ 24 %
  Only in the last pixel column
Dead double column:
  Efficiency loss ~ 73 %
  Charge sharing can recover ~ 27 %

## Slide 29: Thank you

## Slide 30: Back ups

## Slide 31: Runs used in the analysis
Run number | Number of events
3180 | 15 251
3181 | 65 017
3182 | 169 399
3183 | 40 107
3184 | 40 440
3185 | 40 149
3186 | 35 873
3187 | 40 140
3189 | 39 838
3190 | 39 767
3191 | 39 172
3192 | 39 956
3193 | 40 159
3195 | 40 297
TOTAL | 685 562

## Slide 32: Efficiency error calculation

## Slide 33: Calculation of sigma tr
Single point resolution
residual
Track resolution
2.833 μm
6.009 μm
5.229 μm

## Slide 34: Residual Gaussian fit

## Slide 35: 3 analysis
cut
active
3.3 Cluster shapes

## Slide 36: Chi² calculations
Data vs. pixel response from cluster shapes
Pixel response from cluster shapes vs. model

## Slide 37: Efficiency loss calculations
Effect | Integral (µm) | Efficiency loss (%)
Total |  | 
Multiple scattering |  | 
Guard ring |  | 
Effect | Integral (µm) | Efficiency loss (%)
Total |  | 
Multiple scattering |  | 
Guard ring |  | 
Pixel matrix edge
Dead double column
Effect | Integral (µm) | Efficiency loss (%)
Dead double column |  | 
Effect | Integral (µm) | Efficiency loss (%)
Dead double column |  | 

## Slide 38: Dead Double column asymmetry
22.8 μm
20.1 μm

## Slide 39: Bethe-bloch formula