SiW ECAL
2017 Beam Test
New badbcid definition
Retriggers/plane events → same feature?
List of masked channels
Pedestal analysis
Pedestal/width/npeaks map
Tagged events → multiple peaks

---
Tagging bad events: badbcid
- New badbcid definition:
  - if sca+1 is filled with consec bcid, but sca+2 not, then badbcid[sca]==1 && badbcid[sca+1]==2 (bcid+1 issue, events are not bad, just the next sca is bad)
  - if sca+1 is filled with consec bcid, and sca+2 also, then badbcid[sca]==3 && badbcid[sca+1]==3 (retriggering)
  - if sca+1 is not filled with consec bcid, badbcid==0
  - badbcid==0 → ok
  - badbcid==1 → 1st sca of bcid + 1 (keep this for hits)
  - badbcid==2 → 2nd sca of bcid+1 (do not keep it)
  - badbcid==3 → if sca+2 is filled, retriggers (do not keep it)
  - badbcid+=32 → events with ADC=4 (not keep them)

---
 Retriggers vs plane events
- Selection:
  - Up → badbcid==3, nhits<20(64)
  - Down-→ badbcid>-1, nhits>20(64)
- Same pattern in BCID[sca+1]-BCID[sca]
  for retriggers/plane events
- First burst of noise happens in ~bcid+3 with nhits~64.

---
Masked channels
- Smooth run for the 2 weeks with stable configuration
- But some minimal (and manual!) remasking of few channels was done during the MIP runs.
- After the MIPscan → the configuration was not changed.
- List of masked channels:
  - masked_dif_1_X_X.log , 3 columns
  - chip, chn, masked (0 if not masked, 1 if masked)

---
Pedestal analysis
- Good events:
  - badbcid==0
  - Histograms with at least 300 entries (per sca)
  - TSpectrum to search peaks on the pedestal histogram
    - minimum height of secondary peaks = 0.2 max height
  - Only fit histograms with one found peak (but still count number of peaks)
- Tagged events (retriggers/plane events)
  - Badbcid==3 or nhits > 5
  - Histograms with at least 150 entries (per sca)
  - TSpectrum to search peaks on the pedestal histogram
    - minimum height of secondary peaks = 0.05 max height
  - Only fit histograms with one found peak (but still count number of peaks)

---
Pedestal npeaks maps
Grid 0, dif_1_1_2
All grid points, dif_1_1_2

---
Pedestal npeaks (tagged events) maps
Grid 0, dif_1_1_2
All grid points, dif_1_1_2

---
Pedestal maps
Grid 0, dif_1_1_2
All grid points, dif_1_1_2

---
Pedestal map: ratio between single grip points and all runs together
Scale from 0.98,1.02 dif_1_1_2

---
Pedestal width maps
Grid 0, dif_1_1_2
All grid points, dif_1_1_2

---
Pedestal width map: ratio between single grip points and all runs together
Scale from 0.8,1.2 dif_1_1_2

---
Conclusions
- New badbcid definition → production of root files for whole MIP scan is done (to be shared)
- New list of masked channels
- New list of pedestals → this list is convoluted with the masked channels
  - If pedestal = 0 → not consider this channel for analysis because was masked or broken, i.e. double peaks)
- Pedestal looks stable, better shape than before.
- Bad events: clear topological pattern in the slabs of double peaks associated to retriggers/plane events. To be investigated.

---
  Backup

---
RAW2ROOT.C : Data Integrity Checks
- The root macro checks the data bytes and headers.
  - If additional word is found: warning message and shift of the counter
  - If no additional word is found but spill candidate packet has wrong length (in words) → error message and reject spill candidate (count)
  - Else: if bad number of columns → error message and reject spill candidate (count)
  - Else: if bad chip id → error message and reject spill candidate (count)
  - Else: if error in bits → error message and reject spill candidate (count)
    - In this case, we also save (if possible) the bcid andsca were the error happened

---
BCID+1 events
- This are not bad events !!
- Next SCA (NSCA+1) is filled with a zero, but SCA=NSCA is usable → not remove from analysis !
- ~ 15% of chances of happening (reduced to ~0 in skiroc2a)