## Slide 1: Highlights of SpRIT TPC – designed to investigate physics from neutron-star merger to nucleus-nucleus collisions
AT-TPC Workshop, Jan 17-19, 2018 Santiago de Compostella, Spain
LIGO Detects a Neutron Star Merger
Betty Tsang, NSCL/FRIB
Michigan State University
132Sn+124Sn @ E/A=270 MeV

## Slide 2
Nuclear Equation of State determines properties of neutron stars and the fate of merger of Neutron Stars
D Kasen et al. Nature 551, 80–84 (2017) doi:10.1038/nature24453
Pion spectral ratios
Laboratory Experiments
conceived ~ 2007.
Phys. Rev. C 95, 044614 (2017)

## Slide 3: SAMURAI Spectrometer
Will it fit?
Yes!
Summer, 2011
Acknowledgement: Jon Barney for some of the interesting graphics in this talk
Barney, Justin, Chan

## Slide 4
Beam
Thin-Walled Enclosure
Protects internal
components, seals
insulation gas volume, and supports pad plane while allowing particles to continue on to ancillary detectors.
Rigid Top Plate
Primary structural member,
reinforced with ribs.
Holds pad plane and wire planes.
Pad Plane (12096 pads)
Mounted to bottom of
top plate. Used to measure particle ionization tracks
Field Cage
Defines uniform electric field.
Contains detector gas.
Voltage Step-Down
Prevent sparking from cathode (20kV) to ground
Wire Planes (e- mult)
Mounted below pad plane.
Provide signal multiplication and gate for unwanted events
Rails
For inserting TPC into SAMURAI vacuum chamber
Front End Electronics
STAR FEE for testing,
ultimately use GET
Target Mechanism
Calibration Laser Optics
1.5m
1m
0.5m
2011-2013
joined by Korea, China, Poland, Germany
Joint US(DOE) + Japan (MEXT) project
NIMA784, 513-517 (2015)

## Slide 5: Enclosure
Aluminum, plus Lexan windows
Skeleton: Angle bar, welded and polished for sealing.
Sides & Downstream Walls: framed aluminum sheet, to minimize neutron scattering
Bottom Plate: Solid, to support voltage step-down
Upstream Plate: Solid, ready for beamline coupling hole to be machined
A. McIntosh, Texas A&M

## Slide 6: SAMURAI TPC: Exploded View
Rigid Top Plate
Primary structural member,
reinforced with ribs.
Holds pad plane and wire planes.
Front End Electronics
Liquid Cooled
Pad Plane (108x112)
Used to measure particle ionization tracks
Field Cage
Defines uniform electric field.
Contains detector gas.
Thin-Walled Enclosure
Protects internal components,
seals insulation gas volume,
Supports pad pan while allowing particles to continue on to ancillary detectors.
Voltage Step-Down
Prevent sparking from cathode (20kV) to ground
Target Mechanism
Calibration Laser Optics
beam
Rails
Inserting TPC into SAMURAI vacuum chamber

## Slide 7: Field cage
Thin walls for particles to exit
Gas tight (separate gas volumes)
1.59 mm G10
0.035 mm Cu
Field cage wall
Top plate
drift area
50
cm
x
50
cm
y
30
cm
z
Electric field equipotential distribution with ANSYS
avalanche area
exit window electrodes will be evaporated on large Kapton foil
Made of two layer PCB’s
Y.F Zhang, BNU
Justin Estee
Notes:   Field non-uniformities cause electron drift lines to bend (worsens spatial resolution)
  Thin walls allow particles to exit
  Gas-tight to allow different gases in FC and in rest of enclosure
    Prevent sparking, AT mode

## Slide 8
Window modeled by 3D ANSYS
Region of strips
Region of rear strips
Pad plane & wire regions
Window frame
Aluminum entrance window electrodes evaporated on PPTA
Y.F Zhang, BNU

## Slide 9: Pad plane layout for 12,096 pads=112(12mm) x108(8mm)
Jon Barney on xcel sheet
Unit cell = 32+31 + 1(empty) channels
16x12 units
1 unit= 63 (7x9) pads

## Slide 10: Gluing and Assembly of pad planes
Spring loaded connection to pad plane through lid
Cable connection to STAR FEE card
Mock up of lid and pad plane
Choice of
Samtec connector
reduces risks
of connector failure
Bec Shane
Jon Barney
Justin Estee
R Showalter

## Slide 11: Leveling of top plate with laser
0 20 40 X(in)
20 40 60
Y(in)
-.040”
+.010”
-.020”
.000”
Flat to within about o.127 mm.
we adjusted pad-plane–anode wire heights to be within 0.05 mm

## Slide 12: Wire planes
Gating grid (14mm)
Ground (8mm)
Anode (4mm)
[Side view of test setup]
Bottom view of lid
Plane | Height (mm) | Pitch (mm) | diameter(m)
anode | 4.05 | 4 | 20
ground | 8.1 | 1 | 75
Gating grid | 14 | 1 | 75
Anode board circuit
Boards fabricated from Rogers 4003.
Strength of glue bond to wires exceeds twice the required strength.
Ground of Pad plane goes to BNC connector, allowing switch between self triggering, and pulsing or shorting, from the outside of TPC.
Notes:   Field non-uniformities cause electron drift lines to bend (worsens spatial resolution)
  Thin walls allow particles to exit
  Gas-tight to allow different gases in FC and in rest of enclosure
    Prevent sparking, AT mode

## Slide 13: Wire planes –
frame
comb
circuit board with solder pads
comb
Over 3000 tiny wires to solder
Shane
Powell
HiRA
Notes:   Field non-uniformities cause electron drift lines to bend (worsens spatial resolution)
  Thin walls allow particles to exit
  Gas-tight to allow different gases in FC and in rest of enclosure
    Prevent sparking, AT mode

## Slide 14
open: Vgg=-115; Voff=0
Closed: Vgg=-115; Voff=35
Electron Drift Lines
Particle Track
Pads
anode wires
Ground wires
Gating grid wires
Electron Drift Lines
Particle Track
Illustration by S. Tangwancharoen

## Slide 15
Tangwancharoen et al., NIMA 853 (2017) p.44-52
Open the gating grid in less than 0.35 µs
Close the gating grid ~3 µs

## Slide 16: Cathode & Voltage step down
Situated about 6 mm below the cathode
Polycarbonate (6 mm) epoxied to bottom plate of enclosure.
Copper-silver epoxy electrode surface below cathode is biased to the cathode voltage.
Eight concentric copper rings step the voltage down from cathode HV to ground. This has been tested to 20 kV.

## Slide 17
May, 2013
March, 2016
HiRA group

## Slide 18: Packing to ship
–MSU packaging department
“Phase-change” material
Damp out vibrations
Equilibrium pressure
in and out during flight
Constant temp ~23 deg

## Slide 19
May, 2013
Feb, 2014
July, 2014
August, 2015
March, 2016
Feb, 2014

## Slide 20
Scintillator Trigger Array
Katana Veto and trigger wall
Notes: This is the day one experimental setup. THe trigger scintillaroto sits int he magnitic field, so we use MPPC’s Seems to work wel. our open geomety allos us to detector neutrons and charged particle downstream in scintillator arrays.

## Slide 22
J. Crosby
Shane et al., NIMA 784 (2015) 513
Jacob Crosby showing Paul Gueye cosmic shower with Google Cardboard VR.

## Slide 23: Experimental Setup
Easiest thing is spectrometer for pions
Primary | Beam | Target | Ebeam/A | dsys | evt(M) | 2016
124Xe | 108Sn | 112Sn | 269 | 0.09 | 8 | 4/30-5/4
 | 112Sn | 124Sn | 270 | 0.15 | 5 | 5/4-5/6
238Ｕ | 132Sn | 124Sn | 269 | 0.22 | 9 | 5/25-5/29
 | 124Sn | 112Sn | 270 | 0.15 | 5 | 5/30-6/1
Z=1,2,3 |  | 100, 200 |  | 0.6 | 6/1

## Slide 24: Types of events (top views: x vs. z)
Beam pipe
Target
Reaction upstream: before target
Reaction on target: good event
Active Veto
reaction with gas inside TPC:
Active target events;
x(mm)
z(mm)

## Slide 25
132Sn+124 Sn
d
p
Particle ID spectra
t
3He
4He
p+
p-

## Slide 26
collaboration
Other Participants: H. Baba, Chica, Ichihara, Kondo, T. Nakamura, H. Otsu, Saito, Togano
NeuLAND Collaboration: Leyla Atar, Tom Aumann, Igor Gasparic, A. Horvat, H. Scheit
On Site Experimenters
J. Barney (MSU)
G. Cerizza (MSU)
J. Estee (MSU)
B. Hong (Korea U)
T. Isobe (RIKEN)*
G. Jhang (Korea U)
M. Kaneko (Kyoto U)
M. Kurata-Nishimura (RIKEN)
P. Lasko (IFN, Krakow)
H. Lee (RISP)
J. Lee (Korea U)
J. Lukasik (IFN, Krakow)
W. Lynch (MSU)*
A. McIntosh (TAMU)
P. Morfouace (MSU)
T. Murakami (Kyoto U)*
S. Nishimura (RIKEN)
P. Pawlowski (IFN, Krakow)
C. Santamaria (MSU)
R. Shane (MSU)
D. Suzuki (RIKEN)
B. Tsang (MSU)*
Y. Zhang (Tsinghua U)
*spokespersons
Postdoc position available

## Slide 27
construction
Thank you