## Slide 1
Sergey Dmitriev
Flerov Laboratory of Nuclear Reactions
JINR-France symposium
February 15th, 2018, Paris

## Slide 2: FLNR’s BASIC DIRECTIONS of RESEARCH
1. Heavy and superheavy nuclei:
synthesis and study of properties of superheavy elements;
chemistry of new elements;
fusion-fission and multi-nucleon transfer reactions;
nuclear- , mass-, & laser-spectrometry of SH nuclei.
3. Radiation effects and physical groundwork of nanotechnology.
2. Light exotic nuclei:
properties and structure of light exotic nuclei;
reactions with exotic nuclei.
Notes: 2

## Slide 4: Region of superheavy nuclei

## Slide 5
New heavy isotopes
Fusion-fission
Nuclear spectroscopy
SHE chemistry
Multi nucleon transfer reactions;
Reactions with exotic nuclei
Structure of light exotic nuclei;
Ion | Ion energy [MeV/A] | Output intensity
4 He 1+ | - | -
6 He 1+ | 11 | 3107 pps
8 He 1+ | 7.9 | -
16 O 2+ | 5.7; 7.9 | 5 pμA
18O3+ | 7.8; 10.5; 15.8 | 4.4 pμA
40 Ar 4+ | 3.8; 5.1 * | 1.7 pμA
48 Ca 5+ | 3.7; 5.3 * | 1.2 pμA
48Ca9+ | 8.9; 11; 17.7 * | 1 pμA
50 Ti 5+ | 3.6; 5.1 * | 0.4 pA
58 Fe 6+ | 3.8; 5.4 * | 0.7 pA
84Kr8+ | 3.1; 4.4 * | 0.3 pμA
136Xe14+ | 3.3; 4.6; 6.9 * | 0.08 pμA
160Gd19+ | 5.5 | 0.01 pμA
209Bi19+ | 3.4 | 0.01 pμA
U400 CYCLOTRON
stand-alone & post-accelerator

## Slide 6: Dubna gas-filled recoil separator

## Slide 7
We associate our future in continuing and development of ongoing researches in the field of super heavy elements physics and chemistry with the created SHE factory.

## Slide 8: Superheavy Elements (SHE) Factory – the Goals
Experiments at the extremely low (σ<100 fb) cross sections:
Synthesis of new SHE in reactions with 50Ti, 54Cr ...;
Synthesis of new isotopes of SHE;
Study of decay properties of SHE;
Study of excitation functions.
Experiments requiring high statistics:
Nuclear spectroscopy of SHE;
Precise mass measurements;
Study of chemical properties of SHE.

## Slide 9: SHE Factory
High-current cyclotron DC-280
New facilities:
New gas-filled separator
Preseparator
SHELS
Etc.
SHE Factory Building
Notes: The project of the SHE factory includes three principal components: i) high current accelerator, ii) new experimental hall and iii) a number of the next generation facilities.

## Slide 10
DC-280 cyclotron – stand-alone SHE factory
DC280 (expected) E=4÷8 MeV/A |  | 
Ion | Ion energy [MeV/A] | Output intensity
7Li | 4 | 1×1014
18O | 8 | 1×1014
40Ar | 5 | 6×1013
48Ca | 5 | 0,6-1,2×1014
54Cr | 5 | 2×1013
58Fe | 5 | 1×1013
124Sn | 5 | 2×1012
136Xe | 5 | 1×1014
238U | 7 | 5×1010
Synthesis and study of properties of superheavy elements.
Search for new reactions for SHE-synthesis.
Chemistry of new elements.

## Slide 12
Water cooling system
The water cooling system was developed at the FLNR (equipment suppliers: Russia, Italy, Germany)

## Slide 13
Control system
The control system based on FLNR developments and LabVIEW

## Slide 15
DECRIS-PM at the test bench

## Slide 16
Ca11+ =150 µA
Ca9+ =210 µA
Ca charge state spectra

## Slide 17
ION | Z | Beam Intensity from ECR |  | HV platform N | Efficiency of acceleration | Expected beam intensities of (4÷8) MeV/n ions on targets pps
 |  | eA | pps |  |  | 
20Ne | 3 | 150 | 3.1014 | 1 | 50% | 1.5·1014
40Ar | 7 | 300 | 3.1014 | 1 | 50% | 1.5·1014
48Са | 7/8 | 160 | 1.1014 | 1 | 50% | 6.2·1013
50Ti | 8/9 | 75 | 5.1013 | 1 | 50% | 3.1.1013
54Cr | 9 | 125 | 8.1013 | 1 | 50% | 4.1013
58Fe | 9/10 | 125 | 8.1013 | 1 | 50% | 4·1013
64Ni | 10/11 | 125 | 8.1013 | 1 | 50% | 4·1013
70Zn | 11/12 | 100 | 5.1013 | 1 | 50% | 2,5.1013
136Хе | 22/23 | 150 | 4.1013 | 1 | 50% | 2·1013
Expected beam parameters of the DC-280

## Slide 18: New FLNR gas-filled separator (contracted)
Reaction | Transmission
244Pu(48Ca,3n)289114 | 60 %
244Pu(58Fe,4n)298120 | 75 %
Technical Design
Report No 412923

## Slide 19
All parts have been manufactured;
Delivery – November , 2017;
Installation Dec. 2017 - Jan 2018
commissioning – Jan –June/ July 2018
Onset of first-day experiments 48Ca+ 243Am –
- Sept.-Nov. 2018;
DC-280
Gas-Filled Separator GFS-2
Parts of the main analyzing 30o magnet
Additional 10o magnet
Focusing quadrupole

## Slide 20: Gas-phase chemistry with elements 112, 113 and 114
Are elements 112, 113 and 114 volatile metals?
How do relativistic effects influence the chemistry of E112, E113 and of E114?
Chemistry of elements 115-118 ?

## Slide 21: Gas-filled pre-separator GFS-3 (QVDHQHQVD)
Reaction | Transmission
244Pu(48Ca,4n)289114 | 60 %
244Pu(58Fe,4n)298120 | 75 %

## Slide 22: Target block design
old
new
Ø = 120 mm, 1500 r.p.m. synchronous
Beam wobbler or scanner,
Segmented beam diafragm
Is in use at GFS, SHELS, MASHA
Ø = 150mm, 1500 r.p.m. synchronous,
e-beam & optical diagnostic,
water cooling

## Slide 23
TiCl4 + (CH3)5C5Si(CH3)3 Cp*TiCl3 + 3CH3Li Cp*Ti(CH3)3
Synthesis of (trimethyl)pentamethyl-cyclopentadienyl titanium
Development of 50Ti beam using MIVOC method
Benoit Gall, Zouhair Asfari
Institut Pluridisciplinaire Hubert Curien, IN2P3-CNRS, Université of Strasbourg, France
The first step of synthesis was performed at IPHC, the final step at FLNR.
Chemistry laboratory

## Slide 24
First-day experiments at SHE Factory
48Ca+243Am
48Ca+242Pu
Aims of the experiments:
Test of functionalities of all the systems of new accelerator and new gas-filled recoil separator
Accumulate additional statistics for the chosen reactions
Chosen reactions: 48Ca+243Am and 48Ca+242Pu
Enough material to prepare the targets
Relatively large cross sections and, thus, optimum candidates for spectroscopic experiments
Well-studied in previous experiments. Good for testing of the accelerator complex
Existing experimental data

## Slide 25
From 48Ca to 50Ti
Test reactions: 246Cm+48Ca 294Lv* 244Pu+50Ti 294Lv*
V. Zagrebaev and W. Greiner

## Slide 26
First experiments at SHE Factory Synthesis of new elements 119 and 120

## Slide 27
SHE Factory Building: Completion - Dec 2017; commissioning - Jan – April 2018
DC-280 cyclotron: Assembling – Dec 2017; commissioning – Jan - April 2018
Gas-Filled Separator: Installation – Dec 2017; commissioning – Jan - July 2018
Onset of first-day experiments – Sept-Nov 2018
DC-280
Superheavy Element Factory
time schedule

## Slide 28
α-, β-, and γ-spectroscopy of heavy nuclei
Present status of research (January 2018)
CSNSM,
Orsay Campus, France
K. Hauschild, A. Lopez-Martens,
R. Chakma, Blaise Retailleau.
IPHC,
Strasbourg, France
O. Dorvaux, B. Gall, F. Dechery,
H. Faure, Z. Asfari, P. Chauveau
GANIL,
Caen, France
J. Piot , Ch. Stodel, D. Ackermann,
H. Savajols, L. Caceres

## Slide 29
U400 heavy ion cyclotron
α-, β-, and γ-spectroscopy of heavy nuclei at FLNR JINR
SHELS separator (velocity filter)
22Ne ~ 2 pμA
48Ca ~ 1 pμA
50Ti ~ 0.5 pμA,
Heavy (Z>100) nuclei
of interest
GABRIELA detector set up (α,β,γ and SF)
Detailed spectroscopy studies of the transfermium isotopes
244,246,147,249,251Fm, 249,251Md, 250,251,252,253,254,255No, 253,255Lr,
254,255,256,257Rf, 257Db
Present status of research (January 2018)

## Slide 30
SHELS 2018
Modernization of experimental set up
SHELS 2021
3 super wide aperture (300 mm) quadrupole lenses
for first triplet – increase of transmission for slow ERs
for asymmetric combinations by factor of 1.5

## Slide 31
Plans for years 2018 – 2023:
Spectroscopy study of the 257Rf (complete fusion reaction 50Ti + 208Pb → 258Rf*) (model experiment for spectroscopy of element 114)
Spectroscopy study of the 260Sg, 261Sg (complete fusion reaction 54Cr + 208Pb → 262Sg*)
Study of SF of the 254Rf (complete fusion reaction 50Ti + 206Pb → 254Rf + 2n)
Study of SF of the 260Sg (complete fusion reaction 54Cr + 208Pb → 260Sg + 2n)
Study of SF of the 260Rf (complete fusion reaction 22Ne + 242Pu → 260Rf + 4n)
Spectroscopy study of the 259Rf (complete fusion reaction 22Ne + 242Pu → 259Rf + 5n)
Spectroscopy study of the 265Sg, 266Sg (complete fusion reaction 22Ne + 248Cm → 266,265Sg + 4,5n)
Experiment for spectroscopy of element 115 (complete fusion reaction 48Ca + 243Am → 288115 + 3n)
Experiment for spectroscopy of element 114 (complete fusion reaction 48Ca + 242Pu → 287Fl + 3n)

## Slide 32
DC280 heavy ion cyclotron
α-, β-, and γ-spectroscopy of heavy nuclei at FLNR JINR
Gas filled separator
22Ne ~ 20 pμA
48Ca ~ 10 pμA
50Ti ~ 5 pμA,
Heavy (Z>100) nuclei
of interest
GABRIELA 2020 detector set up (α,β,γ and SF)
Detailed spectroscopy studies of the SHE isotopes
287,289Fl, 287,288Mc, 293Lv
Future perspectives of research (2022 - 2023)

## Slide 33
F5
F3
F3
F2
F1
F4
F2
F1
F0
6 m
Setup layout
&
Today status
F0
total length F0-F5 ~53m
39 magnetic elements

## Slide 34
ACCULINNA-2 fragment separator commissioned in 2017 is now ready for day-one experiments.
The first-priority experimental program with RIBs is focused on 6He+d scattering, beta-delayed exotic decays of 11Be and 5,7H study.
Day-two experiment (with RF-kicker and zero angle spectrometer) will be aimed on 26S observation in (p,t) reaction with 28S.

## Slide 35
U400M CYCLOTRON
stand-alone & driving accelerator
Properties and structure of light exotic nuclei;
Astrophysics;
Reactions with exotic nuclei;
Light neutron-rich nuclei;
Deep inelastic scattering;
Producing of RIBs.
U400M E=30 ÷ 50 MeV/A E=4.5 ÷ 9 MeV/A |  | 
Ion | Ion energy [MeV/A] | Output intensity
7Li | 35 | 6×1013
18O | 33 | 1×1013
40Ar | 40 | 1×1012
48Ca | 5 | 6×1012
54Cr | 5 | 3×1012
58Fe | 5 | 3×1012
124Sn | 5 | 2×1011
136Xe | 5 | 4×1011
238U | 7 | 2×1010
Notes: 35

## Slide 36
U400R CYCLOTRON
stand-alone & post-accelerator
Fusion-fission;
Quasi-fission;
Nuclear spectroscopy;
New heavy isotopes;
Multi nucleon transfer reactions;
SHE chemistry;
Reactions with exotic nuclei;
Structure of light exotic nuclei;
U400R (expected) |  | 
Ion | Ion energy [MeV/A] | Output intensity
6He | 2.8  14 | 108
8He | 1.6  8 | 105
7Li | 2-17 | 1×1014
16O | 6,4 -27 | 1×1014
40Ar | 1-5,1 | 6×1013
48Ca | 1,6-11 | 1.5×1013
50Ti | 4,1-21 | 6×1012
58Fe | 1,2-7,5 | 6×1012
84Kr | 0,8-3,5 | 2×1012
132Xe | 0,8-3,5 | 3×1012
238U | 1,5- 8 | 5×1011

## Slide 38
Flerov Laboratory of Nuclear Reactions (JINR)
THANK YOU
FOR YOUR
ATTENTION !

## Slide 39
THANK YOU
FOR YOUR
ATTENTION !
Flerov Laboratory of Nuclear Reactions (JINR)