## Slide 1: GRETINA (+GRETA) Rate Performance
Chris Campbell
Thanks to Mario, Shaofei, Heather, Torben

## Slide 2: What is Rate Performance?
What is Rate?
  Front end rate : gammas per second per crystal
  Event Readout rate : trigger-validate gamma events per second per crystal
  Decomp(osition) rate : processed rate of gamma events per crystal
Performance axes/dimensions impacted by rate
  Front end rate
    Preamp Baseline (ADC range)
    Energy resolution (Integration time / pile-up losses)
  Event rate
    System stability
    Data flow + Processing
    Position resolution: Doppler resolution + Peak-to-Total ratio
What is the Front end Rate?? What does it really mean?

## Slide 3: Baselines vs. Rate
1 kHz
2.6 kHz
4.3 kHz
6.9 kHz
12 kHz
19 kHz
32 kHz
53 kHz
74 kHz
97 kHz
Rate from 60Co
<E> ~ 700keV
Baseline before gamma pulses plotted
Baseline range
-5.5MeV to 5.5MeV

## Slide 4: GRETINA + FMA, push rate limits
Goals :
  50kHz /crystal front end rate, acceptable resolution
  >=2 kHz / crystal Readout+Decomp rate, acceptable position resolution
Readout+Processing chain: FPGA->VME->IOC->Ethernet->Decomp
GRETINA Crystal (triggered)event limit: 1100 Hz
Trigger validation window improved
Enabled by Downsampled Readout
  2 samples @ 100MHz added before writing trace on FPGA
  Decomp changes to fit downsampled data (Mario)

## Slide 6: Downsampled data from the current experiment at FMA/Argonne
Mario has added core slope correction to Preprocessing
  More study needed to measure improvement and study noise sensitivity

## Slide 7: Old/New Rate Limitations
Data rate < 20 MB/sec VME + IOC
  1100 events/sec (100MHz) => 17.6 MB/sec
  2300 events/sec (50MHz) => 16.6 MB/sec
Sort and send IOC
  < 1100 events/sec (100MHz)
  < 2300 events/sec (50MHz)
Decompose signal Cluster CPUs
  43 crystals
  At ~2300 events/sec/crystal (50MHz)
  Cluster: 84 nodes, 1256 cores
  Average 95% CPU
All limitations with ~10% of each other, well-matched

## Slide 8: IOC Limits apply to MAX crystal in array

## Slide 9: Energy resolution (2msec Integration time)

## Slide 10: Position performance
Doppler correction performance maintained at high rate
Interaction point distributions unchanged
Decomp failures similar across rates
P/T consistent at low and high rates
P/T degraded ~10% by downsampling in offline tests

## Slide 11: Decomposed throughput linear with rate

## Slide 12: What is the rate in a real experiment?
Real experiments have multiple variations of rate
  Across crystal
  Over time
  Various time scales

## Slide 16: Gated by TS modulus
The rate variation in the data is NOT an FMA/DAQ/Trigger effect
The true gamma rate is varying over this 0.4 second timescale
Time between gamma hits (microseconds)

## Slide 17: What Front-end rate?
(-10,+25%) rate variation among crystals relative to array average
~20% of ~40msec periodic beam sweep for wheel spokes
  If rate is prompt and not activation/decays, rate should drop dramatically
  Maybe true rate is ~120% x observed rate
~40% rate variation of Periodic (0.4sec) nature, possibly beam?
  Maybe true rate covers (60%,140%) x observed rate
Energy Resolution and Pileup fraction are integrating over these variations of instantaneous rate.

## Slide 18: GRETA rate requirements

## Slide 19: Decomposition Rate Sets Scale of GRETA Computing
Signal decomposition is a online process - interaction point data required to monitor/debug experiments - Need to keep up!
It is the most computationally intensive aspect of array
Cores required:
  Number of crystals - 120
  Rate (/ crystal, post trigger) - 4 kHz
  Time / crystal event - 10 ms / core (2016 Xeon)
  Implies 4800 core cluster (40 cores / crystal)

## Slide 20: Data Rates In/Out of Cluster
Input bandwidth:
  event size - trace (mode 3) - (single crystal) - 8kB
  input bandwidth/crystal from filter boards - 4 kHz * 8kB = 32 MB/s/crystal
  aggregate bandwidth (switch fabric, link between electronics room & cluster) - 32 MB/s * 120 = 3.8 GB/s
Output bandwidth:
  event size - interaction points (mode 2) - 512 bytes
  output bandwidth - 512 bytes * 4 kHz = 2 MB/s/crystal
  aggregate output bandwidth (mode 2) = 240 MB/s