## Slide 1: CMS upgrade New electronics for the CMS RPC upgrade project
I.Laktineh

## Slide 2
IPNL-Tsinghua collaboration
Collaboration between IPNL and Tsinghua started in 2008 on RPC detectors for the SDHCAL prototype
In 2012 a common proposal to upgrade the CMS high eta muon stations with a new generation of RPC with good timing.
The two groups have their collaboration that go beyond the two projects. It Is a scientific partnership
Tsinghua members:
Yi Wang, Dong Han, Xinjie Huang , Pengfei Lyu, Fuyue Wang, Yancheng Yu.
IPNL members:
Imad Laktineh, Laurent Mirabito, Gerald Grenier, Maxime Gouzouvitch, F.Lagarde, Konstantin Shchablo.

## Slide 3
RPC upgrade project
Requirements and specifications
iRPC location:
|η| = 1.8 – 2.5
RE3/1 and RE4/1 (36 chambers/station)
 | Present system | RE3/1-RE4/1
¦η¦ coverage | 0 - 1.9 | 1.8 – 2.4
Max. expect. rate | 3 x 200 | 3 x 700
ϕ resolution | ~ 0.3 degrees | ~ 0.2 degrees
η resolution | O(20 cm) | O(2 cm)
To improve on the muon trigger efficiency at high η
Background mitigation
HSCP search

## Slide 4
Improving rate capability:
Smaller avalanche charge  thinner gas gaps + thinner electrodes
Thinner gap+electrodes allow:
lower Working Voltage- safer operations
Lower charge -> improve aging
Two RPC technologies were proposed: HPL-based (standard CMS) with reduced gas gap and electrode thickness (1.4mm) and glass-based thin RPC (1mm) proposed by Tsinghua-IPNL.
The proposed readout electronics is based on 2-D readout with timing information proposed by IPNL-Tsinghua.
RPC upgrade project
Requirements and specifications

## Slide 5
Large prototypes with the glass technology were produced and tested at GIF++
The tests were done using the standard CMS gas mixture (0.3% SF6) which was found not to be appropriate for the glass technology but CMS collaboration was reluctant to use a gas with higher SF6 rate

## Slide 6
 | Present system | RE3/1-RE4/1
layout | Double gap | Double gap
Gas gap thickness | 2 mm | 1.4 mm
HPL thickness | 2 mm | 1.4 mm
HPL resistivity | 1-6 × 1010 Ω cm | 0.9-3 × 1010 Ω cm
Charge threshold | 150 fC | 50 fC
Eta segmentation | 3 eta partitions | 2D readout
HPL based RPC were thus chosen. Indeed, the new design allows operating at higher particle rates at lower HV and with the same efficiency.
Working Point shift: ~ 300 V (ΔV/V ~ 4 %)
Efficiency drop: < 3 %
Max tested rate: 1.85 kHz

## Slide 7
Electronic readout for the CMS RPC upgrade project
TDC on FPGA
FE electronics
PETIROC
- 32-ch, SiGe, 0,5 -400 pC
-32 trigger output
-NOR32_charge
-NOR32_time
-global&individual threshold adjustment
TDC
-Based on delay line technique. Developed by Tsinghua for medical
applications. Adopted by Lyon group for CMS upgrade project
-TDC on FPGA (25 ps time resolution)
20 ps resolution for Qinj >.3 pC

## Slide 8
To use the 2D readout with good timing FEB (PETIROC)
Motivation
Better Y determination
Y= L/2-v*(t2-t1)/2  σ(Y) = v* σ(T2-T1)/2
2) Less channels (2/eta rather than 5)
3) Good absolute timing: reduced jitter due to better electronics andreduced gas gap.
Y
L
t2
t1
Electronic readout for the CMS RPC upgrade project
32 on-detector strips with 3.5 mm pitch
and 32 off-detector return strips 1 mm pitch
 64 channels = 2 PETIROC + 2 TDC

## Slide 9
The collaboration of the Lyon and Tsinghua led to the adoption of the 2D readout scheme as the baseline for the CMS RPC upgrade TDR.
However, to read out the future CMS RE3/1 and RE4/1 RPC, long PCBs (160 cm) are needed.
No possibility to have 6-layer PCB of large size as the small one was designed and produced before.
Two solutions are proposed :
Electronic readout for the CMS RPC upgrade project

## Slide 10
First solution (coax) : one layer PCB with strips. Return-strips are replaced with coaxial cables with the same impedance (company found : ELVIA).
ASICs and FPGAs on a separate board
This solution is equivalent to the one already tested but simpler and cheaper.
GND
coax
coax
FE
adapt. board
adapt. board
strip
GND
GND
strips
Two large PCB are needed
for the readout of one RPC
chamber
6 petiroc of 32 ch are needed

## Slide 11
Second solution (return) : “3”-layer PCB with strips and return-strips are replaced with the same impedance. Same as for small PCB but with a separate readout electronics.
This solution is as simple as the previous one and provides well controlled impedance
Two large PCB are needed
for the readout of one RPC
chamber
GND
GND
strips
Connectors
Flex will transmit the signal from the two ends of strips to the FEBs

## Slide 12
coax: PEDESTAL ~480 DACunits THR= 510 (30 DACu = 73.5fC / channel)
Real pedestal after alignment
Pedestal channel per channel before alignment
THR
Configuration of the FEBs allow a uniform response

## Slide 13
The two schemes were tested on 2-gap
RE3/1 CMS chambers recently at GIF++
With a muon beam.
COAX HVeff=7300 ATT46
noise
estimate
area
beam
area
noise
estimate area
beam
area

## Slide 14: Efficiency, noise, multiplicity

## Slide 15
Y0-32.5 cm
Y0+24.5 cm
Y0
Y0-32.5 cm
Y0+24.5 cm
Y0
COAX
RETURN
Using the time difference information one can find the Y position even without a very precise calibration (no TOT correction). Return scheme seems to perform better.

## Slide 16: Coax chamber scans
Att: 0
Att : 46
Att: 22
Att: 10
Investigation to understand the efficiency reduction is ongoing. HPL resistivity maybe at the origin of this behaviour

## Slide 17
Conclusion and perspectives
Collaboration between Tsinghua and IPNL have allowed them to play an important role in the CMS RPC upgrade proposal.
Based on the Tsinguha TDC, IPNL is developing a new version allowing to measure precisely the rising and the falling edge of the RPC signal and hence the TOT in the same TDC channel resolution for a signal width of more than 3 ns. Preliminary results show that 17 ps could be achieved.
Collaboration between the two groups will continue to exploit the new electronics on muon tomography projects.