## Slide 1: Holographic Optical Element to measure the atmospheric transmission with AuxTel
Sylvie Dagoret, Jérémy Neveu, Olivier Perdereau and Marc Moniez (LAL-Orsay)
+ Marc Betoule and Laurent Le Guillou (LPNHE)
PCWG-Workshop 25/may/2018

## Slide 2: HOE for AuxTel
Usual gratings:
all wavelengths not focused simultaneously due to optical path variation with the diffraction angle
Distorsions (astigmatism) due to converging beam (not parallel)
Holograms:
Focusing forced on the focal plane at all wavelengths
No distorsions by design of the hologram
Theoretical hologram (linear phase encoding): only -1, 0, +1 orders

## Slide 3: Realization of the HOE (Holographic Optical Element)
Ultimate holography company: makes the best holograms in the world. Director (Mr Gentet) was the head of a Thales laboratory producing holographic windows for rafale planes until the end of cold war.
3 technologies:
  Amplitude holograms: transmission modulation
  Phase holograms: phase modulation (2 techniques)
Tested together with Ronchi and blazed gratings during may-june 2017 CTIO run (18 nights)

## Slide 4: Holograms on a telescope

## Slide 5
Tests on telescope : 27 may-13 june 2017
Objectives
Compare Ronchi, blazed gratings and holograms (phase & amplitude)
Obtain data with various atmospheric conditions
Observations made
16 clear nights with variable conditions
Measures and comparisons of spectra from:
  Standards HST spectro-photométriques (CALSPEC)
  Extended series of consecutive measurements with variable airmass
  Planetary nebulae
    Narrow and strong emission lines
    -> to study the dispersion law and estimate spectral resolution
  Quasars
    Strong redshifted Ha -> to test R et IR spectrscopy

## Slide 6: Disperser performances
HOE designed to compensate geometrical distortions for 1rst diffractive order, by design
  Tests with narrow Ha filter (FWHM = 6.4 nm)
  Best results with the +1 order of the hologram
Ronchi
400 lines/mm
Blazed grating
300 lines/mm
Phase hologram
~365 lines/mm
Order -1 Order 0 Order +1

## Slide 7: Let’s look in more details
SIMULTANEOUS focus procedures with the Ha narrow filter.
  0 order focus (left) vs +1 order focus (right)
Ronchi 400 l/mm
Blazed 300 l/mm
Phase hologram
Amplitude hologram
3.5 mm focus
difference
Ha
Order 0 Order 1

## Slide 8: HOE performances: focus, resolution
Profile width of the dispersed first order light, as a function of the wavelength (Gunn-z passband)
-> Commensurable with the expectations from simulations (ZEMAX)
-> Low performance of the photopolymer hologram due to protective layer (not anti-reflective)
Spectrum profile of CALSPEC standard star
Phase hologram
O2
Ronchi 400 l/mm
Estimates of spectral finesse R=l/Dl @Ha
Gratings
- Ronchi 400 l/mm: R ~ 70
- Blazed 300 l/mm: R ~ 125
Holograms
- Photopolymer : R ~ 130
- Phase argentic : R ~ 280
- Amplitude Ag : R ~ 390

## Slide 9: Disperser performances: 2nd order
Blue filter allows to split 1rst/2nd orders
1rst order
2nd order

## Slide 10: HOE performances: planetary nebula
Why? narrow emission spikes with measured intensities -> l calibration, resolution, and (eCCD x ediffraction)(l) estimates
Planetary nebula PNG032.9-02.8 emission spikes
Dispersion
relation
Argentic phase hologram

## Slide 11
Planetary Nebula SED
Quasar 3C273 SED (redshifted z=0.158)
Blazed grating
300 lines/mm
Amplitude hologram
Polymer phase hologram
Argentic phase hologram
Blazed grating
300 lines/mm
Amplitude hologram
Polymer phase hologram
Argentic phase hologram

## Slide 12: Optical Test-bench at LPNHE
Simulation of the AuxTel convergent beam
  Focus on a LSST-type CCD sub-arcsec equivalent PSF from converging beam
  Focus independent from the wavelength (mirrors)
  Uniform beam density obtained with integrating sphere + 20m hole
  Hologram installed on a XYZ mounting
Measurements to do on every disperser
  Volume of validity DXDYDZ for acceptable use (>10mm10mm4mm)
  Spectral resolution l/Dl with emission line lamp and monochromator
  Transmission as a function of l.

## Slide 13: HOE: schedule
Janvier 2017: tests préparatoires au CTIO (Chili)
Mai 2017: premiers prototypes d'hologrammes
Juin 2017: tests de prototypes sur télescope au CTIO (Chili)
Eté 2017: analyse des tests
Automne-hiver 2017
  simulations optiques et atmosphériques
  Analyse: étude de la largeur équivalente de la bande d'absorption de l’eau (proche IR) et de l'absorption par les aérosols (bleu)
Spring-summer 2018
  production of finalized holograms (several technologies, 2/1 orders minimized; first order could take up to 80% of the light)
  measurements/characterization with the LPNHE test-bench
End 2018-beginning 2019
  Start operations on AuxTel
2019 – 2020
  Calibration of the system
  Extensive observations of the various atmospheric conditions on-site

## Slide 14: Atmospheric attenuation estimation update on CTIO data (jun 2017)
Sylvie Dagoret-Campagne
Marc Moniez
Jérémy Neveu
Olivier Perdereau

## Slide 15: Outline
CTIO may-jun 2015  16 nights
  Focus only on « 4 photometric nights »
  CALSPEC/ 2 Filters Red/Blue / 2 grating, 3 Holograms
Reconstructed the star spectra and wl calibration
  Optimize reconstruction pipeline
  Still systematics under study (disperser dependent)
Extract atmospheric feature (knowing calspec SED)
  Set of time varying « atm. estimators» to be monitored
  To feed into simulation in order to reproduce spectra data
  External required info : overall throughput (telescope + CCD+ disperser)
Predict LSST atmospheric transmission for every exposure

## Slide 16: Software Design & Analysis Progress
Old fashion
Pipeline designed for mass production (>3000 images)
Parallel reconstruction of data & sim spectra (clear sky, aver. Sky, merra2 sky)
Spectrum Extraction (data)  spectra in erg/cm2/s/nm
Being done : the automated close loop with chi2/likelihood func
  Require the effective throughput
Done up april 18
Under progress since may 18,…

## Slide 17: Principle of the Bouguer lines Methods
Generate atm transm.
Airmass : 1-2
Clear sky
Fit bouguer line in wavelength bins
Proof on simulation
Zero point
UV Ozone
Huggins cutoff
400-600 nm
Ozone
Huggins cutoff

## Slide 18: Saturation at molecular absorption 600-1000 nm
Saturated lines (O2, H2O)
Zero point

## Slide 19: Reconstruction of light at TOA (Top of Atmosphere)
Intercept of Bouguer lines (airmass z=0)
O2
H2O
Molecular absorption saturates :
Extinction α z  α √z
O2

## Slide 20: Bouguer line fit : effect of wavelength zero point accuracy : σ(λ)=2nm

## Slide 21: Bouguer line fit : effect of wavelength zero point accuracy : σ(λ)=2nm
80%
Requires a disperser with a very good wavelength accuracy σ(λ)=2nm

## Slide 22: Simulation : Bouguer lines fit method to get back throughput
Magnitude Y scale
Linear Y scale
O2
O2
H2O
H2O
3 atm. simulations :
Clear sky, (no aerosol, no PWV)
Average sky
  (aer=0.05, PWV=4mm)
Merra sky (NASA/GMAO)
Fit Method OK, except
At molecular absorption
Line and bands

## Slide 23
Simulation : Throughput :
Use of Blue/Red filters
Blue Filter
Red Filter

## Slide 24: DATA : Fit of Bouguer lines on HoloAmAg 400-700 nm : ratio = Spectrumflam(λ)/SED(λ)

## Slide 25: DATA :Fit of Bouguer lines on HoloAmAg 700-1000 nm : ratio = Spectrum(λ)/SED(λ)

## Slide 26: Absolute Throughput with Ronchi (Qe x optics x 1st order disperser)
10/17

## Slide 27: Throughput with HOE (Qe x optics x Filter x 1st order disperser)
No filter

## Slide 28
Throughput comparison night 30/05/17
No filter

## Slide 29: Extraction of atmospheric parameters spectrum by spectrum
Estimate the best model parameters:
  PWV,
  aerosols,
  ozone,
  σ(pix) (seeing)
  δλ-shift
  Using LibRadTran as the atmospheric model
  Using the Throughput measured
Extraction performed by MCMC techniques
Model : Order 1+ Order 2
S(x) = [ A1 x ( Simu(x - shift) + A2 x Sim((x-shift) /2) ] * Gaussienne(reso) )
In progress
Jérémy N.

## Slide 30: Ronchi 400 spectrum
In progress
Chi2/Ndf=8.7
model

## Slide 31: Hologram HoloAmAg
In progress
Chi2/Ndf=5.7

## Slide 32: Covariance matrix for Ronchi400
Ozone
PWV
VAOD
σλ(λ)
δλ
ozone: 394.0 PWV: 1.4 VAOD: 0.0729 reso: 8.74 pix
Chi2/dof= 8.7

## Slide 33: Covariance matrix for HoloAmAg
ozone: 382.0 PWV : 3.07 VAOD: 0.00634 reso: 2.08 pix Chi2/dof= 5.7

## Slide 34: Comments on the MCMC fit
First encouraging determinations of atmospheric parameters
Still room for progress
O2 line and H2O band are much better fitted for HoloAmAg than for Ron400

## Slide 35: CONCLUSION
Progress in software chain including:
  Spectrum extraction/background subtraction
  Wavelength calibration, and λ=0 point
  Detector Throughput (Ronchi400, HoloAmAg)
  Extraction of parameters
Still poor in data (only 4 photometric nights)
  Not enough to accumulate variations over time
Need further transmission measurement at HOLOSPEC test-bench

## Slide 36: Mini-Data Challenge for atmospheric calibration
Sylvie Dagoret-Campagne
LAL

## Slide 37: Motivations
Setup methods to estimate atmospheric transmission
Different teams will Evaluate the performances of their methods
Evaluate the relative contribution of LSST alone config and (Auxiliary Telescope + LSST) config
  Set requirements on Auxiliary Telescope
On a fake but realistically simulated Dataset
Notes: The goal would be to evaluate the differents methods differents temas may have in mind to achieve this work.
Performances may be evaluated on an accuracy bias and other criteria to be defined,…
According to
  - Number of visits (1 year / 10 year)
  - Series of visits with same atmospheric conditions (same night or photometric nights)
  - Number of scanned patches of fields
  Number of objects in the FOV of the field
  This evaluation can be undertaken provided a mock dataset
  Freeze the deadline to compare performances
  Need to improve our mock dataset
  Necessary to learn how to deal with our data

## Slide 38: Data Product
Nvis visits ( i=1,…,Nvis) scheduled by minion16 cadence
Nobj objects sampled from a catalog of SED selected (j=1,…,Nobj)
Fi is the filter used for visit i
  Fi = U, G, R I, Z, Y according a cadence (minion16)
Airmasses zi of each visit i and the instrumental magnitude Mij for each object j in the field :
the dataset : { zi , Fi ,{Mij , δMij}j }I
One spectrum (undelivered SED) of a reference star in the field (to combine with auxiliary telescope data)

## Slide 39: List of Tasks
Selection of star catalog : Phoenix  Done
SED Sampling according the magnitude distribution in SNLS  almost done
Atmospheric parameters distribution according MERRA2  Done
Atmospheric transparency calculated by libradtran  Done
True effective LSST Filter  Done

## Slide 40: Last Task : Calculation of Magnitudes and errors
How to go from
cadence (zam, sky) + SED + atm transm. + Fi {Mij , δMij}
Two options can be used:
saunerie (Nicolas R expert), python2
LSST_SIM_MAF (python3) provides official LSST Filter Transmission
  (still need to learn how to use lsst.sims.photUtils)

## Slide 41: Validation of SIMS_MAF use
Learn LSST_SIMS_MAF by comparing the results to saunerie
Check with Nicolas R, how we extract the parameters we want.

## Slide 42: Diffused background light with librandtran comparison of clear sky and sky with aerosols
Sylvie Dagoret-Campagne and Arve Kylling
December 2015

## Slide 43: Scattering properties of atmosphere
Mie scattering peaked forward
Rayleigh scattering
Angular cross-section

## Slide 44: Application to sky diffused background
Libradtran simulate not only direct light
But also diffused background
  Diffused background requires earth albedo
  (albedo for rocks also depend on weather conditions : wet/dry,snow,…)
    To be studied

## Slide 45: Map of Clear sky diffused light sun at 30° zenith angle

## Slide 46: Map of Clear sky diffused light sun at 60° zenith angle

## Slide 47: Map of diffused light with aerosols sun at 30° zenith angle

## Slide 48: Map of diffused light with aerosols sun at 60° zenith angle

## Slide 49: Normalized LIGHT

## Slide 50: Map of Normalised clear sky diffused light sun at 30° zenith angle

## Slide 51: Map of Normalised clear sky diffused light sun at 60° zenith angle

## Slide 52: Map of normalised diffused light with aerosols sun at 30° zenith angle

## Slide 53: Map of normalised diffused light with aerosols sun at 60° zenith angle

## Slide 54: Radiance decrease with zenithal angle
Light diffused above
The horizon
Astronomical twillight : 10^8 radiance drop
-26.74 + 20 magnitudes
= - 6.74 magnitude