## Slide 1
Extreme Light Infrastructure-Nuclear Physics (ELI-NP) - Phase II
Project co-financed by the European Regional Development Fund through the Competitiveness Operational Programme
“Investing in Sustainable Development”
Status of the ELI-NP GBS instrumentation at ELI-NP
and possible future upgrades
Dimiter L. Balabanski for the ELI-NP team
GET Workshop, Bordeaux, France
October 10th – 12th, 2018

## Slide 2
June 7th, 2013

## Slide 3
Extreme Light Infrastructure – Nuclear Physics (ELI-NP)
ESFRI Landmark Laboratory 2017 (together with FAIR and SPIRAL2)
NUPECC 2017 Long Range Plan: Major Nuclear Physics Facility in Europe
Mission:
Nuclear Physics studies with high-intensity lasers and brilliant γ beams
      2 x 10 PW synchronizable lasers
      0.2 – 20 MeV 0.5% bw 95% polarized γ beams

## Slide 4: The laboratory building is fully operational
17 000 m2

## Slide 5
The ELI-NP laboratory building
HPLS
Laboratories
Experiments
Anti–vibration platform
±1 mm @ < 10 Hz
Thermalized building
22⁰ ± 0.5⁰
Clean rooms: ISO-5, 7
GBS
basement
accelerator
bays
laser rooms
A
A
A – A
Platform supported on dampers
anti–vibration
mounts
140 m
120 m
civil construction was commissioned in September 2016

## Slide 6
1.5m thick, 150,000 ton “optical table”
1000 springs + vibration dampers

## Slide 7
GBS control room and utilities
Labs and workshops

## Slide 8
70 m
250 J in 25fs
1 pulse/min
Contrast
1:107 @ 5ps
1:109 @ 10ps
1:1014 @ 100ps
Stations E1 and E6
2 x 10 PW/min
Station E5
2 x 1 PW/1 Hz
Station E4
2 x 0.1 PW/10 Hz

## Slide 9
3 PW performance was confirmed ! (June 2018)

## Slide 10
f=30m
QED
(gas target)
Laser-Gamma
Nuclear Physics
(solid target)
1 PW/1 Hz
Gamma
beam
2x10 PW laser beam transport system in construction
2x10 PW + 1 PW auxiliary beam to three experimental areas
f=30 m, F/50 mirror for electron LWFA at 10 PW
10 PW adaptive mirror upgrade
Commissioning fall 2019
10 PW
10 PW
AM

## Slide 11
10 PW interaction chambers and mirrors under contracting

## Slide 12
Nuclear Physics with High Power Lasers
Extreme light intensity (1023 W/cm2)
Extreme light pressure (10 Tbar)
Radiation Pressure Acceleration of solid density GeV ion beams
Neutron-rich nuclei
Nuclear reactions in plasmas
Ultra-intense
ion, g, neutron sources
Radiation Pressure Acceleration
electrons
ions
100 nm

## Slide 13: Laser System Implementation Schedule
2017
2019
2018
100 TW June
1 PW Sept
10 PW June
Thales Laser System Implementation
10PW Laser Beam Transport System Impl.
Commissioning Exp.

## Slide 14: Nuclear processes in plasmas
observed in cold targets at 10-8 rates in 197Au, 189Os, and 193Ir; never observed in plasmas
never observed
Nuclear (de-)excitations in plasmas
Nuclear lifetimes in plasmas
significant changes of nuclear lifetimes are predicted in hot and dense plasmas

## Slide 15
Fission-fusion scheme (Thirolf et al 2011)
Neutron-rich nuclei production
Requires accelerating solid density heavy ion bunches to ~10 MeV/A
Theory and experiments show promising direction

## Slide 16: Gamma Beam System
low-energy accelerator section:
0.2-3.5 MeV
factory acceptance in Dec. 2015
high-energy accelerator section:
3.0-19.5 MeV
~ 4γ2·EL

## Slide 17: Gamma Beam System – Layout
e– RF LINAC
Low Energy
300 MeV
Interaction Laser
Low Energy
Photo–gun Laser
Interaction Point
Low Energy
Photogun
multi-bunch
e– beam
dump
beam
coll&diag
e– beam
dump
Low-Energy Stage: γ rays up to 3.5 MeV
Control
Room
Racks
Room
Racks
Room
High-Energy Stage: γ rays up to 19.5 MeV
Interaction Point
High Energy
e– beam
dump
beam
coll&diag
e– RF LINAC
High Energy
720 MeV
Control
Room
Interaction Laser
High Energy
Master clock synchronization @ < 0.5 ps

## Slide 18: Gamma Beam System Implementation Schedule
2017
2019
2018
3 MeV May
19.5 MeV June
Gamma Beam System Implementation
Commissioning Exp.

## Slide 19: what to remember
beam size: 1 mm at 10 m away from collimator
energy spread: 50 keV at Eγ=10 MeV
time structure: micropulses at 16 ns
photons/pulse: 105
photons/macro-pulse: 32 x 105=3 x 106
photons/s: 3 x 108

## Slide 20
beam diagnostics
Spatial parameters: source diameter, beam width (at target), beam divergence, beam instability
Temporal parameters: micropulse duration and separation, number of pulses in train, macropulse separation
Spectral parameters: beam bandwidth and beam polarization
Power parameters: average brilliance at peak energy, peak brilliance at peak energy, time-average spectral
density at peak energy and off peak energy
16 ns
10 ms (100 Hz)
>31 pulses for 512 ns @ 0.5J/pulse
16 ns
90°
135°

## Slide 21
Experiments with high-brilliance gamma beams at ELI-NP
g
(Z, N)
g.s.
separation threshold
photoactivation
(Z´±1, N´ 1)
±
n, p, α, ff
(Z´, N´)
TDRs: > 300 scientists involved
Rom. Rep. Phys. 68 (2016)
Nuclear Resonance Fluorescence (NRF)
Giant/Pigmy Resonances (GANT)
Photodisintegration (γ,n), (γ,p), (γ,α)
Photofission (γ,ff)
Applications (positron beams)

## Slide 22
ELIADE
ELIGANT-GN
all mechanical structures are contracted
experimental hall E8

## Slide 23: ELIADE array in collaboration with U. Koeln and TU Darmstadt
γ beam
γγ coincidences
angular distributions
polarization measurements
detector tests are ongoing
array design is at a final stage
day-one experiments are under discussion
NRF experiment at ELI-NP
Rom. Rep. Phys. 68, S483 (2016)
First in-beam test: Dec. 12-18, 2016

## Slide 24: ELI-NP NRF physics cases
Self-absorption measurements (Γ0/Γi)
Low-energy dipole response (e.g. Actinides)
Dipole response and parity measurements for weakly-bound nuclei
Investigation of the Pigmy Dipole Resonance
Rotational 2+ states of the scissor mode
Constraints on the 0νββ-decay matrix elements of the scissors mode decay channel: 150Sm
Sensitivity frontier
week channels
Availability frontier
p-nuclei and actinides
Precision frontier
high statistics
Rom. Rep. Phys. 68, S483 (2016)

## Slide 25
ELIGANT-GN array
30 LaBr3 or CeBr3
20 7Li glasses
30 Lq. Scint.
E8
ELIADE
ELIGANT-GN
GANT experiment at ELI-NP
Rom. Rep. Phys. 68, S539 (2016)
Day ONE:
studies of GDR and PDR decay (90Zr, 208Pb)
combine with information from (γ,n) experiments
combine with information from (γ,γ’) experiments (e.g. polarization)
γ-decay to gs and excited states as a function of excitation energy
key input U. Milano and Konan U.

## Slide 26
ELITPC
Front-end GET electronics
Readout plane PCB
Mountable handles for base-plate manipulation
HV BNC connectors
Vacuum port
Source ports
Beam port
Gas port
Detector upside-down view
The mini-eTPC detector with 256-channel readout was built and successfully tested in-beam at the IFIN Tandem in 2016
flagship experiment: 16O(γ,α)12C
in collaboration with U. Warsaw

## Slide 27
C. Matei et al., exp. at HIγS in March 2017
in collaboration with INFN LNS Catania

## Slide 28: 7Li(γ,t)α w/ SIDAR at HIγS, March-April 2017
addressing the Li-problem and theoretical aspects
using SIDAR array from ORNL
two lamp-shades of YY1: 300, 500, 1000 μm
clean alpha-triton coincidence
proposed by ELI-NP together w/: ORNL, Rutgers U, INFN-LNS, York U, Aarhus U, U Michigan
alphas
tritons
tritons

## Slide 29
Photofission experiments at ELI-NP
Rom. Rep. Phys. 68, S621 (2016)
ELI-BIC
Array of Bragg ICs coupled to
Si DSSD based ∆E-E detectors
BIC prototype tested with sources and in-beam
in collaboration with ATOMKI, Debrecen

## Slide 30
Photofission Instrumentation: ELI-BIC
in production

## Slide 31
Instrumentation: ELITHGEM
Multi-target detector array consisting of position sensitive gas detector modules based on the state-of-art THGEM technology

## Slide 32
Beam
Isobutane at 5 mbar
CAD
Mechanical development
Status
THGEM array has been assembled consisting of 12 THGEM and anode readout boards
After the development of a target holder, the full chamber will be ready for in-beam tests
Instrumentation: ELITHGEM
Total target thickness: 20 mg/cm2
(10 x 2 mg/cm2)
For E = 6 MeV,
~ 300 fissions / sec are expected for 238U
(from Geant4 simulations)
Array of 12 THGEM detectors
D. Choudhury et al., Acta Phys Pol. 48, 559 (2017)

## Slide 33
Instrumentation: ELITHGEM
tests ongoing
good position sensitivity
stable with time
Voltages
Transfer Zone : ~ -680 V
THEM front surface : ~ -650 V
THEM back surface : -150 V
Anode : Ground
Gas
Isobutane (C4H10) at pressure of 5 mbar
252Cf

## Slide 34
Considered upgrades
Si detectors
ELISSA array: next generation DSSD detectors (higher granularity)
Gas-filled detectors
ELI-BIC array: improved A/Z resolution
ELITHGEM array: improved sensitivity

## Slide 35
ELI-NP Team, March 5, 2013
Thank you!