## Slide 1: Imaging the hard X-ray sky with the ECLAIRs telescope onboard the SVOM mission
@SVOM_mission
Nicolas Dagoneau (CEA/AIM) 2nd year PhD student

## Slide 2
Gamma ray bursts
CGRO/BATSE GRB
(iso)
NASA
Emission of matter jets: the Fireball model
Internal shocks: prompt emission (gamma)
External shocks with interstellar medium: afterglow (X  radio)
Gamma ray burst: fast and variable flash of gamma photod, random in the sky. Most energetic EM phenomena.
Frédéric Daigne talk

## Slide 3
The SVOM mission
White paper: Wei,Cordier+2016 arXiv:1610:06892
Spaced based multi-band astronomical Variable Object Monitor (Phase C)
French (CNES) – Chinese (CNSA/CAS) collaboration
Launch in December 2021 in China (Xichang, Long March rocket)
A multi wave-length mission with space based and ground based instruments
Goal: build a homogeneous sample of GRBs with a good time and spectral coverage and redshift measurement.
Henri Triou talk

## Slide 4
FSC
CSC
T0=trigger GRB
T0+30s
Inside SVOM
Outside SVOM
From space
From ground
T0+5min
T0+hours/days
Alert Broadcast
Other space missions
Auto slew
VHF
The SVOM mission
Constrains:
Earth in the field of view 66% of the time
South Atlantic Anomaly crossing
Henri Triou talk

## Slide 5
How to detect and localize?
X-ray imaging: use coded-mask telescope (Granat/SIGMA, Beppo-SAX/WFC, INTEGRAL, Swift/BAT, Astrosat/CZTI)
Diego Götz talk

## Slide 6
How to detect and localize?
X-ray imaging: use coded-mask telescope (Granat/SIGMA, Beppo-SAX/WFC, INTEGRAL, Swift/BAT, Astrosat/CZTI)
Titanium-Tantalum-Titanium mask
ECLAIRs telescope (4-150 keV)
Localization error < 10arcmin
Field of view: 2sr (~90*90 deg2)
80 x 80 pixels, 1024 cm²
UGTS: Unit for detector manaGement, Triggering and Scientific processing with 2 triggers (Count rate and image triggers)
From detector image to sky image: deconvolution knowing mask pattern (inverse problem)

## Slide 7
= (Mean( ) – Mean( ) )) / sqrt(Var)
= (Mean( ) – Mean( )) / sqrt(Var)
Deconvolution
At the source position
At other positions
Under mask holes
(photons seen from position)
Under mask opaque pixels
(photons from other positions)
SNR sky image

## Slide 8
Cosmic X-ray Background (Moretti et al. 2009)
X-ray sources
Detector image (1000s) Sky SNR image (64 x 20s stacked)
CXB: 8.74 ph/cm²/s/sr + internal noise: 0.003 cnt/cm²/s/keV
Sky SNR pixels distribution. Expected SNR distribution for a clean sky is .
Detector image (100 ph/cm²) Sky SNR image
Bright sources lead to coding noise (ghosts) in sky images  cannot just mask source peaks in the sky
sources will be seen by ECLAIRs in 20 min, in 4-120 keV
Catalog of source being built…
Background: 2 components and 2 effects
Sujay Mate talk

## Slide 9
2 methods :
Fit CXB model + source contributions simultaneously
  CXB model:
  Source contributions: known from source positions in Fov
Remove CXB with wavelets then fit source contributions
  Wavelets: “à trou algorithms” (Stark et al. 2007) remove large scales in detector images (Krivonos et al. 2010 used wavelets on Integral/IBIS sky images, not relevant here because background is not flat)
  Source contributions are fitted after background subtraction
  Faster, does not need assumption on background shape
Example of a fitted model (in counts) with an Earth-modulated CXB + 5 source illumination functions.
Earth in Fov (66% of time) changes the CXB counts shape in the detector.
Cleaning background

## Slide 10
Methods : performance
Images of 20 s with a GRB in the totally coded Fov (random fluence in 5-10 ph/cm², canonical Band spectrum, ), no Earth, no source, only CXB, no energy redistribution by the mask.
A: no cleaning B: fit C: wavelets on the detector D: wavelets in the sky
Stdev of sky SNR pixel (=1 for a clean sky)
SNR of the GRB
GRB SNR normalized by the stdev of the sky SNR distribution
Execution time increases if additional sources fitted
Cleaning background
Preliminary result

## Slide 11
Methods : performance
Images of 20 s with a GRB in the totally coded Fov (random fluence in 5-10 ph/cm², canonical Band spectrum, ), no Earth, sources (Cyg X-1, X-2, X-3, Her X-1), only CXB, no energy redistribution by the mask.
A: no cleaning B: fit C: wavelets on the detector D: wavelets in the sky
Stdev of sky SNR pixel (=1 for a clean sky)
SNR of the GRB
GRB SNR normalized by the stdev of the sky SNR distribution
Execution time increases if additional sources fitted
Cleaning background
Preliminary result
Currently tuning wavelets parameters (number of scales to remove, size of the filter)

## Slide 12
ECLAIRs: opening a discovery space for Ultra-long GRBs
ECLAIRs allows long pointing durations (up to 1 day) which may help to monitor transient events on long timescales.
Classical long GRB are detected on smallest scales of the image trigger, no detection from 160 s up to 20 min for Goldstein sample at z = z0 (arXiv:1810.12052).
Difficult to really define duration of such GRBs and simulate their detectability (only few events, all different … )
Simulation of Swift GRBs through ECLAIRs image trigger prototype. Most GRB are detected in 20s image.

## Slide 13
Conclusion
SVOM/ECLAIRs can image the X-ray sky thanks to coded mask and deconvolution
Image processing (fit of the background model or wavelets + fit of known sources)
  Methods are being implemented on the UGTS
  Performances will be tested with a more detailed background model (albedo, reflection… )
ECLAIRs may be useful to detect long transient (such as ultra long GRBs)

## Slide 14: Thank you for your attention!
Mission white paper
svom.fr/en
On Twitter @SVOM_mision