## Slide 1
The CHEAP-Hunter project
(Compact High-Energy Ambitious Pion-bump Hunter )
All together: a very interesting and productive Scientific Discussion!
Francesco, Francesco [Hardware]
Gaia [Target Search]
Luca[Performances],
Marco[Logistic Engineering],
Martina[Software, Science Topic]

## Slide 2
Science Topic
67,5 MeV
PION BUMP DETECTION (Kelner06, Giuliani11, Ackermann13, Cardillo14 )
W44
Importance of no detection:
Confirmation of the theoretical model predicting low-energy CR exclusion from clouds (Gabici16)
Giuliani,Cardillo et al. 2011
Cardillo et al. 2014
W44
Jogler et al. 2016
W51c
Ackermann et al. (2013)

## Slide 3
Instrument – Requirements
Only-Silicon microstrip double-layer tracker for direction end energy reconstruction:
    Compton effect (E~<10 MeV) and pair production
    Imaging
    low-energy photons and avoid the background due to Compton Scattering
    Radiation Length: 0,5 X0
Calorimeter
    Caesium Iodide (CsI) pixels
    Radiation Length: 1,3 X0
Anti-Coincidence System and time of flight:
    Particle rejection efficiency >95 %
Sensitivity: 7,85 x 10-8 ph/cm2/s [30-100 MeV, 1yr]
Effective Area: 400 cm2 [constant] (Geometric Area*Efficiency(trigger, reconstruction, interaction) )
Angular Resolution and FoV to be estimated
Energy range: 1 MeV – 1 GeV
  we want focus our mission on the "pion-bump" feature research

## Slide 4
Target Sources
Sources | Fluxes (30-100 MeV)[ph/cm2/s]
W44 | ≈ 1e-6
IC443 | ≈ 5e-7
W51c | ≈ 4e-7
RX J0852.0-4622 | ≈ 2,8e-7
RX J1713,7-3946 | ≈ 2.2e-7
Cas A | ≈ 5e-8
Cardillo et al. 2014
Tavani et al. 2010
Abdo et al 2009
W44
IC443
W51c

## Slide 5
Instrument - Requirements
Physical parameter:
    35 kg detector
    24,5 cm x 24,5 cm x 28,2 cm
    1mm between two Si slices of a single layer and 3mm between two layers
Launcher: Kourou – Vega [shared]
    cheap, small mission, at the Equator
    250 kg: total weight [J. Wijker 2008], including margins
Orbit: LEO (i < 10°)
    between radiation belt and the densest atmosphere layer
    one revolution every 95 minutes
Ground segment: Kourou
    telemetry (up/down link, S band)  10 minutes every 95 minutes (LEO)
    data (down link, X band)
Power:
    triple junction in solar panel (1,6m2 total, (400 +/- 10%) Watt)
    battery capacity (Li Ion) = 500 W/h
Issues | Budget [beginning + 1yr]
Industrial Cost | 5 millions
Launch | < 10 millions
Support, ground Segment, Team | < 2 millions/yr
Payload | < 3 millions
Contingency | < 3 millions/yr
 | 23 millions
ESA call for small Missions (< 50 million €)

## Slide 6
Instrument - Software
Instrument Response Function in fits format:
    PSF (r68% or Gaussian)
    Effective Area
    Dispersion Energy
    Background  MeV diffuse emission model (Ajello 2016)
Kalman-Filter recoursive algorithm (Giuliani 2006)
    fundamental for the albedo photon rejection
Maximum Likelihood analysis (Mattox 1996)
    optimized for extended sources
    Flux, coordinates and spectral index (several spectral assumptions: power law w HE cut-off, log-parabola…)

## Slide 7
Comments and Summary
Every estimation is very raw due to the limited time
   possible performance and target selection improvement
A "hot" scientific topic
   a detection of "pion bump" can finally confirm the CR origin from SNRs
A very cheap payload for a brief "life time" (with possible time extension)
Possibility of analysis of other kind of gamma-ray sources
Thank you
very much!