## Slide 1: GRANDProto35 status
GRAND workshop
IAP, August 23, 29018

## Slide 2: Radio selftriggering challenges
Feedback from TREND:
2011-2012 data
TREND antenna
Reconstructed source position
HV transformer
Even in remote areas, background sources (HV, planes, tranes, etc) generate many more events than air showers.
Major issue for GRAND: detect & identify neutrino signals out of ultra-dominant background

## Slide 3: TREND results
Offline algorithm to select air-shower candidates from their specific features (wavefront shape, trigger pattern at ground etc)
Results in an excellent background rejection (huge fraction of background events killed: from 7.3 108 to ~500 background events)
Data: selected candidates
Simulated air shower events

## Slide 4: TREND issues
«You get what you pay for»: system reliability questionnable
  Sudden drops in gain
  Aging (antennas, amplifiers, optical system, computers…)
- Significant maintenance effort required
- Reduced detection efficiency
- Determination of efficiency &
absolute calibration (very) challenging
50-100MHz noise level (dB)

## Slide 5
S. Le Coz, FCPPL2018

## Slide 6: Motivations from GRANDproto35 (2013)
Confirm TREND results: autonomous radiodetection works.
Improve detection efficiency etot = edet xesel
  Improve edet with upgraded detectors allowing for a larger fraction of detctor up-time.
  Goal: edet >90%
  Improve background rejection with new tools. Goal: esel >80%

## Slide 7: GRANDProto35 developments (2014-2017)
Antennas
Electronics
Ground array

## Slide 8: GP35 antennas
3xASIC LNA
(6V supply, 67mA consumption)
Production: SUBATECH (D. Charrier) + XiDian U (Zhang Fushun)with NAOC funding
Tested and validated as early as 2014

## Slide 9: GP35 electronics

## Slide 10
Input: bipolar pulse 200ns 30mVpp
Output = enveloppe

## Slide 11: Enveloppe detection
A vulnerable system
(ex: measurement @ Mingantu)

## Slide 12: GRANDproto detector reliability
26 days
Preliminary tests in 2016 (proto boards)
 Clean pulses measured
 observation of the galactic fluctuation for 26 consecutive days
100% detection efficiency ( ~1h test run, tested in Dec 2016).

## Slide 13: GRANDproto35 electronics production
Completed December 2017
34 boards fully tested & calibrated (1 dead).
31 units shipped to Ulastai early 2018 (+3@LPNHE).
Nov 2017, STAE company @ Antony
Dec 6, 2017

## Slide 14: Deployment status
deployed
connected
All fibers + power cables installed. Full deployment can be done within days.

## Slide 15: Commissioning
DISCLAMER: VERY early tests
  Spent few hours only so far
  Remote connection, communication to site going through Gu Junhua@Beijing
  DAQ not adapted to multiple detectors yet
  Firmware loaded on FPGA not up to date
    Freezes if burst of event. Requires run restart
     fixed in next firmware version
    Up/down link collision sometimes leads to antenna becoming deaf. Requires board reboot (ie power OFF/ON)
     Could not be reproduced @ lab in next firmware version

## Slide 16: Commissioning
All boards have correct voltages & ADC behavior. GPS data coming in.
Main voltage
-3V
+4V
LNA1: 11.4V
LNA3: 11.4V
LNA2: 11.2V
1 SLC measurement every 10s
101010101010
010101010101

## Slide 17
Normal pulses (bumpy?) observed on 5 antennas out of 6.

## Slide 18: Issues
Response to commands seems heratic
Connection lost more often than before
Galactic signal not clear on several tested channels

## Slide 19: Scintillator array
21+3 air light-guide scintillator (tilted orientation)
6 already deployed for tests in 2015… Status = idle.

## Slide 20
Expected efficiency of the scintillator array for cosmic ray showers with an incoming direction within ±20°from North, zenith angle 70> q> 40◦.
95% efficiency for E>2 1017 eV
All recons has to be done!!
Zenith (top) and azimuth (bottom) distributions of events reconstructed with the 6-scintillators prototype array (2015) .
Scintillator array
3-fold coincidences are shown in red, larger multiplicities in green
Notes: 201

## Slide 21: ToDo
Upgrade DAQ and push on tests (Beijing, August 26-28).
Upgrade firmware (September?)
Complete GRANDproto35 manual (late September)
Train Chinese researchers (XiangLi, JianLi,… ) under Gu Junhua supervision for data taking&analysis.
Deploy more antennas (all?)
Develop reconstruction software
 First reconstructed radio-events by October
Ground array???