## Slide 1: hipeCTA: High Performance Computing for CTA CTA Réunion de groupe, 19/12/2018 Jean Jacquemier, on behalf of the hipeCTA team: J. Jacquemier, T. Vuillaume, P. Aubert, G. Maurin

## Slide 2: observation

## Slide 3: how to reduce the computation time ?
Make the most out of the capabilities of modern CPUs
  vectorization
    SIMD process multiple data elements at the same time, with a single instruction.
  data prefetching techniques
    CPU automatically fetchs instructions or data from their original storage in slower memory to a faster local memory before it is actually needed

## Slide 4: Pipeline

## Slide 5: HiPeCTA, HiPeData and HiPeRTA
  uses vectorization and makes the most of data prefecting
    R0 to DL1 : Calibration , integration , cleaning, hillas parameters
    It is developed to be used under the ctapipe framework.
      Same functions API, unit tests based on ctapipe comparison
    HiPeRTA
      Real time analysis
      share code/algorithms with HiPeCTA
  a vectorization ready data format.
    memory access patterns designed to make the most of data prefetching
      Contiguous data, Cache Friendly
  proposed to CTA
    Being benchmarked vs other formats
LST1

## Slide 6: Benchmarks with uncompressed simtel and HiPeData
Computing performance benchmarks
Format\Software | ctapipe | hipeCTA
simtel | ~130hz (36 MB/s) | ~196hz (54MB/s) *
hipedata | ~165hz (45 MB/s) | ~350hz (98MB/s)
Format\Software | ctapipe | hipeCTA
simtel | ~185hz | ~370hz *
hipedata | ~280hz | ~6300hz
I/O bound
Note: 1hz = 1 image/s R0 ➡ DL1
From hard drive (~100 MB/s max)
From RAM (DDR4) : target = RTA
*limited speed factor because of required copy data to 1, 2 or 3D aligned numpy array
CPU bound
Notes: I/O bound refers to a condition in which the time it takes to complete a computation is determined principally by the period spent waiting for input/output operations to be completed
CPU-bound (or compute-bound) when the time for it to complete a task is determined principally by the speed of the central processor