## Slide 1: Triggering with ATLAS
Rainer Stamen
Kirchhoff-Institut für Physik
Universität Heidelberg
GDR Terascale @ Heidelberg
14.10.2009

## Slide 2: Content
Trigger Challenge
Concepts and Implementation
The Trigger Strategy
Examples

## Slide 3: Disclaimer
I am talking about ATLAS. Most of what I am going to say also holds for CMS.
Most plots are outdated. The message given by these plots is still valid.

## Slide 4: The Trigger Challenge
High luminosity: Linst = 1034 cm-1s-1
ATLAS
- 108 channels
Eventrate
- 40 MHz
(20 events per BX)
Datarate
- 60TB/s
Data Storage (forseen)
~ 200 Events/s
~ 300 MB/s
(limited by offline
ressources)
Reduction: 1/200 000

## Slide 5: Physics Objects
Objects needed for
event selection
-> also needed for Trigger:
- Electrons
- Photons
- Muons
- Jets
- b-Jets
- forward jets
- Taus
- Missing Energy
- (B-physics triggers)
Trigger object close to offline Physics objects required

## Slide 6: Realisation
Complete data readout not possible (60TB/s (already with zero supression))
Need quick decision based on reduced information
Then readout data and perform refined decision
But: Whatever is rejected by the trigger cannot be recovered

## Slide 7: Trigger Design
Available
ressources
Prozessing time
Level 1
Hardware
Calorimeter, Muons
(2.5 ms)
Level 2
CPU-Farm
All detector (RoI based)
(~10 ms)
Event Filter
CPU-Farm
All detector
(partly RoI based) (~1s)
Event rate
Data volume
ATLAS-PPr-System
(KIP Heidelberg)

## Slide 8: Trigger and Data Acquisition
In Reality the Trigger is
intimately connected with
the Data Acquisition System
ATLAS TDAQ Group:
~400 persons

## Slide 9: Level 1 Calorimeter Trigger
trigger towers map
0.1x0.2
3.1 <||< 3.2
0.4x0.4125
3.2 <||< 4.9
0.2x0.2
2.5 <||< 3.1
0.1x0.1
||< 2.5
 x 
Position
Reduced Granularity
- Trigger Tower
- sum up to 60 cells
- still finer granularity
than e.g. CDF
LAr Calorimeter
Granularity
f
h

## Slide 10: Level 1 Calorimeter Trigger
Cluster Processor
ECAL+HCAL
Sliding Window technique used to identify electrons, taus and jets
Sum up Trigger Towers to determine ETmiss and Etsum (no muons incl.)
e/t Algorithm
Jet Algorithm

## Slide 11: Jet Trigger efficiencies (MC)
These are efficiencies which you will see in one or two years from now
At the beginning this will be much worth
Trigger figure merit

## Slide 12: Level 1 Muon-Trigger
Predefined patterns
- special Trigger
layers
- seeded from
middle layer
- different hardware
- overlap removal

## Slide 13: Higher-Level-Trigger
Level 1 uses only coarse granularity information
Objects found by Level 1 can still be very much refined using information of finer granularity
Use L1 to guide the reconstruction on HLT
Region of Interest (RoI) approach
Only small amount of ressources needed on L2 (2%)

## Slide 14: HLT Algorithms
-> As close to offline as possible, but still fast
Outdated, just for illustrational purpose

## Slide 15: Trigger strategy and Trigger menu
Bring everything together
  Physics selection (importance of signatures)
  Calibration Triggers
  Monitor Triggers

## Slide 16: Trigger Strategy
What defines the thresholds?
  Operational Parameters
    Rates and stability of data taking
  Physics
    Standard candles (Z,W, incl. Jets, ...)
    Higgs (SM Higgs: mH > 100 GeV)
    SUSY, Black Holes, ...
    B-Physics (at least some)
How can we ensure to be as open to new physics as possible?
  Inclusive strategy

## Slide 17: Trigger Chains
Hardware
L2 cluster alg.
L2 track alg.
EF cluster alg.
EF track alg.
EF Bremsstrahl.
recovery
The Trigger processes the
data in Chains
Decisions are taken after
each step and chains/paths
are stopped and eventually
events are rejected
You gain lots of performance
w.r.t a system where you fully
reconstruct the event

## Slide 18: Trigger Chains

## Slide 19: Trigger menu Level 1
Outdated, just for illustration purposes

## Slide 20: Trigger menu HLT
Outdated, just for illustration purposes

## Slide 21: Rastafari Diagram of difficulty
ET of objects
# of objects
Black holes
SUSY
Compositness
Leptoquarks

## Slide 22: Trigger rates
Overall rate is mostly
dominated from QCD
Dijets (not only jet
triggers)
-> Going to low ET gives huge rates
(What about jet cross sections at low ET?)

## Slide 23: Prescales
3 different lumi scenarios
How to handle high
rates of low ET objects?
-> introduce low thresh-
holds and apply prescales
Prescale P -> only take
every Pth event
Powerful tool to keep low ET physics (reduced rate, low effective lumi),
-> calibration triggers, monitor triggers, etc ...
unprescaled
prescaled

## Slide 24: Triggering low ET physics (B-physics)
E.g. Hadronic BS -> fp
(no chance to trigger on this)
b
b
_
BS
m + X
Do not trigger on your signal but about something which comes
with your signal (similar to VBF for Higgs physics) (small eff.)

## Slide 25: Summary
Trigger is very essential for the experiments
Trigger is very challenging
Currently most new physics processes are well covered (unprescaled)
Concepts for low ET high s processes in place
Concepts for low ET small s processes in place (low efficiency)