## Slide 1: Future Accelerators
Frank Zimmermann
CERN, BE Department
Helmholtz School CALC2018 Dubna
Work supported by the European Commission under Capacities 7th Framework Programme, Grant Agreement 312453
Geneva site
Qinhuangdao site
Kitakami site
Frank Zimmermann, CERN
Ecole GIF 2019, Ecole Polytechnique
Lecture 2: electron-positron colliders

## Slide 2
Super KEKB – pushing the frontiers of L & b*
Phase-2 goal of by* = 3 mm achieved in spring 2018
Further commissioning in progress this year but impacted by budget constraints.
double ring e+e- collider as B-factory at 7(e-) & 4(e+) GeV; design luminosity 8 x 1035 cm-2s-1; by* 0.3 mm; nano-beam – large crossing angle collision scheme (crab waist w/o sextupoles); beam lifetime5 minutes; top-up injection; e+ rate up to 2.5 1012 /s ; under commissioning
Y. Funakoshi, Y. Ohnishi

## Slide 3
3
double ring e+e- colliders as t-c factory at Ec.o.m. of 2-7 GeV; design luminosity 2 (1) x 1035cm-2s-1; by*= 0.5 (0.6) mm; crab waist collision scheme; beam lifetime10 minutes; top-up injection, e+ rate up to 1011 /s ; polarized electron beam; concept designs complete.
Super Charm Tau Factories
new CDR in October 2019
Values in brackets refer to HIEPA
HIEPA, China
E. Levichev
Q. Guo

## Slide 4
FCC-ee & CEPC – circular lepton energy frontier
FCC-ee and CEPC are part of integrated proposals and each followed by a hadron collider with common footprint.
Circumference 100 km
Presently 2 IPs, alternatives with 3 / 4 IPs under study
Synchrotron radiation power 50 (30) MW/beam at all beam energies, cf. LEP2 with 11 MW/beam; SR power/length factor 10 below light sources
Top-up injection scheme requires booster synchrotron in collider tunnel
double ring e+e- colliders as Z, W, H and t factory at Ec.o.m. of 90 - 365 GeV; As Higgs factory: design luminosities 17 (6) x 1034 cm-2s-1 (2 IPs) ; by*= 1.0 (1.5) mm; crab waist collision scheme; beam lifetime >12 minutes; top-up injection, e+ rate 1x1011 /s ; CDRs complete
values in brackets
refer to CEPC
FCC-ee
FCC-hh
CEPC
SppC

## Slide 5
Collider (all double rings) | Beam energy [GeV] | Peak luminosity (per IP) [1034 cm-2s-1] | by* [mm] | beam current [mA] | Collision scheme | Beam lifetime [min] | e+ top-up rate [1011/s]
SuperKEKB | 4 (e+), 7 (e-) | 80 | 0.3 | 3600 (e+), 2600 (e-) | Nano-beam | <5 | 10
BINP c-t | 1-3 | 5-20 | 0.5 | 2200 | Crab waist | <10 | 1
HIEPA c-t | 1.5-3.5 | 10 | 0.6 | 2000 | Crab waist | <10 | 1
FCC-ee (Z) | 45.6 | 230 | 0.8 | 1500 | Crab waist | 68 | 7
FCC-ee (H) | 120 | 8.5 | 1.0 | 29 | Crab waist | 12 | 1
FCC-ee (t) | 182.5 | 1.6 | 1.6 | 5 | Crab waist | 12 | 0.2
CEPC (Z) | 45.5 | 32 | 1.0 | 460 | Crab waist | 150 | 1.1
CEPC (H) | 120 | 3 | 1.5 | 17 | Crab waist | 26 | 0.2
Collider (all double rings) | Beam energy [GeV] | Peak luminosity (per IP) [1034 cm-2s-1] | by* [mm] | beam current [mA] | Collision scheme | Beam lifetime [min] | e+ top-up rate [1011/s]
SuperKEKB | 4 (e+), 7 (e-) | 80 | 0.3 | 3600 (e+), 2600 (e-) | Nano-beam | <5 | 10
BINP c-t | 1-3 | 5-20 | 0.5 | 2200 | Crab waist | <10 | 1
HIEPA c-t | 1.5-3.5 |  | 0.6 | 2000 | Crab waist | <10 | 1
FCC-ee (Z) | 45.6 | 230 | 0.8 | 1500 | Crab waist | 68 | 7
FCC-ee (H) | 120 | 8.5 | 1.0 | 29 | Crab waist | 12 | 1
FCC-ee (t) | 182.5 | 1.6 | 1.6 | 5 | Crab waist | 12 | 0.2
CEPC (Z) | 45.5 | 32 | 1.0 | 460 | Crab waist | 150 | 1.1
CEPC (H) | 120 | 3 | 1.5 | 17 | Crab waist | 26 | 0.2
key parameters of future circular e+e- colliders
Many similar parameters and strong synergies for design

## Slide 6
crab-waist crossing for flat beams
regular crossing
crab waist -
vertical waist position
in s varies with horizontal
position x
allows for small by* and for small ex,y
and avoids betatron resonances (→higher beam-beam tune shift)
P. Raimondi, M. Zobov,
et al.

## Slide 7
DAFNE: “crab waist” collisions
DAFNE Peak Luminosity
CRAB-WAIST Collision Scheme
Design Goal
M. Zobov
M. Zobov et al., “Test of “Crab-Waist” Collisions at the DAΦNE Φ Factory”, Phys. Rev. Lett. 104, 174801 (2010).

## Slide 8
Marica Biagini
B-factories: KEKB & PEP-II:
double-ring lepton colliders,
high beam currents,
top-up injection
DAFNE: crab waist, double ring
SuperB-factories, S-KEKB: low by*
LEP: high energy, SR effects
VEPP-4M, LEP: precision E calibration
KEKB: e+ source
HERA, LEP, RHIC: spin gymnastics
combining successful ingredients of several recent colliders → highest luminosities & energies
L/IP
future circular lepton factories based on proven concepts and techniques from past colliders and light sources

## Slide 9
similar solutions for FCC-ee and CEPC
FCC
Double ring colliders with full-energy top-up booster ring,
CEPC evolved from initial 54 km - single-ring design, practically to the FCC-ee 100 km design.
2 IPs, 2 RF straights, tapering of arc magnet strengths to match local energy
Asymmetric IR layout to limit SR of incoming beams towards detectors and generate large crossing angle
Common use of RF systems for both beams at highest energy working point (ttbar/ZH for FCC-ee/CEPC)

## Slide 10
three sets of RF cavities to cover all options for FCC-ee & booster:
high intensity (Z, FCC-hh): 400 MHz mono-cell cavities (4/cryom.)
higher energy (W, H, t): 400 MHz four-cell cavities (4/cryomodule)
ttbar machine complement: 800 MHz five-cell cavities (4/cryom.)
installation sequence comparable to LEP ( ≈ 30 CM/shutdown)
WP | Vrf [GV] | #bunches | Ibeam [mA]
Z | 0.1 | 16640 | 1390
W | 0.44 | 2000 | 147
H | 2.0 | 393 | 29
ttbar | 10.9 | 48 | 5.4
“Ampere-class” machine
“high-gradient” machine
FCC-ee machine evolution and RF staging
O. Brunner

## Slide 11
JLAB, Oct 25, 2017
F. Marhauser et al
FCC-ee cavities
Z running:
single cell cavities,
400 MHz,
Nb/Cu at 4.5 K,
like LHC cavities
ttbar running:
five-cell cavities,
800 MHz,
bulk Nb at 2 K,
in addition to
400 <MHz
four-cell cavities
at 400 MHz
ttbar FCC-ee: 396 four-cell 400 MHz + 852 five-cell 800 MHz cavities
Z-pole FCC-ee: 116 single-cell cavities

## Slide 12
SLC/SuperKEKB-like 6 GeV linac accelerating; 1 or 2 bunches with repetition rate of 100-200 Hz
same linac used for e+ production @ 4.46 GeV e+ beam emittances reduced in DR @ 1.54 GeV
injection @ 6 GeV into of Pre-Booster Ring (SPS or new ring) and acceleration to 20 GeV
injection to main Booster @ 20 GeV and interleaved filling of e+/e- (below 20 min for full filling) and continuous top-up
CEPC: 10 GeV linac, no prebooster
FCC-ee injector layout
S. Ogur, K. Oide, Y. Papaphilippou

## Slide 13
curved orbit of e- in magnetic field
L. Rivkin

## Slide 14
L. Rivkin

## Slide 15
linear collider advantage:
little synchrotron radiation at high energy
synchrotron radiation in a storage ring of bending radius r0
energy loss per turn
synchrotron-radiation power
for one electron
for muons mm200 me→ SR 2003 107x less
for protons mp2000 me→ SR 20003 1010x less

## Slide 16: ILC
total length (main linac)
30 km (500 GeV)
- 50 km (1 TeV)
Parameters | Value
C.M. Energy | 250 GeV
Peak luminosity | 1.35 x1034 cm-2s-1
Beam power | 5 MW
Beam Rep. rate | 5 Hz
E gradient | 31.5 MV/m +/-20%

## Slide 17: Main Linac Unit
Accelerating cavities
O(65%) of linac length
Accelerating cavities
Beam guiding quadrupole
Beam position monitor
Corrector kicker
Total length for 500 GeV cms 31 km, some length for beam cleaning and focusing

## Slide 18
Slowed down by factor of approximately 4x109
Input RF power at 1.3 GHz
~1 m
Niobium
ILC cavity
500 GeV ILC: 16,000 9-cell cavities in 31 km linac

## Slide 19: ILC Achieved Gradient
From N. Walker

## Slide 20: Note: Pulsed Operation
0.9ms
0.73ms
5 RF pulses of 1.6 ms per second (1312 bunches in 0.73 ms):
Because field leads to losses in the wall
About 1 W/m
With no pulsing losses would be O(100) times worse
RF power in pulse: 5 MW / (5 x 0.73 ms) = O(1500 MW) = O (150 klystrons) for 250 GeV

## Slide 21: CLIC
total length (main linac) 11 (500 GeV) - 48 km (3 TeV)

## Slide 22: CLIC Accelerating Structure
12 GHz, 23 cm long, normal conducting
Loaded gradient 100 MV/m
Allows to reach higher energies
140,000 structures at 3 TeV
But strong losses in the walls
50 RF bursts per second
240 ns, 60 MW, 312 bunches
Power during pulse 8.5 x 106 MW (3000 x ILC)
Power flow
1/3 lost in cavity walls
1/3 in filling the structure and into load
1/3 into the beam
Average RF power about 3 kW/m
About 1 kW/m into beam

## Slide 23: CLIC complex
Drive Beam Generation Complex
Main Beam Generation Complex
Goal: Lepton energy frontier
CLIC at 3TeV shown
Stages at Ecms=0.38, 1.5 and 3TeV L=6x1034cm-2s-1 at 3TeV
Beam power 30MW at 3TeV
50km

## Slide 24
Examples of ILC and CLIC Main Parameters
Parameter | Symbol [unit] | SLC | ILC | CLIC | CLIC
Centre of mass energy | Ecm [GeV] | 92 | 250 | 380 | 3000
Luminosity | L [1034cm-2s-1] | 0.0003 | 1.35 | 1.5 | 6
Luminosity in peak | L0.01 [1034cm-2s-1] | 0.0003 | 1 | 0.9 | 2
Gradient | G [MV/m] | 20 | 31.5 | 72 | 100
Particles per bunch | N [109] | 37 | 20 | 5.2 | 3.72
Bunch length | σz [μm] | 1000 | 300 | 70 | 44
Collision beam size | σx,y [nm/nm] | 1700/600 | 516/7.7 | 149/2.9 | 40/1
Vertical emittance | εx,y [nm] | 3000 | 35 | 30 | 20*
Bunches per pulse | nb | 1 | 1312 | 352 | 312
Bunch distance | Δz [mm] | - | 554 | 0.5 | 0.5
Repetition rate | fr [Hz] | 120 | 5 | 50 | 50

## Slide 25
e-
e+
long RF sections w. e.g. 2 x 125 (2 x 1500) GV voltage
both beams lost after single collision
supply full energy for each collision
requires small spot size to get target luminosity
full energy must be provided to beam
for every collision
in linear colliders

## Slide 26
positron challenge
Routinely achieved positron rates:
SLC, 1 bunch/pulse, 65 nC , 120 Hz, 5x1012 e+/s
KEKB, 2 bunches/pulse 2x0.6 nC, 50 Hz, 4x1011 e+/s
Under commissioning:
SuperKEKB, 2 bunches/pulse 2x4 nC, 50 Hz, 2.5x1012 e+/s,
1.0x1012 e+/s already achieved
SuperKEKB injector
 | FCC-ee | S-KEKB | SLC | CLIC380 | ILC250
e+ / s | 7x1011 at Z | 3 x 1012 | 6 x 1012 | 1014 | >2x1014
FCC-ee
e+ source flux
concentrator
SLC complex

## Slide 27
Key technology for e+e- colliders: RF system
 | fRF [MHz] | #cavities | #cells/cavity | VRF,tot [MV] | acc. gradient [MV/m] | technology
SuperKEKB | 509 | 30 (ARES) 8 (SCC) | 1 1 | 15 12 | 2 6 | warm Cu bulk Nb
charm-tau | 500 | 1 / ring | 1 | 2x1 | 6 | bulk Nb
FCC-ee-H | 400 | 136 / ring | 4 | 2000 | 10 | Nb/Cu
FCC-ee-t (addt’l) | 800 | 372 | 5 | 6930 | 19.8 | bulk Nb
CEPC | 650 | 240 | 2 | 2200 | 19.7 | bulk Nb
ILC250 | 1,300 | 8,000 | 9 | 250,000 | 31.5 | bulk Nb
ILC1000 | 1,300 | 32,000 | 9 | 1,000,000 | >31.5? | bulk Nb
CLIC380 | 10,000 | 20,368 | 33 | 380,000 | 72 | warm Cu
CLIC3000 | 12,000 | 140,000 | 33 | 3000,000 | 100 | warm Cu
preference for SC cavities,
FCC-ee RF system optimized for each working point, CEPC features single system

## Slide 28: green accelerators
subsystems with high energy efficiency & low power consumption: SC RF (=SRF), efficient RF power sources, low-power NC magnets, SC magnets
recover beam energy (storage ring, ERL)
recycle particles (e+ ,pbar …)

## Slide 29
design of low-power magnets for FCC-ee and CEPC
Twin-dipole design with 2× power saving
16 MW at 175 GeV
Twin F/D arc quad with 2× power saving
25 MW at 175 GeV
dipole prototype
quadrupoleprototype
FCC-ee
CEPC
Twin arc magnet combined function dipole with sextupole component
Twin F/D arc quad with 2× power saving
power reduction by factor 2 w.r.t. single-aperture magnets
challenge of low-field magnets !
500 G collider, 30 booster

## Slide 30
RF R&D activities – towards higher efficiency
FCC R&D aims at improving performance & efficiency + reducrf cost:
  Improved Nb/Cu coating/sputtering (e.g. ECR fibre growth, HiPIMS)
  New cavity fabrication techniques (e.g. EHF, improved polishing, seamless…)
  Coating of A15 superconductors (e.g. Nb3Sn)
  Bulk Nb cavity R&D at FNAL, JLAB, Cornell, also KEK and CEPC/IHEP
  High efficiency klystrons (e.g. COM, BAC, CSM) – synergy with HL-LHC and CLIC
  MW-class fundamental power couplers for 400 MHz
800 MHz 5-cell Nb
prototype / JLAB
80%
Klystron R&D - FCC CSM

## Slide 31
e-
e+
beams collide many times, e.g. 2x / turn
RF compensates SR loss
(1% Ebeam / turn)
RF system 100x smaller than for LC
#collisions / (beam energy) 200x
circular accelerator/collider concept
“There's just no use trying to build this up. You may get a few million volts. That's limited. What we've got to do is to devise some method of accelerating through a small voltage, repeating it over and over. Multiple acceleration.” E.O. Lawrence, 1929

## Slide 32: comparison of parameters FCC-ee & ILC
Parameter | LEP2 | FCC-ee |  |  | ILC |  | 
 |  | Z | H | t | H | 500 | 1 TeV
E (GeV) | 104 | 45.6 | 120 | 182.5 | 125 | 250 | 500
<I (mA)> | 4 | 1390 | 29 | 5.4 | 0.021 | 0.021 | 0.021
P SR/b,tot [MW] | 22 | 100 | 100 | 100 | 5.9 | 10.5 | 27.2
PAC [MW] | ~200 | ~260 | ~280 | ~360 | ~129 | ~163 | ~300
hwall→beam [%] | ~30 | 30-40 | 30-40 | ~30 | 4.6 | 6.4 | 9.1
Nbunch/ring (pulse) | 4 | 16’640 | 328 | 48 | 1312 | 1312 | 2450
fcoll (kHz) | 45 | 50000 | 4000 | 294 | 6.6 | 6.6 | 9.8
b*x/y (m/mm) | 1.5/ 50 | 0.15 /.8 | 0.3 /1 | 1.0/1.6 | .013/.41 | .011/.48 | .011/.48
ex (nm) | 30-50 | 0.27 | 0.63 | 1.46 | 0.04 | 0.02 | 0.01
ey (pm) | ~250 | 1 | 1.3 | 2.9 | 0.14 | 0.07 | 0.03
xy (ILC: ng) | 0.07 | 0.13 | 0.12 | 0.126 | (1.91) | (1.72) | (2.12)
nIP | 4 | 2 | 2 | 2 | 1 | 1 | 1
L0.01/IP | 0.012 | 230 | 8.5 | 1.55 | 0.5 | 1.05 | 2.2
L0.01,tot (1034 cm-2s-1) | 0.048 | 460 | 17 | 3.1 | 0.5 | 1.05 | 2.2

## Slide 33
early linear-collider proposals
Maury Tigner, “A Possible Apparatus for Clashing-Beam Experiments”, Nuovo Cimento 37, 1228 (1965)
Ugo Amaldi, “A possible scheme to obtain e-e- and e+e- collisions at energies of hundreds of GeV”, Physics Letters B61, 313 (1976)
these early proposal always
recovered the energy of the spent beam!

## Slide 34: LHeC: Recirculating Linac with ERL Operation
Two 1 km long, 10 GeV
SC LINACs with
3 accelerating and
3 decelerating passes in CW operation
SRF sees 6*current
at the IP (≈ 4ns spacing)
 Q0 = 1010 requires
cryogenic system
comparable to LHC
system! Q0 > 1010
Super Conducting Recirculating Linac with Energy Recovery
Choose ⅓ of LHC circumference 
944 cavities; 59 cryo modules per linac
ca. 9 km underground tunnel installation
more than 4500 magnets (same magnet design as for RR option)
lepton-hadron collider based on the LHC

## Slide 35
LHeC 1034 cm-2 s-1 Luminosity reach | PROTONS | ELECTRONS
Beam Energy [GeV] | 7000 | 60
Luminosity [1033cm-2s-1] | 16 | 16
Normalized emittance gex,y [mm] | 2.5 | 20
Beta Funtion b*x,y [m] | 0.05 | 0.10
rms Beam size s*x,y [mm] | 4 | 4
rms Beam divergence s*x,y [mrad] | 80 | 40
Beam Current @ IP[mA] | 1112 | 25
Bunch Spacing [ns] | 25 | 25
Bunch Population | 2.2*1011 | 4*109
Bunch charge [nC] | 35 | 0.64
Over 600MW Beam power in electron Beam!!!
ERL is a must for efficient operation!!!
O. Brüning

## Slide 36: FCC-ee ERL upgrade – recent proposal from BNL Green FCC ee w. 10% of R-R power consumption
ERL based FCC ee at 10 MW SR
ERL based FCC ee at 100 MW SR
*Luminosity scaled linear with SR power – would see other limitations
?
?
FCCee
V. Litvinenko, T. Roser, M. Chamizo

## Slide 37
DC = lRF/2
7 MeV
DE = 80 MeV
7 MeV
1 : 3 : 5
2 : 4 : 6
dump
injector
DE = 80 MeV
2 Linacs (Four 5-Cell 801.58 MHz SC cavities)
3 turns (160 MeV/turn)
Max. beam energy 500 MeV
Footprint: 24 x 5.5 x 0.8 m3
Multi-pass high-current ERL test facility for LHeC (and FCC-ee-ERL?)
under construction at LAL Orsay
W. Kaabi, A. Bogacz, O. Bruning
arXiv:1705.08783

## Slide 38
a bit of history

## Slide 39
circumference 27 km
in operation from 1989 to 2000
maximum c.m. energy 209 GeV
maximum synchrotron radiation power 23 MW
LEP/LEP2: highest energy so far
LEP energy close to FCC-ee target + record synchrotron radiation with ~MeV photons

## Slide 40
“An e+-e - storage ring in the range of a few hundred GeV in the centre of mass can be built with present technology. ...would seem to be ... most useful project on the horizon.”
B. Richter, Very High Energy Electron-Positron Colliding Beams for the Study of Weak Interactions, NIM 136 (1976) 47-60
(original LEP proposal, 1976)
Burt Richter
1976
350 GeV c.m.
↔
~90 km
cost-optimized
circumference

## Slide 41
SLC: the first & so far only linear collider
Burton Richter et al, “The Stanford Linear Collider”, 11th Int. Conf. on High-Energy Accelerators, CERN (1980)
20 pb-1 from 1989 to 1998

## Slide 42
commissioning time & performance of the first linear collider
CERN-SL-2002- 009 (OP), SLAC–PUB–8042 [K. Oide, 2013]
SLC
LEP1
(per IP)
SLC design
SLC
½ design value reached after 11 years
LEP1 design

## Slide 43
back to the future

## Slide 44
C NZZ
FCC
CLIC
proposed linear & circular colliders
to go beyond
the LHC we
need larger
machines
ex. Geneva basin

## Slide 45
J-ILC
J-ILC
proposed linear & circular colliders
Tristan-II
(1983)
Tsukuba site
Fukushima site
Kitakami site
F. Takasaki
F. Takasaki
ex. Japan
circular
machines
appear closer
to Tokyo
Tristan-II
(1983)
not pursued

## Slide 46
1)
2)
3)
4
1
2
3
4
5
6
1) Qinhuangdao, Hebei Province（Completed in 2014）
2) Huangling, Shanxi Province（Completed in 2017)
3) Shenshan, Guangdong Province(Completed in 2016)
4) Baoding (Xiong an), Hebei Province (Started in August 2017)
5) Huzhou, Zhejiang Province (Started in March 2018)
6) Chuangchun, Jilin Province (Started in May 2018)
J. Gao
proposed circular colliders
ex. China

## Slide 47: the nanobeam challenge

## Slide 48
1. final focus optics
2. bunch length
3. beamstrahlung
(for bx)
IP spot size
ILC
(adiabatic damping)
FCC-ee:
1. (synchr. rad.)
2. beam-beam tune shift
smaller emittances
needed for linear colliders

## Slide 49
year
b* [m]
PETRA
SPEAR
PEP, BEPC, LEP
CESR
DORIS
TRISTAN
DAFNE
CESR-c, PEP-II
KEKB
BEPC-II
SuperKEKB
FCC-ee
SLC
ILC

## Slide 50: vertical rms IP spot size
collider / test facility | [nm]
LEP2 | 3500
KEKB | 940
SLC | 700
ATF2, FFTB | 41 (35), 77
SuperKEKB | 50
FCC-ee-H | 44
ILC | 5 – 8
CLIC | 1 – 2
collider / test facility | 
LEP2 | 3500
KEKB | 940
SLC | 700
ATF2, FFTB | 41 (35), 77
SuperKEKB | 50
FCC-ee-H | 44
ILC | 5 – 8
CLIC | 1 – 2
in regular
font:
achieved
in italics:
design
values
by*:
5 cm→
1 mm
ey:
250 pm→
1.3 pm
by*:
1.5 mm→
0.5 mm
ey:
90 pm→
0.1 pm

## Slide 51: beam-beam effects

## Slide 52
schematic of betatron oscillation around storage ring
tune Qx,y= number of (x,y) oscillations per turn
focusing elements:
quadrupole magnets
quadrupole magnet
(many)
betatron oscillation & tune

## Slide 53
beam-beam tune shift
center of
opposing
beam
at small amplitude similar to effect of focusing quadrupole
(for head-on collision)
beam-beam tune shift
beam-beam
deflection

## Slide 54: ee luminosity w crab waist and its constraints
synchrotron radiation power / beam:
beam-beam tune shift
Piwinski
angle
luminosity
constant
with
maximum
acceptable
luminosity formula for H, Z, W, t factory

## Slide 55
beam-beam tune shift for FCC-ee
tune shift limit empirically scaled from LEP data (4 IPs)
in reasonable agreement with simulations
R. Assmann & K. Cornelis, EPAC2000
J. Wenninger
S. White
crab waist collision scheme allows for even larger tune shifts

## Slide 56: linear collider luminosity and parameter drivers
Beam Quality
(+bunch length)
Need to ensure that we can achieve each parameter
Can re-write normal luminosity formula
Luminosity
spectrum
Beam power
Disruption
enhancement

## Slide 57: beam-beam effect in linear colliders
Z direction [μm]
Beam-beam force off
Dense beams to reach high luminosity
Beam focus each other
Y direction [nm]
Beam-beam force on

## Slide 58
beam-beam disruption at the SLC
at highest luminosity
more than 100% luminosity
increase

## Slide 59: beam-beam effect: beamstrahlung
Z direction [μm]
Emit beamstrahlung
Develop luminosity spectrum
Beam-beam force on
Typically aim for O(1)
degraded
energy
spectrum

## Slide 60: comparison of e+e- colliders

## Slide 61
design luminosity vs. energy
D. Schulte, B. List
Luminosity versus c.m. energy for e+e- Higgs Factories.
Two IPs are assumed for the circular colliders FCC-ee and CEPC.

## Slide 62
Foreseen integrated luminosities versus year.
ILC
CLIC
FCC

## Slide 63
a figure of merit for collider efficiency
E. Jensen, M. Seidel

## Slide 64: physics operation plans for all post-LHC colliders

## Slide 65
in years and starting at time T0
D. Schulte,
timelines of various collider projects,

## Slide 66: what is time T0? readiness timelines
Timeline | ~ 5 | ~ 10 | ~ 10 |  |  | ~ 15 |  | ~ 20 |  | ~ 25 | ~ 30 | ~ 35 | 
Lepton Colliders |  |  |  |  |  |  |  |  |  |  |  |  | 
SRF-LC/CC | Proto/pre-series | Construction | Construction |  |  |  |  | Operation |  |  | Upgrade |  | 
NRF—LC | Proto/pre-series | Construction | Construction | Construction |  |  |  | Operation |  |  | Upgrade |  | 
Hadron Collider (CC) |  |  |  |  |  |  |  |  |  |  |  |  | 
8~(11)T NbTi /(Nb3Sn) | Proto/pre-series |  | Construction |  |  |  |  | Physics Experiment | Operation |  |  | Upgrade | Upgrade
12~14T Nb3Sn | Short-model R&D |  |  |  | Proto/Pre-series |  |  |  | Construction | Construction to Physics Experiment | Operation |  | 
14~16T Nb3Sn | Short-model R&D |  |  |  |  |  | Prototype/Pre-series |  |  |  | Construction | Construction | 
Note: LHC experience: NbTi (10 T) R&D started in 1980’s --> (8.3 T) Production started in late 1990’s, in ~ 15 years
A. Yamamoto
A relative timeline expected for realizing future lepton and hadron colliders (from A. Yamamoto, presented at the Open Symposium in Granada, and updated based on the discussion followed).

## Slide 67: next frontier collider summary table
Project | Type | Energy [TeV] | Int. Lumi. [a-1] | Oper. Time [y] | Power [MW] | Cost
ILC | ee | 0.25 | 2 | 11 | 129 (upgr. 150-200) | 4.8-5.3 GILCU + upgrade
 |  | 0.5 | 4 | 10 | 163 (204) | 7.98 GILCU
 |  | 1.0 |  |  | 300 | ?
CLIC | ee | 0.38 | 1 | 8 | 168 | 5.9 GCHF
 |  | 1.5 | 2.5 | 7 | (370) | +5.1 GCHF
 |  | 3 | 5 | 8 | (590) | +7.3 GCHF
CEPC | ee | 0.091+0.16 | 16+2.6 |  | 149 | 5 G$
 |  | 0.24 | 5.6 | 7 | 266 | 
FCC-ee | ee | 0.091+0.16 | 150+10 | 4+1 | 259 | 10.5 GCHF
 |  | 0.24 | 5 | 3 | 282 | 
 |  | 0.365 (+0.35) | 1.5 (+0.2) | 4 (+1) | 340 | +1.1 GCHF
LHeC | ep | 60 / 7000 | 1 | 12 | (+100) | 1.75 GCHF
FCC-hh | pp | 100 | 30 | 25 | 580 (550) | 17 GCHF (+7 GCHF)
HE-LHC | pp | 27 | 20 | 20 |  | 7.2 GCHF
D. Schulte
1 GILCU=109 ILC Units= 1G$ 2012

## Slide 68
V. Shiltsev

## Slide 69
European Strategy for Particle Physics
Update

## Slide 70: European Particle Physics Strategy Update (EPPSU)- 2019/20
H. Abramowicz – Chair of the EPPSU Secretariat

## Slide 71: EPPSU meeting in Granada
Great progress in n physics since 2013 EPPSU at accelerator and non-accelerator based facilities. Experiments ongoing to address:
  order of the n masses,
  absolute value of n masses,
  n nature (Dirac or Majorana)
  existence of sterile neutrinos
Hidden (Dark) sector searches and identifications of portals to this sector:
  An increasing number of experiments are extending/focussing their analysis in this area in the LHC (LHC experiments, FASER) and in the SPS North Area (NA62 and its possible extension)
  New experiments proposed: SHiP and beam dump facility, e-SPS
G. Arduini

## Slide 72: EPPSU meeting in Granada
Synergies with astro-particle physics highlighted once more:
  Theory
  The new Einstein Telescope (3rd generation underground Gravitational Wave interferometer) has requested CERN to help on:
      Underground infrastructure, cryogenics
      Vacuum, material and surface science
      Electronics and data acquisition, computing
Consensus that an e+-e- collider for precision physics is the next required step:
  Higgs factory  Higgs could be one of the portals to the Dark Sector
  t-tbar physics
  Providing large event set at the Z-pole (~90 GeV)
A hadron collider at ~100 TeV C.o.M. energy is the long term goal
G. Arduini

## Slide 73: EPSSU longer term perspective
More promising but (by far) less developed and uncertain:
  Muon colliders
  Plasma wakefield acceleration
  …and their possible combination..
….but they are in this stage since long….
Need to be studied to assess how realistic the schemes are and to identify the key questions to answer
While for plasma wakefield acceleration effort is ongoing driven by interest for potential applications, muons are of interest only for particle physics.
G. Arduini

## Slide 74: EPPSU discussions in Granada
Strategy = A plan of action designed to achieve a long-term or overall aim
we are looking at a time scale of several decades
  Cost but also Upgradeability
Whatever large scale collider project requires O(1000) accelerator experts - Oide’s principle - out of ~4500 accelerator experts worldwide.
Clearly we (CERN) need to maintain and further develop our expertise in accelerator physics/design/technology
G. Arduini

## Slide 76
conclusions
FCC study develops high-performance energy frontier circular colliders for post-LHC era – input to ESU’19/20
consensus that an e+e- collider for precision physics is the next required step:
  Higgs factory → Higgs could be one of the portals to the Dark Sector
  t-tbar physics
  providing large event set at the Z-pole (~90 GeV)
hadron collider in the 100 TeV C.o.M. energy is the long term goal
coherent strategy needed
effort to design greener accelerators
a lot of activity in France, esp. FCC, also g-F., PERLE & LAL