## Slide 1
Les expériences du future: détecteurs
École de GIF 2019, 2-6 Septembre 2019
École polytechnique - Palaiseau
D. Contardo - IP2I CNRS/IN2P3

## Slide 2
Tracking systems
Provide most precise measurement of charged particle trajectories to form primary (interaction) and secondary (decay) vertices,
to estimate momentum from curvature in magnetic field
ATLAS
cτ c(b) quarks ≃ 120(470) µm

## Slide 3
Charged particle energy loss in matter
* Particle Data Booklet http://pdg.lbl.gov/2019/reviews/rpp2018-rev-passage-particles-matter.pdf and https://arxiv.org/pdf/1804.11246.pdf
Detectors are in the range 0.1 GeV to TeV
Trackers are measuring ionization
e
Bethe & Bloch formula (MeV g-1 cm2), M ⨠ me
In composite material
Notes: Low speed more time for ionization, 1/β2
relativistic rise (⊥ field increase with γ frather interactions more probable) ln β2γ2
Plateau polarization effect δ/2
Rise from bremsstrahlung radiation
At very low energies, also shell corrections –C/Z

## Slide 4
Charged particle energy loss in matter: signal
Signal in thin material layers is described by Landau-Vavilov-Bichsel distribution
In Silicon dE/dx = 3.88 MeV/cm and average e-h pair pair energy is 36 eV/
 S ≃ 106(70) e-h pairs/µm average(maximum probability)
* Particle Data Booklet http://pdg.lbl.gov/2019/reviews/rpp2018-rev-passage-particles-matter.pdf and https://arxiv.org/pdf/1804.11246.pdf

## Slide 5
Charged particle energy loss in matter: Bremsstrahlung
For electrons Bremsstrahlung dominates for E ≥ 8 MeV:
Where the radiation length g cm-2 ∝ A/Z2
, for composite: 1/X0 = Σj wj/Xj
* Particle Data Booklet http://pdg.lbl.gov/2019/reviews/rpp2018-rev-passage-particles-matter.pdf and https://arxiv.org/pdf/1804.11246.pdf

## Slide 6
Charged particle passage in matter: multiple scattering (MS)
Multiple scattering is a limitation to trajectory measurement precision
Gaussian approximation sufficient for most application

## Slide 7
Track parameters
  Transverse (xy) and longitudinal (rz) projections, Impact Parameters (IP) d0 and z0
Tracking systems design: momentum measurement in B-field
Transverse momentum
  pT (GeV/c) = 0.3 B(T) R(m)
  R = L2/8s + s/2 ≃ L2/8s
  L = path in B-field
Resolution1): σ(pT)/pT = 8pTσ(s)/0.3BL2
With N equally spaced points of resolution σ(rΦ): σ(s) = √(720/(N+4)) . σ(rΦ)/8 (Gluckstem formula)
σ(rΦ) has a constant term from intrinsic precision + a multiple scattering term ∝ 1/(pT sin1/2 (θ)) √(L/X0)
σ(pT)/pT = apT ⊕ b/sin1/2(θ)
Where a depends on 1/BL2, number of layers & intrinsic resolution and b depends on B, L number of X0
Detectors are aligned with muons (from collisions and cosmic) and measured field MAP is corrected from mass measurements (ex. J/Ψ)

## Slide 8
Φ
x
Track origin resolution determines quality of association to collision vertex and decays
  Geometry term: σ2geom. (d0) = [(r1σ1)2 + (r2σ2)2 ]/(r2 – r1)2
    r1 - r2 and σ1/σ2 inner/outer radii and hit resolutions
  MS term: σ2MS(d0) = Σnj (rj σ(Φ))2 , n number of layers
    σj(d0) = rjσ(Φ) = (r/sin(θ)p)13.6(MeV)√(x/sin(θ) X0) [1 + 0.38 log (x/sin(θ)X0)]
      x layer thickness, X0 radiation length θ track polar angle, Φ scattering angle
Tracking systems design: transverse (longitudinal) IP resolution
Transverse IP resolution: σ(d0) ≃ a ⊕ b/pT sin1/2 (θ)
Constant term depends only on geometry, multiple scattering term depends on material, transverse momentum and pseudo-rapidity η1)
σ(d0) is driven by the vertex detector performance (Si-pixel detector)
η = -log [tan(θ/2)]

## Slide 9
Intrinsic resolution is driven by channel pitch, charge sharing across channels, and Signal to Noise ratio (S/N)
  In binary readout (no amplitude measurement) position is given by the center of the channel or 1/2 depending on cluster size, eg number of channels with S/N above threshold: σ(x) = d/√12 to d/2√12
  In digital readout position can be weighted with signal amplitude: σ(x) ∝ 1/(S/N)
Tracking systems design: hit position resolution
Diffusion σ = √(2Dtd), td drift time, D = µ kT/q  σ ≃ 8 µm for 300 µm thickness
S/N degrades with irradiation and cross-talk effect should be considered
Ultimate resolution is also limited by δ-rays emission that shift center of gravity (favoring small thickness but allowing lower diffusion),
Compensating or not Lorentz angle in B-field and/or tilting modules compared to ⊥ incidence
Charge sharing depends on diffusion1) in sensitive element, S/N2), incident angle and B-field, Resolution3) optimization is a compromise in layer thickness, pitch and configuration parameters4) It should also consider 2-tracks separation, requiring thorough simulation and measurements
pitch d
Si-sensor
CMS HL-LHC pixel sensors
150 µm thick, 50x50 µm2

## Slide 10
Tracking system design: physics parameters
Measuring low momentum tracks is important for hard scatter vertex and for pile-up mitigation

## Slide 11
Current trackers: ATLAS and CMS examples
4 barrel layers and 3 disks
precision ≃ 10 -15 µm
Silicon Pixels
50 x 250-400 µm2 ~ 1.7 m2 ~ 80 Mch
Silicon Pixels
100 x 150 µm2 ~ 1.3 m2 ~ 124 Mch
Barrel Silicon Strips
80 µm pitch ~ 60 m2 ~ 6 Mch
Barrel Silicon Strips
80 - 180 µm pitch ~ 200 m2 ~ 9.6 Mch
36 TRT 4 mm straws precision ≃ 120 - 140 µm, 4x2 Si strips layers precision ≃ 120 - 140 µm
10 x 2 barrel layers and 9 disks
precision ≃ 20 - 30 µm
ATLAS
CMS

## Slide 12
Future Silicon trackers: ATLAS and CMS optimizations at HL-LHC
Overall configuration drivers
Both trackers extend Inner Tracker pixel (IT) coverage up to η ≃ 4 for VBF-H and VBS physics
ATLAS has a 5 layers barrel pixel detector
  Should optimize IP resolution (depending on MS), and also improve two track separation
CMS has a design to provide Outer Tracker (OT) track parameters in hardware trigger at 40 MHz
  Possible thanks to the high B-field, requires a pixelated layer close enough to the beam for z-coordinate measurement, but prevents a 5th pixel barrel layer
Inner pixel layers are replaceable both in ATLAS and CMS
Stereo for z/r-coordinate in OT
OT
IT
39 mm
291 mm
29 mm
160 mm

## Slide 13
Future Silicon trackers: ATLAS and CMS optimizations at HL-LHC
Main configuration parameters
Number of hits per track: the figure of merit is the efficiency, including redundancy
https://cds.cern.ch/record/2669540/files/ATL-PHYS-PUB-2019-014.pdf
total
Pixels only
Not fully comparable ATLAS plots include overlaps

## Slide 14
Future Silicon trackers: ATLAS and CMS optimizations at HL-LHC
Main configuration parameters
Detector weight: divided by 2, with less layers, lighter mechanics, tilted modules in forward regions, new CO2 cooling, DC-DC powering to reduce cable material and better arrangement of services, figures of merit:
  Low fraction of radiation length reduce MS, γ-conversion and e-bremsstrahlung
  Large interaction length reduce hadron interaction rates
Tracker acceptance volume
CMS seems to have slightly lower X/X0 (particularly in endcaps)

## Slide 15
Future Silicon trackers: ATLAS and CMS optimizations at HL-LHC
Detector weight:
  Thorough weighting of parts and registration of material at construction needed for simulation
  Photon conversion and hadron interaction radiographies from data allow to correct description

## Slide 16
Future Silicon trackers: ATLAS and CMS optimizations at HL-LHC
Sensor parameters: the figure of merits are hit occupancies and resolutions
  Number of channels has been increase by ≃ 4 to 6 x present trackers1)
    Pixel sizes ≃ 25 x 100 µm2, 100 - 150 µm thickness
    Strip pitch ≃ 75 to 90 µm and length ≃ 2.5 to 5 cm length (likely 290 µm thickness)
    n-in-p and 3D sensors, radiation tolerance up to NIEL ≃ 2 x 1016 1 MeV neq/cm2 and TID of 1 Grad
1) High # of channel is more a density and power issue in FE electronics than a data bandwidth issues with zero suppression in FE

## Slide 17
Future Silicon trackers: ATLAS and CMS optimizations at HL-LHC
Performance criteria: efficiency and fake rate
interactions
https://cds.cern.ch/record/2669540/files/ATL-PHYS-PUB-2019-014.pdf
https://cds.cern.ch/record/2272264/files/CMS-TDR-014.pdf

## Slide 18
Future Silicon trackers: ATLAS and CMS optimizations at HL-LHC
Performance criteria: transverse Impact Parameter resolution
  ATLAS studies:
    Smaller radius of first layer dominates geometry factor compared to benefit of 5th layer
    ≃ GeV track resolution is dominated by MS1)
    Digital clustering is beneficial compared to binary mostly at high pT
    25 x 100 µm2 form factor is better than 50 x 50 µm2
Jet tracks are in the range 1 -10 GeV, similar behavior in longitudinal direction with slightly smaller performance due to angle and MS
MS dominates
MS limit

## Slide 19
Future Silicon trackers: ATLAS and CMS optimizations at HL-LHC
Performance criteria: pT resolution
  ATLAS studies:
    σ(pT) up to > 10 GeV dominated by MS
    σ(pT) 100 GeV sensitive to resolution
CMS has a better σ(pT) due to higher B-field
MS limit
Bending &
resolution limit
Resolution effect

## Slide 20
Future Silicon trackers: CMS Track Trigger
Example of efficiency and background rate reduction for a muon trigger threshold at 20 GeV

## Slide 21
Future Silicon trackers: CMS HL-LHC OT modules example
Two types of modules: < 50 g, power consumption
FE 20(50) ns peaking(full) time, 0.5 mW/channel
Total cooling power (-35∘): 100(50) kW Outer(Inner) Tracker

## Slide 22
Future Silicon trackers: next colliders performance target
e-e experiments (ILC/CLIC/FCC-ee/CepC): track PT and Impact Parameter resolutions ≃ /5 LHC
    σ(pT)/pT2 ≃ 3 x 10-5 GeV-1 (p ≤ 100 GeV)
    σ(d0)/d0 ≃ 2/3-5/10-20 µm (100/10/1 GeV at 90∘)
  R&D challenge
    ≃ 3 µm hit resolution with ≃ 0.2 % X0 per layer in pixel vertex detector
h-h experiments FCC-hh/SppC need similar detectors
    Resolutions ≃ x 2 e-e (due to larger inner layer radius (rates/radiation) and mass (power/cooling))
  Additional R&D challenge
    Hit rate readout capability ≃ 30 GHz/cm2 in inner pixel layer
    Current technology would not survive R ≤ 30 cm for radiation tolerance

## Slide 23
Tracker parameters / experiments | ILD-ILC | SiD-ILC | CLICdet-CLIC | CLD-FCC-ee | IDEA FCC-ee/CepC | Baseline-CepC | FCC-hh (SppC)
Silicon: Planar, 3D sensors, HR/HV CMOS, hybrid/3D/SoI interconnection or monolithic readout |  |  |  |  |  |  | 
In/Out layer radius (mm) | 16/60 | 14/60 | 30/60 | 17/60 |  | Same as ILD | 25/200
Number of layers/disks | 3 x double layers | 5/4 | 3x double-layers | Same as CLICdet | Same as CLD |  | 
Thickness (µm) | 50 to 100 (depending on elctronics) |  |  |  |  |  | 50 to 100
Pitch/cell size (µm x µm) | ≤ 25 x 25 |  |  |  |  |  | 25 x 50 - 33 x 400
Hit resolution (µm) | 3 |  |  |  |  |  | 7
(X0)/layer (%) | 0.2 |  |  | 0.3 |  |  | 1
σ(Δd0) (µm) (1/10/100 GeV) | 10/3/2 |  | 20/5/2 | 20/5/2 |  |  | 30/10/5
Max NIEL (1 MeV neq/cm2)/TID (Mrad) | 1011/0.1 | 1011/0.1 | 1011/0.1 | 2 x 1212/1 |  |  | 6 x 1017/ 30 x 103
Outer Tracker technologies | TPC1) + Si | Si | Si | Si | DC2) + Si | Si | Si
Layer/Outer radius (mm) | 153/300/1800 | 1200 | 1500 | 2100 | 2000 | Same as ILD | 200/1600
Number of layers/disks (IT/OT) | 2/1 double Si inner/outer TPC | 5/4 | 3+3/7+4 | same as CLICdet | 12 layers 1 cm2 x 1.2 m |  | 
Transverse pitch (µm) | 50 |  |  |  |  |  | 33
Transvers hit resolution (µm) | 7 |  |  |  | 100 |  | 10
X0/layer (%) (Barrel) | 1 |  |  |  | 1.6 (total) |  | 2/2.5
σ(ΔpT)/pT2 (GeV-1) (< 100 GeV, 90∘) | 2-3 x 10-5 |  |  |  |  |  | 5 x 10-5
Min NIEL (1 MeV neq/cm2)/TID (Mrad) |  |  |  |  |  |  | 5 x 1015 / 10
Time integration window | 0.5 - 5 µs | 0.5 - 5 µs | 5 ns | 1 µs | 1 µs | 1 µs | 25 ns
Outer Tracker Vertex pixel detector
Future Silicon trackers: next colliders concepts
Number of hits in TPC ≃ 225 with expected resolution of ≃ 150 µm
Number of hits in DC ≃ 122 with expected resolution of ≃ 100 µm

## Slide 24
ILD
ILD
SiD
σ(pT)/pT2 = a ⊕ b /psin3/2(θ)
hit resolution
Future Silicon trackers: e-e collider performance simulations
TPC(DC) + Si seems to do slightly better than full Si for MS (small pT)
FCC-ee
FCC-ee IDEA DC +Si
Θ =90∘
CLIC
CLIC
Dominated by MS
Dominated by σ(hit)

## Slide 25
Future Silicon trackers: e-e collider performance simulations
Impact parameter resolution is more sensitive to multiple scattering than intrinsic resolution
CLIC, ILD and SiD designs provide similar precision
At high momentum resolution seems better than expected from parametrization
σ(d0) ≃ a ⊕ b/pT sin1/2 (θ) = a ⊕ b/psin3/2 (θ)
SiD
ILD
CLIC
CLIC

## Slide 26
  δpT/pT ≃ 0.5(2)% at 0.1(1) TeV (η<2)
Cell size down to 25 x 50 µm in inner layers for low occupancy and ≃ 5-10 µm hit resolution for 2-track separation in boosted objects
Tilted design to minimize MS, conversions, interactions
10 GHz/cm2, fluence ≃ 1018 1 MeV neq /cm2 and ≃ 30 GRad for 30 ab-1 at inner layer radius 2.5 cm
Current sensor and readout technologies would not
sustain radiation for R < 40 cm,
effective Pile-Up of ≃ 50 would require ≃ 5 ps Time of Flight precision**
* Compared to 6 x 109 and 2.2 x 109 for ATLAS/CMS Phase-II Trackers; ** Compared to 30-40 ps in ATLAS/CMS HL-LHC MIP Timing Detectors
Future Silicon trackers: FCC-hh design proposal
Φ = 3 m, L=2 x 16, ηmax ≃ 6, ≃ 400 m2, 16 x 109 channels*, cell size 25 µm x 50 µm - 33 µm x 400 µm - 33 µm x 2-50 mm
d0 resolution of 5/10/30 μm at η= 0 for pT = 100/10/1 GeV/c at 90∘

## Slide 27
Si-crystals semiconductor properties:
  Small energy gap 1.2 eV (between valence & conduction band), E (e-h pair creation)1) ≃ 3.6 eV
  High density 2.33 g/cm3; dE/dx (MIP) ≈ 3.8 MeV/cm ≈ 106 e-h/μm (average)
  High carrier mobility: μe(μh) =1450(450) cm2/V.s,
    v = μE, fast charge collection can go down to O(1) ns
  Material used in industrial process, relatively low cost
Tracking systems: Silicon technology
≃ 30 eV LAr and 100 eV in scintillators
Alternative semi-conductors: Ge need cryogeny with liquid nitrogen at 77k, Diamond less signal and expensive

## Slide 28
Tracking systems: Silicon sensors
≃ 104 more free carriers in Si than MIP signal
CMOS and DepFET
Monolithic Active Pixel:
Microelectronic process, collection electrodes readout with MOS electronics grown on substrate
CMOS not depleted (no E-field) e- are collected through diffusion, DepFET has some low voltage depletion
Works for small pitch, thin sensors slow signal time integration
Hybrid design pixels/strips: planar and 3D
More complex process (double sided) to allow depletion voltage
  p/n doping (acceptors (B, …)/donors (P, As, …) allow to work as a p-n junction with reverser bias and full depletion of free carriers (noise)1)
Electrodes connected to electronics through bump(wire) bonding in pixels(strips)
50 µm
p+
p+
n-in-p
n-in-n
300 µm 1 µm
Several Si-sensors types and design, differences are in depletion, electronic readout implementation and eventually in performance, hybrid designs much more radiation tolerant

## Slide 29
Detector equivalent scheme
DC coupling
DC coupling
AC coupling
Tracking systems: Si-sensors electronic scheme and noise
Noise:
  ENCC = a + b .C dominates total noise, b ∝ 1 / τ (integration time) and C electrode capacitance (proportional to size)
  ENCI = (e/2)√(Ileakτ/e) leakage current noise becomes important after irradiation
  ENCRp = (e/e) √[kTτ/2Rp] (bias resistor)
  ENCRs = 0395C √(RskT/τ)
  e euler number, e electron charge
DC coupling used for small size pixels/mini-strips (small C and Ileak)
AC coupling preferred for strips to avoid large Ileak (strips have also larger C)
Typical noise for Si-sensors today is ≃ 100(1000) e- for pixels/strips
Choice of S/N threshold is an optimization of hit efficiency versus noise occupancy (bandwidth), a minimum of 1/5 of S is considered acceptable1)2)
In pixels a higher threshold ≃ 10 x N is needed to contain absolute bandwidth
Precise timing measurements need higher S/N to reduce noise contribution to resolution

## Slide 30
Tracking systems: Si-sensors irradiation effects
Irradiation introduces default in the crystal lattice that reduce signal and/or increase noise
  Mostly displacement of Si-atoms and doping modification (affecting band gap levels) result in:
    Increased leakage current1) , and therefore noise
    Modified doping concentration mostly toward p-type, requiring Vd increase
    Creation of trapping2) centers that captures electrons and holes, reducing
    Charge Collection Efficiency, the most critical effect at high irradiation level
  Surface damage (SiO2 layer) that do not affect CCE but can create operation issues
    Typically solved with design features
  Annealing decrease Ileak and allows diffusion of defaults/change of
  doping but beneficial annealing is followed is by reverse annealing
Operation optimizations
  Temperature as low as possible, annealing scenarios during maintenance
Sensor optimizations3)
  n-in-p (p-type bulk) collect electrons (less trapping), avoid some micro discharges creating noise
    ATLAS, CMS and LHCb choice for LHC upgrade
  Thinner sensors (deep signal is not collected), reduce Vbias and Ileak and allow higher electric field
  Material and fabrication process details are important
Ileak varies exponentially with Temperature x 2 every 7∘, hence operation at low temperature for noise and also to avoid thermal runaway
Trapping is characterized by collection time  prefer electron collection (faster), and higher electric field
Non-Ionization Energy Loss concept do not fully apply at highest irradiation, requiring thorough testing with all particles (n,p,γ)

## Slide 31
Tracking systems: Si-sensors Outer Tracker S/N (depleted case)
In Si-sensors with full depletion, charge collection efficiency before irradiation is ≃ 100%
  Ex. 200 µm thickness: max probability(average) charge1) number is ≃ 14000(21200) e-
  This allows comfortable S/N, typically ≥ 15 for all type of designs2)
Example of CMS at HL-LHC n-in-p sensors after irradiation
  S/N remains comfortable at 12 with sufficient margin, sensor specification to sustain 800 V to provide further margin, but would approach thermal runaway limit
For S/N seed strip signal (after charge sharing) needs to be considered
S/N referring to the collected charge assumes that the preamplifier-shaper integrate all the charge
PS strip sensors, S/N ≃ 12 at 1.5 x 3000 fb-1
2S strip sensors, S/N ≃ 12 at 2 x 3000 fb-1

## Slide 32
1016 neq/cm2
6400 e-
1) 1st layer in CMS is closer to the beam line than in ATLAS with about 1.6 x more fluence
CMS planar pixel sensors ongoing tests: 2nd layer can sustain 3000 fb-1 at 600 V
CMS pixels 1st (2nd) layers are exposed to 2(0.5) 1016 1 MeV neq/cm2 for HL-LHC 3000 fb-1
  Efficiencies measured for S/N threshold (RD53) = 1200 (10-6 noise occupancy ≃ 1% of hits in layer 4)
3D pixel sensors ongoing tests with RD53 chip:
1st layer in CMS1) should sustain at least ½ of 3000 fb-1 with full efficiency at 150
Tracking systems: Si-sensors Inner Tracker S/N (depleted case)
CMS
ATLAS

## Slide 33
Silicon trackers state of the art: LHCb vertex (pixel) detector
LHCb VELO upgrade for installation during 2020
  12 disks of 4 modules, inner radius ≃ 4.5 mm
  Planar n-in-p sensors fully depleted up to ≃ kV
  200 µm thick, 55 x 55 µm2 pixels, ≃ 10 µm hit resolution
  120 x 120 μm2 micro cooling-channel etched in sensor substrate
    ≃ 1.5% X/X0 per disk
  Radiation tolerance ≃ 1015 1 MeV neq/cm2 (T ≃ -20∘)
R measuring strips
with double metal r/o
Phi measuring strips
Original strip detector new one with pixels
old
new
.
ATLAS
.
ALICE ITS2 - Belle-II vertex

## Slide 34
Silicon trackers state of the art: ALICE ITS2 (installation 2020)
7 layers of MAPs ≃ 10 m2 with 12.5 Gpix up to η = 1.3
3 inner layer each 0.35% X/X0 from 22 to 40 mm
4 outer layers of 1% X/X0 up to 400 mm
Installation in 2020
    Sensors CMOS TowerJazz 180 nm technology (no depletion :
      Epitaxial 50 µm thick, pixels, 29 x 27 µm2, ≃ 5 µm resolution
    Binary zero suppressed readout 100 kHz, ≃ 5 µs integration time
    Radiation tolerance ≃ 2 x 1013 neq/cm2 and ≃ 3 Mrad
Monolithic Active Pixels (MAPs): CMOS standard process with readout grown on Si-sensors
lightest and most precise designs, relatively slow readout and low radiation tolerance
.
.
ATLAS
CMS
Outer Barrel Stave (1.5 m long)

## Slide 35
Silicon trackers state of the art: BELLE-II pixel detector
Pixel detector1): 2 layers at 1.4 cm and 2.2 cm, 0.03 m2
  Thickness ≃ 75 µm, pixels ≃ 50 x 50/85 µm2 , σ(hit) ≃ 15 μm resolution ≃ 0.2% X0/layer
  Binary readout continuous row by row, 20 µs integration time
  Radiation tolerance ≃ 1013 neq/cm2 and ≃ 10 Mrad
Monolithic Active Pixels (MAPs) in depFET technology
σ(d0) = 20 µm for pT = 1 GeV
1) SVD is ≃ 1m2, 4 double side stereo layers at 3.9, 8, 10.4, 13.5 cm,
3D-prointed support cooling blocks

## Slide 36
Silicon sensors: R&D goals
An ideal detector would be monolithic with high:
hit and time precision, speed and rate capability, radiation tolerance; and low cost
  Improve hit precision  e+-e- colliders
    Smaller pitch and thickness: deeper sub-micron technology
    Improve charge sharing: new design ex. ELAD
  Improve radiation tolerance  h-h colliders
    Smaller pitch and thickness, deeper sub-micron technology
      Planar, 3D to maintain high field and small electron path
    Work on material and fabrication process to reduce damages
  Improve integration of electronics  e+-e- colliders, h-h colliders
    Monolithic, new connection scheme to electrodes, ASICs interconnection
  Improve cost  e+-e- colliders, h-h colliders
    Develop process as close as possible to standards used in microelectronics and imaging industries

## Slide 37
pixels < 50 x 50 µm2
Design for charge sharing
process variants for pitch
3D sensors
Silicon sensors: R&D examples1)
AC connection through insulating glue
can also apply here
Interconnection
Through SiO2 via process
Hybrid design
Monolithic devices
CMOS modified process for depletion HV-CMOS (left)and HR-CMOS (right)
1) Design of sensors particularly for field configurations is supported by simulation tools ex. TCAD, it can be interfaced with GEANT to assess signal fluctuation effects, ex CLIC studies

## Slide 38
Silicon sensors: R&D demonstrators (not exhaustive)
Sinergy with 1) CERN MEDIPIX, 2) Mu3e experiment
Modified HR-CMOS
depletion (6V)
Modified HV-CMOS
depletion (< 100 V)
SoI process
Si/ASIC wafers connected
through Insulator Oxyde layer
Smaller pitch and thinner planar and 3D pixels bump bonded
Planar/3D finer pitch for resolution
Capacitive Coupling (PD) of HV CMOS design to ASIC through insulating glue
CMOS modified process for radiation tolerance
faster and higher rate readout
with faster and higher rate readout capabilities
CLIPS
MALTA
Demonstrators ≃ 2 x 2 cm2
Connection to high rate capability ASIC planar and CMOS
CLICPix1)
Cracov SoI
CLIPS
MALTA
ATLASPix2)
ALICE investigator
CCPD C3DP
CLICTD

## Slide 39
Silicon sensors: R&D demonstrators (not exhaustive)
Silicon sensor R&D | Hybrid | SoI |  | CMOS Monolthitic |  |  |  | CCPD | CCPD
Demonstrator | CLICpix | Cracov | CLIPS (CLIC) | ALICE investigator | CLICTD* | Malta/Monopix | ATLASpix(Mu3ePix) | C3DP/CLICpix | C3DP+CLICpix
Sensor | planar | planar | planar | HR-CMOS standard | HR-CMOS modified process |  | HV-CMOS |  | 
Connection to readout electronics | bump bonding | SoI | SoI | momolithic | monolthitic | monolithic | monolitic | CC with glue | 
ASIC technology (nm) | 65 | 200 | 200 | 180(TJ) | 180 (TJ) | 180(TJ)/150(LF) | 180(AMS)/150(LF) | 65 | 
Thickness (µm) | 50 / 200 | 300 / 500 | 100 / 500 | 50 | 50 / 100 | 100 | 60 | 50 | 
Pitch/cell size (µm x µm) | 25 x 25 | 30 x 30 | 20 x 20 | 28 x 28 | 30 x 300 | 36 x 36 | 40 x 130 | 25 x 25 | 
Hit resolution (µm) | 9 / 3 | 5/2 |  | 5 |  | 4 | 13 | 6 | 
Time resolution (ns) | 7 |  |  | 6 |  | < 10 | 7 | 7 | 
Max NIEL (1 MeV neq/cm2)/TID (Mrad) | O(1016)/Grad |  |  | O(1013)/300 |  |  | O(1015)/100 |  | 
* In production
Cracov SoI
CLIPS
MALTA
ALICE investigator
CCPD C3DP
CLICTD
CLICPix1)
ATLASPix2)
Sinergy with 1) CERN MEDIPIX, 2) Mu3e experiment

## Slide 40
  CMOS MAPs suitable for outer trackers and close to fulfil needs for ee- collider vertex detectors
    3 µm hit resolution likely needs < 25 x 25 µm2 pixels (charge sharing1) too small with 50 µm thickness)
    ≃ 200 MHz/cm2 hit rate capability and ≃ 5 ns time precision (CLIC requirement achieved)
      However CLIC inner pixel layer hit rate requires 6 GHz/cm2
    Enlarged sensor size 15 x 15 cm2 with stitching process is being investigated
  New ASIC connection techniques still at early stage, bump-bonding difficult with smallest pixels
  O(100) better radiation tolerance achieved in HR/HV CMOS modified process 2 x 1015 neq/cm2
    Still marginally at the level of requirement for an outer tracker FCC-hh/SppC layer
Silicon sensors: R&D demonstrators outcome and outlook
Deeper sub-micron technologies 65 nm or less can improve in all aspects
    Ex. ALICE ITS3 upgrade proposal: CMOS MAPs in 65 nm technology, 10 x 10 µm2 pixels, ≃ 20 µm thick sensors for 0.05% X0
  FCC-hh/SppC remains a challenge for hit rate and radiation tolerance
    Also alternative material R&D for radiation tolerance, ex. pCVD diamond CERN RD42
1) Some design studies (ELAD) with implants in depth of sensors to control charge sharing through E-field configuration

## Slide 41
Topics not addressed in this section
  Other tracking technologies
    TPC, MPGDs in Gas detector section
    Scintillating devices in calorimeter section
  Si-sensors for other purpose
    Pad-sensors for High Granularity Calorimeters in calorimetry section
    Exploitation of precision timing with regular sensors1)
    LGAD technology for precision timing in MIP Timing Detector section
  Other silicon technologies used for photodetection
    APDs, HPDs, SiPMs, in calorimetry section
CMS HGC measurement of time resolution in Si-diodes
    1) Regular silicon sensors could provide ultimate timing precision of ≥ 70 ps at S/N ≥ 10
NA62 vertex detector achieve ≃ 115 ps precision https://indico.cern.ch/event/577856/contributions/3420172/attachments/1878363/3093866/eps2019_na62_kleimenova.pdf

## Slide 42
Topics not addressed in this section: LHCb scintillating Fiber Tracker
3 stations, each 2.5% X/X0 - 4 plans (X-U-V-X) with ± 5∘ stereo angle - 50-75 µm resolution
  3 M fibers Φ 250 µm x 2.5 m (10 000 km)
    3 Mrad in inner region
    High precision assembly of fiber mats
  Readout with 128 SiPM array 250 µm pitch
    40∘C cooling to sustain 1.2·1012 neq. /cm2
2x 3m
2x 2.5 m

## Slide 43
Additional information

## Slide 44
Charged particle interaction in matter: parameters

## Slide 45
Charged particle interaction in matter: Bethe-Bloch terms

## Slide 46
Charged particle interaction in matter: particle energies
Energy Range | Sources of Radiation
eV | visible light, secondary electrons, thermal neutrons
keV | X-rays, electrons from radioactive β decay
MeV | α particles, photons from excited nuclei, acceleration with cyclotrons, solar neutrinos
GeV | air showers from cosmic rays, acceleration with synchrotrons
TeV | high-energy accelerators (e.g. LHC) TeV gamma rays from galaxy
> TeV | cosmic accelerators: quasars, super-massive black holes, supernova remnants, …