## Slide 1: Data versus simulation
Yannis, Corinne, Thodoros, et al,
Mars 2019

## Slide 2
Input to the simulation
Tumulus Description
Truncated cone
Inner Material Dirt with density 2.2 g/cm3, nothing else
Nb of detectors 3x2. Detector size (m) 2x0.07m 0.8m, 0.8m
Detector Rotations 10 deg in q (polar) and 188 deg in f (azimuthal) looking south
Detector digitization by Corrine
Need precise direction !

## Slide 3
Missing or more matter
Tumulus in CATIA
Input data file
GEANT4 approximation
The tumulus seen by the detector

## Slide 4: Acceptance
The acceptance with Geant 4 is computed using 50M geantinos
We generate geantinos covering all the surface of the most far detector with : q=0-50 degrees and f= +-40 degrees
For each q/f bin we count the number of events with 3(6) hits, one per detector and we divide by the number of generated events in the same bin

## Slide 5: q and f for m, normalized to the acceptance distributions
Distribution divided by acceptance
??
q=0 means horizon !

## Slide 6
Ratios simulation only : Monument / No monument

## Slide 7: Reconstruction
Data
  Events are filtered by Thodoros to validate hits (ADC <200 )
  Use channel id, get coordinates in the detector system, fit a straight line in 2 directions and measure q and f in the detector system ! Reject bad tracks
  ~5M events
Simulation
  Use channel id after Corrine’s digitization, fit a straight line in 2 directions and measure q and f in the detector system !
Residuals from fit
q Versus f Data
q Versus f Simulation

## Slide 8
True
Reconstructed
Simulation

## Slide 9: Data versus simulation
Cosmic muons angular distribution models
  Simulation is done with both polar and azimuthal angles distributions uniform
  Using a given law f(q,f) we compute for every bin q,f a weight = ratio of f(q,f) / uniform
  The q,f distribution from simulated muon events, after reconstruction is multiplied by the weights to obtain a new q,f distribution . In this way we can change the model without regenerating all muons with Geant4
Normalising data and simulation
  The normalization between data and simulation is computed using the events above the tumulus

## Slide 11
We make the ratio of Data / (Normalized weighted simulation events)
When ratio = 1 means it means > 1 !!!!

## Slide 12
Ratio data / simulation integrating over 1 dimension

## Slide 13
Nb of events data in red and simulation in black versus f for 2 degrees slices in q

## Slide 14
Ratio versus f for 2 degrees slices in q

## Slide 15: Conclusions and projects
We need a reliable muon angular distribution in open sky
  Use backward tracks
Work on the geometrical tumulus model. Read geo-points and build an adequate solid in Geant4
We need precise geometry for the detector position and pointing
Optimist that the method works
The detector should be positioned below the horizon if we search for a monument inside a tumulus