## Slide 1
Fast timing on monolithic CeBr3 detectors with digital Si-PM
M. Z. Hmissi (1) , A. Iltis (2), C. Tata Zafiarifety (2), G. Zeufack Tadonkenga (2), L. Malaghes Rodrigues (2), B. Mehadji (3), C. Morel (3), H. Snoussi (1)
(1) University of Technology of Troyes, UMR CNRS 6281 – France
(2) Damavan Imaging, F10430 Rosières Près Troyes - France
(3) CPPM/IN2P3, Marseille, France
19/06/2019
Portorož-Slovenia
Notes: Je me presente
Good afternoon everyone, prior to waste management operations, a camera that can image the contamination field, identify and quantify the contaminants would be a great progress. We propose in this presentation a binocular CeBr3 Compton camera for nuclear decommissioning and nuclear waste management.

## Slide 2
2
Damavan Imaging in short
Damavan : Images from time
A Start-Up founded to develop breakthrough innovation: Temporal Imaging
Leading the program Temporal: Investments for the Future Program (PIA) conducted by ANDRA
H2020 SME Instrument Phase 1 laureate

## Slide 3: Temporal Imaging with digital SiPM
M. Z. HMISSI - A. ILTIS – Animma 2019
Notes: Our technology is based on Temporal imaging.

## Slide 4: Temporal Imaging with digital SiPM
Using both light and time distribution
Nb of photons/pixels
Time of arrival of the first photon for each pixel
To obtain in real time the characteristic vector for each gamma photon
X,Y
Z (DOI)
T = time of scintillation event
E = Energy of the photon
A monolithic fast scintillating crystal
(LYSO, CeBr3, LaBr3:Ce…)
Alain Iltis/Hichem Snoussi,J. Imaging 2015, 1(1), 45-59
Alain Iltis, FR 1260596. Nov 2012
The basics of Temporal imaging
Notes: Which use the light and the time distribution in monolithic fast scintillating crystal coupled to a digital SiPM Philips. This concept allows to obtain in real time the characteristic vector for each gamma ray defined by the position of the interaction of the gamma photon inside the crystal, its depth of interaction, the time of the scintillation event and the deposit energy.

## Slide 5: Temporal Imaging with digital SiPM
Why does time matters for localizing a photo-electric event?
Index gap crystal/detector  only the photons emitted inside a cone bonded by the critical angle qc are detected directly (a)
The other photons are delayed (b,c)
A 1ns « snapshot » image could allow to recognize the location of the cone
M. Z. HMISSI - A. ILTIS - Animma 2019
Notes: The time information is very important to localize the interaction event. As we see in this image, time information allows to select only photons emitted inside the cone bounded by the critical angle, the other photons are delayed so they are not used to calculate the position.

## Slide 6: Temporal Imaging with digital SiPM
Pixels (light distribution): 4x4mm
Die (time distribution): 8x8 mm
Phillips Digital Si-PM acquisition
Time stamp on 1st photon/die possible
One Die
One pixel
Notes: To collect optical photons, we use as photodetector an SiPM Philips providing a digital sum of detected photons. It is composed of 8 by 8 pixels. each set of 4 pixels forms one die.

## Slide 7: Temporal Imaging with digital SiPM
Light distribution
  Number photons/pixel
  Color + number
Time distribution
  Delay since first photon detection (20ps pitch)
  Number in white
Building a « matrix of event » for each valid scintillation event
Key
  Z = calculated from diameter of undiffused photon circle
  X,Y = barycenter of undiffused photon region
  T = Time correction for propagation in LYSO
  E = Total number of photons collected
Event 80, 3682, X = 21.9mm, Y = 22.1 mm,
Z = 14.5 mm, T = 38.32 ps, E = 562 keV
Notes: In this slide, we show an example of a light and time distribution measured by the digital SiPM. Optical photons are collected per pixel. Time is posted per die in timestamp unit. Time and light intensity tell us probably where the interaction of the gamma ray occurs. The depth of interaction is calculated from the diameter of undiffused photon circle. The deposit energy is determined by the total number of collected photons.

## Slide 8: Detector performance and camera lay-out
M. Z. HMISSI - A. ILTIS - Animma 2019
Notes: Now, we are talking about our detector performances in energy resolution, position localization and time resolution.

## Slide 9: Detector performance and camera lay-out
Monolithic detectors performances
)
Energy resolution
6.2% @ 662 keV
Resolution XY = 1 mm FWHM
CRT 20mm thick CeBr3 (235 ps)
Resolution Z = 2.5 mm FWHM
9
Notes: We measure a CRT of 235 ps in 20mm thick CeBr3 without correction, the energy resolution was 6.2% measured at 662 keV. Transversal gamma ray position resolution was 1 mm FWHM and the DOI resolution was 2.5. All of them are measured in 12mm thick CeBr3.

## Slide 10
Timing performance (22Na FWHM)
CRT 20mm thick CeBr3 (235 ps)

## Slide 11: Detector performance and camera lay-out
Temporal imaging Compton Camera CeBr3
Low noise level
2 CeBr3 crystals 27mm distant
High sensitivity
17 cm3 detector
High temporal resolution
High X,Y,Z position accuracy
32x32x12mm
32x32x5mm
11
Notes: A Compton camera is a detector which aims to image gamma rays in the energy range from about a few hundred keV to several MeV, so that Compton scattering effect is dominant. A Compton camera generally consists of two detectors, often referred to scatterer and absorber. An incident gamma ray is first Compton scattered at the scatterer providing a part of its energy to recoil electron, and then scattered photon is absorbed at the absorber depositing the rest energy. Using these observed quantities, the scattering angle θ is calculated. From θ and the information of interaction positions, the direction of each incident gamma rays can be constrained within a cone which has the vertex at the scattered position, that is called Compton cone. Therefore, accuracy of determination of energy and interaction position in the detector directly influence the performance of Compton camera.
Our Compton camera prototype consists in 5 mm thick CeBr3 diffuser plate and a 12 mm thick CeBr3 absorber plate separated by 27 mm. each scintillator is coupled optically to a digital SiPM philips and sealed hermetically inside an aluminum housing.

## Slide 12: Detector performance and camera lay-out
A camera designed for noise rejection to allow imaging of weak sources
CeBr3 has no intrinsic background
The time veto between diffuser and absorber plate is <300ps: very efficient background rejection
Only events fulfilling Compton equation conditions are recorded: Partial energy deposit events excluded from our spectrum
But we still record 88% of the events forecasted by our camera’s GATE simulation!!!
Notes: Our prototype is designed to image weak radioactive sources. Its interesting features are:
The absence of intrinsic background in CeBr3 allows imaging of week sources.
Background rejection using time veto between diffuser and absorber plate.
Only 12% of true Compton events are lost by the processing electronics.

## Slide 13: Camera imaging performance
M. Z. HMISSI - A. ILTIS - Animma 2019
Notes: characteristic vectors defined previously are used then to reconstruct radioactive sources.

## Slide 14: Camera imaging performance
Position calibration
(-45°,45°)
(0°,45°)
(-45°,0°)
(45°,0°)
(0°,0°)
(-45°,-45°)
(45°,-45°)
(45°,45°)
(0°,-45°)
Notes: To evaluate our camera in experimental case, we used at first a punctual Sodium source situated at different positions in the field of view of the camera. In each sub image, the source is well reconstructed using a correct number of Compton valid event.

## Slide 15: Camera imaging perform-ance
Angular resolution test 8°
137Cs contrast 3/1
137Cs (700 MBq)
137Cs (220 MBq)
Notes: Also, we assess the angular resolution of the camera with two Cesium sources separated by an angular distance of 8°, the most intense source is correctly reconstructed the second source is barely shown due to its low activity. The two sources are well separated.

## Slide 16: Camera imaging performance
Cylinder phantom 180x30 mm² filed with 18F.
Observed in 511 eV lines: 18000 valid events.
Number of iterations = 10.
Distance from the source: 20cm.
Image of an extended source
The overall shape of the cylinder is correctly captured !!!
Notes: The response of our prototype in front of extended sources was tested, we can see correctly the shape of the source reconstructed by 18000 valid events, such reconstruction needs high counts so more acquisition time.

## Slide 17: Conclusion: High performance imaging for nuclear decomissioning
Dimension WxDx
230x290x160 mm
Weight
3,9 kg
Power source
110-220V
Operating temperature
-20°C to +40°C
Our prototype will hold 2 heads
Notes: The prototype is ready now, it has the following specifications such as suitable size, light weight, correct consumption and a wide operating temperature.

## Slide 18: Detector performance and camera lay-out
Partnership sought!
Making a demo PET with monolithic CeBr3 scintillators
Time resolved compton imaging of pulse beams
Hybrid PET/Compton systems
Mini sattelite for Gamma ray bursts!
Notes: Our prototype is designed to image weak radioactive sources. Its interesting features are:
The absence of intrinsic background in CeBr3 allows imaging of week sources.
Background rejection using time veto between diffuser and absorber plate.
Only 12% of true Compton events are lost by the processing electronics.

## Slide 19: Possible satellite concept
Possibility of a micro-satellite demonstrator
Instrument is a cube 378 x 378 mm
Mass < 5kg

## Slide 20: Possible satellite concept
6 detectors covering all the sky
4Pi field of view

## Slide 21: Compton Camera Medical Imaging
21
Imaging large animals
3D vision with binocular camera

## Slide 22: Compton Camera Medical Imaging
22
Hybrid PET/Compton

## Slide 23
Questions?