## Slide 1: Development of front-end readout systems FOR DIAMOND hodoscope
F. RARBI
A. Bes, G. Bosson, J. Collot, S. Curtoni, D. Dauvergne, L. Gallin-Martel, ML Gallin-Martel, A. Ghimouz, C. Hoarau, J.-Y. Hostachy, A. Lacoste, J. Livingstone, S. Marcatili, J-F. Muraz, O. Rossetto, N. Rosuel, L. Tribouilloy, M. Yamouni

## Slide 2: Outline
Project overview
Electronic design
  COTS amplifier version
  ASIC Front-End version
Conclusion

## Slide 3: Project overview
Medical physics
  Particle therapy hodoscope: position + time stamp
Using diamond as detector material:
  Intrinsic radiation hardness
  Fast signal risetime enables timing precision of a few tens of ps
  Low noise
  Cost
  Availability of large area
Beam tagging hodoscope for online ion range verification in hadrontherapy:
  Time resolution of 100 ps
  Count rate of 10 MHz/channel
  Spatial resolution ≈ 1 mm
  Radiation hard
Diamonds
double side stripped detectors

## Slide 4: Electronic design
Diamond characterization made with a Fast Current Preamplifier
  DBA III from GSI
  Broadband amplifier from Cividec
Towards a beam tagging hodoscope
  Dozens read-out channels  Home made preamplifier
DBA III GSI
Bandwidth: 2 GHz
Gain: 40 dB
Impedance: 50 Ω
Dynamic range: ~ +/- 1 V
Power Supply: 12 V / 100 mA

## Slide 5: COTS amplifier version
Commercial NPN and PNP bipolar transistor
  1st stage TIA amplifier with resistive feedback followed by a non-inverter amplifier
    Total gain of 92dB
    Cut-off frequency about 520MHz

## Slide 6: ASIC Front-End version
Timing resolution defined by:
For fast system, , with and
  We define a new expression:

## Slide 7: ASIC Front-End version
Design of a multi channel Integrated Circuit:
  CMOS 130nm process technology
  Radiation tolerant technology
  8 channel Trans Impedance Amplifier (TIA) + Fast Discriminator
TIA Parameters | Value
A0 | > 60 dB
F-3dB | 560 MHz
Zin | 20 Ω
Vn,out (output noise) | < 1 mVRMS
Input Dynamic range | 3 µA – 120 µA (<1% linearity)
PTOT | 2.5mW @ 1.2V

## Slide 8: ASIC Front-End version
RMS Output noise about 1.5mV
Timing resolution about 400ps (@ 20fC) due to issues in output buffer (BW about 100MHz) and discriminator stages
Analog output signal for different input charge (10fC, 20fC, 30fC, 50fC and 100fC)
Chip On Board
1st prototype

## Slide 9: ASIC Front-End version
  Part of DIAMASIC (IN2P3 fund project) in collab. with LPC Caen
  2nd prototype improvements:
    Differential signal propagation (immunity to noise issues)
    Multi-gain amplification through voltage control
    Wideband output buffer
  Expected timing resolution about < 120ps (@ 10fC)
    Improve noise in the first stage
Channel Read-Out Parameters | Value
A0 | > 80 dB
F-3dB | 560 MHz
Zin | 60 Ω
Vn,out (output noise) | < 5 mVRMS
Input Dynamic range | 3 µA – 150 µA
Estimated jitter @10fC
Chip On Board
2nd prototype

## Slide 10: Testing Results
Preliminary testing results
A RMS Output noise of about 3.7mV
A Minimum detectable Current input amplitude of about 3µA
Pulse Generator
DUT
WaveCatcher

## Slide 11: Conclusion
Several design at LPSC Grenoble
  COTS components + ASIC versions TIA
ASIC development through IN2P3 project: DIAMASIC
Many improvement still needed!
Thank you for your attention