Study of energy shower profile
and
1m3 energy resolution
Jan Blaha
Laboratoire d'Annecy-le-Vieux
de Physique des Particules
MicroMegas Physics Meeting
LAPP, 22 Avril 2009

---
PART 1
Study of energy shower profile

---
Calorimeter configuration
Properties of the absorber materials:
absorber	Z	ρ [g.cm-3]	λ [g.cm-2]	λ [cm]	1 abs. [cm]	80 planes [cm]
Fe	26	7.87	132.1	16.78	1.9	200
W	74	19.30	191.9	9.97	1.127	170.16
Pb	82	11.35	199.6	17.6	1.993	239.44
Calorimeter with Fe absorber:
Passive layer: 9 λ (including 4 mm thick steel cover)
Active layer: 6 mm (3 mm of gas)
Calorimeter with W and Pb absorbers:
Passive layer: 9 λ
        Active layer: 6 mm (3 mm of gas) + 4 mm of Al (32 cm in total (0.8λ))
22/04/09
 J. Blaha

---
Longitudinal profile – Fe Abs
Longitudinal energy and hit profile (Fe abs, 9 )

---
Longitudinal profile – Fe Abs
Longitudinal energy (hit) profile and energy fraction in shower

---
Lateral profile – Fe Abs
Lateral energy (hit) profile as an energy (hit) density vs radius

---
Lateral profile – Fe Abs
Lateral energy (hit) profile and energy fraction in shower

---
Long. and lateral profile – Fe Abs
Comparison of the long and lateral profiles for 1m3
95 %
95 %
95 %
95 %

---
Analog vs Digital – Fe Abs
Comparison of the longitudinal energy (hit) profiles for different energies

---
Analog vs Digital – Fe Abs
Comparison of the lateral energy (hit) profiles for different energies

---
Longitudinal profile
Longitudinal energy profile for different absorbers (Fe, W, Pb)
100 GeV pions

---
Longitudinal profile
Longitudinal hit profile for different absorbers (Fe, W, Pb)
100 GeV pions

---
Lateral profile
Lateral energy profile for different absorbers (Fe, W, Pb)
100 GeV pions

---
Lateral profile
Lateral energy profile for different absorbers (Fe, W, Pb)
100 GeV pions

---
Mean shower radius
Pb abs
Fe abs
100 GeV pions
W abs

---
PART 2
Study of 1m3 energy resolution
(preliminary results)

---
Configuration
1m3 calorimeter
Fe absorber, 40 planes (4.5 )
No threshold for digital mode
Statistics
(GeV)
3 10 50 100 150 200

---
Dep. energy distributions

---
Hit distributions

---
Nb. of Hits vs dep. energy

---
Nb. of Hits vs dep. energy

---
Energy resolution and linearity
Energy resolution
Linearity

---
Summary and prospectives
Energy shower profile:
Longitudinal shower profile behaves as expected: similar profile for W and Pb
(high Z materials) in comparison with Fe
Lateral shower profile shows surprisingly similar behavior for Fe and W and
slightly worsen behavior for Pb – this need to be explained
Different shower profile behavior for higher energy in case of analog and digital mode
has been found – this could be due to the saturation effect and need to be verified
with in threshold study
1m3 energy resolution:
Digital energy resolution has been found superior to analog contrary to the linearity
which is better in analogue mode (comparable results were found for 8m3)
Energy leakage plays important role and need to be take into account (leakage
corrections?)
Up to which energy we are interested?
As in previous case, an optimal threshold(s) need to be found with respect to
energy resolution and linearity performance
Next work:
Threshold study!