## Slide 1: Cells integration tool overview
Jean-Philippe LOGIER | Mathieu NICLAS | Eric Vigeolas
Cells integration meeting | 03/09/2019

## Slide 2
Cells integration tool overview
JP. Logier | M. Niclas | E. Vigeolas
2
03/09/2019
Longeron handling frame status
  Prototype first version completed (3D+drawings)
  Submitted to Oreka for discussion with the design office
  Prototype to be ordered in October
Pending points
  Carbon truss design
  Interfaces finalization
    with longeron (proto for L3 longeron ok?)
    with cell integration tool

## Slide 3
Cells integration tool overview
JP. Logier | M. Niclas | E. Vigeolas
3
03/09/2019
Longeron + HF configurations
Side covers removed: Test configuration
Central cover removed + longeron rotated:
Cells integration configuration
With covers: shipping configuration

## Slide 4
Cells integration tool overview
JP. Logier | M. Niclas | E. Vigeolas
4
03/09/2019
HF interfaces with cells integration tool
  Design TBD with Oreka
  Positionning tolerances TBD:
    Accurate repetability on HF vs cells integration tool positionning?
    Accurate positionning of the longeron vs cells integration tool ?
Allow cells reworking without re-alignment
Avoid any global alignment system (or some axis)
BUT depends on manufacturing tolerances between base blocks and longeron mounting interfaces + HF tolerances
Located centering holes
Common zone flatnesses
+ perpendicularity

## Slide 5
Cells integration tool overview
JP. Logier | M. Niclas | E. Vigeolas
5
03/09/2019
Cells integration tool layout
Structure
Global alignment system
Pitch /TY
Flexible hinge
+ local alignment system?
Screw holder /
Screwdriver
Kinematic mount
Z
X
Slot alignment system
TY-TZ
RX-RY-RZ
TX
Insertion system
Cell holding system
Aiming/overlap control system
Preliminary integration procedure
  HF mounted on cells integration tool
  Global alignment tool vs longeron (TY-TZ-RX-RY-RZ)
  Cell mounted on the holding system
  Holding system plugged on the tool (kinematic mount)
  Cell insertion (TX) on the longeron with flexible hinge
    No stress applied to the cell/longeron
    Overlap control
    Local alignment if necessary
  Screws installation throught longeron structure
  Screws tightening with torque tool
  Tool removed from the cell
  Pitch offset to aim another cell location
Position of the global alignment system? Adjustable axis TBD
Need local alignment (1 by cell)? Depends on accuracy dispersion between base blocks
Configuration of aiming system: Cells overlap control for safety or target position measurement?
….

## Slide 6
Cells integration tool overview
JP. Logier | M. Niclas | E. Vigeolas
6
03/09/2019
Workpackages on cells integration tool development
 | CPPM | LAPP | LPSC | CERN | UniGe
Integration baseline procedure | X |  |  |  | 
Reworking procedure |  | X |  |  | 
Structure + If with HF | X |  |  |  | 
Global alignment system |  |  |  |  | 
Slot alignment system |  |  |  |  | 
Insertion system |  |  |  |  | 
Aiming/overlap control system |  |  |  |  | 
Cell holding system |  |  |  |  | 
Flexible hinge + local alignment system | X |  |  |  | 
Kinematic mount | X |  |  |  | 
Screw holder/ tightening tool | X | X |  |  | 
Screw design | X |  |  | X | 
To be done firstly
  Integration baseline procedure definition
  Adjustable axis needed (tolerances study on longeron + HF)
  Screws definition