## Slide 1
Initial RI Beam Commissioning of the RAON ISOL Facility
Jinho Lee
on behalf of Rare Isotope Science Project
Institute of Rare Isotope Science (IRIS, RISP)
The 4th International Conference on Advances in Radioactive Isotope Science
ARIS 2023, June. 4~9, 2023. Palais des Papes, Avignon, France

## Slide 2
1. Introduction to the RAON
2. Current status of ISOL facility
3. ISOL beam commissioning
4. Summary & future Plan
Contents

## Slide 3
Bird’s-eye-view of RAON
3
Assembly Bd.
SRF Test Bd.
Waste Storage
Guest House
HQ Office
Electricity Bd.
Control Center
Utility Bd.
Cryogenics Bd.
Low Energy B
Low Energy A
High Energy A
High Energy B
SCL3
SCL2
Accelerator
ISOL
IF
● Experimental System
● Conventional Utilities
● Accelerator System
● RI producing System
Campus Area : 952,066㎡ (including the reservation area of 144,640㎡)
Building Area : 76,259㎡(11 bldgs) with total bldgs. Area of 116,252㎡

## Slide 4
RI beam Production at RAON
 | KoBRA | ISOL | IF Separator
RIB production & acceleration mode | ECR (SIB) SCL3 KoBRA Prod. Target | Cyclotron (p) ISOL (RIB) SCL3 | ECR (SIB) or ISOL (RIB) SCL3 SCL2 IF (RIB)
Production Mechanism | Direct reactions Multi Nucleon Transfer | p induced U fission | PF, U fission
RIB Energy | < a few tens of MeV/u | > a few of keV/u | < a hundreds of MeV/u
 | KoBRA | ISOL | IF Separator
RIB production & acceleration mode |  |  | 
Production Mechanism | Direct reactions Multi Nucleon Transfer | p induced U fission | PF, U fission
RIB Energy | < a few tens of MeV/u | > a few of keV/u | < a hundreds of MeV/u
ISOL + IF
  ISOL : direct fission of 238U by 70 MeV protons
  IF : 200 MeV/u, 8.3 pμA of 238U
  132Sn : 10 keV/u (ISOL)  25 MeV/u (SCL3)  250 MeV/u (SCL2)  more exotic RI (IF)
  (up to ~108 pps)
KoBRA : Korea Board acceptance Recoil spectrometer & Apparatus ISOL : Isotope-Separator Om-Line
IF : In-flight Fragmentation separator SCL 3: (Low-energy) Super Conduction Linac 3 SCL2 : (High-energy) Super Conduction Linac 2

## Slide 5
Expected RIs from RAON
RAON will provide access to unexplored regions of the nuclear chart

## Slide 6
SCL3 beam commissioning
The first successful beam commissioning of the low-energy superconducting linac (SCL3) with 40Ar9+ beam in May 23, 2023 (have been performed by Accelerator Division in IRIS)
Ar9+ beams accelerated by entire SCL3(QWR/HWR)
17.581 MeV/u
21.256 μA

## Slide 7
Superconducting linac SCL3
QWR & HWR Cryomodules
Cryogenic Distribution to Cryomodules
CM/Cryogenic Control Rack and SSPA
Clean beam line assembly
Tunnel and galley
Installation completed in 2021

## Slide 8
1. Introduction to the RAON
2. Current status of ISOL facility
3. ISOL beam commissioning
4. Summary & future Plan

## Slide 9
RAON ISOL facility
U fission target for 80 < A < 160 neutron-rich isotope production and delivery
Driver using Cyclotron : proton 40<K<70 MeV, up to 0.75 mA
Target: UCx & non-fissile target (SiC, BN, MgO, LaC2, TiC, CaO etc)
Ion source : SIS. RILIS, FEBIAD
Pre-mass separator, Rm ~400
RIB: 10< K< 60 keV, up to 40 pi mm mrad, 108 pps(Sn), > 90% purity @Exp.
RFQ-Cooler/buncher + EBIS charge breeder
A/q separator, RA/q ~250
10 keV/u, A/q<6 to RFQ of post accelerator (SCL3) for RIB acceleration
Remote handling system for TIS/module
‘19. 10 ~ ‘21.05 | ISOL system installation and performance tests
’21.11 | ISOL system integration using a stable beam
’22.10 ‘22.11 | 70 MeV Cyclotron SAT ISOL stable beam commissioning with Sn1+, K1+, Na1+and Cs1+ using SIS and RILIS
‘23.01 ‘23.03~ | Cyclotron beam commissioning Initial beam commissioning using a SiC target

## Slide 10
ISOL system layout
Cyclotron
Target station
Pre-sep
FODO
RFQCB
EBIS-CB
CLS
MMS
A/q Sep.
FODO
RIID
Laser
UCx target room
TIS assembly
TIS module test room
Used TIS storage
Module storage
Hotcell
On-line test facility
(1)
(2)
(3)
(4)
(5)
(6)
(7)
< First basement floor >
ISOL Experimental hall
TIS/module remote operation
& maintenance area

## Slide 11
70 MeV Cyclotron
Specifications of 70 MeV Cyclotron
< Cyclotron & beam transportation line >
Energy | 40 ~ 70 MeV
Max. proton intensity | 750 uA
Simultaneous extracted beams | 2
Injected H- current | 10 mA (H-), Multicusp IS
Number of sectors | 4
Hill field | 1.6 Tesla
Harmonic mode | 4
Frequency (fixed) | 62 MHz
Total weight | 140 tons
Cyclotron dia. | 3.8 m
Cyclotron Cro-pumps | 6
40~70 MeV proton, 0.75mA max with two beam lines connecting to ISOL bunker (two target station)
Schedule
Contract(’19.6), pre-survey(’19.11), Design finalized (’20.4), FAT (’21.6) , Shipping(’21.8), Installation completed(’22.4.28), SAT(’22.10)

## Slide 12
SAT of 70 MeV Cyclotron
bunker A
Beam stability and uniformity test at ISOL target position of bunker-A
- 40 MeV & 70 MeV / beam diameter 2 cm & 5 cm / Wobbling on & off
- using BPM & beam dump
Max. beam power test at ISOL bunker B : 5 hours at 50 kW
bunker B
ISOL bunker-A
ISOL bunker-B
Beam dump
Collimator
(50 mm, 20 mm)
BPM (2 wire X, Y scan)
Beam dump (50 kW)
Beam line transmission > 96% FC: 25 μA at bunker A & bunker B
Maximum Beam current : 711.8 μA @ 5hours, stability > 95 %
Beam wobbling : beam uniformity < ±10 % (@ 20 mm)
Wall
Wall

## Slide 13
10 kW target ion-source
TIS was benchmarked on SPES(INFN) & ISOLDE system
Target container & disks
Ta Heater
< Thermal distribution & power deposition of 10 kW UCx targets >
< TIS system >

## Slide 14
10 kW UCx target fabrication
 | MWCNT |  | sintered density (g/cm3)
 | Avention (wt%) | Nanocyl (wt%) | 
virgin U3O8 | 100 | 0 | 2.96±0.01
 | 95 | 5 | 2.37±0.12
 | 90 | 10 | 2.07±0.10
 | 80 | 20 | 1.66±0.17
< UCx density according to MWCNT composition >
Density | Thickness | Diameter | Number of disks | Total uranium mass thickness
~2.5 g/cm3 | 1.3 mm | 50 mm | 18 | 5.32 g/cm2
Manufacturing of UCx/MWCNT target prototype
U3 O8 + 19C 3UO2 + 18C + CO2 (600 ~ 1,000℃)
3UO2 + 18C 3UC2 + 6C + 6CO (1,250 ~ 2,000℃)
* Manufactured at KEPCO-NF in Korea
< UCx target microstructure (before(L) and after(R) heat treatment) >
* UCx fabrication procedure was based on Nano-UCx of CERN-ISOLDE

## Slide 15
Non-fissile target
Characteristic test results for SiC targets
< Thermal shock test (3 cycle) and SEM image >
Diffusivity
Emissivity
Weight loss
< Heat treatment result at 1,800 ℃, 8h >
Grain size distribution
#1
#4
#3
#4
#3
#2
SiC target manufacturing (for RI beam commissioning) : Density 1.7~2.0 g/cm3, grain size < 1 um, thick. 1.3 mm
Non-fissile target preparation

## Slide 16
ISOL RILIS Laser system
Laser system for laser ion source
< Laser ionization scheme of Sn >
< Laser system and setup>
Laser | ㆍTi:Sa Laser (4), Nd:YAG Laser (1)
Specification | ㆍPump laser power : 100 W @ 532 nm ㆍFrequency tuning range : 750 ~ 940 nm ㆍClean booth : 4.2 m x 4.2 m x 2.4 m
< Laser beam transport >
to TIS
Laser Room
Laser pass ~25m

## Slide 17
RI production module in ISOL bunker
< RI production module system in ISOL bunker >
TIS module / Proton beam module / RI beam module
Movable concrete blocks filled up around the modules inside the bunker
All module in ISOL bunker is removed and mounted with precise alignment within 1 mm remotely
Remote operation and TIS exchange in hot cell
Quick line connection/disconnection by person access
Radio-activated vacuum exhaust gas treatment system
※ TIS module benchmarked ISAC(TRIUMF) system

## Slide 18
RI production module in ISOL bunker
Proton beam module is composed of Wire grid, F-cup, Collimator and BPM for minimum beam losses between TIS and cyclotron
Distance between collimator and ISOL target : ~1.2m  X-Y slit was located in front of TIS chamber
Beamline remotely connected/disconnected by pillow seal
< TIS & Front-end system >

## Slide 19
TIS remote handling system
RHS in Target hall

## Slide 20
ISOL Beam separation and transport system

## Slide 21
Beam diagnostics for ISOL beamline
Wire scanner
Faraday cup
Wire grid
Pepper-pot
Scintillator
Slit
Beam selection
point for AQ separator
Beam selection point for pre-mass separator
For beam tuning
1. Tuning using stable beam such as Cs, K,…
- FC, Wire scanner, Wire Grid, Beam viewer, Emittance meter
2. Changing magnetic field of MD
3. Tuning for RIB
- Plastic scintillator(50x50x50 mm3) covered by thick aluminum
- Low intensity beam monitor of MCP (max. 106 pps)
< Typical diagnostic chamber >
< Position for beam diagnostics >
< Plastic Scintillator + Aluminum layer + PMT >

## Slide 22
RIID Station
< RIID Station >
10~80 keV RI identification at ISOL beamline γ-spectroscopy (HPGe)
RI stop position move using Linear Guide
Tape speed (linear guide) > 2.5m/s (position resolution <1 mm)
< The first RI ID with HPGe (’23.3.2) >
After 2 days

## Slide 23
1. Introduction to the RAON
2. Current status of ISOL facility
3. ISOL beam commissioning
4. Summary & future Plan

## Slide 24
Stable beam commissioning
40 mm
20 mm
<F1 beam viewer >
< Beam size measurement by F2 slit >
< Sample preparation in TIS chamber >
Beam emittance of TIS extracted Cs beam
X(2σ) : 15 π mm mrad
Y(2σ) : 17 π mm mrad
First ion beam extraction test in ISOL on-line (133Cs1+ with energy of 20 keV)
Beam transport efficiency from RI module to F1 is ~100%
Mass resolving power of Pre-mass separator is ~1,000
2.11 nA
2.06 nA
1.19 nA + K1+, Na1+

## Slide 25
Stable beam commissioning
Sn beam separation and charge breeding
< Result of mass scan >
< Sn bunching beam profile from RFQCB >
< A/q spectrum for 120Snn+ >
< Charge state distribution of 120Snn+ >
< Beam profile of 120Sn1+ delivered to RFQ-CB (in M6 wire scanner) >
In EBIS,
SC magnet 6T
E-gun 1A
Breeding time 40 ms
Cooling time ~100 ms
Repeatation rate 10 Hz

## Slide 26
Stable beam commissioning
Sn beam transport to end of ISOL beamline
< Resolving power of A/q spectrum >
 | Current [A] | Number of ions | Transmission from previous point | Transmission from EBIS
EBIS Magnet | 5.40E-9 | 2.34E+7 | - | -
after A/q Separator | 4.35E-9 | 1.88E+7 | 80.50 % | 80.50 %
after Deflector | 4.25E-9 | 1.84E+7 | 97.70 % | 78.70 %
at End | 4.07E-9 | 1.76E+7 | 95.76 % | 75.37 %
Beam transport efficiency from EBIS to end of beamline

## Slide 27
Purpose of the RAON ISOL system
Experimental procedure
RI beam commissioning
stable beam tuning using 39K1+ with energy of 20 keV
optimization of proton beam (70 MeV, 1 ~ 1.4 uA) delivered to a SiC target (using a collimator, beam diagnostics and a double slit in front of target)
beam extraction from TIS and mass separation of RIBs
RI beam measurement & decay test using a scintillator + PMT
RIB transport to RIID for RI confirm

## Slide 28
Purpose of the RAON ISOL system
SiC targets for initial RI experiments
RI beam commissioning
[1] R.G. Munro, J. Phys. Chem. Ref. Data, Vol 26, No 5, 1997
< Release time of Na isotopes for density and grain size >
Characteristic analysis results of SiC commissioning targets
25Na
20Na

## Slide 29
Purpose of the RAON ISOL system
transport a low-power proton beam to ISOL target
RI beam commissioning
Wall
< ISOL tunnel & bunker-A >
(1)
(2)
(3)
< Cyclotron beamline >

## Slide 30
Purpose of the RAON ISOL system
1st RI beam experiments using #1 SiC target (Feb. 27 ~ Mar. 15, 2023)
RI beam commissioning
Proton beam transmission - Source current : 12 μA - Stripper current, position (1) : 1.1 μ A - Cyc. beam line Faraday cup, position (2) : 1.1 μ A - Proton module F-cup, position (3) : 0.53 μA
* 50 % loss from the last faraday cup of cyclotron vault  Beamline misalignment between CYC beamline and ISOL target
RI beam measurement
- Scintillator + PMT configuration
- Scintillator : 50 x 50 x 20 mm3, BC408, covered by aluminum foil
- Signal from PMT is discriminated and with counted by Hamamatsu devices
 beamline re-alignment performed
21Na Half-life
: 22.49(4) s
25Na Half-life
: 59.1(6) s
24Na Half-life
: 14.99 h
< Measurement results and Na beam decay analysis >

## Slide 31
Purpose of the RAON ISOL system
2nd RI beam experiments (’23, May 23~)
RI beam commissioning
Beam profile at wire grid : X 35 mm, Y 30 mm (focusing condition)
Beam size at slit :
X ~20 mm, Y ~17 mm
Focusing, centering and profile change tests for proton beam using quadrupoles (Q14 & Q15)
Proton beam current : 7 μ A @ Ion Source, 1.2 uA @ Stripper, 1.2 uA @ Proton module
 > 95% beam transmission from the last faraday cup of Cyclotron vault to Proton module
< Proton beam current of 4-jaws collimator in Proton module >
< Proton beam current of 4-jaws slit in front of ISOL target >
X-Y slit current
signal line problem

## Slide 32
Purpose of the RAON ISOL system
Experimental results
RI beam commissioning
Proton beam 70 MeV, 1.2 μ A
SiC target temperature ~1,400℃ (Ta heater ohmic heating 1.8 kW)
Measured RIs (so far June 1)
< Measurement results using scintillator + PMT >
Yield :
2.4 x 106 cps
(preliminary)
Yield :
7.4 x 106 cps
(preliminary)
26mAl

## Slide 33
Purpose of the RAON ISOL system
Measured results for 20Na (half-life : 0.447.9 s)
RI beam commissioning
< Measurement result of 20Na using scintillator + PMT >
Na RIs detected by HPGe at RIID
Yield :
1.7 x 105 cps
(preliminary)

## Slide 34
Purpose of the RAON ISOL system
After completing the ISOL system installation in June 2021, the design requirements of the ISOL system were verified through the separation/transport test using a stable beam
RI production/separation tests using high- and low-density SiC targets are ongoing from March 2023
RI beams (20~22Na, 24~25Na, 26mAl isomer) were measured and confirmed using scintillator + PMT and HPGe
through the measurement of the 20Na at low power (~100W), the possibility of measuring various short-lived RI beams was confirmed
for the time being, we plan to perform RI production/release tests according to the target environment using low-density SiC target
Future Plans
2nd half of 2023: production of 26Al beam using laser ion source and delivery to MMS or CLS
1st half of 2024: start ISOL RI beam transport to SCL3 injector
plasma ion source is currently under development
from 2025, the UCx target will be used, and the beam power will be gradually increased to 5 kW
We will continue to cooperate with foreign ISOL organizations
Summary & future plan

## Slide 35
Thank you for your attention !
“We thank the international ISOL reviewers for their valuable advice and assistance”