## Slide 1
06/06/2023
○Mizuki Uenomachi1, Taisei Ueki2, Kenji Shimazoe2, Hideki Tomita3, Ryohei Terabayashi2, Tetsu Sonoda4, Momo Mukai3, Yudai Shigekawa4, Akira Sugiyama2, Sachiyo Nomura2, Takeshi Sato2
1Kyoto University, 2The University of Tokyo, 3Nagoya University, 4RIKEN
Simultaneous pH sensing and gamma-ray imaging via angular correction measurement using cascade nuclides

## Slide 2: Research Background –nuclear medicine–
Nuclear Medicine
One of medical specialty to diagnose and treat disease by visualizing metabolic and functional information from the distribution of injected radioactive drug
Conventional imaging modality
・・PET * and SPECT **
* Positron emission tomography
** Single photon emission computed tomography
PET
Positron emitter (511keV annihilation gamma-rays)
Early detection of malignant tumors
SPECT
Single photon emitters (< 400 keV)
Blood flow, molecular dynamics, antibody imaging
Detector
Detector
Gamma-rays
Glucose imaging
Receptor imaging
Coincidence
detection
18F-FDG (annihilation gamma) etc…
99mTc (141keV),67Ga (300keV), 111In (171,245keV) etc..
Tumor
cell
However, these technologies can only visualize the distribution of a radioactive drug

## Slide 3: Cascade nuclides for medical imaging
Radionuclides in nuclear medicine
PET Positron emitter | SPECT Single photon emitter | Therapy Beta- or Alpha- emitter
18F 15O 11C etc | 99mTc (140.5 keV gamma) 111In (171, 245 keV gamma) 67Ga (93, 300 keV gamma etc) etc | 131I (beta, 364 keV gamma etc) 177Lu (beta, 113, 208 keV gamma) 223Ra (alpha, 145 keV gamma etc) etc
Cascade nuclides emits two or more photons via intermediate states from a nucleus
Coincidence detection of double photons can localize a radionuclide

## Slide 4: Cascade nuclides for medical imaging
Conventional method
Coincidence method
“Estimate”
the radionuclide position
“Specify”
Coincidence
Conventional
[1] Mizuki Uenomachi et al., Sci. Rep., (2021): 13330
Our experimental results of double photon coincidence imaging [1]
We succeeded to demonstrate double photon coincidence imaging for cascade nuclides.

## Slide 5: Cascade nuclides for PAC spectroscopy
Cascade nuclides have been used to measure magnetic and electric fields in crystal structures
Perturbed angular correlation (PAC) spectroscopy
D.V Filososofv. et al., Appl Radiat Isot., (2002): 437-443
source
detector
detector
coincidence unit
+7/2
+5/2
+3/2
+1/2
-1/2
-3/2
-5/2
-7/2
+5/2
+3/2
+1/2
-1/2
-3/2
-5/2
+1/2
-1/2
γ1
±h
γ2
Z: quantization axis
Angular correlation between emitted gamma rays is changed via intermediate state by the external field
Mainly caused by nuclear quadrupole interaction with an electric field gradient
spin
111In decay
L: Angular momentum, M: Z-component of angular momentum
Distribution of gamma-ray emission possibility

## Slide 6: Objective
In this study, we demonstrated a novel imaging technology, which combines the double photon coincidence imaging and PAC principle, for detection of inter-molecular interaction in vivo.
External electromagnetic field
Coincidence detection of cascade photons
Specify the nuclide position : Imaging
Angular correlation measurement
: Extraction of local environment information
Ex.) pH, intermolecular interaction etc..
Filossofov, D. V., et al., Appl Radiat Isot., 57.3, (2002): 437-443

## Slide 7: Detector setup for angular correlation depending on pH
Detector
SiPM
+
3.2 mm
3.2 mm
2.5 mm
2.5 mm
- Scintillator : High-resolution type Ce:GAGG (fabricated by Tohoku Univ.)
8 x 8 array, pixel size: 2.5 mm x 2.5 mm, pitch size: 3.2 mm x 3.2 mm
Thickness: 4 mm
- Optical sensor : SiPM (Hamamatsu, S-13361-3050N-08)
8 x 8 array, pitch size: 3.2 mm x 3.2 mm
HR-GAGG
Signal process
- 64 ch dynamic Time over Threshold (dToT) method [2]-based circuits
Improved linearity between ToT width and energy
Low power consumption
Parallel individual readout
Data Acquisition System
[2] K.Shimazoe et al., IEEE trans. On Nuc. Sci., (2012): 3213-3217
[3] S. Sato et al., IEEE trans. On Nuc. Sci., (2021): 1801-1806
FPGA-based parallel ToT DAQ [3]
Time resolution : 128 ps
List mode data
Ch, time width, time information

## Slide 8: Experimental setup for measurement of angular correlation[4]
Experimental setup
[4] K.Shimazoe , Mizuki Uenomachi et al., Commun. Phys., (2022): 24
InCl3 Liquid tracer
(SPECT application)
pH 13 InCl3 + NaOH
pH 9 InCl3 + NaOH pH9 pH7
pH 7 InCl3 + NaOH pH9 pH4
pH 5 InCl3 + pH7
pH 3 InCl3 + pH9
pH 1.9 InCl3 solution
0.6~1MBq - 30min

## Slide 9: Measurement of angular correlation depending on pH [4]
Distribution of the emission angles
The change in angular correlation around pH 3~5 was observed.
Coincidence timing histogram
pH3 ~ 5
Correlation ratio = C coin (θ)/ C backgropund (θ)
, C (θ): Count
coincidence event
background event
background event
[4] K.Shimazoe , Mizuki Uenomachi et al., Commun. Phys., (2022): 24

## Slide 10: Why angular correlation was changed depending on pH?
Reaction with NaOH and InCl3 vs pH
Electric Quadrupole Interaction
Charge non-uniformity in nuclei interact with external field (electric gradient) and perturbed
Simulation with PHREEQC
Dominant Chelator changed depending on pH
＋
−
＋
−

## Slide 11: Demonstration of imaging and pH sensing using point sources [4]
pH of a point source was estimated by calculating the correlation ratio of 90° and 180° direction
Imaging was performed with parallel hole collimators
We succeeded to perform 111In imaging and pH estimation simultaneously
[4] K.Shimazoe , Mizuki Uenomachi et al., Commun. Phys., (2022): 24

## Slide 12: Demonstration of imaging and pH sensing using a distribution source
pH12
pH5
pH1.7
Phantom
Experimental setup
pH | Volume(μl) | Activity(MBq) | Solution
1.7 | 30 | 0.42 | InCl3
5 | 30 | 0.34 | InCl3 + NaOH + HCl
12 | 120 | 1.26 | InCl3 + NaOH
Measurement time: 32hour

## Slide 13: Demonstration of imaging and pH sensing using a distribution source
parallel hole collimator
slat hole collimator
γ1 and γ2 : coincidence event
c: Channel
t: detection time
E: Energy
Collimator configuration: Parallel hole and slat hole collimators

## Slide 14: Demonstration of imaging and pH sensing using a distribution source
Calculate 90° and 180° emission ratios only for channels that exceed the threshold of detectors with parallel hall collimators
x
y
z
(Emission ration)= R count (90°)/ R count (180°)
R count (θ): Count ratio with background correction
Emission time difference spectrum of 111In
Time difference between 171keV and 245keV [ns]
coincidence event
background event

## Slide 15: 111In Imaging results
The shape of the phantom can be determined from the imaging results.
pH12
pH5
pH1.7
Raw imaging results
Imaging results after smoothing

## Slide 16: pH imaging results
pH | Average of ratio | standard deviation
1.7 | 1.157 | 0.293
5 | 0.595(0.973) | 0.378
12 | 0.836 | 0.133
pH12
pH5
pH1.7
pH imaging results
Preliminary
Preliminary

## Slide 17: Summary and future works
We proposed a novel nuclear medicine imaging that extracts a local environment information as well as visualization of radionuclide via nuclear-spin.
We succeeded to observe the angular correlation change of 111In solution depending on pH
The demonstration of imaging and pH estimation was succeeded with parallel hole collimators-based detectors.
Future works
In vivo application: observation of pH changes when the radioactive drug is taken into a cell
Extraction of other local environment information, such as temperature, viscosity, molecular size

## Slide 18
Thank you for your attention

## Slide 19: Angular correlation changes depending on types of molecules
Psyche-DOTA vs pH7 vs InCl3
Antibody-bonding detection with photon pair