## Slide 1: ERL R&D and initiative to Launch a PERLE@Orsay TDR:
Walid Kaabi-LAL/CNRS
Journées FCC France
Paris, 14-15 novembre 2019

## Slide 2
lRf
Energy supply  acceleration
EInj
EOut = EInj
E = Einj +DE
(b ~ 1)
L = n · l + l / 2
E = Einj +DE
Deceleration = “loss free” energy storage (in the beam)  Energy recovery
Introduction- Energy recovery in RF fields
L = n · l
E = Einj +DE
E = Einj +2 DE
W. KAABI

## Slide 3
ERL concept was proposed first in 1965 by Maury Tigner [1]
[1] M. Tigner: “A Possible Apparatus for Electron Clashing-Beam Experiments”, Il Nuovo Cimento Series 10, Vol. 37, issue 3, pp 1228-1231,1 Giugno 1965
First test was done at Stanford & Los Alamos (1986) for normal conductive facilities accelerating beams at rather low power (for FELs)
Concept become only viable with recent advances in SRF technology (access to CW operation and high current beams acceleration).
Introduction- ERL concept
W. KAABI

## Slide 4
[2] J.L. Abelleira Fernandez et al, “ A Large Hadron Electron Collider at CERN: Report on the Physics and Design Concepts for Machine and Detector “, J.Phys. G39 (2012) 075001, arXiv:1206.2913
PERLE: A proposed 3 pass ERL based on SRF technology, to serve as testbed for studying, testing and validating a broad range of accelerator phenomena & technical choices for future projects.
Particularly, design challenges and beam parameters are chosen to enable PERLE as the hub for technology development (especially on SRF) for the Large Hadron Electron Collider (LHeC)[2]:
Target Parameter | Unit | Value
Injection energy | MeV | 7
Electron beam energy | MeV | 500
Normalised Emittance γεx,y | mm mrad | 6
Average beam current | mA | 20
Bunch charge | pC | 500
Bunch length | mm | 3
Bunch spacing | ns | 25
RF frequency | MHz | 801.58
Duty factor |  | CW
Introduction to PERLE:
W. KAABI

## Slide 5
PERLE in the global landscape:
PERLE
legacy, decommissioned
Operating (SC, NC)
potential future machine
planned
cERL-KEK
W. KAABI

## Slide 6
DC = lRF/2
7 MeV
DE = 80 MeV
7 MeV
1 : 3 : 5
2 : 4 : 6
dump
injector
DE = 80 MeV
2 Linacs (Four 5-Cell 801.58 MHz SC cavities)
3 turns (160 MeV/turn)
Max. beam energy 500 MeV
PERLE configuration:
Footprint: 24 x 5.5 x 0.8 m3
W. KAABI

## Slide 7
DC in arc 6 = lRF/2
7 MeV
DE = 80 MeV
DE = 80 MeV
7 MeV
1 : 3 : 5
2 : 4 : 6
dump
injector
Three passes ‘up’ to reach the maximum energy
PERLE configuration:
W. KAABI
Electron beam at maximum energy could be used for:
Elastic electron-proton scattering with polarised beam (Particle physics)
Exploration of proton densities in exotic nuclei by electron scattering (Nuclear physics)
Gamma ray production between 0.2 and 5 MeV (wide applications in Photo-nuclear physics),

## Slide 8
7 MeV
DE = 80 MeV
DE = 80 MeV
7 MeV
1 : 3 : 5
2 : 4 : 6
dump
injector
Three passes ‘down’ for energy recovery
PERLE configuration:
W. KAABI
Several benefits from this manipulation:
The required RF power (and its capital cost and required electricity) is significantly reduced to that required to establish the cavity field and make up minor losses.
The beam power that must be dissipated in the dump is reduced by a large factor.

## Slide 9
Development and further R&D toward PERLE TDR :
W. KAABI
Lattice design: optimization of arcs and switchyards lattice, study of optics tolerances, prototyping of main magnets, start to end simulation..
Development of high-average-current, low-emittance electron gun: upgrade of existent DC gun, photo-cathode development for both unpolarized and polarized electron beam.
Injection line design: design of a buncher, an SRF booster and a merger matching the injector and the main linac.
BBU study in high average current environment: cavity design optimization for an efficient extraction of HOMs considering PERLE parameters: bench pattern recombination, current threshold, cryogenic efficiency…
Design and prototyping of a full dressed SRF cavity: demonstration of level of SRF performance required in CW, high-average current environment, adequate damping of HOM.
Design and prototyping of input power coupler.
Linac cryomodule design: study the possibility of SPL cryomodule adaptation to PERLE need, complete design of a cryomodule for PERLE later.
Collective effects study: effects of coherent synchrotron radiation on beam quality, Ion cloud mitigation.
Particle tracking studies of halo formation and control of beam loss:
LLRF and feedback system development: RF control and stability under maximum practical QLoad, development of multi-bunch BBU feedback systems.
Beam diagnostics development

## Slide 10
PERLE transport optics:
Appropriate recirculation optics are of fundamental concern in a multi-pass machine to preserve beam quality. The design comprises different regions:
The Spreader optics: The beams need to be directed into the appropriate energy dependent arc. Spreaders separate vertically beams and match optics functions to arcs.
The Arc optics: Disturbing effects on beam space charge such as cumulative emittance and momentum growth have to be counteracted through a pertinent choice of the basic optics cell
The Re-combiner optics: Re-combiners and spreader are mirror symmetric.
W. KAABI

## Slide 11
Switchyard- Vertical Separation of Arcs (1, 3, 5):
87 MeV
247 MeV
407 MeV
40 cm
40 cm
Energies1 : 3 : 5
35 cm
20 cm
Dipoles: (20 and 40 cm long), B = 0.8 Tesla
LAL/IPNo – JLAB Collaboration
W. KAABI

## Slide 12
Arc optics, Arc 1 (87 MeV) as example:
15.71
0
20
0
2
-3
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
1800 Arc
2-step vert. Spreader
Arc dipoles :
4450 bends
L = 45.6 cm
B = 4.5 kGauss
2-step vert. Recombiner
Spr. dipoles:
4 450 bends
L = 20 cm
B = 9.5 kGauss
Rec. dipoles:
4 450 bends
L = 20 cm
B = 9.5 kGauss
quads: L = 10 cm G  1 kGauss/cm
Isochronous Arc
pathlength: 42 × lRF
LAL/IPNo – JLAB Collaboration
W. KAABI

## Slide 13
50.8316
0
20
0
2
-2
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Pass-1 ‘up’
7 MeV
87 MeV
167 MeV
167 MeV
50.8316
0
20
0
2
-2
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
87 MeV
7 MeV
Pass-1 ‘down’
1 pass up + 1 pass down optics:
LAL/IPNo – JLAB Collaboration
W. KAABI

## Slide 14
Bunch recombination pattern:
Basic RF structure, without recirculation: Bunches are injected every 25 ns
When recirculation occurs  bunches at different turns in the linacs:
       Ovoid bunches in the same bucket
       Recombination pattern adjusted by tuning returned arcs length of the required integer of λ
Maximize the distance between the lowest energy bunches ( & ): ovoid reducing the BBU threshold current due to the influence of HOMs kicks
Achieve a nearly constant bunch spacing: minimize collective effects
1
6
LAL/IPNo – JLAB Collaboration
W. KAABI

## Slide 15
The PERLE injector consists of:
A DC photoemission electron gun (The ALICE DC gun to be upgraded).
A bunching and focusing section: 401 MHz normal conducting buncher cavity placed between two solenoid.
A superconducting booster with five 802 MHz cavities individually feeded and controlled on amplitudes and phases.
Merger to transport the beam into the main LINAC,
Beam diagnostics to be placed between components.
Spin manipulator for the polarised electrons option.
Electron source and injector:
LAL/IPNo – STFC Daresbury- Univ. Liverpool Collaboration
Photocathodes choice:
Sb-based photocathodes (unpolarized electrons) operated at 350 kV
GaAs photocathodes (polarized electrons) operated at 220 kV
Photocathode gun
Focusing solenoids
Light box
Buncher
SRF booster
Photocathode laser choice:
Nd:YAG laser (532 nm) or Ti:Sapphire laser (400 nm).
Courtesy to Ben Hounsell
W. KAABI

## Slide 16
Electron source and injector:
Optimisation of the electrode geometry, the laser pulse spatial and temporal profile and the field in the first solenoid to preserve the emittance in the gun and first solenoid section and to reduce transverse beam size in the focusing and bunching section.
The electrode geometry optimisation was also performed so that the same electrode shape must be used for both voltages (350 and 220 kV)  Use of a mlti-objective optimisation algorithm NSGAIII.
Studies on ALICE gun upgrade to operate at up to 500 pc (B. Hounsell PhD thesis):
LAL/IPNo – STFC Daresbury- Univ. Liverpool Collaboration
Optimisation of the buncher frequency (401 MHz or 802 MHz) in order to minimise emittance growth.
Hounsell et al. «Re-optimisation of the ALICE gun upgrade design for the 500 pC bunch charge requirements of PERLE», IPAC 19, Melbourne-Australia
W. KAABI

## Slide 17
Electron source and injector:
LAL/IPNo – STFC Daresbury- Univ. Liverpool Collaboration
PERLE injector (up to the booster exit) was optimised using NSGAIII: a many objective optimisation algorithm
Variables: laser parameters, solenoid settings, buncher amplitude and phase, distances between elements and the booster cavity amplitudes and phases.
Constrains: injection energy of 7 MeV & final bunch length of 3 mm
The objectives were all minimised at the point of the booster exit. They were rms transverse emittance, rms longitudinal emittance, rms energy spread, x halo parameter and z halo parameter.
The solution was not only selected for its transverse emittance but also the shape of the bunch distributions:
For more: See the poster B. Hounsell « Status of the PERLE injector optimisation » @ERL 2019
=> The PERLE injector is capable of achieving the specification at the booster exit. The possibility of improving the bunch distributions and longitudinal phase space will be investigated (linearizing the longitudinal phase space)
Achieved bunch parameters | 
Transverse emittance/ mm mrad | 4.0
Longitudinal emittance/ keV mm | 25.1
Bunch length/ mm | 3.0
Energy/ MeV | 7.0

## Slide 18
Electron source and injector:
LAL/IPNo – STFC Daresbury- Univ. Liverpool Collaboration
Still to be done:
The final step towards a complete injector design is the merger=> Work is ongoing.
A 'first ‘ start-to-end simulation: Tracking initial particle distribution, as defined by the injector and using magnet error tolerances would validate beam transport through the entire ERL complex.
Studies on the tolerances required for the injector.
The possible options for a polarised beam injection will be considered.
Relatively short lifetimes of the photocathode impose their frequent replacement (on a daily basis for GaAs and weekly for Alkali antimonides)  Need of preparation and transfer chambers for each photocathode material. For GaAs photocathodes an existing design of photocathode preparation facility produced for ALICE could be easily implemented.
W. KAABI

## Slide 19
Cavity fabrication and test:
The first Nb 802 MHz 5-Cell cavity fabricated October 2017 at JLAB
LAL/IPNo – CERN - JLAB Collaboration
Courtesy to Frank Marhauser
W. KAABI

## Slide 20
PERLE requirements
Q0 (2k) = 3 e10 @ ~27 MV/m
Quench @ Eacc ~ 30 MV/m
Parameter | Unit | CRN5
Eacc at quench | MV/m | 30.1
Epk at quench | MV/m | 68.1
Bpk at quench | mT | 126.3
FE onset field | MV/m | ~25
FE-induced radiation(max) | mR/hr. | 0.06
Max. Q0-value | /1e10 | 4.72
Q0-value at 25 MV/m | /1e10 | 3.12
Lorentz Force Detuning | Hz/(MV/m)2 | -1.5
For more details: F. Marhauser’s talk in the FCC Week, April 2018, Amsterdam, Netherland
Cavity fabrication and test:
LAL/IPNo – CERN - JLAB Collaboration
W. KAABI

## Slide 21
Cryomodule design study:
SPL cryomodule: designed to integrate 4 elliptical 5-cells 704 MHz cavities
IPN-Orsay & CERN are studying the SPL cryomodule adaptation for PERLE.
LAL/IPNo – CERN Collaboration
Cavity string equipped with magnetic shield, CTS, cryogenic lines and thermal shield
Insertion of the complete assembly inside the vacuum vessel
Closing of the top lid and of the beam ports
Déformée du train de cavités (poids propre seul)
Max: 0.12 mm
Displacement of the cavity string alone (weight only)
Courtesy to Gilles Olivier
W. KAABI

## Slide 22
First results:
Thermal and magnetic shielding are well sized for PERLE operation parameters. Their design could be modified if needed.
Vacuum vessel could be reused without refurbishing
Input coupler designed for SPL cavity could be easily adapted to meet PERLE requirement
Further studies will define if Cryogenic lines have to be adapted
Space liberated due to cavity frequency difference give a little margin for auxiliaries integration.
Pending issues:
HOM study to define the design and the number of HOM couplers to be used for PERLE cavities.
       Risk of interference between CTS and HOM dampers
 Big impact on the decision to adapt the SPL cryomodule for PERLE or not.
Cryomodule design study:
LAL/IPNo – CERN Collaboration
W. KAABI

## Slide 23
LAL/IPNo – CERN and JLAB Collaboration
W. KAABI
HOM coupler studies
Several HOM coupler types were investigated for adaptation to the new cavity :
- Waveguide couplers could be ‘overkill’ for PERLE since 3-pass peak beam current is comparably small (< 100 mA)
- Yet, trapped TE111 and TM110 dipole modes with high impedances could be better captured with coaxial couplers (cf. Supercond. Sci. Technol. 30 (2017) 063002)
JLAB High current (HC) WG HOM coupler type

## Slide 24
LAL/IPNo – CERN and JLAB Collaboration
W. KAABI
HOM coupler studies
TM01-TEM transmission (Monopole coupling)
TE11-TEM transmission (Dipole coupling)
* Impedances are for bare cavity and the peaks are not fully resolved.
DQW HOM Coupler
The DQW HOM coupler can deliver a high value of transmission at both first higher order dipole and monopole band.
Cg = 3 mm
Cg = 1 mm
2 DQW

## Slide 25
LAL/IPNo – CERN and JLAB Collaboration
W. KAABI
HOM coupler studies

## Slide 26
Project staging strategy:
Phase 1: Installation of a single cryomodule in the first straight and three beam lines in the second (consideration motivated by the SPL cryomodule availability)
          To allow a rather rapid realisation of a 250 MeV machine.
To test with beam the various SRF components.
To prove the multi-turn ERL operation.
to gain essential operation experience.
The PERLE configuration entails the possibility to construct PERLE in stages. We propose in the following two main phases to attend the final configuration.
Phase 2: Realisation of PERLE at its design parameters as a 10MW machine:
Upgrade of the e- gun
Installation of the 2nd Spreader and recombinar
Installation of the second cryomodule in the second straight.
PERLE Phase 1 layout
PERLE Phase 2 layout
W. KAABI

## Slide 27
Project staging strategy:
Phase 1 is divided in two sub-stages:
Studies and prototyping stage: Mainly for design completion of the main sub-systems, the beam dynamics studies and the prototyping of the main components (cavity, power coupler, HOM, dipoles…). All the outcomes will be included in the PERLE Technical Design Report.
Assembly, test and installation stage: of all the subsystems according to their final design (injection line most likely without the upgrade of the DC gun, the SPL cryomodule, the 6 arcs, a spreader & a recombiner), leading to PERLE-Phase 1 configuration.
It is foreseen that phase 1 includes also the realisation of infrastructure work and the installation of equipment sized as for their final use (beam dump, cryogenics, cooling circuit, shielding, electrical power, etc.).
W. KAABI

## Slide 28
Project staging strategy:
Milestones, Timeline & Collaborator Involvement
Phase 1
Phase 2
W. KAABI

## Slide 29
Thank you for your attention