## Slide 1: Quelle stratégie de développement de nos installations de physique nucléaire?
Groupe de réflexion: physiciens et ingénieurs des labos de l’IN2P3
- Angot, Julien, LPSC - Assié, Marlène, IJCLab - Ascher, Pauline, CENBG - Beaumel, Didier, IJCLab - Blank, Bertram, CENBG - Blumenfeld, Yorick, IJCLab - Bougault, Rémi, LPC Caen - Càceres, Lucia, GANIL - Cheikh Mhamed, Maher, IJCLab - Clément, Emmanuel, GANIL - De France, Gilles, GANIL - Delahaye, Pierre, GANIL - De Oliveira, François, GANIL - Dorvaux, Olivier, IPHC - Dubois, Mickaël, GANIL - Ducret, Jean Eric, GANIL - Estienne, Magali, Subatech Nantes - Fallot, Muriel, Subatech Nantes - Flavigny, Freddy, LPC Caen - Franberg, Hanna, GANIL - Gall, Benoît, IPHC - Georgiev, Georgi, IJCLab - Grévy, Stéphane, GANIL / CENBG - Harakeh, Muhsin, KVI | - Ibrahim, Fadi, IJCLab - Jardin, Pascal, GANIL - Leblanc, François, IJCLab - Lecesne, Nathalie, GANIL - Lewitowicz, Marek, GANIL - Liénard, Etienne, LPC Caen - Lunney, David, CSNSM - Matta, Adrien, LPC Caen - MacCormick, Marion, IJCLab - Maunoury, Laurent, GANIL - Mattea, Iolanda, IJCLab - Minaya Ramirez, Enrique, IIJCLab - Orr, Nigel, LPC Caen - Porta, Amanda, Subatech Nantes - Perrot, Luc, IJCLab - Piot, Julien, GANIL - Quéméner, Gilles, LPC Caen - Serani, Laurent, CENBG - Savajols, Hervé, GANIL - Stefan, Iulian, IJCLab - Stodel, Christelle, GANIL - Thuillier, Thomas, LPSC - Verney, David, IJCLab - …
Consultation aussi large que possible
Hormis les agents du GANIL, le CEA n’a pas participé
Plusieurs sous groupes créés pour l’étude de différents scénarios
Etudes très préliminaires

## Slide 2: Radioactive ion beam facilities in France
2 facilities: ALTO @IJCLab and GANIL-SPIRAL2

## Slide 3: Photofission (installation pilote)
JCLab
Orsay
Experimental areas
500W e- sur cible UCx
Faisceaux ISOL de basse énergie
Décroissance, piégeage
Ex: 3⋅107 pps of 132Sn
1011 fissions/s
BEDO
TETRA
Identification station
PARRNe mass separator
MLLTRAP
POLAREX
LINO
Existing experiments
Experiments under construction
RILIS station
ISOL ROOM
e- LINAC
Target ion source

## Slide 4: GANIL-SPIRAL 2 – Phase 1
SPIRAL 2 LINAC
NFS
S3
DESIR
GANIL
High intensity beams of light particles and heavy ions
p, d, He (1-5mA) 30-40 MeV
Heavy ions (1-10 pµA) 14.5 AMeV
Neutron for Science
Neutrons up to 30 MeV
Experimental areas for very low energy beams: below 1 eV to 60 keV
Super Separator Spectrometer
In flight radioactive ion beams + gas cell
Fusion/transfer reactions
Experimental areas and cyclotrons: heavy ions (pµA) up to 95AMeV
SPIRAL 1 facility: RIBs from fragmentation

## Slide 5: In-flight fragmentation in LISE
GANIL: pioneer facility for in-flight fragmentation techniques
since the 80’s at LISE, SPEG and SISSI
Method still used and continuously evolving at LISE
Is an international in-flight facility a plausible upgrade plan for GANIL-SPIRAL2?

## Slide 6: Re-accelerated beams at SPIRAL 1
Stable ions up to 95 AMeV
Re-acceleration of radioactive ion beams up to 20A MeV
Heavy ion fragmentation on graphite targets
« Cyclotron d’ions de moyenne énergie »
Isotope Separation On Line (ISOL) techniques in GANIL
Since 2001
Heavy ion sources and C0
(12C up to 238U)
CSS1
CSS2
CIME
Target station
LIRAT
Ex:
6He@10keV 3⋅108pps
6He@20AMeV: 5⋅106pps
38mK@9 AMeV: 7⋅105pps

## Slide 7: Gas cell in S3 - LEB
Ex:
100Sn@30keV ~10 pps
A few pps to 105 pps
N=Z beams and
superheavies
Commissioning in 2023
Nominal intensities with A/q=7 injector
 2027
in cell (6 GHz)
in jet (400 MHz)
towards DESIR
diff. pumping
mRFQ
QMF
(m/Dm ~ 100)
RFQ
Cooler
Buncher
bender
Ar: 200 - 500 mbar
l1,2
l2
l1
in-gas-cell
Ionization
(low resolution)
EVRs
Neutralized EVRs
Photoions
in-gas-jet
Ionization
(medium resolution)
gas cell
S-shape RFQ
From S3
E~0.1 MeV/u
Pulse up
(~ 3 kV)
PILGRIM
MR ToF MS
He: 10-2 - 10-3 mbar
Entrance window
SEASON
Decay detector
REGLIS (Rare Element in Gas-jet Laser Ionisation and Spectroscopy)

## Slide 8
A/Q = 7 Injector
A/Q=7 injector
High Intensity
(HI≤ 1015 pps, p-U)
A/Q=7
7 years project: estimated cost ~12 MEuro
Construction -> End starting year+7 (2027!?)
Preliminary Definition Phase
Detailed Definition Phase
Starting year (2020!?) | Starting year+1 (2021!?) | Starting year+2 (2022!?) | Starting year+3 (2023!?)
I. Stefan Scientific Coordinator M. H. Moscatello Technical Coordinator
New injector for Linag presented in:
Spiral2 Physics Case, page 171 (2006)
A/Q=3 (existing): E<=14.5 MeV/A
A/Q=7 : E<=7 MeV/A
New line
New beamline?
not part of this project
good future opportunity
independent of S3
advantageous use of heavy
beams (Pb,U)

## Slide 9
Collaboration S3-LEB-SIRIUS-DESIR
9
A/Q = 7 Injector
9
Ions | Intensity (pµA) [A/Q=3] | Intensity [A/Q=7]
18O | 216 | 375
19F | 57 | 50
36Ar | 35 | 40
40Ar | 5.8 | 30
36S | 9.2 | 30
40Ca | 6 | 20
48Ca | 2.5 | 15
58Ni | 2.2 | 10
84Kr | 0 | 20
124Sn | 0 | 10
139Xe | 0 | 10
238U | 0 | 2.5
A/Q=7
Solidify and strengthen the existing physics plan for S3, LEB & DESIR
(see talks by L. Caceres and A. Lopez-Martens)
New opportunities
inverse kinematics, multi-nucleon transfer, fusion-fission
D. Ramos et al PRC 97, 054612 (2018)
I. Stefan et al PLB 779, 456 (2018)
Future workshop to solidify those options
✕~5
✕10x

## Slide 10
DC-280
RILAC
RRC
UNILAC
LINAG
A/Q=6 or 7
A/Q=1 and 3
+ cw-LINAC
beam intensities [particles/s]* | SPIRAL2 GANIL, Caen |  | SHE factory FLNR, Dubna | RIKEN Nishina Center Wako (Tokyo) |  | GSI Darmstadt
 | LINAG A/q=3 | LINAG A/q=7 (project) | DC-280 | RILAC | RRC (RILAC(2) as injector) | UNILAC (cw-linac project >10)
18O | 1.3x1015 | 2.3x1015 | 1x1014 | 6.2x1013 |  | 6.2x1012
19F | 3.5x1014 | 3.1x1014 |  |  |  | 
36Ar | 2.2x1014 | 2.5x1014 |  |  |  | 
40Ar | 3.1x1013 | 1.9x1014 | 6x1013 | 6.2x1013 | 5x1012 | 5x1013
36S | 5.5x1013 | 1.9x1014 |  |  |  | 
40Ca | 0.4x1014 | 1.2x1014 |  |  |  | 
48Ca 100% enriched | 0.2x1014 | 0.9x1014 | 0.6-1.2x1014 | 1.9x1013 | 1.6x1012 | 5x1012
54Cr | (5x1012) | (2x1013) | 2x1013 |  |  | 
58Ni | 1.4x1013 | 6.2x1013 |  |  |  | 1.3x1012
58Fe |  |  | 1x1013 | 6.2x1013 |  | 
70Zn |  |  |  | 6.2x1013 | 6.2x1013 | 4x1012
86Kr | 0 | 1.2x1014 |  | 6.2x1013 |  | 
124Sn | 0 | 6.2x1013 | 2x1012 |  |  | 
136Xe | 0 | 6.2x1013 | 1x1014 | 6.2x1013 | 1.6x1012 | 
238U | 0 | 1.6x1013 | 5x1010 | 1.2x1012 | 3.1x1012 | 
* 1 particle A = 6.2 x1012 particles/s |  |  |  |  |  | 
Best intensity
Relevant beams for the exiting Spiral2 program (see talks by L. Caceres and A. Lopez-Martens)
Opportunity to be developed in the future
A/Q = 7 Injector: competition

## Slide 11
Very low energy beams:
Spectroscopy of ground state properties of exotic nuclei produced at S3-LEB and SPIRAL 1
Traps, laser systems, and decay spectroscopy
2024-…
DESIR facility
Beams from S3-LEB and SPIRAL1

## Slide 12: Production at ALTO, SPIRAL 1 & S3-LEB
SPIRAL 1
ALTO
Fragmentation targets
Fusion - evaporation targets
S3
Pioneering facility for photofission
Comparable to ISOLDE for 132Sn when using p beam on n converter (~ 107pps)
Facility with unique perspectives for fusion evaporation reactions
  Projected yields are unique for N=Z nuclei
  Projected yields are very competitive for Superheavy nuclei
ISOL facility with very intense beams from fragmentation
  A<80:
    Unequalled intensities for some beams
    competitive yields for others
    Interesting estimates from the upgrade
  A>80: Interesting estimates using fusion-evaporation reactions, with a possibility of reacceleration

## Slide 13: Present situation
Today - 2020
  2 weeks to 1 month of radioactive beam time at ALTO
  3 months beam time at GANIL per year
  Includes 5 weeks SPIRAL 1 operation, 1 week beam R&D and 3 weeks LISE experiments
  ~1 new beam per year for each RIB facility (ALTO/SPIRAL1)
    With very little time for R&D, the in-beam physics program at SPIRAL 1 is difficult to prepare
    High level physics program for the next ~10 years, what about thereafter?
S3 et S3-LEB: from 2024 onwards
  Unique yields foreseen for N=Z, and Very Heavy / Superheavy nuclei
  Highly ambitious program depends on the A/q=7 upgrade (2027)
    The physics accessible offers perspectives for a part of the community
    N=Z and Superheavy nuclei require extensive beam time, DESIR program in danger at startup
SPIRAL 2 Phase 2: suspended
  Projection of unique yields for long lived fission products (132Sn)
  Rich physics program was very attractive
    No clear timescale and no resources allocated
      Loss of competitiveness compared to HIE-ISOLDE and SPES
      DESIR physics program with neutron rich nuclei will be missing
      Role of ALTO as an R&D facility for SPIRAL 2 is strongly weakened

## Slide 14
As a foreword to the following, our considerations were based on…
Bottom line
Ambitions
Optimizing the use of existing facilities and in particular SPIRAL 2
Maintaining a high quality level of scientific production
Assuming constant human ressources
Attempting to meet the desires of the community as a whole
Providing attractive facilities for original scientific production
Consolidating GANIL relations with IN2P3 labs and CEA/IRFU
Attracting new communities; developing interdisciplinary science; addressing societal questions

## Slide 15: What should we do?
Continue to dream of phase 2?

## Slide 16: 2015: analysis of the phase 2 physics program
high:
World leading
medium:
Important
contribution
Low:
Marginally
competitive or
not feasible
Présentation H. Savajols (GANIL 2025)
2015: The international context has since evolved

## Slide 17: International context – ISOL/fission
HIE-ISOLDE operational
  The EPIC project: 2 GeV upgrade, more target stations, new experimental areas…
SPES starting in 2022
TRIUMF: ISAC2
  ISAC2 p+UCx already operational
  ARIEL (photofission) will be coming up around 2023
Phase 2: 203x?
  200kW 2H impinging on C converter
  Uses 2.5kg UCx HD targets
  Aims for 1014 fissions/s
    Latest evaluation predicts 3⋅1013 fissions/s
    ENSAR/ACTILAB (2014) studies show long diffusion times from UCx HD targets
     a real penalty for short-lived isotopes
All these facilities potentially reach ~1013 fissions/s
A late phase 2 is no longer competitive
+Projets at Asian facilities
RISP(RAON), BISOL

## Slide 18: What should we do?
Continue to dream of phase 2?
  Too late, no longer competitive
  Technically cumbersome: high fission rate for comparatively modest yields
Create a new in-flight facility?

## Slide 19: International context – In-flight fragmentation
Radioactive Ion Beam Factory (RIBF) at RIKEN operational (>500M$)
  Record in-flight beam intensities; ~350A MeV beams with 4 cyclotrons
  Ongoing upgrade to multiply primary beam intensities x30 (40M$ upgrade)
FRIB coming on-line in 2022 (>500M$)
  Key Feature is 400kW beam power (200 MeV/u 5 x1013 U8/s)
FAIR 203x (>1B€)
  Will be the most advanced in-flight facility with antiprotons and nuclei from rest to 4.9A GeV
  Physics program started (“FAIR 0”)
A competitive in-flight facility seems out of reach
+Projets at other ASIAN facilities
RAON, HIAF

## Slide 20: What should we do?
Continue to dream of phase 2?
  Too late, no longer competitive
  Technically cumbersome: high fission rate for comparatively modest yields
Create a new in-flight facility?
  A competitive facility seems out of reach
Improve on what we already do (or will do)?
  LISE
    Very difficult to compete with in-flight facilities
  SPIRAL 1

## Slide 21: SPIRAL 1 estimates
Let’s imagine
  From today (2020) to tomorrow (20XX)
2001 - 2013
2020 –
With target developments

## Slide 22: SPIRAL 1 estimates
Let’s imagine
  From today (2020) to tomorrow (2020+50?)
2001 - 2013
2020 –
1 target station with 5-10 weeks/year
Present objective of ~1 new element / year

## Slide 23: SPIRAL 1 estimates
Let’s compare
Technical limitations strongly limit the pace of beam development at SPIRAL 1
100% ISOL based facility
~25-30 target ion source systems on-line per year
A. Gottberg, Proceedings of the EMIS 2015 Conference, NIMB 316
2 target stations, being extended to 4
ISOLDE today (1970-2015)
~2 - 6 target ion source systems on-line per year
1 target station
SPIRAL 1 tomorrow (20XX?)
1+ beam intensities (pps)

## Slide 24: What should we do?
Continue to dream of phase 2?
  Too late, no longer competitive
  Technically cumbersome: high fission rate for comparatively modest yields
Create a new in-flight facility?
  A competitive facility seems out of reach
Improve on what we already do (or will do)?
  LISE
    Very difficult to compete with in-flight facilities
  SPIRAL 1
    Only one target station + time sharing with the rest of GANIL strongly limits the potential of the facility
  Take advantage of improved LINAC capabilities with A/Q=7

## Slide 25: What should we do?
Continue to dream of phase 2?
  Too late, no longer competitive
  Technically cumbersome: high fission rate for comparatively modest yields
Create a new in-flight facility?
  A competitive facility seems out of reach
Improve on what we already do (or will do)?
  LISE
    Very difficult to compete with in-flight facilities
  SPIRAL 1
    Only one target station + time sharing with the rest of GANIL strongly limits the potential of the facility
  Take advantage of improved LINAC capabilities with A/Q=7
    Good idea for S3
    Also brings new opportunities for ISOL production in dedicated target stations
Planning one step ahead
  Several options based on a common preparatory stage: consolidated ISOL production
    Consolidated: not necessarily world leading, but highly competitive
    High intensity ISOL beams >106 pps are an asset for each option
  Each option aims to be world-leading
Our suggestion
YES
YES

## Slide 26: What should we do? Summary
Possible development | Analysis | 
Phase 2 | Too late | 
New in-flight facility | Out of reach | 
Improved LISE as a baseline scenario | Difficult competition from in-flight facilities | 
Improved SPIRAL 1 as a baseline scenario | Technical limitations for beam development | 
A/Q=7 | Interesting perspectives for ISOL production | 
Planning one step ahead | Preparing the next move by consolidating ISOL production at SPIRAL2 | 

## Slide 27: Prospectives nationales: a new momentum?

## Slide 28: Our suggestion
Converging views towards:
  A consolidation phase (2020 – 2030)
    Extending the use of the LINAC beams
      R&D for medical isotope production
      ISOL/Gas cell production with A/q=7
    (Photo)fission with a dedicated commercial accelerator
Production building
Goal: 1012 to 1013 fissions/s
More modest than phase 2, but potentially equivalent yields for many isotopes
Hopefully, faster to build than phase 2 – adapting ambitions to available means
Fully dedicated driver for fission would guarantee reactive beam developments
  Off-the-shelf driver ; maintenance contract with an external company

## Slide 29: Our suggestion
Converging views towards:
  A consolidation phase (2020 – 2030)
    Extending the use of the LINAC beams
      R&D for medical isotope production
      ISOL/Gas cell production with A/q=7
    (Photo)fission with a dedicated commercial accelerator
Production building
Gain in coherence of a multi-user facility:
Both DESIR and S3 physics programs become achievable
Role of ALTO as an R&D base is strengthened
Reactive beam R&D with multiple drivers and target stations
Optimised use of the LINAC becomes possible for other applications
Preparation of the ambitious phase can be done
Goal: 1012 to 1013 fissions/s

## Slide 30
Phase de consolidation
Utilisation des paquets non utilisés par NFS pour les applications médicales
Rhodotron® TT300-HE
High Energy Electron Generator
Plusieurs caves de production ISOL / gas cell avec driver dédié qui supplémente le LINAC
Réactions de fusion/transfert avec les faisceaux du LINAC
Photofission/fission induite par particule légère (p,d, 3He/4He): jusqu’à~1013 fissions/s en utilisant l’expertise d’ALTO
<10 ans

## Slide 31: Our suggestion
Converging views towards:
  A consolidation phase (2020 – 2030)
    Extending the use of the LINAC beams
      R&D for medical isotope production
      ISOL/Gas cell production with A/q=7
    (Photo)fission with a dedicated commercial accelerator
Goal: 1012 to 1013 fissions/s
Production building
Multi-user ISOL facility

## Slide 32: Our suggestion
Converging views towards:
  A consolidation phase (2020 – 2030)
    Extending the use of the LINAC beams
      R&D for medical isotope production
      ISOL/Gas cell production with A/q=7
    (Photo)fission with a dedicated commercial accelerator
  An ambitious phase (>2030)
    Three alternative scenarii
      1) Electron scattering on trapped radioactive ions
      OR
      2) Radioactive Ion Beam reacceleration up to 100A MeV
      OR
      3) Storage ring for transfer reactions
Production building
Common prerequisite
Goal: 1012 to 1013 fissions/s
Multi-user ISOL facility

## Slide 33
Phase plus ambitieuse
1 option au choix…
Concept de cyclotron
C400 ARCHADE
Réaccélération à ~100 AMeV
Physique in-beam aux énergies de Fermi
Anneau de stockage à ~10 AMeV
Réactions de transfert et physique atomique
Ex:
TSR @HIE-ISOLDE
M. Grieser et al,
EPJ ST 207
Diffusion d’électrons (~500-750 MeV)
Sonde électromagnétique pour les noyaux
exotiques : (e,e’), (e,e’p), fission, etc.
10 m
40 m
e- intensity
100-200 mA
Design préliminaire:
Chancé
(CEA)
GANIL 2025

## Slide 34: Detailed study of the scenarii
Consolidation phase
  Adapting the ambitions to the desired timescale
  A step-by-step approach for a production building is possible
    Allowing successive upgrades of target stations
    Adapting the fission rate to relatively easy-to-achieve objectives
    Re-visiting the preparatory studies of SPIRAL 2 phase 2
Ambitious phase
  Selection of the best scenario for the whole community
    Requires a detailed investigation of the physics cases
      Scientific impact?
      How universal are these? Do they serve the community as a whole or, only part of it?
      What is the international context?
    Requires a detailed feasibility study
These studies require time, and this time will have to be allocated in the laboratories
In the following we only expose general ideas!

## Slide 35
e- scattering on radioactive nuclei
Motivations (pres. F. Flavigny)
Incomparable spatial sensitivity  more constraining for theory
Covers or complements a vast range of nuclear physics interests
Strategic advantages:
Uniqueness - No overlap with other facilities (for now)
Could benefit from all RIB sources at GANIL
French expertise (trapping, e- acc., etc.)
Could fit inside existing buildings
Other applications with high-intensity e- beams:
  Material science, Hadron Physics, Medical Physics
Example: Energy Recirculating LINAC (ERL) + SCRIT
10 m
I(e-) = 200 mA
Technique
SCRIT-like design – trapping of radioactive ions by e- beam
Targeted Luminosity: 1029 cm-2s-1
  Ions piégés: 106
  Ie : 200 mA
  Energie: 500-750 MeV
  sx,sy at IP: 10-10 m2
  ERL demonstrator necessary: L = 1027-28 cm-2s-1
  Possibility: PERLE @ Orsay - synergy with particle physics
     R&D + 1st Physics towards optimal machine at GANIL
Preliminary study
CEA (GANIL 2025)
No showstoppers
multi-turn

## Slide 36
Nuclear reactions in a heavy-ion storage ring at GANIL
The CRYRING at GSI/FAIR
Beam cooling  Excellent energy and position resolution of the beam (emittance ~0.05 mm·mrad), maintained after each passage through the target, negligible straggling effects.
Use of ultra-thin in-ring gas-jet targets ~1013-1014/cm2. Effective target thickness increased by ~106 due to revolution frequency (at 10 A MeV).
Pure targets, pure beams, (no backing, no contaminants)!
The E* resolution is only limited by the detector resolution.
Target-like reaction residues with very low energies can be detected.
Beam-like reaction residues can be separated with the ring dipoles.
Cooling time 200 ms - 1 s
Challenge: Detectors in Ultra-High Vacuum (10-11-10-12 mbar)
Beam
10 A MeV, ~ 1 MHz
Nuclear structure : transfer reaction with post accelerated Spiral1, S3 and possible future FF
In beam decays
Lifetime measurements
Isomer selection  nuclear reactions with pure isomeric beams
Astrophysics : (n,g) by surrogate reactions, (p,g), (a,g)
Atomic physics
M. Grieser et al., EPJ Special Topics 2017(2012)1

## Slide 37: Reacceleration to intermediate energies (10~100A MeV): physics case
Geant resonances - ACTAR
Pick up and Stripping – MUGAST/GRIT
COULEX; PDR - PARIS
Equation of State – FAZIA/INDRA
Great expertise from GANIL with the physics in this energy range
Wide physics program, very well adapted to the topic “Compact stars and matter at extreme conditions (F. Gulminelli)
only RAON in Korea has long term projects at this energy using ISOL beams, no definite time scale
Optimal use in GANIL of the ‘SPIRAL 2 detectors’: ACTAR, FAZIA, GRIT, PARIS…
Competition of beams slowed down at in-flight facilities (OEDO …) but with much higher optical qualities

## Slide 38: Reacceleration to intermediate energies (10 – 100A MeV): Cyclotron or LINAC
Superconducting Compact Cyclotron
  K1600 (for instance inspired from C400 for ARCHADE shown above):
    Q>27 for Xe at 70A MeV
    Requires state-of-the-art charge state booster (EBIS or ECRIS)
  Readily available SCC from KVI or NSCL?
  How much transmission?
The possibility to inject in the GANIL cyclotrons has additionnaly to be studied (requires stripping)
Could be inspired from the EURISOL LINAC
Simultaneous acceleration of different charge states (to be studied)
Expensive option: achievable energy depends on length…
Where within GANIL-SPIRAL 2?

## Slide 39: Working groups – what follow-up?
Phase 1 de SPIRAL 2
Phase de consolidation
  Autres faisceaux que la fission
  Photofission à la ALTO
  Applications médicales
Phase ambitieuse
  Option diffusion d’électrons sur noyaux radioactif
  OU
  Option ré-accélération de qqs 100 keV à 100 AMeV
  OU
  Option anneau de stockage d’ions
Ces études, mêmes préliminaires, sont une restitution des souhaits, idées ou attentes de notre communauté
Nous suggérons qu’elles soient transmises au groupe d’experts qui évaluera les options pour le futur du GANIL
Nous suggérons en outre qu’elles soient approfondies dans les mois prochains par les personnels scientifiques et techniques qualifiés pour en évaluer plus précisément la pertinence et la faisabilité

## Slide 40: Summary – our suggestion
Possible development | Analysis | 
Phase 2 | Too late | 
New in-flight facility | Out of reach | 
Improved LISE as a baseline scenario | Difficult competition from in-flight facilities | 
Improved SPIRAL 1 as a baseline scenario | Technical limitations for beam develp’t | 
A/Q=7 for ISOL production | Rich and coherent perspectives for existing communities; attractive for new communities / interdisciplinary research | 
Multi-user ISOL facility |  | 

## Slide 41: Summary – our suggestion
A/Q=7 for ISOL production | Rich and coherent perspectives for existing communities; attractive for new communities / interdisciplinary research | 
Multi-user ISOL facility |  | 
Consolidation phase 2021-2030

## Slide 42: Summary – our suggestion
A/Q=7 for ISOL production | Rich and coherent perspectives for existing communities; attractive for new communities / interdisciplinary research | 
Multi-user ISOL facility |  | 
electron scattering | New probe for nuclear structure | ?
10A MeV storage ring | Transfer reactions at their very best | ?
Re-acceleration to 100A MeV | Rich physics program up to Fermi energies | ?
Consolidation phase 2021-2030
Ambitious phase - 1 of the 3 options - 2030 -…

## Slide 43: Backup

## Slide 44: Estimated timescale

## Slide 45
N = Z
LOI
S3 workshop (June 18)
Science with A/Q=7 injector : impact for N=Z physics
Known masses

## Slide 46
N = Z
LOI
S3 workshop (June 18)
A/Q = 3
Science with A/Q=7 injector : impact for N=Z physics
Known masses

## Slide 47
N = Z
LOI
S3 workshop (June 18)
Known masses
A/Q = 3
A/Q = 7
Science with A/Q=7 injector : impact for N=Z physics
Access to nuclei unavailable for other facilities
The most relevant beams: 48Ca, 50Cr, 58Ni

## Slide 48: SHE Physics Cases
252Rf
256Sg
257Sg
268Sg
272Hs
276Ds
276Cn
12 Letters of intent for S3
1 Letter of intent for DESIR
people.physics.anu.edu.au/
272Ds
Map nuclear structure
Bridge the gap between hot and cold fusion
Probe the limits of stability
SHE synthesis
Opportunity to produce a new element
N=126
N=162
N=152
Z=100
A/Q=3
A/Q=7
A/Q=3
A/Q=7
A/Q=7
Science with A/Q=7 injector: SHE physics – A/Q=3 & 7 compared
S3 unique advantage => dM/M<1/300
Notes: Flash setups here

## Slide 49
https://groups.nscl.msu.edu/frib/rates/fribrates.html
https://u.ganil-spiral2.eu/chartbeams/
 | I S3 (A/Q=3) | I S3 (A/Q=7) | FRIB1 | FRIB2 | FRIBFinal
100Sn | 6,70 | 34 | 0,08 | 0,40 | 3,25
101Sn | 170 | 850 | 3,40 | 17 | 136
97In | 0,26 | 2,60 | 0,00 | 0,00 | 0,00
98In (g.s) | 1,07 | 11 | 0,04 | 0,19 | 4,10
98In (iso) | 1,53 | 15 | 0,06 | 0,28 | 5,90
99In (g.s.) | 80 | 800 | 4,49 | 6,25 | 267
99In (iso) | 80 | 800 | 4,49 | 6,25 | 267
100In | 740 | 7400 | 389 | 1950 | 15600
98Cd | 3600 | 18000 | 851 | 4260 | 88700
97Cd(g.s) | 19 | 95 | 11 | 54 | 172
97Cd (iso) | 19 | 95 | 11 | 54 | 172
96Cd (g.s.) | 2,96 | 15 | 0,41 | 2,08 | 76
96Cd (iso.) | 0,84 | 4,18 | 0,10 | 0,53 | 19
95Cd | 0,38 | 1,90 | 0,01 | 0,04 | 1,94
94Ag (g.s.) | 136 | 680 | 0,10 | 0,48 | 27
94Ag (iso. 7+) | 524 | 2618 | 0,37 | 1,83 | 105
94Ag (iso 21+) | 16 | 82 | 0,01 | 0,06 | 3,29
95Ag | 870 | 4350 | 52 | 258 | 12500
91Pd | 81 | 405 | 0,05 | 1,32 | 31
92Pd | 810 | 4050 | 2,86 | 14 | 1600
90Rh(g.s.) | 210 | 1050 | 0,10 | 0,49 | 74
90Rh(iso) | 18490 | 92450 | 0,60 | 2,99 | 452
91Rh(g.s.) | 7500 | 37500 | 141 | 705 | 85500
91Rh(iso) | 7500 | 37500 | 141 | 705 | 85500
92Rh(g.s.) | 2222 | 11109 | 7583 | 37964 | 1883700
92Rh(iso.) | 78 | 391 | 267 | 1336 | 66300
88Ru | 820 | 4100 | 16 | 80 | 12000
86Tc | 18 | 90 | 20 | 100 | 2380
87Tc | 180 | 900 | 1380 | 6890 | 605000

## Slide 50: Rôle de la diffusion, effusion et ionisation
ISOLDE
  Temps de réponse: diffusion et effusion
  Efficacité d’ionisation/formation de molécule
A. Gottberg, Proceedings of the EMIS 2015 Conference, NIMB 316
Spallation
Fission « chaude »
Challenges: produire des éléments chimiques réfractaires/isotopes de temps de vie courts

## Slide 51
La phase 2 n’est pas nécessairement la solution technique la plus évidente
  200kW d sur convertisseur carbone
    3⋅1013 fissions/s, avec un but affiché de 1014/s
  2.5kg UCx HD
    Etudes menées dans le cadre d’ACTILAB / ENSAR montrent que la diffusion sera pénalisante pour les isotopes courts temps de vie
    relative inutilité d’avoir autant de fissions dans la cible
  Solutions alternatives existent
    Exemple: fission induite par ions légers (type SPES):
    d à 40 AMeV (1kW) à SPIRAL 1 (cas théorique, pas acceptable dans l’installation actuelle)
    1.4⋅1012 fissions/s, facteur 20 par rapport à SPIRAL 2 phase 2

## Slide 52: Calculated intensities
Release (Diffusion + effusion): PARRNe data
Optimistic assumption for SPIRAL 2 large targets
Target aging in the case of SPIRAL 1 to consider
Chart: Accelerated Kr isotopes intensities (pps)
| 85 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100
I (pps) SP2 200kW | 1041467.0184 | 137395335.9935 | 664774551.2607 | 1532344461.9224 | 3030700598.2688 | 3220119487.9892 | 1879187617.2703 | 671604581.0815 | 112406231.8958 | 12766670.4099 | 1453879.2813 | 105236.3443 | 5063.6265 | 155.0706 | 1.3156
I (pps) SP2 50kW | 71825.3116 | 9475540.4133 | 45846520.7766 | 105678928.4084 | 209013834.3634 | 222077206.0682 | 129599146.0186 | 46317557.316 | 7752153.9239 | 880460.0283 | 100267.5366 | 7257.6789 | 349.2156 | 10.6945 | 0.090731
I (pps) 2H 40AMeV | 12039273.1673 | 89419709.2082 | 181155491.8026 | 159912265.5535 | 163859683.1822 | 88459100.6719 | 49838940.7159 | 16245427.3471 | 5938078.9245 | 1121510.3694 | 686858.9744 | 117675.7456 | 28044.7005 | 8559.3568 | 0
SPIRAL 1: 2H at 80 MeV
1kW - 1.4 1012 fissions/s
Résultats WP2 GANIL 2025
Calculs dont la validité reste à vérifier
Exemple de chaîne isotopique plutôt favorable

## Slide 53
Strong request (shutdown of research reactors)
Neutron source using the SP2 converter
  Designed for SP2 Phase2
  40 MeV; 5 mA d (200 kW)/proto 50 kW (1.25 mA)
  Converter (200 kW): 1012 n/cm2.s
  Non reactor based
Une source de neutrons compact a SP2?

## Slide 54: Une source de neutrons compact a SP2?
Neutron converter
  Neutron Converter: 1012 n/cm2.s
  Rotating wheel (400-600 turns/min) with graphite as converter material
  Working temperature up to 1850 °C
  Radiation cooling 50 kW (tested)
  Focusing ~1pi forward angles
  Neutron irradiation
  Neutron radiography
  Radioelements
  Material science

## Slide 55
Structure en temps sélecteur de paquets en LME
Kicker+déviateur en LHE
Pas 99% mais 60% de la puissance « récupérée »
Probablement plus simple côté LHE (voir sûreté)
Des opportunités multipliées pour SPIRAL2
SAFARI
Future salle interdisciplinaire
Nouveau kicker