Study of shower profile
for a test beam
Jan Blaha
Laboratoire d'Annecy-le-Vieux
de Physique des Particules
MicroMegas Physics Meeting
LAPP, 18 May 2009

---
Calorimeter configuration
Geometry:
25 planes (50 cm of Fe (3 λ) in total)
Passive layer: 2 cm of steel absorber (0.12 λ thick)
Active layer: 6 mm (3 mm of gas), steel cover was not used
Calorimeter dimension: 30x30x65cm3
Readout:
Chamber with 32x16 pads (1cm2 cell size)
Data:
Electron and pions: 1, 3, 6, 10 GeV
(100 000 events for each energy)
19/05/09
 J. Blaha

---
Longitudinal profile: pions
Longitudinal energy profile and energy fraction in shower (Fe abs, 3 )
Nb of planes
Cal. Depth []
Cal. Depth []
Normalized Edep Edep
Fraction Fraction

---
Lateral profile: pions
Lateral energy profile, energy fraction in shower, and mean radius
Lateral distance [mm]
Lateral distance [cm]
Lateral distance [cm]
Lateral distance [cm]
Normalized energy density Energy density
Yield [a.u.] Fraction

---
Longitudinal profile: electrons
Longitudinal energy profile and energy fraction in shower (Fe abs, 3 )
Cal. Depth []
Cal. Depth []
Normalized Edep Edep
Fraction Fraction

---
Lateral profile: electrons
Lateral energy profile, energy fraction in shower, and mean radius
Lateral distance [mm]
Lateral distance [cm]
Lateral distance [cm]
Lateral distance [cm]
Normalized energy density Energy density
Yield [a.u.] Fraction

---
Comparison: pions vs electrons
Longitudinal and lateral energy shower profiles for 3 GeV electrons and pions
Lateral distance [mm]
Lateral distance [cm]
Cal. Depth []
Normalized Edep Edep
Normalized energy density Energy density

---
Comparison: pions vs electrons
Longitudinal and lateral energy fraction in shower for 3 GeV electrons and pions
Fraction Fraction
Fraction Fraction