## Slide 1: A Proposal for the Timing Distribution System in Hyper-Kamiokande
stefano russo 17/10/19 LPNHE Paris

## Slide 2
From Yoshinari Hayato for WG4 presentation

## Slide 3
From Yoshinari Hayato for WG4 presentation

## Slide 4
From Yoshinari Hayato for WG4 presentation

## Slide 5: What Do We Need?
The requirements calls for a bidirectional data exchange link
The requested bandwidth seams low (not exactly defined yet)
Extra bandwidth can be useful
The goal is to implement a synchronous, phase deterministic protocol with as large as possible bandwidth

## Slide 6: How Do We Implement it?
R&D already started!
Many solutions are under consideration but 2 of them seam promising
CERN White Rabbit
Custom solution

## Slide 7: How Many Nodes?
8k large single PMT in the outer detector
20k large single PMT in the inner detector
Up to 20K multi-PMT spheres in the inner detector
320 FE for the outer detector
800 FE for the large PMTs inner detector
800 FE for the multi-PMTs inner detector
HK PMTs numerology :
HK FE numerology :
Each Front-End gathers signals from 25 PMTs

## Slide 8: CERN White Rabbit
Single master many slaves
The master receives GPS’s signals, generate a clock and distributes it
Propagation delay actively compensated
Synchronization requires very few bandwidth (~400 Bps)
White Rabbit node can talk with standard ethernet nodes
18 ports white rabbit switches are ”of-the-shelf”
CERN distributes hardware and firmware design and support them
Fully deterministic gigabit ethernet-based solution to distribute data and time

## Slide 9: CERN White Rabbit
A possible architecture
WR switch
FE
…
25
FE
…
25
8
…
DAQ
8 links
WR switch
FE
…
25
FE
…
25
8
…
…
8 links

## Slide 10: Custom Solution
Point-to-point
Each master can receive GPS’s signals or signal from clock fanout generate a clock and distributes it
Synchronization doesn’t require any data bandwidth
Slave’s clock phase delay is proportional to the signal propagation
Custom FE link with tailored bandwidth
DAQ link is standard (i.e. 10Gbps ethernet)
Concentrator connections depends on the requested bandwidth
Hardware and firmware design is custom
Based on FPGA’s ser-des fixed phase locking system

## Slide 11: Custom Solution
A possible architecture (assuming 1Gbps to FE)
Custom Concentrator
FE
…
25
FE
…
25
8
…
DAQ
10 Gbps Eth
Custom Concentrator
FE
…
25
FE
…
25
8
…
10 Gbps Eth
Alternative CLK fanout

## Slide 12: Cost Estimation
White Rabbit
28.000 large PMTs (inner + outer)
(1.120/8) x 5.300 = 742.000 euro
4.000 multi-PMT
(160/8) x 5.300 = 106.000 euro
20.000 multi-PMT
(800/8) x 5.300 = 530.000 euro
TOTAL COST
Baseline: 1.038.800 euro
Extra 4.000 multiPMT: 148.400 euro
Extra 20.000 multiPMT: 742.000 euro
Total cost is calculated adding 20% contingency and 20% spares
Custom Solution
28.000 large PMTs (inner + outer)
(1.120/8) x 4.000 = 560.000 euro
4.000 multi-PMT
(160/8) x 4.000 = 80.000 euro
20.000 multi-PMT
(800/8) x 4.000 = 400.000 euro
TOTAL COST
Baseline: 784.800 euro
Extra 4.000 multiPMT: 112.400 euro
Extra 20.000 multiPMT: 560.000 euro

## Slide 13: Summary
White Rabbit
Pros
Very good timing distribution performances.
Very reliable since is developed and supported by CERN.
Cons
Higher price
Custom Solution
Pros
Link tailored to the experiment’s needs.
Lower price.
Cons
Design process is time consuming and prone to delay.