## Slide 1: Data versus simulation
Yannis, Corinne, Sabine, Thodoros, et al,
October 2019

## Slide 2
Input to the simulation
Tumulus Description
From Grigoris et al measurements to GEANT4
Inner Material Dirt with density 2.2 g/cm3, nothing else
Nb of detectors 3x2. Detector size (m) 2x0.07m 0.8m, 0.8m
Detector Rotations 10 deg in q (polar) and 188 deg in f
Detector digitization by Corrine

## Slide 3
Tumulus in CATIA
Input data file
GEANT4 approximation
The tumulus seen by the detector

## Slide 5: Reconstruction
Data
  Events are filtered by Thodoros to validate hits (ADC >200 )
  Use channel id, get coordinates in the detector system, fit a straight line in 2 directions and measure q and f in the detector system ! Reject bad tracks (see Corrine’s talk)
  ~5M events
Simulation
  Use channel id after Corrine’s digitization, fit a straight line in 2 directions and measure q and f in the detector system !

## Slide 6
True
Reconstructed
Simulation

## Slide 7: Data versus simulation
Cosmic muons angular distribution models
  Simulation is done with both polar and azimuthal angles distributions uniform
  Using a given law f(q,f) we compute for every bin q,f a weight = ratio of
  f(q,f) / uniform
  The q,f distribution from simulated muon events, after reconstruction is multiplied by the weights to obtain a new q,f distribution . In this way we can change the model without regenerating all muons with Geant4
Normalising data and simulation
  The normalization between data and simulation is computed using the total number of events above the tumulus

## Slide 9
Ratio data / simulation integrating over 1 dimension
Detector center at H=1,06m and 10 deg polar rotation

## Slide 10
We make the ratio of Data / (Normalized weighted simulation events)
When ratio = 1 means it means > 1 !!!!

## Slide 11
Detector center at H=1,5m
Detector rotated by 13 deg

## Slide 12: Conclusions and projects
We need a reliable muon angular distribution in open sky
  Use backward tracks
Very close to a final data / simulation comparison
Think the future