## Slide 1
Claudia Nones
CEA IRFU – Saclay
CUPID-Mo
December 11th, 2019
Fourneaux, France
CUPID-Mo
inauguration

## Slide 2
Outline
Structure and assembly
Technical performance
Background discussion
Prospects

## Slide 3
CUPID-Mo collaboration
7 countries, 15 institutions, 90 collaborators
arXiv:1909.02994v1 – commissioning paper – accepted by EPJC
arXiv:1911.10426v1 – first data including background – TAUP 2019 proceedings

## Slide 4
Outline
Structure and assembly
Technical performance
Background discussion
Prospects

## Slide 5
The CUPID-Mo demonstrator
CUPID-Mo in a nutshell
20 100Mo-enriched (97%) Li2MoO4  2.3 kg of 100Mo
20 Ge light detectors
5 towers with 4 detectors each
EDELWEISS set-up @ LSM (France)
History of the installation
Installation in cryostat: January 2018
First cryogenic problem (1K pot valve) delay
First commissioning: Spring 2018
Second cryostat failure: Summer 2018
- long time to fix cryogenics
- take advantage to improve light detector
performance (change NTD, add reflectors)
Second commissioning: Winter 2019
Cooling water problem up to March 2019
From April 2019 in steady data taking with satisfactory performance
CUPID-Mo
Phase I
EDELWEISS

## Slide 6
Low thermal gradient Czochralski
Crystals are grown with a special technology with the following features:
Low thermal gradient with respect to traditional Czochralski (0.05 – 1 C/cm)
Fully closed platinum crucible (70×130 mm)  monitor growth by weight
Grow rate: 0.5 – 0.75 mm/h (a boule is grown in about 10 – 12 days)
Double crystallization is applied  the second step crystallization is made from the outcome of the first step and form the scraps of the preceding final element preparation  crucial to reduce K content
Li2MoO4 crystals are produced at the Nikolaev Institute of Inorganic Chemistry, Novosibirsk, Russia
Enriched material from ITEP, Moscow, Russia (previously used in NEMO-3)
J. Mat. Sci. Eng. B 7 (2017) 63-70

## Slide 7
Single-module
Four modules in each tower
Five towers: 20 heat & 20 light channels
Absorber: Li2100MoO4 - Ø 44 x 45 mm, 210 g
Light detector: Ge wafer Ø 44 mm x 170 mm with antireflective SiO coating on both sides
NOSV copper holders
PTFE for thermal and mechanical coupling
CUPID-Mo: detector details
X20
Notes: 56% e’ molibdeno
56% x 90% in 100Mo

## Slide 8
Conception, realisation and tests of above-ground prototypes done at CSNSM and CEA/DPhP
Designed by CEA/SPEC, realisation at the LAL mechanical workshop
Design and realisation

## Slide 9
Gluing: performed in a temporary clean room at CSNSM
Cleaning, bonding and assembly: performed in a LAL clean room (class 1000 and 10)
Gluing, cleaning, bonding, assembly

## Slide 10
20 modules
side view
crystal-side view
light-detector-side view
5 towers in the cryostat
top view
Detector details and installation

## Slide 12
Scheme of installation – channel status
CUPID-Mo
*Heavy noise related not to the detector but to the read-out line
High energy calibration
Low energy calibration
Light detector calibration

## Slide 13
Outline
Structure and assembly
Technical performance
Background discussion
Prospects

## Slide 14
EDELWEISS cryostat in Modane
CUPID-Mo took advantage of the cryogenics, electronics, DAQ developed for EDELWEISS

## Slide 15
Pre-commissioning @ 20 & 19.25 mK Jan 5th – Feb 28th
Commissioning @20.7 mK Mar 23rd – Apr 8th
Neutron activation Apr 9th
Physics data taking @ 20.7 mK Apr 15th – Oct 9th
@ 21.0 mK Oct 10th – Nov 7th
@ 22.0 mK Nov 8th – now
CUPID-Mo data taking
L. Marini, this inauguration
analyzed up to now
Notes: very good we are awesome
change the info on the total\analyzed exposure
Three things: energy res
discrimination
radiopurity

## Slide 16
Pulses: basic features
Pulse time parameters
Sensitivity and
signal-to-noise ratio
Large dispersion: to be understood
Light detectors are calibrated using X-ray fluorescence induced by a high-activity 60Co source used by EDELWEISS for the regeneration of the ionization detectors.
Notes: very good we are awesome
change the info on the total\analyzed exposure
Three things: energy res
discrimination
radiopurity

## Slide 17
Heat-channel calibration
DEFWHM = 5.3 keV @ 2615 keV
(0.2 %)
Summed calibration spectrum
for 19/20 Li2MoO4 bolometers
 all the major peaks are labeled.
The inset shows a fit of the 208Tl g peak at 2614.5 keV.
DEFWHM = 7.7 0.4 keV @ 3034 keV
Thorite source:
Th + U lines
Linearity
Calibration above 2615 keV is necessary  56Co campaign
(extrapolated)
Notes: very good we are awesome
change the info on the total\analyzed exposure
Three things: energy res
discrimination
radiopurity

## Slide 18
Scatter plot zoology
> 99.9% a rejection with > 99.9% b/g acceptance for all the 20 channels
Light vs. Heat and a rejection
HEAT 
LIGHT 

## Slide 19
Radiopurity of Li2100MoO4
Exposure: 0.5 kg  y
Looking the a region:
Minimal cuts (pile-up cut)
> 97% signal acceptance
Estimate contamination in ± 15 keV window
210Po (210Pb)  158(3) mBq/kg
190Pt  0.37(15) mBq/kg
Degraded alphas [3,4] MeV:
0.16(2) counts/kev/kg/y
Contamination for both Th- and U-series are  10 x better than assumed in CUPID preCDR
U:  0.5 mBq/kg
Th:  0.3 mBq/kg
arXiv:1911.10426v1 – TAUP 2019 proceedings

## Slide 20
CUPID goals achieved
With a view to CUPID, technical detector performance in terms of energy resolution, a rejection power and internal radiopurity has been achieved by CUPID-Mo
FWHM  5 keV
> 99.9% a rejection
< 1 mBq/kg
U, Th
M. Pavan, this inauguration

## Slide 21
Outline
Structure and assembly
Technical performance
Background discussion
Prospects

## Slide 22
CUPID-Mo total background
TAUP data – 0.54 kg  y
ROI accessible (zero background)
3034 keV  50 keV
new data – 0.86 kg  y
ROI blinded
More details: L. Marini, this inauguration

## Slide 23
CUPID-Mo total background
Exposure: 0.54 kg  y
Adding new data
b < 1.410-2
c/keV/kg/y
in 3084-3200 keV
2984-3084 keV
L. Marini, this inauguration
1.4 kg  y

## Slide 24
Background components
60Co collimated external source
or localized internal source ?
Rate in the 2615 keV peak
(CUPID-Mo / R&D before CUPID-Mo) 0.66 / 1.1(2) cnts/day/kg
To be compared
-CUORE-0  0.08 cnts/day/kg -CUPID-0  0.14 cnts/day/kg
-CUORE  0.013 cnts/day/kg
We have 232Th contaminated connectors close to the detectors (from EDELWEISS readout)
Challenge
Simultaneous absorption of 2614 keV and 583 keV or 510 keV from 208Tl

## Slide 25
Outline
Structure and assembly
Technical performance
Background discussion
Prospects

## Slide 26
CUPID-Mo as a 0n2b experiment

## Slide 27
100Mo nuclei: 1.37 × 1025
ROI = 10 keV
Efficiency = 69%
CUPID-Mo as a 0n2b experiment

## Slide 28
Final considerations
CUPID-Mo in the most important demonstrator for CUPID since it tests directly the selected technology
It has clearly demonstrated that the LMO bolometric performance is adequate (energy resolution + alpha rejection)
It has shown that LMO crystals with ernriched molybdenum can be grown with a radiopurity level an order of magnitude better than CUPID requirements
It is potentially the most sensitive ever neutrinoless double beta decay experiment on the promising isotope 100Mo
The program of CUPID-Mo is to take data until the end of February 2020, in order to set the best limit on neutrinoless double beta decay half life of 100Mo and to develop an accurate background model
March 2020 will be dedicated to a 56Co gamma calibration with peaks at energies higher than the Q-value of 100Mo
Final considerations

## Slide 29
BACK UP

## Slide 30
Light-detector calibration
Notes: very good we are awesome
change the info on the total\analyzed exposure
Three things: energy res
discrimination
radiopurity

## Slide 31
The EDELWEISS cryostat was conceived to detect WIMPs looking at a signal in the keV region and is not ideal to run low-background scintillating bolometers for 0n2b
Important microphonic noise induced by the thermal machines
Instabilities of the noise conditions (it depends on closing-opening of the shield, liquid helium refill, cryostat suspension status)
AC bias – resistances higher than 1 Mohm are not tolerated
 Base temperature around 20 mK  low sensitivities
Difficult stabilization (cross-talks induced by heater signals – double response to pulser excitation) – not important for DM, critical for 0n2b
Instabilities of the base temperature – critical role of the cooling water used for thermal machine compressors and electronics
232Th internal contamination (connectors, kapton, solder, ….)
Set-up issues in Modane
Reverse geometry makes difficult the isolation of vibrations
Finally, the cryogenic infrastructure is old and would need deep refurbishing

## Slide 32
Light yield
The light yield (not corrected by light collection efficiency) reflects the tower structure
 H. Khalife, this inauguration
Additional information provided by double light detector

## Slide 33
Without
reflecting foil
With
reflecting foil
Light yield with/without reflectors
Light-yield plots with 232Th calibration
a/b separation is sufficient even without reflecting foil
Significant LY reduction without reflecting foil
( 50%)
In first assembly, after results from CUPID-Mo precursors, reflectors were not used
In second assembly, reflectors were added for a safer rejection