## Slide 1
CEPC collider ring studies in EDR
Yiwei Wang
for the CEPC Accelerator Physics Group
8-11 Apr. 2024, The CEPC workshop 2024 EU edition, Marseille, France

## Slide 2: Outline
Introduction to the parameter, lattice design and geometry
Progress of the lattice design toward the EDR by iteration between the engineering design and the accelerator physics

## Slide 3: Overall design requirement of the CEPC collider ring
SR power per beam 30 MW (50 MW upgradable), 100 km, 2 interaction points
Higgs mode hold the 1st priority and compatible with the ttbar/W/Z modes.
Compatible with SPPC: 100km, section length, two machines share the most tunnels
Tunnel in the arc regions
CEPC detectors
CEPC+SPPC complex

## Slide 4: Lattice design requirement of the CEPC collider ring
Ref: CEPC TDR, arXiv 2312.14363
Basically 2 folded symmetry
2 interaction regions @ IP1 and IP3
  crab waist collision
  local chromaticity correction for the interaction region
2 RF acceleration regions @ IP2 and IP4
  shared cavities for two beam @ ttbar, Higgs
  flexible switching between compatible modes
8 arc sections
  dual aperture dipole and quadrupole magnets
4 short straight section
  on/off axis injection regions for different modes
  beam dumping, gamma source
Providing polarized beam
SS4
SS1
SS2
SS3
SS: short straight section
one short auxiliary tunnel per km

## Slide 5
Design Parameters
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch spacing (ns) | 591 (53% gap) | 23 (18% gap) | 257 | 4524 (53% gap)
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 317/317 | 317/317 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.0/1.7 | 1.05/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (min) | 18 | 77 | 22 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch spacing (ns) | 591 (53% gap) | 23 (18% gap) | 257 | 4524 (53% gap)
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 317/317 | 317/317 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.0/1.7 | 1.05/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (min) | 18 | 77 | 22 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5
- 𝛽y∗ and emittance chosen for luminosity
- adequate bunch population Ne for the luminosity and the achievable energy acceptance for lattice design
Ref: CEPC TDR, arXiv 2312.14363

## Slide 6
Lattice of the CEPC collider ring
ttbar: β=1.04m/2.7mm, εx=1.4nm, μ=90/90 deg
Higgs: β=0.30m/1mm, εx=0.64nm,
μ=90/90 deg
W: β=0.21m/1mm, εx=0.87nm, μ=60/60 deg
Z: β=0.13m/0.9mm, εx=0.27nm, μ=60/60 deg

## Slide 7: Geometry of the collider ring
SS4
SS1
SS2
SS3
4 curved arc sections, each with a length of 10270.44 m
4 curved arc sections, each with a length of 10185.70 m
2 interaction regions (IRs), IP1/IP3, each with a length of 3337.13 m
2 linear sections for RF, IP2/IP4, each with a length of 3776.90 m
4 linear sections, each with a length of 986.84 m

## Slide 8: Beam lifetime of lattice + beam beam(s-s) + Beamstrahlung
Using an integrated simulation code in APES-T (IHEP homemade, in progress) which can implement element-by-element tracking with strong-strong beam-beam interaction and lattice*
Ref: Z. Li, Y. Zhang, K. Ohmi, D. Zhou, Y. Wang, G. Xu, paper submitted
 | Equilibrium bunch (e-) | Injected bunch (e+)
(nm) | 0.66 | 1.26
(pm) | 1.35 | 13
Bunch length (mm) | 4.1 | 1.85
Energy spread (%) | 0.17 | 0.099
 | Equilibrium bunch (e-) | Injected bunch (e+)
 | 0.66 | 1.26
 | 1.35 | 13
Bunch length (mm) | 4.1 | 1.85
Energy spread (%) | 0.17 | 0.099
The injection pattern reaches a stable state equivalent to the equilibrium collision after 2000 turns, with a lifetime of approximately 40-60 minutes (33 min required). The particle loss before stability is about 0.06%.

## Slide 9
Vertical emittance generated by solenoid field
The detector solenoid are compensated locally with anti-solenoids as the skew quadrupole will introduce additional chromaticity.
  From IP to the entrance of Q1A: ∫Bzdz cancled between the IP and the entrance of final quadrupole with strong anti-solenoid field in 1.1m to 1.9m.
    Field configuration optimized to get emittance minimum and iterate with anti-solenoid technical constraints
  From the entrance of Q1A to Q3: Bz canceled to be zero.
  From the Q3 and the last bend: the ∫Bzdz from detector only < 0.5 T*m. An short anti-solenoid will be installed next to the Q3. The fringe field configuration need to be optimized due the significant radial deviation from the Z axis to the beam line.
Detector solenoid field @ W/Higgs/ttbar
Chart: Z(m)
by Feipeng Ning
tentative, to be optimized with the evolution of the detector design
Version | ttbar | Higgs | W | Z
(pm) | 4.7 | 1.3 | 1.7 | 1.4
op. design (pm) | 0.03 | 0.26 | 0.85 | 0.67
V6 (pm) | 0.04 | 0.41 | 1.35 | 1.07
V7 (pm) | 0.04 | 0.36 | 1.20 | 0.95
Version | ttbar | Higgs | W | Z
 | 4.7 | 1.3 | 1.7 | 1.4
 | 0.03 | 0.26 | 0.85 | 0.67
 | 0.04 | 0.41 | 1.35 | 1.07
 | 0.04 | 0.36 | 1.20 | 0.95
Compensated solenoid field from IP to the entrance of Q1A
Emittance contribution from the from IP to the entrance of Q1A
by Ande MA, Yiwei Wang, Yingshun Zhu

## Slide 10: Super conducting final quadrupoles for all modes
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -142 | -142 | -95 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -57 | +65
Q2IRU | 1.5 | 4.7 | -51 | +97 | +65 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -59 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -51 | +97 | +65 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -142 | -142 | -95 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -57 | +65
Q2IRU | 1.5 | 4.7 | -51 | +97 | +65 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -59 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -51 | +97 | +65 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
The final quadrupole parameters near the IP are chosen based on a trade-off between the beam dynamics and the machine detector interface.
Constraint by the SCQ technology, the gradients of the two aperture of the SCQs should be same to get better filed quality.
  The asymmetric beta functions in the upstream and downstream of the IP will be generated by additional normal-conducting quadrupoles in the final telescope (FT).
Q1AIRU
Q1BIRU
Q2IRU
Q1AIRD
Q1BIRD
Q2IRD
Q1AIRD
Q1BIRD
Q2IRD
Q1AIRU
Q1BIRU
Q2IRU
Layout of the dual aperture SCQ final quadrupoles
Y. Zhu, C. Shen, J. Geng, H. Shi, S. Bai, Y. Wei, Y. Wang
Parameters of the twin-aperture SCQs between the IP
Notes: 加清晰区等

## Slide 11: Super conducting final quadrupoles for all modes
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -142 | -142 | -95 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -57 | +65
Q2IRU | 1.5 | 4.7 | -51 | +97 | +65 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -59 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -51 | +97 | +65 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -142 | -142 | -95 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -57 | +65
Q2IRU | 1.5 | 4.7 | -51 | +97 | +65 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -59 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -51 | +97 | +65 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
Dipole field aberration due to cross talk of the two aperture
  Three types of SCQ design are undergoing.
  Beam dynamics: integrated dipole field should be corrected
  Radiation and particle loss: maximum 450/300/200/100 gs in the good field region along the SCQs for ttbar/Higgs/W/Z modes (the requirement will be updated with simulation of an integrated model of the quadrupoles, dipole error and solenoid)
Layout of the dual aperture SCQ final quadrupoles
Y. Zhu, C. Shen, J. Geng, H. Shi, S. Bai, Y. Wei, Y. Wang
Parameters of the twin-aperture SCQs between the IP
Q1AIRU
Q1BIRU
Q2IRU
Q1AIRD
Q1BIRD
Q2IRD
Q1AIRD
Q1BIRD
Q2IRD
Q1AIRU
Q1BIRU
Q2IRU
Notes: 加清晰区等

## Slide 12: IP tuning
Waist position tuning
  Knobs: 1) final quadrupoles, 2) quadrupoles in matching section
  Constraints: and η at waist, localized and η in the matching section
Dispersion tuning
  Knobs: 1) final quadrupoles, 2) quadrupoles in dispersive region, dispersion suppressor and matching section 3) skew trims on crab sextupoles
  Constraints: η at IP, localized and η in the matching section
Yuanyuan WEI, Yiwei WANG
Preliminary result for Higgs mode
More work to be done to get the magnet parameters

## Slide 13: IP tuning
Coupling tuning
  Knobs: 1) skew coils on magnets final quadrupoles 2) skew trims on crab sextupoles
  Constraints: Coupling parameters(R1 R2 R3 R4) and ηy at IP, localized coupling parameters in the matching section
Yuanyuan WEI, Yiwei WANG
Preliminary result for Higgs mode
More work to be done to get the magnet parameters

## Slide 14: Lattice design of the ARC region
FODO cell to provide a large filling factor of dipole.
90/90 degrees’ phase advances for the Higgs and ttbar modes due to the emittance and nonlinearity cancelation.
60/60 degrees’ phase advances for the W and Z modes to fulfil the collective instability requirement.
The distance 0.35m and opposite polarity between two beams fulfill the requirement technical design of the twin-aperture of dipoles and quadrupoles.
The distribution of sextupoles for Higgs & ttbar mode allowed to select –I sextupole pairs for W &Z modes.
Dual aperture quadrupole and bend with opposite polarity in two ring
0.35m
Distribution of sextupoles

## Slide 15
Update of the ARC lattice
FODO cells in the arc to provide a large filling factor of dipole
  Dual-aperture dipoles and quadrupoles in the arc to save magnet power
  Single-aperture sextupoles for independent nonlinearity optimization of e+ e- rings
  Two kind of dipole length to use the space where no sextupoles
Single aperture magnets in the RF, injection and interaction regions
Correction of the energy sawtooth effects require adjusting range of magnets strength 2.5% with the trim coils
Running at energy up to 180 GeV
The layout of the lattice in the arc area were updated based on the space required for vacuum, BPM, magnets, and mechanical equipment.
Work undergoing
Exploring less alignment sensitivity arc lattice

## Slide 16
Magnet Power Supplies
Arc regions
  In principle, the dual-aperture dipoles and quadrupoles can be connected in series as same FODO cells in the arc. Actually powered by many power supplies due to the large scale of CEPC.
  Correctors, trim coils for the tapering, each pair of sextupoles for nonlinearity optimization should be powered independently (single-aperture)
RF, injection and interaction regions
  most magnets should be powered independently (single-aperture)
The stability requirement of magnet PS
  from the stability of the collision energy, working point, beta* and the beam lifetime.
Magnet Power Supplies | Quantity | Stability /8hours
Dipole-D-aperture | 32 | 10ppm
Dipole-S-aperture | 38 | 10ppm
Quadrupole-D-aperture | 328 | 10ppm
Quadrupole-S-aperture | 600 | 10ppm
Sextupole | 1096 | 20ppm
Corrector-H & V | 7088 | 100ppm
Trim | 11904 | 100ppm
Superconducting magnets | 88 | 10ppm
Total | 21174 | 
  Preliminary calculation show that
  the accuracy of the collision energy measurement from the HEP experiment would require better dipole stability esp. at Z pole
  The working point and beta* stability would require better quadrupole stability
Ref: Yiwei Wang, Note on the stability of power supply, 20230814, v2.1

## Slide 17
Superconducting RF System and RF Power Source
1st priority of the Higgs running and flexible switching
Stage 1: High luminosity Higgs and W; medium or low luminosity at Z
  2-cell SC RF cavities are shared by two rings for the Higgs running; Half the number of H cavities are bypassed for W and Z running.
The RF power source number is determined by the synchrotron radiation power and klystron power.
Work to be done: engineering design of the beamlines in different stages; synchrotron radiation due to errors and so on

## Slide 18: Alignment requirement
Requirement of the relative alignment accuracy of the adjacent equipment is basically 100um based on the current error correction simulation.
Simulation will be done with the long range alignment data.
Accuracy of the collider circumference due to alignment doesn’t pose an issue as the RF frequency and timing can be change slightly.
Requirement of the relative difference of the two-ring circumferences need investigation as the adjustment limited very high magnetic rigidity
  Contribution form the ARC would be limited due to the application of dual aperture dipole and quadrupole ( with order(2Pi*10s um) )
  Possible approaches: soft and long alternating bending in straight sections (prop. by G. Xu), closed orbit correction

## Slide 19
Wiggler and bends for gamma source
Comparison of the dynamic aperture with (left) and without (right) wiggler at Higgs energy.
The strength of wiggler is required by the experiment and its length is limited by the beam performance for collision.
The introduction of an additional wiggler for the SR γ-ray source leads to a slight increase in energy loss per turn ∆U0/U0 increment of 0.6%.
Synchrotron radiation effects of wiggler on beam dynamics can be mitigated by adjusting the magnet strength to accommodate the beam (COD 2um)
The reduction in luminosity due to the SR from the wiggler is ~3% as the total bunch length increasing is ~3%.
further investigation to restore luminosity will be done

## Slide 20: Summary
Update of the lattice design toward the EDR were done for several prospect with the iteration between beam physics simulation and hardware engineering design.
The beam lifetime simulation will be optimized with the updated lattice.
Work on exploring less alignment sensitivity arc lattice and simulation with the long range alignment data are undergoing.
Thanks to beneficial discussion with colleague of CEPC Accelerator Physics Group!

## Slide 21: backup

## Slide 22: EDR plans for the collider ring lattice
Further tradeoff between the collider lattice, MDI, booster to get a more adequate machine design and further improve the dynamic aperture for the bare machine.
Establish the more realistic lattice with polarization systems, energy measurement systems, the complex interaction region components, realistic finite length fringe field and so on.
Face to the engineering design, trade off the accelerator physics requirements and the technology to establish parameters for future engineering.
Improve the global corrections and emittance tuning with errors.
Investigate more static errors including effect of BPM errors and multi-field errors, the long range alignment errors and the beam-based alignment for the main magnets et al.
Investigate on the dynamic error effects and possible feedback, including the injection jitter, the power source jitter, the ground motion with realistic data from the candidate sites.
Perform tracking simulations with a realistic lattice and strong-strong beam-beam interaction, to study the effects of machine errors on the beam-beam performance and the interplay with the luminosity-tuning knobs.
Establish the detailed procedures for the first turn injection, tuning, operation, different modes switching et al. Establish the tools and soft wares for tuning and operation.

## Slide 23
Mechanical Systems
Independent support for dual aperture dipole as long length (~5m)
Independent support for dual aperture quadrupole as long length (3m)
One support per 3 adjacent sextupoles
The resolution of the support should be better than 10 um due to the sensitivity of the closed orbit to the magnets
 | Number
Mechanical Systems | 
Dipole support | 13314
Quadrupole support | 4128
Sextupole support | 1128
Corrector support | 3544
Vacuum device support | 98979
BI Support | 4254
Collimators | 120
MDI mechanical devices | 8
RF support | 100
Adjustment range and resolution of supports
Direction | Range of adjustment | Direction | Resolution
X | ≥±20 mm | X | ≤10μm
Y | ≥±30 mm | Y | ≤10μm
Z | ≥±20 mm | Z | ≤10μm